3GPP TSG-RAN WG3 #111	R3-211037

25 January-04 February 2021

Online

Agenda Item:

Source:	Nokia, Nokia Shanghai Bell - Moderator

Title:	Summary of Offline Discussion on Onbaording- Cell Access

Document for:	Approval

# Introduction

CB: # 1101_PRN_Onboarding

- Which messages carry onboarding support indication? What information is signaled (e.g. indication granularity)?

- Impact on NNFS? How RAN knows if AMF supports onboarding?

- May discuss other issues based on contributions submitted

- LS to SA2

- If there is progress, attempt to agree BL CRs

(Nok - moderator)

Summary of offline disc R3-211037

# For the Chairman’s Notes

Propose the following:

Agree TP … .

# Discussion

## Cell Access for onboarding

This section deals with access for onboarding, which is part of key issue#4 by SA2. The questions below correspond to points raised in the papers and aim to seek companies’ opinion.

Q1: Can O-NPN (Onboarding NPN) be a PLMN or an SNPN?

| Company | Comment |
| --- | --- |
| Nokia | According to SA2, O-NPN can be either a PLMN or an SNPN. We can further call them O-PLMN and O-SNPN in what follows. |
| Qualcomm | Yes to both |

Q2: Do all AMF(s) of the O-NPN necessarily support onboarding?

| Company | Comment |
| --- | --- |
| Nokia | No. only a subset of the AMF(s) may support onboarding. |
| Qualcomm | Agree with Nokia |

Q3: If answer to Q2 is “no”, which information should NG-RAN node receive about connected AMF(s) in order to enable proper selection of AMF at cell access?

| Company | Comment |
| --- | --- |
| Nokia | NG-RAN node needs to know whether AMF supports onboarding function or not. |
| Qualcomm | Agree with Nokia |

Q4: how should NGRAN node receive this information?

| Company | Comment |
| --- | --- |
| Nokia | AMF can provide this information in NG Setup Response message as proposed in tdocs 160/161. |
| Qualcomm | This is P1 in R3-210359: Onboarding support indications should be added to the NG SETUP RESPONSE message, and possibly also in configuration update messages from the AMF |

Q5: should AMF also send the SO-SNPN IDs to the NG-RAN node?

| Company | Comment |
| --- | --- |
| Nokia | We don’t see the need for this but this could be double-checked with SA2 (see below proposed LS). |
| Qualcomm | Actually this seems to have no use at all, it should be transparent to RAN. Not sure there is need to double check for now. |

UE is assumed to send the onboarding register type to the AMF over NAS and UE indicates also this over RRC to trigger NG-RAN node for proper AMF selection.

Q6: Do you think that NG-RAN node should additionally relay over NGAP Initial UE Message the “onboarding” indication received in RRC setup complete? If Yes, why?

| Company | Comment |
| --- | --- |
| Nokia | There seems no such agreement in SA2 at this time. |
| Qualcomm | This is proposed in P4 of R3-210359. A possible justification is just that it might simplify handling in the AMF. It also provides a checkpoint for ensuring consistency of the NAS and AS indications (which was used for NNSF). But for sure it is not essential or requested by SA2. |

Onboarding uses a specific “restricted PDU session” for UP remote provisioning.

Q7: Do you think that NG-RAN node shall be informed of this special PDU session at PDU Session Setup Request?

| Company | Comment |
| --- | --- |
| Nokia | We don’t see any reason why at this time. |
| Qualcomm | Cannot also see need at this point. |

Q8: Do you think that all NG-RAN nodes shall support onboarding or is it possible that only a subset of them supports onboarding?

| Company | Comment |
| --- | --- |
| Nokia | To keep it simple we think onboarding feature support should be uniform in the whole O-NPN in R17. |
| Qualcomm | It is not clear what impact this would have. The UE finds support from SIB, the SIB should be set based on OAM / availability of supporting AMFs. |

Q9: If answer to Q8 is “only a subset of NG-RAN nodes supports onboarding is possible” do you think that NG-RAN nodes should indicate to AMF whether it supports onboarding?

| Company | Comment |
| --- | --- |
| Nokia | We don’t see the need at this time. |
| Qualcomm | No, in fact it is not clear what the AMF does with this information. Non-support in the RAN basically means no SIB so nothing will happen. |

Q10: do you see the need for onboarding as a criterion for the NGAP Overload control??

| Company | Comment |
| --- | --- |
| Nokia | We don’t see the need at this time. |
| Qualcomm | This could be considered but it is not a priority item. Since it is about AMF overload, we should not go too far without checking with SA2. |

Moderator’s summary:

Majority of companies think …

Proposal 1: TP...

## Cell Access for external credentials

This section deals with access for authentication via external credentials, also called key issue#1 by SA2.

Q11: Which information should NG-RAN node receive about connected AMF(s) in order to select a proper AMF

| Company | Comment |
| --- | --- |
| Nokia | The NG-RAN node needs to receive the support of the feature of authentication by external credentials and may also receive the Group IDs of the partners. |
| Qualcomm | Nothing: this is transparent to the RAN. |

Q12: How should NG-RAN node receive this information?

| Company | Comment |
| --- | --- |
| Nokia | The NG-RAN node can receive this information from the NG Setup Response message as proposed in tdocs 160/161. |
| Qualcomm | There is no need |

Q13: Do you think that some information needs to be sent in the NGAP Initial UE Message at access time and if yes which one?

| Company | Comment |
| --- | --- |
| Nokia | We don’t see the need at this time. |
| Qualcomm | No, and there is no way to derive it either |

Moderator’s summary:

Majority of companies think …

Proposal 1: TP...

## Baseline CRs

A baseline CR is proposed for TS 38.300 in tdoc 160. Please indicate comments on it.

| Company | Comment |
| --- | --- |
| Nokia | OK as starting point. |
| Qualcomm | Could be ok but only 16.6.y. We don’t see RAN impact from subs/credentials from a separate entity. |

A baseline CR is proposed for TS 38.413 in tdoc 161. Please indicate comments on it.

| Company | Comment |
| --- | --- |
| Nokia | OK as starting point. |
| Qualcomm | Delete everything to do with external credentials. Rest could be ok. |

## Possible LS to SA2

Which question would you like to ask to SA2 for access for onboarding?

| Company | Comment |
| --- | --- |
| Nokia | Q1: Does AMF needs to indicate a list of supported SO-IDs to NG-RAN nodes in addition to “onboarding support” (in analogy with sending the list of supported GIDs for authentication with external credentials). Q2: Whether information needs to be included in NGAP Initial UE Message for the case of access for onboarding |
| Qualcomm | We don’t see the need for Q1 as there is no such requirement or associated functionality. If we are going to send an LS, we could ask about AMF overload control related to onboarding. Note that it would be possible anyway for the AMF to remove the supporting indicator. |

Which question would you like to ask to SA2 for access using eternal credentials?

| Company | Comment |
| --- | --- |
| Nokia | Q1: Whether information needs to be included in NGAP Initial UE Message for the case of authentication with external credentials. |
| Qualcomm | At most, suggest stating that RAN3 thinks there is no impact either in setup or initial UE Message procedures, and request confirmation. |

# Conclusion

The following is proposed:

Proposal 1: TP...

# References

R3-20xxxx