3GPP TSG-RAN WG3 #111	R3-211037

25 January-04 February 2021

Online

Agenda Item:

Source:	Nokia, Nokia Shanghai Bell - Moderator

Title:	Summary of Offline Discussion on Onbaording- Cell Access

Document for:	Approval

# Introduction

CB: # 1101_PRN_Onboarding

- Which messages carry onboarding support indication? What information is signaled (e.g. indication granularity)?

- Impact on NNFS? How RAN knows if AMF supports onboarding?

- May discuss other issues based on contributions submitted

- LS to SA2

- If there is progress, attempt to agree BL CRs

(Nok - moderator)

Summary of offline disc R3-211037

# For the Chairman’s Notes

Propose the following:

Agree TP … .

# Discussion

## Cell Access for onboarding

This section deals with access for onboarding, which is part of key issue#4 by SA2. The questions below correspond to points raised in the papers and aim to seek companies’ opinion.

Q1: Can O-NPN (Onboarding NPN) be a PLMN or an SNPN?

| Company | Comment |
| --- | --- |
| Nokia | According to SA2, O-NPN can be either a PLMN or an SNPN. We can further call them O-PLMN and O-SNPN in what follows. |
| Qualcomm | Yes to both |
| Huawei | Yes to both. Also in R3-210476, we list the three scenarios for UE onboarding, in the following table. Scenarios ON SO 1 SNPN0 SNPN1 2 PLMN SNPN 3 PLMN PNI-NPN |
| China Telecom | Yes, both PLMN and SNPN can be the O-NPN. |
| ZTE | Yes to both |
| Ericsson | Discussions on onboarding PLMNs are ongoing in SA2 (see SA2 email discussion). Therefore, we prefer to leave this to SA2 to conclude. |
| CATT | Yes to both |

Q2: Do all AMF(s) of the O-NPN necessarily support onboarding?

| Company | Comment |
| --- | --- |
| Nokia | No. only a subset of the AMF(s) may support onboarding. |
| Qualcomm | Agree with Nokia |
| Huawei | No, this is clearly indicated in the conclusion part in SA2 TR. - This information will be specified only for SNPN and allows NG-RAN to select an appropriate AMF that supports onboarding procedures. |
| China Telecom | No, Agree with NOKIA |
| ZTE | No |
| Ericsson | No. We agree with Nokia. |
| CATT | No. |

Q3: If answer to Q2 is “no”, which information should NG-RAN node receive about connected AMF(s) in order to enable proper selection of AMF at cell access?

| Company | Comment |
| --- | --- |
| Nokia | NG-RAN node needs to know whether AMF supports onboarding function or not. |
| Qualcomm | Agree with Nokia |
| Huawei | At this stage, this can be FFS. Either the AMF just indicates its support of UE onboarding, or indicates its supported SOs/DCSs, which can be dependent on progress of the normative phase of SA2. |
| China Telecom | Agree with Nokia |
| ZTE | It can be configured by OAM, there is no need to introduce on boarding supporting of AMF on the NGAP. Furthermore, is olny “onboarding supporting indication” enough? Whether to support onboarding is the cell level configuration parameter, which need considering certain geographical deployment factors. When OAM configure the related SIB information, OAM shall be aware of AMF supporting, so we think it will be more convenient to configure by OAM. |
| Ericsson | No. We agree with Nokia. |
| CATT | Agree with Nokia |

Q4: how should NGRAN node receive this information?

| Company | Comment |
| --- | --- |
| Nokia | AMF can provide this information in NG Setup Response message as proposed in tdocs 160/161. |
| Qualcomm | This is P1 in R3-210359: Onboarding support indications should be added to the NG SETUP RESPONSE message, and possibly also in configuration update messages from the AMF |
| Huawei | This is P2 in R3-210476: The AMF shall provide its support of onboarding to the NG-RAN in the interface management messages. The granularity of the indication (e.g., AMF node level, or SO/DCS level) can be further studied. |
| China Telecom | NG-RAN can receive the onboarding support related information of AMF during the NG Setup Procedure. |
| ZTE | No need to introduce on boarding supporting information on the NG interface, but configured by OAM. |
| Ericsson | There are 2 options: a. dynamic configuration using NGAP setup procedure b. static pre-configuration using O&M It should be FFS if dynamic configuration is justified. |
| CATT | This is P3 in R3-210104: It is proposed to include an indicator in NGAP message from AMF to NG-RAN for supporting Onboarding procedures. |

Q5: should AMF also send the SO-SNPN IDs to the NG-RAN node?

| Company | Comment |
| --- | --- |
| Nokia | We don’t see the need for this but this could be double-checked with SA2 (see below proposed LS). |
| Qualcomm | Actually this seems to have no use at all, it should be transparent to RAN. Not sure there is need to double check for now. |
| Huawei | This can be further studied, and dependent on the normative phase of SA2. (we are ok to send LS) |
| China Telecom | This information can be sent to UE through NSA signaling by AMF, it should be transparent to RAN. |
| ZTE | This can be further studied, if necessary,this can be configured by OAM. |
| Ericsson | We don’t see the need for this. This information is transparent to the RAN. |
| CATT | Agree to send LS to SA2 to check it. |

UE is assumed to send the onboarding register type to the AMF over NAS and UE indicates also this over RRC to trigger NG-RAN node for proper AMF selection.

Q6: Do you think that NG-RAN node should additionally relay over NGAP Initial UE Message the “onboarding” indication received in RRC setup complete? If Yes, why?

| Company | Comment |
| --- | --- |
| Nokia | There seems no such agreement in SA2 at this time. |
| Qualcomm | This is proposed in P4 of R3-210359. A possible justification is just that it might simplify handling in the AMF. It also provides a checkpoint for ensuring consistency of the NAS and AS indications (which was used for NNSF). But for sure it is not essential or requested by SA2. |
| Huawei | We think we can keep this question FFS (included in the LS). See our P3 in R3-210476 - It can further studied whether to indicate an “onboarding” indication or the selected SO/DCS (if available) in Initial UE message for verification. |
| China Telecom | Not needed, AMF can get this information over NSA signaling. |
| ZTE | Yes. According to 23.700-07, it is concluded that “Upon registration to an SNPN for onboarding, AMF restricts the usage when the UE indicates that the registration is for onboarding, or the UE provides an indication at RRC level that the RRC connection is for onboarding. ” It can be used for AMF to double check the UE access. |
| Ericsson | This was discussed in SA2 and we think it should be discussed together with SA2 if the AMF should be able to check the indications for consistency. |
| CATT | We are not sure that onboarding register type to the AMF is over NAS. This question may be also included in LS. |

Onboarding uses a specific “restricted PDU session” for UP remote provisioning.

Q7: Do you think that NG-RAN node shall be informed of this special PDU session at PDU Session Setup Request?

| Company | Comment |
| --- | --- |
| Nokia | We don’t see any reason why at this time. |
| Qualcomm | Cannot also see need at this point. |
| Huawei | We think we can keep it FFS at this time. See our P4 in R3-210476 - Study whether to indicate the type of PDU session for onboarding in the PDU session management procedures over NG and the bearer context management procedures over E1. |
| China Telecom | Not sure at this time. |
| ZTE | Yes. RAN shall be aware of the restricted PDU session for some RRM reason. For example, not handing over the restricted session to other cell for load balance. |
| Ericsson | We currently don’t see any justification for this. |
| CATT | It may be not necessary for NG-RAN to know it. Not sure at this time. |

Q8: Do you think that all NG-RAN nodes shall support onboarding or is it possible that only a subset of them supports onboarding?

| Company | Comment |
| --- | --- |
| Nokia | To keep it simple we think onboarding feature support should be uniform in the whole O-NPN in R17. |
| Qualcomm | It is not clear what impact this would have. The UE finds support from SIB, the SIB should be set based on OAM / availability of supporting AMFs. |
| Huawei | We think it is possible that only a subset of them supports onboarding. The standard impact include, e.g., whether the O-NPN should verify the UE access based on the on-boarding support of O-NPN nodes (which is similar to evaluation based on the cell supported CAG list in R16) |
| China Telecom | Should not, as it is a strong constraint for operator that all NG-RANs in a network should support onboarding. |
| ZTE | Agree with QC. Whether to support onboarding is the cell level configuration parameter, which need considering certain geographical deployment factors. When OAM configure the related SIB information, OAM shall be aware of AMF supporting and cell supporting.. |
| Ericsson | We don’t see a need for such a requirement. |
| CATT | We think only a subset of them supports onboarding. |

Q9: If answer to Q8 is “only a subset of NG-RAN nodes supports onboarding is possible” do you think that NG-RAN nodes should indicate to AMF whether it supports onboarding?

| Company | Comment |
| --- | --- |
| Nokia | We don’t see the need at this time. |
| Qualcomm | No, in fact it is not clear what the AMF does with this information. Non-support in the RAN basically means no SIB so nothing will happen. |
| Huawei | Yes, in case this is finally found necessary. |
| China Telecom | Not sure at this time |
| ZTE | Seem no need. |
| Ericsson | Agree with Nokia. |
| CATT | AMF may do not need the indicator now. |

Q10: do you see the need for onboarding as a criterion for the NGAP Overload control??

| Company | Comment |
| --- | --- |
| Nokia | We don’t see the need at this time. |
| Qualcomm | This could be considered but it is not a priority item. Since it is about AMF overload, we should not go too far without checking with SA2. |
| Huawei | Too early to discuss the NGAP overload control in RAN. This is dependent on the SA2 normative phase |
| China Telecom | Not sure at this time |
| ZTE | Seem no need. |
| Ericsson | Agree with Nokia |
| CATT | Maybe too early to discuss it. |

Moderator’s summary:

Majority of companies think …

Proposal 1: TP...

## Cell Access for external credentials

This section deals with access for authentication via external credentials, also called key issue#1 by SA2.

Q11: Which information should NG-RAN node receive about connected AMF(s) in order to select a proper AMF

| Company | Comment |
| --- | --- |
| Nokia | The NG-RAN node needs to receive the support of the feature of authentication by external credentials and may also receive the Group IDs of the partners. |
| Qualcomm | Nothing: this is transparent to the RAN. |
| Huawei | We can keep it FFS. This is not specified in the conclusion of SA2 TR. Wait for their progress |
| China Telecom | Agree with NOKIA |
| LGE | Agree with Nokia |
| ZTE | Nothing |
| Ericsson | Agree with Qualcomm. |
| CATT | Agree with Nokia |

Q12: How should NG-RAN node receive this information?

| Company | Comment |
| --- | --- |
| Nokia | The NG-RAN node can receive this information from the NG Setup Response message as proposed in tdocs 160/161. |
| Qualcomm | There is no need |
| Huawei | See our answer to Q11. |
| China Telecom | The NG-RAN node can receive this information from the NG Setup Response message. |
| LGE | The AMF can provide this information to NG-RAN by using NG SETUP RESPONSE message |
| ZTE | No need. |
| Ericsson | Agree with Qualcomm. No need. |
| CATT | An indicator in NGAP message from AMF to NG-RAN and/or pre-configured by OAM for supporting UE access via home SP credentials procedure. And include supported Group IDs (GIDs) in NGAP message from AMF to NG-RAN. |

Q13: Do you think that some information needs to be sent in the NGAP Initial UE Message at access time and if yes which one?

| Company | Comment |
| --- | --- |
| Nokia | We don’t see the need at this time. |
| Qualcomm | No, and there is no way to derive it either |
| Huawei | Too early to say NO at this time, better to treat as FFS. See P1 in R3-210476 - Whether to indicate the “access using external credentials” and the selected H-SP group (if available) in Initial UE message for e.g. AMF verification. |
| China Telecom | We don’t see the need at this time. |
| LGE | We don’t see the need at this time. |
| ZTE | We can keep this question FFS. |
| Ericsson | No, we don’t see a need. |
| CATT | No need |

Moderator’s summary:

Majority of companies think …

Proposal 1: TP...

## Baseline CRs

A baseline CR is proposed for TS 38.300 in tdoc 160. Please indicate comments on it.

| Company | Comment |
| --- | --- |
| Nokia | OK as starting point. |
| Qualcomm | Could be ok but only 16.6.y. We don’t see RAN impact from subs/credentials from a separate entity. |
| Huawei | Too early to have BL CR at this first meeting, especially given the fact that SA2 has not officially started their WI. Our thinking is that we have some agreements/assumptions in this meeting. |
| LGE | OK as starting point. |
| ZTE | Agree with HW. Too early to have BLCR. |
| Ericsson | To early at this meeting, we agree with Huawei. |
| CATT | Agree with HW. Too early for the first meeting. Since the impact of RAN is not clear. |

A baseline CR is proposed for TS 38.413 in tdoc 161. Please indicate comments on it.

| Company | Comment |
| --- | --- |
| Nokia | OK as starting point. |
| Qualcomm | Delete everything to do with external credentials. Rest could be ok. |
| Huawei | Too early to have BL CR at this first meeting, especially given the fact that SA2 has not started their WI. Our thinking is that we can have some agreements/assumptions in this meeting. Note that we also have R3-210477 just including UE onboarding over interface management messages. |
| LGE | OK as starting point. |
| ZTE | Agree with HW. Too early to have BLCR. |
| Ericsson | Too early at this meeting. |
| CATT | Too early to have BL CR. |

## Possible LS to SA2

Which question would you like to ask to SA2 for access for onboarding?

| Company | Comment |
| --- | --- |
| Nokia | Q1: Does AMF needs to indicate a list of supported SO-IDs to NG-RAN nodes in addition to “onboarding support” (in analogy with sending the list of supported GIDs for authentication with external credentials). Q2: Whether information needs to be included in NGAP Initial UE Message for the case of access for onboarding |
| Qualcomm | We don’t see the need for Q1 as there is no such requirement or associated functionality. If we are going to send an LS, we could ask about AMF overload control related to onboarding. Note that it would be possible anyway for the AMF to remove the supporting indicator. |
| Huawei | First we propose to have a LS to SA2, since we will have a long period till next meeting. We have provided the LS draft in R3-210476. We think we can list all possible questions to facilitate RAN’s work, including: Q3: Whether the AMF of ON just indicate its support of UE onboarding, or indicate its supported SOs/DCSs as well? Q4: Whether the ON-RAN shall notify to the ON-CN about its support of UE onboarding, and/or its supported SOs/ DCSs? Also the question on the initial UE message can be asked. |
| ZTE | The question on the initial UE message can be asked. And the following question can be asked: Q1: Whether the AMF indicate its support of UE onboarding to RAN? or it is a OAM issue? Q2: Whether the AMF indicate the restricted PDU session only for onboarding to RAN? (RAN shall be aware of the restricted PDU session for some RRM reason. For example, not handing over the restricted session to other cell for load balance.) |
| Ericsson | We don’t see a need for an LS. We can wait for the next SA2 TR update. |
| CATT | 1. Whether the NG-RAN node should know SO-SNPN IDs from AMF 2. Whether onboarding register type to the AMF over NAS |

Which question would you like to ask to SA2 for access using eternal credentials?

| Company | Comment |
| --- | --- |
| Nokia | Q1: Whether information needs to be included in NGAP Initial UE Message for the case of authentication with external credentials. |
| Qualcomm | At most, suggest stating that RAN3 thinks there is no impact either in setup or initial UE Message procedures, and request confirmation. |
| Huawei | We have provided the LS draft in R3-210476. We think we can list all possible questions to facilitate RAN’s work, including: Q1 Is the support for external credentials homogeneous among all AMFs within an SNPN, i.e. whether all AMFs within an SNPN shall support UE access with credentials owned by separate entity? Q2 Whether the SNPN-RAN shall notify to the SNPN-CN about its support of UE access using the credentials from a separate entity, and/or its supported group IDs, and/or its support of UE access that are not explicitly configured? Also the question on initial UE message can be asked. |
| Nokia | Agree with Nokia |
| ZTE | The question on the initial UE message can be asked. And the following question can be asked: Q1: Whether the AMF indicate its support of UE onboarding to RAN? or it is a OAM issue? Q2: Whether the AMF indicate the restricted PDU session only for onboarding to RAN? (RAN shall be aware of the restricted PDU session for some RRM reason. For example, not handing over the restricted session to other cell for load balance.) |
| Ericsson | Nothing needed. |
| China Telecom | Q1: Whether AMF need to indicate its support of external credential to RAN or all AMF should support the external credential? |
| CATT | Q1: whether the AMF notify NG-RAN about it support UE access with credentials owned by separate entity? Q2: whether the UE indicate it access with credentials owned by separate entity in initial UE message? Q3: whether the all AMF connected to one NG-RAN support UE access using the credentials from a separate entity |

# Conclusion

The following is proposed:

Proposal 1: TP...

# References

R3-20xxxx