3GPP TSG-RAN WG3 #111	R3-211127

25 January-04 February 2021

Online

Agenda Item:

Source:	Nokia, Nokia Shanghai Bell - Moderator

Title:	Summary of Offline Discussion on “Ethernet Compression Sync”

Document for:	Approval

# Introduction

CB: # 110_EthernetCompressionSync

- check issue

- LS to RAN2?

(Nok - moderator)

0053 rev in R3-211128

Summary of offline disc R3-211127

# For the Chairman’s Notes

Propose the following:

Agree TP … .

# Discussion

## Coordination of compression

As explained online, the issue to be checked with RAN2 is the case where CU UP decides to not run ethernet compression, but CU CP has configured the UE with ethernet compression.

RAN2 is asked if the call can continue with this de-synchronization between UE and CU UP. They can answer for DL and UL.

Situation is different than ROHC because for ethernet we have a new protocol designed by RAN2.

We need official confirmation from RAN2 whether there is an issue or not. If there is an issue we will need to find some solution to synchronize the CU UP and UE. If no issue confirmed topic is closed.

I have uploaded the LS in current draft with revised number.

Please comment on the draft LS:

| Company | Comment |
| --- | --- |
| Nokia | OK. |
| Huawei | Ok to check with RAN2. To us, it is not clear in such case, whether the CU-UP will still include the EHC header or not (in case Ethernet header compression is not performed)? if the ECH header is anyway included, maybe no issue, but if EHC header is not included by the CU-UP in such case, things are not clear.. |

Moderator’s summary:

Majority of companies think …

Proposal 1: TP...

# Conclusion

The following is proposed:

Proposal 1: TP...

# References

R3-20xxxx