3GPP TSG-RAN WG3 #111-e	R3-210964

Online, 25 January – 4 February 2021

Agenda Item:	9.3.4.3

Source:	Huawei (moderator)

Title:	Summary of Offline Discussion on PDCP SN for 4G to 5G Handover

Document for:	Approval

# Introduction

This contribution is to kick off the following discussion.

CB: # 11_DirectDataFwd_PDCP_SN_4G-5G_HO

Nok

X2AP impact: Add an indicator to the SN Release procedure to indicate if the numbering is to be removed for forwarding

HW,CATT

St2 impact: Update info note so that it is not applicable to handover from EPC to 5GC

E///

E1AP impact: target CU-UP should be aware that the Bearer Context Setup procedure is associated to an inter-system HO

SS

E1AP impact: add PDCP SN Discard Required IE to the E1AP BEARER CONTEXT Modification REQUEST message

- is st2 clarification enough or is st3 impact needed? If so, which AP?

(HW - moderator)

Summary of offline disc R3-210964

# For the Chairman’s Notes

Propose to capture the following:

Proposal 1: to be added

It is proposed to implement the proposal 1 as follows

Proposal a: to be added.

# Discussion

The discussion addresses the following informative note in TS 36.300, for the inter-RAT handover from E-UTRAN.

- NOTE:	Any assigned PDCP SNs are not forwarded because of PDCP reset.

## Phase I: Whether the note is applicable to handover from EPC to 5GC?

Generally the candidate options are provided as follows (as observed in R3-210806).

- Option 1: this note is applicable for EPC to 5GC handover.

- Option 2: this note is not applicable for EPC to 5GC handover

  - Option 2.1: The target NG-RAN node removes the PDCP SN and transmits the data to the UE

  - Option 2.2: The target NG-RAN node discards the PDCP SDUs with PDCP SN.

Possible impacts of option 1

- In R3-210806, stage 3 impacts are observed for option 1:

-	The MN sends PDCP SN not needed to the SN in SgNB Release Request message (X2AP impact).

-	The CU-CP sends PDCP SN not needed to the CU-UP in Bearer Context Modification Request message (E1AP impact)

- In R3-210450, some analysis are provided for option 1:

-	In case of EPC to 5GC handover (including EN-DC to SA handover), the target NG-RAN node can simply ignore the PDCP SN in the GTP-U header, and just forwards the PDCP packets to the UE, based on the Handover Type IE. Also in case the target node decides to setup dual connectivity or in case of split case, the no signalling of the SN status transfer can be used to hint to ignore the PDCP SNs.

-	In case the source eNB is having the dual connectivity, following the note, there is a need to indicate the peer node so that the peer node does not forward any assigned PDCP SNs. This complicates the signalling design.

Possible impacts of option 2

- In R3-210806, stage 3 impacts are provided for option 2.1

  - The CU-CP sends PDCP SN Removal to the CU-UP in Bearer Context Modification Request message (E1AP impact)

- In R3-210742, also stage 3 impacts are provided for option 2.

  - The target CU-UP should be aware that the Bearer Context Setup procedure is associated to an inter-system HO

Observation: as the first step of the discussion, the moderator think it is beneficial to decide which option is the way forward.

Please provide your view on this.

| Company | Option 1/ Option2.1/ Option 2.2 | Comment |
| --- | --- | --- |
| Huawei | Option 2.1 | It seems to us that both option1 and option 2.1 have stage 3 impacts. Though option 2.2 has no impact, the performance is a little worsen compared with the legacy inter-system handover. Of these options, option 2.1 is preferred since the change can be limited compared to the option 1. |

Moderator’s summary:

## Phase 2: Stage 2 CR (can be discussed at the 2nd round)

### Stage 2 CR for TS 36.300

In R3-210450, the update of the Note is highlighted as follows:

NOTE: Any assigned PDCP SNs are not forwarded because of PDCP reset except for handover from EPC to 5GC.

Please provide your view on this CR.

| Company | Comment |
| --- | --- |

### Stage 2 CR for TS 38.300

In R3-210451, the update is provided as follows:

In case of direct data forwarding, user plane handling for inter-System data forwarding from EPS to 5GS follows the following key principles: - For each E-RAB accepted for data forwarding, the source eNB forwards data to the target NG-RAN node in the corresponding E-RAB data forwarding tunnel. - Until a GTP-U end marker packet is received, the target NG-RAN node prioritizes the forwarded packets over the fresh packets for those QoS flows which are involved in the accepted data forwarding. NOTE: The target NG-RAN node ignores the PDCP SNs if any for those forwarded PDCP SDUs for which delivery was attempted by the source eNB.

Please provide your view on this CR.

| Company | Comment |
| --- | --- |

## Phase 2: Stage 3 CR (can be discussed at the 2nd round)

Three CRs are provided in this meeting.

Option 1:

  - Option A: R3-210088 for X2AP - An indicator is added to the SN Release procedure to indicate if the numbering is to be removed for forwarding

Option 2:

  - Option B: R3-210806 for E1AP - to add PDCP SN Discard Required IE to the E1AP BEARER CONTEXT Modification REQUEST message

  - Option C: R3-210743 for E1AP - The target CU-UP should be aware that the Bearer Context Setup procedure is associated to an inter-system HO

Please provide your views on this.

| Company | Option A/ Option B/ Option C | Comment |
| --- | --- | --- |

# Conclusion, Recommendations [if needed]

If needed

# References

- R3-210088 Enabling direct data forwarding for inter-RAT HO with SN-terminated bearers, Nokia, Nokia Shanghai Bell

- R3-210450 PDCP SN issue for EPC to 5GC handover, Huawei, CATT

- R3-210451 PDCP SN issue for EPC to 5GC handover, Huawei, CATT

- R3-210742 PDCP SNs for forwarded PDCP SDUs from 4G to 5G, Ericsson

- R3-210743 Inter-system indicator for Bearer Context Setup, Ericsson

- R3-210806 PDCP SN Handling for EPC to 5GC HO, Samsung

- R3-210840 PDCP SN Handling for EPC to 5GC HO, Samsung