3GPP TSG-RAN WG3 #111-e	R3-210966

Online, 25 January – 4 February 2021

Agenda Item:	9.3.6

Source:	Samsung (moderator)

Title:	Summary of Offline Discussion on Lossless intra-system HO

Document for:	Approval

# Introduction

CB: # 13_LosslessIntraSysHO_CP-UPsplit

Nok

The solution for lossless intra-system HO mobility for disaggregated architecture shall support scenarios involving QoS flow to DRB remapping during handover

AltB and AltC should be supported by standards for the disaggregated case to be on par with the aggregated case.

Introduce an explicit data forwarding completion indication for AltB to have performance on par with the aggregated case.

Introduce an explicit data forwarding completion indication from CU-UP to CU-CP for AltC as well to enable CU-CP to trigger the release unnecessary resources in a timely manner.

Introduce changes at E1 to support Alt C in backward compatible manner.

SS,HW,LGU+,CT,Intel

To have the same performance for aggregated and dis-aggregated scenario, Sol1 should be supported for dis-aggregated scenario.

add “Qos Flows Information To Be Updated” to the E1AP BEARER CONTEXT SETUP REQUEST messge.

CATT

introduce a new structure Data Forwarding Request list IE in E1 interface to enable the target CU-CP request data forwarding tunnel according to the flow to DRB mapping in source side in Bearer Context Setup Request message. The target CU-UP provides the data forwarding tunnel in the response message accordingly via Data Forwarding Response list IE

ZTE

Sol2 is able to guarantee the lossless handover without any impact on the existing specification

- is sol2 enough? If not, consensus for sol1? Multiple alternatives? Which release?

(SS - moderator)

Summary of offline disc R3-210966

# For the Chairman’s Notes

Propose the following:

# Discussion – Second Round

Based companies views, majority companies support Solution 1.  Therefore the proposal is:

Proposal 1: Agree Solution 1 as the basis in principle.

Continue to discuss whether explicit data forwarding completion indication from CU-UP to CU-CP.

For solution 1, the fundamental thing needed in CU-UP is Qos flow to DRB mapping information in both source and target. Among Solution 1.1, Solution 1.2 and Solution 1.3, minimal information is transmitted in Solution 1.1 and Solution 1.1 got support by more companies. The main concern is backward compatibility issue. Solution 1.1 was updated accordingly in backward compatible way. The updated CR for Rel-15 were uploaded.

Pls provide your comments on the revised CRs for solution 1.

| Company | Comments |
| --- | --- |
| Nokia | Regardless of solution 1 or 2, introduction of an indication to inform that data forwarding has completed from CU-UP to CU-CP is necessary. Thus, a general agreement is needed for these two general points: * Support for both Solution 2 and Solution 1 * Introduce an indication from CU-UP to inform that data forwarding has completed to CU-CP. Details on how to introduce these two aspects (St.3 signaling of Solution 1 and data forwarding completion) should be treated as a second step after the above agreements. In regard to the CR proposed in comeback folder for St.3 for Solution 1, we still see some issues. In our view, the proposed solution in the CR in CB folder can only work when QFIs do not overlap between different DRBs at old source and new target configurations. Otherwise it cannot be guaranteed that QoS and PDCP configuration used at source for a given DRB is still suitable for a DRB at target after remapping occurs. In other words, taking the examples in disc paper in R3-210252 Case #1 for instance, QoS and PDCP configuration at target CU-UP for “DRB2” may not be suitable after remapping. Thus, in practice the correct approach would be to establish a new bearer for target configurations that need different treatment. This in place requires the source and target configurations to be clearly delimited in the signaling from CU-CP to CU-UP with their individual QoS and PDCP configuration accordingly as proposed in Solution 1.2. |
| Intel | From our understanding, Solution 2 without explicit indication is the current behavior. So the current formulation of agreeing Solution 1 in principle and discuss further about explicit “forwarding completion” indication from CU-UP (though we agree the need for this indication) makes sense to us. Responding to Nokia’s comment about Solution 1, from our understanding, when CU-UP receives the CU-CP’s request to establish a DRB with old mapping together with the updated mapping (to be reflected after transmitting the forwarded PDCP SDUs are completed), CU-UP should consider both old mapping and new mapping together when it decides to admit this DRB. For Case #1, for DRB2, the QoS parameter for QFI2 is provided for DRB1 (here we are talking about “remapping”) and CU-UP should consider this QFI2 as well when deciding to admit DRB2. After transmitting the forwarded PDCP SDUs, the DRB should serve new fresh packets from CN with the updated mapping. CU-UP should not just take only the old mapping into account. That’s why the updated mapping is provided together to the CU-UP when establishing bearer contexts. |
| CATT | First，we would like some clarification on solution 1.For the forwarded data,when transmitted from target NG-RAN node to UE,new PDCP configuration is used or old PDCP configraution is used? Secondly,as to the CR,we still think more discussion is needed.It seems we need to have a common undersanding on the meaning QoS Flows Information To Be Setup IE.In last RAN3 meeting,in your porpsoed CR,the meaning of this IE is the current flow to DRB mapping for the DRB.With the proposal in the CR raised in this meeting,I think there is following assumption(I just copy my reply to Intel as below): If the BEARER SETUP procedure is triggerred by handover procedure with flow to DRB mapping,then legacy CU-UP would regard this IE as the old flow to DRB mapping If the BEARER SETUP procedure is triggerred by handover procedure without flow to DRB mapping,then legacy CU-UP would regard this IE the current FLOW to DRB mapping information If the BERER SETUP procedure is triggerred by UE access procedure, then legacy CU-UP would regard this IE as the current FLOW to DRB mapping information First, it seems there is no any description on that CU-UP should have different understanding on the QoS Flows Information To Be Setup IE in different cases. Secondly, even if the CU-UP would do as what described above, how could CU-UP know that the bearer setup procedure is trigger by handover or connection setup and whether there is remapping or not if it is handover procedure? Based on that, it seems it is not possible for the legacy CU-UP to behavior as what is assumed above. I think the behavior of legacy CU-UP would just use the received QoS Flows Information To Be Setup to perform flow to DRB mapping. This is also the reason we think in case of CP-UP separation, if lossless is required, the target node could only perform flow to DRB remapping after handover procedure not during handover. procedure. Then since the behavior of legacy CU-UP is to regard the QoS Flows Information To Be Setup as the current flow to DRB mapping information for the DRB,for the CR which change it as the source flow to DRB mapping,we think it is not backward compatible. |
| Samsung | Reply questions from CATT Old PDCP configuration is used in target side. RLF/MAC configuration can be new in the target side. To assure lossless handover, PDCP configuration should be not changed. The information included in Bearer Context Setup Request includes combined in formation in source and target. Even for the remapping case, the QoS Flows Information To Be Setup IE indicate the current mapping (e.g. for forwarded data). Qos Flow to be Updated will be used after some time. So QoS Flows Information To Be Setup IE has the same meaning in all cases. |

# Discussion - First Round

There was preliminary discussion on lossless intra-system handover in CP-UP separation scenario at last meeting. The agreements were copied below for reference:

- Supporting Lossless handover when a QoS flow is mapped to a different DRB at handover has been agreed before.

- For supporting lossless handover when a QoS flow is mapped to a different DRB at handover, the old DRB needs to be configured in the target cell for transmitting the forwarded packets

- The above mechanism is already supported if the target node is aggregated.

According to the submitted contributions, two groups of solutions were preferred to support “Lossless handover when a QoS flow is mapped to a different DRB at handover in disaggregated gNB scenario”.

Solution 1:  Both the old QoS flow to DRB mapping and new mapping are provided to the target CU-UP at bearer context setup. The CU-UP utilizes the old mapping until it determines that data forwarding has completed. At that point, the CU-UP switches to the new DRB configuration and transmits data utilizing the new mapping [1][2][3][4][5][6].

Solution 1bis:  Both the old QoS flow to DRB mapping and new mapping are provided to the target CU-UP at bearer context setup. The CU-UP utilizes new DRB configuration to first transmit the forwarded data from source side and then transmit the new data from CN[6].

Solution 2:  The old QoS flow mapping would be set at the target CU-UP, and then have CU-CP determine whether and when a change to the new QoS flow to DRB mapping would be appropriate to be carried out. This could take place implicitly (e.g., CU-CP estimates the required time for data forwarding to complete), or explicitly (CU-UP indicates to the CU-CP when data forwarding has completed) [1][2][7].

Which solution(s) are you ok in order to support lossless intra-system handover in CP-UP separation scenario?

| Company | solution | comments |
| --- | --- | --- |
| Samsung | Prefer Solution 1 | As explained in [3], solution 2 will bring error handling or bring interruption for data transmission The CU-CP doesn’t know when the CU-UP has finished transmiting the forwarded data to the UE. If the CU-CP sends the BEARER CONTEXT MODIFICATION REQUEST messge too early, the CU-UP may release the old configuration and use the new configuration to handle the forwarded data which will bring data loss. Alternatively the CU-UP knows when data forwarding finishes thanks to the end maker. After the CU-UP receives the end marker, it can send an indication to the CU-CP, so that the CU-CP can transmit the new DRB configuration and the new mapping to the target CU-UP and the target DU. But this will bring interuption for data transmission. Soluton 1 has no interupption and assure the same performance for dis-aggregated scenario and aggregated scenario. |
| Intel | Sol 1 | Agree with Samsung, if we want the same performance as in the aggregated case. |
| Huawei | Solution 1 | Agree with Intel that the disaggregated case can also support the QoS flow remapping during the handover, the same as aggregated case. |
| CATT | Solution 1bis. | For solution1, we have some different views. After UE access to the target node, it would use the new configuration to receive/transmit user plane data no matter the data are forwarded from source or sent from CN. Similarly, in the network, the target CU-UP should always use the new configuration to transmit data to UE, even the data is forwarded from source. So, we add 1bis as above |
| Nokia | Both Solution 2 and Solution 1 should be supported | Both Solution 2 and Solution 1 should be supported for the disaggregated architecture. Further, Solution 1 should be introduced in a backwards compatible manner. |
| ZTE | Solution 2 | As mentioned above by Samsung, “ If the CU-CP sends the BEARER CONTEXT MODIFICATION REQUEST message too early, the CU-UP may release the old configuration and use the new configuration to handle the forwarded data which will bring data loss. ” We think that it is up to the receiving side (i.e. CU-UP) to decide the time applying the new configuration. The CU-UP could keep using the old configuration until the transmission of the forwarded data is finished. After the forwarded data has been handled (CU-UP could estimate the time via end marker), the CU-UP will apply the new DRB configuration. In this case, there is no data loss. |
| Ericsson | Solution 2 | CU-CP is able to estimate, and CU-UP is able to implicitly understand that new mapping is for new packets |
| Samsung1 | Clarification to ZTE and Ericsson | CU-CP has no any clue on when the data forwarding ends in the CU-UP. The CU-UP may release the old mapping and use the new mapping to handle the forwarded data which will bring data loss. |

## How to support solution 1 in stage 3

For solution 1, three different flavours were proposed regarding how to let the CU-UP know the source mapping and the target mapping.

Solution 1.1: Add “Qos Flows Information To Be Updated” to the E1AP BEARER CONTEXT SETUP REQUEST message [3][4][5]

- The existing QoS Flows Information To Be Setup is used to transmit the source mapping.

- “Qos Flows Information To Be Updated” is used to transmit the target mapping

Solution 1.2: Add “Enhanced DRB to Setup List” IE in the BEARER CONTEXT SETUP REQUEST message. “Enhanced DRB to Setup List” is used to transmit the DRB configuration at the target side.

Add “Enhanced DRB To Setup List Used” IE in the BEARER CONTEXT SETUP RESPONSE message [1][2]

Solution 1.3: Add “Data Forwarding Request list” IE in Bearer Context Setup Request message to enable the target CU-CP request data forwarding tunnel according to the flow to DRB mapping in source side. The existing QoS Flows Information To Be Setup is used to transmit the target mapping.

Add “Data Forwarding Response list” in Bearer Context Setup Response message to enable the target CU-UP providing the data forwarding tunnel [6].

Which option do you prefer to transmit the source and target mapping to the CU-UP?

| Company | Solution | comments |
| --- | --- | --- |
| Samsung | Prefer Solution 1.1 | Comparing the three options, Solution 1.1 only impacts Bearer Context Setup Request message and doesn’t include redundant information in Bearer Context Setup Request and Bearer Context Setup Response message. |
| Intel | Solution 1.1 | Solution 1.2 looks too complicated given that all we need is to tell CU-UP to update flow-to-DRB mapping for a DRB after finishing transmitting forwarded PDCP SDUs. Solution 1.3 is not clear on how to handle between the proposed new list IE and the existing mechanism using the DRB Data forwarding information Request IE and QoS Flows forwarded on the forwarding tunnel(s) IE within, when a DRB is continued and mapping changes during HO. |
| Huawei | Solution 1.1 | Solution 1.1 is the simple solution (just add a new QoS flow list IE) Solution 1.2 seems too much complicated to have a whole new set of DRB To Setup List. Solution 1.3 could work by introducing the data forwarding request list carrying the old mapping at the source, and data forwarding Response. But it is complicated compared to solution 1.1. |
| CATT | Solution 1.3 | Solution 1.1 has backward compatibility issue since it changes the meaning of the existing IE. For example, for a legacy CU-UP, it would still regard the flow list included in QoS Flows Information To Be Setup IE as the mapping in target side while it actually refer to the mapping in the source side. In this case, there would be misalignment between network and UE. For solution 1.2,as we clarified in session 3,the target CU-UP does not need to know the old DRB configuration since it would always use the new configuration to transfer data to UE. So, we think some redundant IE are introduced which is not preferred. Solution 1.3 does not has backwards compatibility issue and also has no redundant IE. |
| Nokia | Solution 1.2 | We see backwards compatibility issues with both solutions 1.1 and 1.3. Solution 1.1 is not backwards compatible with existing CU UP which can only understand the setup of the old configuration, and not of the new and old configurations at same time. Further, CU-UP will reject the message if the “new target configuration” cannot be understood, and which is included in the proposed new QoS Flows To Be Updated IE. This unnecessary fails the procedure, and forced the CU-CP to reattempt only with the “old source configuration”, delaying the whole handover. Solution 1.3 is also not backwards compatible, given that an existing CU-UP would expect the “old source configuration” to be included using the existing QoS Information To Be Setup IE. [CATT]:I could not agree with you. CU-UP just do the flow to DRB mapping according to the Qos information to be setup IE it received. The reason we discuss this lossless intra-system handover is that target CU-UP does not have the old flow to DRB mapping information in the source side. Solution 1.2 on the other hand, allows meaning and handling of the existing QoS Information To Be Setup IE to be kept and represent the “old source configuration”, and have a new IE to indicate the “new target configuration” with criticality ignore. Similarly, a simple indication introduced in the response message indicates the CU-CP if the new IE was utilized or not. Hence this allows for any permutation of CU-CP and CU-UP support without changing behavior of existing IEs or failing procedures unnecessarily. |
| Intel2 | Responding to CATT and Nokia | @CATT, UP doesn’t care whether the requested QoS flows to be setup is for target configuration or source configuration. From my understanding, there is no principle that the meaning of the requested QoS flows to be setup is only for the target configuration. UP just tries to establish as requested or reject. Here, the solution direction of Solutions 1.1 and 1.2 are simple – establish DRBs and tell how mapping needs to be changed after finishing transmitting the forwarded PDCP SDUs. If a source DRB is continued, CP will request DRB-level forwarding for this DRB together with how the mapping should be updated after finishing transmitting the forwarded PDCP SDUs. The updated mapping will serve fresh QoS flows from CN. If CP establishes a totally new DRB (that was not in the source), CP won’t request DRB-level forwarding for this DRB and there is no need to tell how the mapping should be updated. [CATT]:I agree with you that CU-UP does not care the received the QOS flow to be setup is for old configration or new configuration.The CU-UP just do the flow to DRB mapping according to the information. With the CR in 1.1,CU-CP send the flow to DRB mapping information in the source side to the CU-UP,the legacy CU-UP would just do the flow to DRB mapping for the new date from core network which is not correct.This is the reason we think it is not backward compatible. [Samsung1]. In the specification, there is no description on whether the existing Qos information to be setup IE indicates the target mapping or the source mapping, we should assume one anyway. @Nokia, I don’t think that Solution 1.1 is not backward compatible. Having “reject” doesn’t mean it is not backward compatible. But you are right that UP will reject if it doesn’t comprehend the new IE, and then CP has to try establishing again. But this can be easily fixed (i.e. changed to “ignore”) by introducing an indicator in the response from UP like Enhanced DRB To Setup List Used IE in your CR. |

For the scenario that the number of DRBs in the source side is more than the number of the DRBs at the target side, some DRB(s) is only used for data forwarding. When data forwarding ends, the resource for those DRB(s) could be released. [1][2] proposed to introduce an explicit data forwarding completion indication from CU-UP to CU-CP to enable CU-CP to trigger the release unnecessary resources in a timely manner.

Proposal: Introduce an explicit data forwarding completion indication from CU-UP to CU-CP

Do you agree the proposal?

| Company | option | Comments |
| --- | --- | --- |
| Samsung |  | It could be acceptable in order to release the unnecessary resources timely. |
| Intel |  | I think this indication is needed. Regardless of whether CU-UP is allowed or not allowed to autonomously release an old DRB that is no longer used (after it receives end-marker for that DRB tunnel and finishes transmitting forwarded PDCP SDUs), CU-CP needs to tear down this old DRB in the UE side. In terms of stage-3, a new class-2 procedure seems more appropriate rather than enhancing the class-1 CU-UP initiated Bearer Context modification procedure. |
| Huawei | Not necessary | In E1AP, the class 2 procedure (Bearer Context Inactivity Notification) is already there to indicate the inactivity in a DRB/PDU session level. With the solution 1.1, the CU-UP would know some DRBs are only used for data forwarding case. When it receives the end marker for the DRB, it can trigger this class 2 procedure. |
| CATT | Not necessary | For the case that some DRB configured in the source side is removed in the target node, following option 1 in session 3, we don't think the DRB would be established in the target. For example, if there is DRB1(flow 1) and DRB 2(flow 2) configured in the source side while only DRB 1(flow 1 and flow 2) is configured in the target, the UE could only be configured with DRB1. If DRB 2 without flow included is established when UE access to the target side and then is released after transmission of forwarded data is completed, we think it is better to keep the mapping unchanged and then do remapping afterwards. Anyway, reconfiguration to UE is needed for both of the options while there is no extra signaling impact for the latter. |
|  |  | Regardless of Solution 2 or Solution 1, this is needed. CU-CP needs to know when data forwarding has completed in order to correctly trigger a reconfiguration and modify/release existing/unnecessary DRBs, and which is triggered toward CU-UP, DU, and UE. In regard to how this can be introduced, either existing procedure or a new class 2 procedure are acceptable. Similarly, reuse of Bearer Context Inactivity Notification procedure (proposed above by Huawei) will not solve any issue. This existing procedure has multiple levels of monitoring inactivity. Even if “per DRB” were to be used, this will lead to hanging resources, as well as possibly further dragging unnecessary DRBs to yet another node if another handover is executed prior to receiving this indication. |
| Ericsson | Not needed | CU-CP is able to estimate, and CU-UP is able to implicitly understand that new mapping is for new packets |

## How to support solution 2 in stage 3

For solution 2, two different flavours were proposed regarding how to let the CU-UP know the source mapping and the target mapping.

Solution 2.1: Add “explicit data forwarding completion indication” to the E1AP BEARER CONTEXT MODIFICATION REQUIRED message [1][2]

Solution 2.2: No stage 3 change [7]

Solution 2.3: Add a new Class 2 procedure to explicitly indicate to CU-CP that data forwarding has completed.

If solution 2, which option do you prefer?

| Company | option | comments |
| --- | --- | --- |
| Samsung |  | Solution 2.2 doesn’t solve the problem. As explained in [3]. The CU-CP doesn’t know when the CU-UP has finished transmiting the forwarded data to the UE. If the CU-CP sends the BEARER CONTEXT MODIFICATION REQUEST messge too early, the CU-UP may release the old configuration and use the new configuration to handle the forwarded data which will bring data loss. |
| Intel |  | If CU-CP didn’t configure both old and new mapping when establishing bearer context in the CU-UP, then I think this can be used as an alternative to timely configure new mapping for a DRB (though having some interruption compared to Solution 1 family). And again, in terms of stage-3, a new class-2 procedure seems more appropriate. |
| Huawei | Neither option | For solution 2.1, in E1AP, the class 2 procedure (Bearer Context Inactivity Notification) is already there to indicate the inactivity in a DRB/PDU session level. |
| Nokia | Solution 2.1 or 2.3 | Regardless of Solution 2 or Solution 1, this is needed. CU-CP needs to know when data forwarding has completed in order to correctly trigger a reconfiguration and modify/release existing/unnecessary DRBs, and which is triggered toward CU-UP, DU, and UE. In regard to how this can be introduced, either existing procedure or a new class 2 procedure are acceptable. Similarly, reuse of Bearer Context Inactivity Notification procedure (proposed above by Huawei) will not solve any issue. This existing procedure has multiple levels of monitoring inactivity. Even if “per DRB” were to be used, this will lead to hanging resources, as well as possibly further dragging unnecessary DRBs to yet another node if another handover is executed prior to receiving this indication. |
| ZTE | Solution 2.1 or Solution 2.3 | Our intention is that the CU-CP could estimate the data forwarding completion by implementation. While, based on the above analysis by companies, the explicit indication for data forwarding completion should be considered to support the Solution 2, regardless of reusing the existing procedure or introducing a new procedure. |
| Ericsson | 2.2 | 2.1/2.3 will also add delay and therefore data interruption |

# Conclusion, Recommendations [if needed]

If needed

# References

| [1] R3-210146 | Discussion on Lossless intra-system HO in disaggregated architecture (Nokia, Nokia Shanghai Bell) |
| --- | --- |
| [2] R3-210147 | Lossless intra-system HO in disaggregated architecture (Nokia, Nokia Shanghai Bell) |
| [3] R3-210252 | Lossless intra-system HO in disaggregate gNB scenario (Samsung, Huawei, LGU+, China Telecom, Intel Corporation) |
| [4] R3-210253 | Correction of intra-system HO in CP-UP separation scenario (Samsung,Huawei, LGU+, China Telecom, Intel Corporation) |
| [5] R3-210254 | Correction of intra-system HO in CP-UP separation scenario (Samsung,Huawei, LGU+, China Telecom, Intel Corporation) |
| [6] R3-210290 | Support of data forwarding for intra-system HO in CP-UP Separation Scenario (CATT) |
| [7] R3-210797 | Discussion on Lossless Intra-system HO in CP-UP Separation Scenario (ZTE) |