3GPP TSG-RAN WG3 #108-e	R3-210969

Online, 1-11 June 2020

Agenda Item:	20.1.

Source:	Huawei (moderator)

Title:	CB: # 24_NTN_general - Summary of email discussion

Document for:	Approval

# Introduction

This is Summary of offline discussion on CB: # 24_NTN_general - Summary of email discussion.

Please provide your view and correction in the document uploaded by 28th Thursday CET 10am.

Thursday a first status will be provided online with an update, some first agreements and a Way Forward (WF) for next step, if any.

The discussion is in 2 sections, first the update of the BL CR including the new proposal and how to proceed on RAN2 overlap.

# For the Chairman’s Notes

TBC:

Recommendation for online session Thursday keep the CB open and continuing the review of R3-21xxxx_BLCR_update

# Discussion

## Stage 2 update

All proposals from [1 to 6] are merged in single document R3-21xxxx_BLCR_update_v0 available in the draft folder. It is propose to work on this document directly.

Please raised you concern on the question below only if there is major objection on proposal in the document:

Please note that the R3-210361 [8] proposes an alternative (or possible merge) way to capture last meeting agreement on NR CGI fixed on geographical area for ULI as alternative of R3-210703. Only the first sentence should consider in the proposal for the agreement see (4.x.3 Signalling)

Question #1: Is there any major comment against the BL R3-210014 [1]?

| Company | Comment |
| --- | --- |
| Thales | To be at least aligned with RAN2 stg2 running CR in R2-2100229. Note that HIBS abbreviation should be removed since only HAPS is considered as per RAN agreements endorsed in RP-202907 |
| Nokia | The definition for Transparent Payload somehow only describes one-way communication and claims there will always be frequency conversion. Suggest change it to: Transparent payload: NTN payload that filters and amplifies the uplink RF signal before transmitting it on the downlink, and vice versa. It may also change the carrier frequencies. |

Question #2: Is there any major comment against the alignment on RAN2 structure R3-210703 [2]? Please also consider R3-210361 [8] first sentence of 4.x.3 Signalling as alternative, merge, or complementary text for capturing the NRCGI fixed on earth.

| Company | Comment |
| --- | --- |
| Thales | No major comments. |
| Huawei | About R3-210361 first sentence could be captured as QC proposed with the editor’s note. Please note that 4. Section should remain short as Stage 2 rapporteur wish and the new section in subclause 16. is proposed FFS for the title that may change … |
| CATT | No major comments, fine to capture the first sentence of 4.x.3 in R3-210361. |
| Intel | So now we are sometimes using the term “the NTN payload” and sometimes “the satellite or the HAPS” to refer to the same thing. Why? Suggest to settle on a single term. |
| Nokia | Ok. Agree with Huawei. |

Question #3: Is there any major comment against the agreements integration and emails comments R3-210704 [3]?

| Company | Comment |
| --- | --- |
| Thales | No major comments. |
| Nokia | Question: will RAN3 BL CR include the RAN2 text, e.g. 16.x.3 Mobility and State transition? We prefer the RAN3 BL CR only have the RAN3 related part. |

Question #4: Is there any major comment against the response paper R3-210987 [4]?

| Company | Comment |
| --- | --- |
| Thales | We recommend to introduce NTN vehicle, NTN station and NTN control function. This will be beneficial for the understanding by all RAN WG during standardisation work although these concept won’t be defined in 3GPP We suggest to replace “satellite Ephemeris” by “Ephemeris” to make it applicable to both satellite and HAPS RAN2 has decided to remove the definition of “transparent payload” since there is a text in clause 4.x that clarifies what transparent means " NTN payload transparently forwarding the radio protocol received from the UE (via the service link) to the NTN Gateway (via the feeder link) and vice-versa " => RAN3 to align with RAN2 |
| CATT | It’s ok to replace “satellite Ephemeris” by “Ephemeris”. On the introduction of the terminology NTN vehicle, NTN station and NTN control function proposed by Thales, we understand it’s needed if we capture the Figure X.Y in R3-210020. |
| Intel | Don’t fully understand the question. Is the proposal to agree R3-210987? |
| Ericsson | We provided a further version. Not absolutely sure about the informative annex, but if we do something about it, then in maximum what we have shown there. Please avoid introducing terms only used in the informative annex in the normative definition section please avoid using RRH |
| Nokia | For the 1st comment on gNB, we disagree the “gNB box” in the figure. In Terrestrial network, a gNB includes CU and DU. There are transport network nodes between the CU and DU, but RAN3 do not define the gNB including those transport network nodes. So we do not see the need to have a figure showing a gNB includes GW and payload. If really need to capture the GW/payload, it should be in informative annex section showing the transport network nodes including GW/Payload, rather a gNB box including GW/Payload. |

Question #5: Is there any major comment against the NTN architecture update R3-210020 [5]?

| Company | Comment |
| --- | --- |
| Huawei | We are supportive of the comment on NTN-RRH and NTN-Control center, however these are not RAN3 e.g. NTN-RRH. We see benefit on the proposal for the global understanding but it seems to us difficult to standardize. We would like then to suggest an Informative Annex to describe the full NTN system (the architecture figure of R3-210020 should be improve to remove confusion on gNB). Same we also see some benefit on the RAN2 figure remove by R3-210987 (response paper), this could be added in Annex… |
| Thales | We support the addition of an informative annex clarifying the overall NTN architecture and its interaction with NG-RAN functions for global understanding including the introduction of NTN concepts such as NTN infrastructure, NTN control function, NTN vehicle, NTN station and NTN Remote Radio Head or NTN Remote Radio System. The proposed “Figure X.Y: NTN based NG-RAN architecture (transparent payload scenario)” can be further improved by removing confusion between gNB and gNB-CU/DU. The naming “NR-Uu(*)” on the interface NTN-Gateway – gNB-DU may not be needed since it is not to be defined. Moreover an editable figure should be provided as per below: |
| CATT | Anyway, we need to capture an overall architecture for NTN. Now, we see figure 4.x.1 of R3-210987, and figure X.Y provided in R3-210020. As Figure X.Y provide more detail info, maybe we could capture it in the annex to further clarify the overall NTN architecture. We could treat the NTN Radio Remote System as a part of NG-RAN, the RRH of NG-RAN. As we will not specify the interface between the “Non RF gNB functions” and the NTN-GW, it’s fine to remove the NR-Uu(*). |
| Intel | NR-Uu(*) is very misleading, should be removed. But the main point is that we now have multiple architecture figures floating around and it is not clear which one is on the table for inclusion in the spec. |
| Ericsson | We provided a further version. Not absolutely sure about the informative annex, but if we do something about it, then in maximum what we have shown there. Please avoid introducing terms only used in the informative annex in the normative definition section please avoid using RRH |
| Nokia | Most of them are not related to RAN3. The text for “… for CIoT supported by 5GCN.” is not needed. CIOT is not considered in this release. |

Question #6: Is there any major comment against the UL SYNC R3-210152 [6]?

| Company | Comment |
| --- | --- |
| Thales | We support the clarification brought by this paper related to the Ephemeris. The introduction of PVT abbreviation can be decided later upon decision of the Ephemeris format. |
| CATT | Seems correct. But it seems we do not need to specify here on how to use the ephemeris info in the UE. Suggest to delete the later part of the last sentence, as below: The gNB shall process the Ephemeris provided by the NTN control function to broadcast PVT data to all UEs of a given cell, so that it can be used for uplink synchronization in order to mitigate the Doppler and propagation delay variations. |
| Intel | “The gNB shall process the Ephemeris provided by the NTN control function to broadcast PVT data to all UEs of a given cell” – that’s not an OAM requirement. Also seems to be in RAN2 scope? |
| Ericsson | Is this RAN3 business? Is this 3gpp business at all? |
| Nokia | The TP has following major parts Definition for Ephemeris Configure Ephemeris in gNB. RAN3 does not define how the gNB is configured. SA5 define the OAM configuration, e.g. regular, or on demand, or format, etc. gNB use Ephemeris: It is in RAN2 scope on broadcast the PVT over Uu. So we suggest that this should be discussed in RAN2. |

Expectation, summary and/or conclusion:

The TP for the Stage 2 BL CR should be revised in a merge and revised document in R3-21xxxx_BLCR_update. Endorse the R3-21xxxx_BLCR_update has new BL CR

## Communication with RAN2

There are overlap on stage 2 between RAN2 and RAN3 proposals. Note that RAN2 did not endorsed any document yet. It seems that there is no other action needed for now against RAN2 e.g. LS to RAN2.

The agreements of RAN3 #111 within the RAN3 stg2 BL CR endorsed after the meeting will be captured in RAN2 Running CR by the WI rapporteur. If any issue, the WI rapporteur will trigger an email on RAN3 reflector.

Question #7: Is there any need for now to communicate with RAN2?

| Company | Comment |
| --- | --- |
| Huawei | No action is needed, the WI Rapporteur should manage, if any issue |
| Thales | Agree with HW |
| CATT | WI Rapporteur could manage this. |
| Nokia | WI Rapporteur could manage this. |

# Conclusion, Recommendations

TBC; Endorse the R3-21xxxx_BLCR_update has new BL CR

# References

R3-210014 Support Non-Terrestrial Networks (Huawei)

R3-210703 (TP for  BL CR TS 38.300) NTN Stage 2 completion: Alignment with RAN2 (Huawei)

R3-210704 (TP for BL CR TS 38.300) NTN Stage 2 completion: Last email discussion comments and Agreements integration (Huawei)

R3-210987	Response paper to R3-210704 and R3-210703 (Ericsson)

R3-210020 NTN architecture aspects (Thales, Rakuten Mobile, Eutelsat, Inmarsat, Hughes Network)

R3-210152 NTN uplink synchronisation (Thales, Rakuten Mobile)