3GPP TSG-RAN WG3 #111-e	R3-210970

25 January – 5 February 2021

Agenda Item:	20.2.1

Source:	Qualcomm Incorporated (moderator)

Title:	Summary of Offline Discussion on NTN Network IDs

Document for:	Approval

# Introduction

CB: # 25_NTN_nwID

CATT

RAN obtains the geographical fixed Cell ID regarding to the momentary coverage of the earth moving cell; this is preferred to provide geographical fixed Cell ID to CN without any impact to Uu/Xn/F1 interfaces.

UE location info, if available in the NG-RAN node, could be used to do the mapping towards a geographical fixed CGI.

If NG-RAN is not able to get the detail UE location, momentary coverage of UE’s serving cell could be used to do the mapping, how to do the mapping is up to the implementation.

Nok

cell ID used in mobility related messages is the “Uu” cell ID.

cell ID used in the other messages that only involves the CN is the “Virtual” cell ID.

cell ID used in the procedures related to INACTIVE need further study.

QC,HW,Th

It is possible to define CGI/TAI lists that each correspond to a geographical area, where a gNB “owns” a number of these that correspond to its own coverage area (based on connected gateways and the NTN constellations).

Layers of reporting granularity may be enabled by using layers of CGI/TAI.

Capture TP

Capture access restriction info in NGAP and XnAP according to SA2 decision

- if agreeable, capture TPs/CRs to align with SA2

- anything to add to st2 w.r.t. current agreements?

- check details, revise if needed

(QC - moderator)

Summary of offline disc R3-210970

# For the Chairman’s Notes

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

R3-20xxxd rev [in xxxh] – agreed

R3-20xxxe rev [in xxxi] – agreed

R3-20xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion [if needed]

## Principles of usage of “fixed cells”

RAN3 has previously agreed that “A Cell ID provided to the 5GC within the User Location Information corresponds to a fixed geographical area.”.

Two papers address some of the principle-related aspects of using fixed cells (ignoring for now how the information is acquitted to do the mapping) e.g. [1] and [2].

Ref [1] proposes that

- RAN obtains the geographical fixed Cell ID regarding to the momentary coverage of the earth moving cell; this is preferred to provide geographical fixed Cell ID to CN without any impact to Uu/Xn/F1 interfaces.

Ref [2] proposes that

- the cell ID used in mobility related messages is the “Uu” cell ID.

- the cell ID used in the other messages that only involves the CN is the “Virtual” cell ID.

- the cell ID used in the procedures related to INACTIVE need further study.

Both proposals seem to be going in the same general direction, i.e. that “fixed cell” concept is used for signalling towards the CN, but generally not otherwise. [2] analyzes some of the functions in the RAN, from which the proposals derive. It points out particularly that the RNA in inactive (based on a cell list) would not necessarily correspond to a fixed geographical area, which may be problematic. It also points out that for paging optimization, the “fixed cells” should be used.

To make further progress, we could take a working assumption as follows:

- Fixed cells are used in NGAP in signalling towards CN only.

And to add to that it could be noted that

- Further work is needed to analyze impacts of earth moving cells on inactive state and/or other functionality. Exceptions or special cases (i.e. cases where fixed cells are used in other interfaces, and cases where Uu cells are used in NGAP) can be considered on case by case basis as needed.

Please provide any view / comments on this topic and the proposals in bold below:

| Company | Comment |
| --- | --- |
| CATT | We agree with the working assumption, CGI associated to fixed cells could be used in ULI report to 5GC only, this could satisfy the requirement of SA2 with no or minimum impact to the Uu/Xn interfaces. The other aspects could be kept in an Editor’s note and to be further discussed. |
| Nokia | The term “fixed cell” is already used for Earth-Fixed Cell. Is the WA for all NGAP messages to CN, or only for those NGAP messages including ULI? Suggest following working assumption: The cell ID reported to CN in the ULI IE corresponds to a fixed geographical area. |
| Samsung | We are fine to discuss further usage case by case |
| Huawei | The WA should be clarify like: Fixed geographical cells are always used in NGAP in signalling towards CN only Which is fine and enough for now: it looks difficult to mix multiple cells concept with the CN But may be this should be clarified online |

## Performing mapping to fixed cells

It should be noted that we are expecting a response from RAN2 on this topic. However documents [1], [3] and [4] touch on this.

Ref [1] proposes that the UE location info, if available in the NG-RAN node, could be used to do the mapping towards a geographical fixed CGI. In addition, if NG-RAN is not able to get the detail UE location, momentary coverage of UE’s serving cell could be used to do the mapping, how to do the mapping is up to the implementation.

Ref [3] states that the UE does not need to report the location information to the RAN, otherwise it is necessary to wait until the AS security is enabled before considering acquiring the UE location info. It also proposes that GNSS based UE location information and network-based positioning solution could be considered and worth to further discuss in the following meeting.

Ref [4] addresses the topic of handling rough information (e.g. on initial access) in passing, by proposing that the network can configure two or more layers of fixed cells with different granularity.

It seems however difficult to make further progress before receiving an LS reply from RAN2 first. Depending on this answer, there may or may not be additional work for RAN3 to perform.

A possible way forward is to state that RAN3 can wait for the LS reply from RAN2 before considering resulting issues (e.g. handling lack of information if applicable, role of network based location if applicable, etc).

Please provide any view / comments on this topic and the proposals in bold below:

| Company | Comment |
| --- | --- |
| CATT | We believe such kind of mapping is done in NG-RAN node by implementation, no matter whether and how to get the accurate UE location info. Anyway, we agree to wait for the LS reply from RAN2. |
| Nokia | Suggest waiting for RAN2 reply. |
| Samsung | Can wait for RAN2. |
| Huawei | Same view as CATT, Nokia, Samsung, …. |

## NTN RAT Identification

References [5] and [6] contain CRs for NGAP and XnAP, which are based on the impact analysis of SA2 agreements (S2-2006591).

The CRs add explicit access restriction for all types of NR RATs based on satellite constellations, i.e. NR(LEO), NR(MEO), NR(GEO) and NR(OTHERSAT), that may be used as 3GPP access in 5GS.

In addition, since the access restriction should apply on initial access, i.e. the AMF should be aware of the satellite access type, on a TA basis. The CRs support this by adding additional codepoints to the RAT Information IE.

If agreeable, the content of the CRs could be part of a baseline in the usual manner i.e. subject to further checks etc in the upcoming meetings.

Please provide any view / comments on the CRs, specifically on the concept, approach taken and details:

| Company | Comment |
| --- | --- |
| CATT | Following the agreements of SA2, different satellite constellations could be treated as different RAT types. The “RAT Restriction Information”is used to control the mobility of a UE. But currently, the UE capability on the different access type is not clear. And handover between the different RAT types is not discussed in RAN2 and RAN3. If the handover between the “RAT types” is not allowed/ supported for a UE in Rel-17, we do not need to introduce the “RAT types” during the initial access and mobility restriction. Above all, we suggest to hold on the discussion on RAT type now, and to further clarify if the mobility between the different RAT types is allowed/supported in Rel-17 first. |
| Nokia | For NGAP CR 9.3.1.125, SA2 agreed different TAC is used for LEO/MEO…, so this change is not needed. |
| Samsung | We are open to discuss. |
| Huawei | CR can be endorsed for us (we co-source). If there is some doubt on access and mobility with regards to the RAT-Type, we can send LS to SA2 to clarify now. |

## Further aspects

Please add any further aspects that are in scope and were not included in the above:

| Company | Comment |
| --- | --- |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-210470, “Discussion geographical fixed CGI reporting”, CATT

R3-210492, “Discussion on cell ID handling on NG interface and Xn interface”, Nokia et al

R3-210911, “Discussion on Network Identifier Handling”, CMCC

R3-210361, “(TP for BL CR for TS 38.300) Handling of cell identity signalling towards the CN”, Qualcomm Inc

R3-210362, “Support of NTN RAT identification and NTN RAT restrictions”, Qualcomm Inc et al

R3-210363, “Support of NTN RAT identification and NTN RAT restrictions”, Qualcomm Inc et al