3GPP TSG-RAN WG3 #111-e                                                                       R3-210972

25 Jan - 4 Feb 2021

Online

Agenda Item:	20.2.3

Source:	ZTE (moderator)

Title:	Summary_of_offline_disc_CB # 27_NTN_CellRelation

Document for:	Approval

# Introduction

CB: # 27_NTN_CellRelations

CATT

In Rel-17, it should be assumed that the NTN gNB can get aware of cell neighbor relation information from OAM.

In Rel-17, it should be assumed that NTN gNBs do not include any “Neighbor Information NR” in any XnAP messages.

NTN gNBs should still exchange the cell information (i.e. “Served Cell Information NR”) of their own over XnAP to facilitate mechanisms such as measurement gap configuration. This information is not assumed to be provided by the OAM.

Nok

Enhance XnAP to introduce the timing information for the NTN cell

HW

gNBs should exchange the Validity time window list and Periodicity via Xn.

NTN Operation IE should added to the Validity time period

Validity time window should also apply to the schedule of the TAC for the moving cells.

ZTE

Introducing the neighbor schedule has no impact on current specification

- Whether and how to exchange neighbor information?

- Whether to exchange validity time window list and periodicity? (alternative: exchange satellite ephemeris as per 0520?)

(ZTE - moderator)

Summary of offline disc R3-210972

# For the Chairman’s Notes

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

R3-20xxxd rev [in xxxh] – agreed

R3-20xxxe rev [in xxxi] – agreed

R3-20xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion

## Whether and how the neighbor information should be exchanged over Xn/NG?

In [1], the NTN gNB can get aware of cell neighbouring relation information from the OAM, but the NTN gNBs should still exchange the cell information (i.e. “Served Cell Information NR”) of their own over XnAP.

In [2],  it is proposed to provide a “super set” of served cell information and to associate cell information with a “validity time” over Xn, and reduce the OAM effort.

In [3], the Validity Time Window information should be included in the Served Cell Information NR IE within the Xn Setup and the NG-RAN Node Configuration Update procedure over Xn. The validity time window related to TACs could be introduced in NG Setup procedure and RAN Configuration Update procedure over NG.

In [4], for the NTN cells, the neighbor information can be deduced by the predictable ephemeris from NTN control center, so this information is unnecessary to be exchanged over Xn.

| Company | Comment |
| --- | --- |
| ZTE | Not needed. In general, once the transparent LEO constellation is stable, its NTN coverage topology is not supposed to be fundamentally changed. And The neighbor cell relationship for satellites in the same orbit can be kept as stable as possible. The neighbor information can be deduced by the predictable ephemeris from NTN control center.With this information, the NTN gNBs could be aware of whether the neighbor cells are available or not. In this way, there in no impact on current XnAP/NGAP specification. |
| InterDigital | The XnAP protocol exchanges Neighbour Cell information and we believe that should continue. We recognize that it could be done by O&M, but if we do it by O&M do we exchange basic information over XnAP for neighbours or not send it at all? Not clear to me why we would handle Satellite neighbours differently |
| CATT | Not needed. One gNB could know the internal cell relations clearly as they are controlled by itself. Considering the neighbor cells generated by the other gNBs, they may change along with the movement of the satellites. To exchange the neighbor relations requires a gNB to know the neighbor cells generated by the other gNB. But how can a gNB get the neighbor cells generated by the other gNB? Via OAM? If it’s yes, OAM could configure the proper neighbor relations to all the NTN gNBs. Thus, we see the exchange of the neighbor relations via Xn/NG is not needed at all. |
| Huawei | It seems we are going in wrong debate here. It will be a big step back to rely only on OAM when Xn is present for the neighboring information exchange. The issue to solve is related to the cells which are not always “available/activate”. We had agreement to avoid periodic configuration update from last meeting. An indication of activity solve the issue. |
| Intel | The “validity time” idea appears to be beneficial. |
| China Telecom | Not needed. The NTN gNB can obtain neighbor information and know when the neighbor cells are available via NTN control functions. In this way, there is no impact on Xn / NG. |
| Nokia | It is beneficial for Xn interface, which already supports the exchange of serving cell/neighboring cell info. The only thing is to match the NTN case that some cells may appear/disappear. A gNB may or may not know the satellites used by the neighboring gNB. There is no proposal on NG. It is not needed for NG interface, since the AMF does not need to know the cell info. |
| Apple | Not needed since the NTN control functions and ephemeris provide this input except for some TN(NTN scenarios. |
| Ericsson | For not-moving/stationary payload I guess we agree that exchanging served cell/neighbor cell information makes sense as this represents semi-static information, neighbor cell info could even be gained by means of UE reports. But for moving payloads, we assume that the control of feeder/service link switches to be highly dependent on centrally configured knowledge of the payloads current position and speed, that cannot be managed in a distributed way. Exchange of config info via Xn was made for distributed control of RAN, moving payloads change this assumption completely. Only if it can be shown that there is benefit of localized / distributed decisions, we would agree on further discussing that, but we don’t see this. |
| Rakuten Mobile | Not necessary. |
| Qualcomm | Not essential but has limited use Intel had a good discussion in R3-210751 (not listed here) which makes a good case for providing cell coverage area and coverage movement to gNBs rather than, or as well as, satellite ephemeris data. We think both types of data are needed. Satellite ephemeris can be provided by OAM. Cell coverage area and coverage movement could be provided by the serving gNB using Xn or by OAM. It has to be provided to the serving gNB using OAM so provision using OAM to other gNBs would be the simplest solution. However, Xn could be used to indicate precisely when served cells will be switched on and off, which might be more reliable or more accurate than OAM. |

## If the exchange of the neighbor information is considered over Xn/NG, as described in 3.1, how to understand the “validity time”[2] or “validity time window”[3] in detail? e.g. whether the validity time window list and period should be exchanged?

| Company | Comment |
| --- | --- |
| InterDigital | We believe in the validity time window as described in [3] but also could support the validity time as in [2] |
| Huawei | We are open to investigate more this aspects related to time management. It was commented last meeting to provide more information, we suggest here a list period or an ephemeris. There is pros and cons in both and in the fact to propose a choice…. |
| Nokia | We think the timing information in both contributions are similar, i.e. to indicate when the cell appear or disappear. The detail may be discussed later. |
| Qualcomm | Validity time equated to cell activation and deactivation time makes sense. |

## Whether the validity time window should be distinguished between moving cells and feeder link cells?

In [3], the NTN Operation IE is proposed to be added to the validity time window.

| Company | Comment |
| --- | --- |
| Huawei | First from a neighbor’s point of view, the moving cells and feeder link cells are same, they are cells active in a time frame. Then from resource management, it is essential to know if the activation is by a signal that could fade away or on/off … |
| Nokia | It may be no needed. In both cases, the timing information is to indicate when a cell appear/disappear, so it is similar in both cases and no need for the differentiation. |
| Qualcomm | Does not seem needed |

## Further aspect?

Please add any further aspects that are in scope and were not included in the above:

| Company | Comment |
| --- | --- |
| Huawei | The TAC aspect could be manage later one … |
| Qualcomm | While OAM detailed content would be proprietary, we think the type of data to be included is in scope – e.g. satellite ephemeris, cell parameters, cell coverage area and movement, cell activation/deactivation times. |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-210473, “Discussion on cell neighbouring information”, CATT

R3-210494,	“Discussion on Cell relation handling”, Nokia

R3-210705, “Support for non-terrestrial networks”, Huawei

R3-210807, “Further Discussion on Cell Relation for NTN”, ZTE