3GPP TSG-RAN WG3 Meeting #111-e	R3-210978

25 January - 4 February 2021

Online

Agenda Item:	23.2.3

Source:	Ericsson

Title:	Application Protocol - Summary of offline discussion

Document for:	Discussion and Decision

# 1	Introduction

The scope of the email discussion has been captured as followed:

CB: # 33_eNBarchEvol_AP E/// For section 1 to section 7, add the new eNB logical entities names to each occurrence of the gNB-CU-CP and gNB-CU-UP For sections 8 and 9, add a note establishing the equivalence between all the CP logical entities and between all the UP logical entities Further discuss if all the E1 functions and procedures are applicable to LTE CP-UP separation Reuse the existing UE AP IDs for the new logical entities HW 0867 The new interface shall support bearer context management function includes the Bearer Context Setup function, the Bearer Context Release function, and the Bearer Context Modification function. The bearer context management of the new interface function should provide the QoS flow to DRB mapping configuration and the S-NSSAI. HW 0868 The new interface management function includes the Reset function, the Error Indication function, the Interface Setup function, the Configuration Update function, and the Status Indication function. During the Interface Setup procedure or the Configuration Update procedure, the CU-UP should provide the supported ECGI, S-NSSAI and PLMN-ID. - Whether to start from the ground up or to directly conclude that E1AP can be reused? If the latter, go for E1AP BL CR (E/// - moderator) Summary of offline disc R3-210978

This contribution captures the email discussion.

# 2	For the chairman’s notes

Propose to capture the following:

For the interface used for the CP-UP split in eNBs (FFS) and ng-eNBs:

- Bearer context setup, Bearer context release and Bearer context modification procedures are supported

- In NG-RAN, the control plane entity decides the flow-to-DRB mapping and provides the generated SDAP configuration. In both E-UTRAN and NG-RAN, the control plane entity provides the PDCP configuration to the user plane entity

- In NG-RAN, the control plane entity provides the S-NSSAI to the user plane entity in the bearer context setup (as mandatory IE) procedure in the bearer context modification procedure (as optional IE)

- Reset procedure, Error Indication procedure, Interface Setup procedure (both ways), Configuration Update procedure and Status Indication procedure are supported

- The CU-UP signals the supported ECGI(s), S-NSSAI(s) and Supported PLMN(s) at interface setup/configuration update

The following proposal can be agreed if E1 interface is agreed to be used for (ng-)eNB CP/UP split:

- Introduce the new logical node names in sections 7 and 8 of E1AP

To be continued:

- FFS how to capture the new logical entities in section 9 of E1AP

- FFS if existing E1AP UE AP IDs can be reused

# 3	Email discussion

## 3.1 Which interface to be used for the CP-UP split

RAN plenary tasked RAN3 to study the feasibility of reusing the E1 interface for the CP-UP split in eNBs and ng-eNBs (see WID in [1]). This is discussed in [2], [3] and [4]. However, this question is also addressed in CB: # 31_eNBarchEvol_General. Therefore, it is proposed to not discuss this point in this CB.

## 3.2 Bearer context management and interface management

While waiting for an agreement on the previous point, some Application Protocol topics can still be discussed in an independent manner. For example in [4] and [5], it is proposed to list the existing E1AP bearer context management and interface management functions and procedures, and decide if it is applicable to the interface for the CP-UP split in eNBs and ng-eNBs.

Question 2.1: Please list the existing E1AP bearer context management functions and procedures which are also applicable to the interface for the CP-UP split in eNBs and ng-eNBs.

| Company | Response |
| --- | --- |
| Ericsson | Bearer context setup, Bearer context release, Bearer context modification |
| Deutsche Telekom | Agree with Ericsson covering Huawei’s proposal in [4] |
| Huawei | Bearer context setup, Bearer context release, Bearer context modification |
| Nokia | Bearer context setup, Bearer context release, Bearer context modification |

In [4], it is also proposed that the CU-CP decides the flow-to-DRB mapping and provides the generated SDAP and PDCP configuration to the CU-UP.

Question 2.2: Should the CU-CP decides the flow-to-DRB mapping and provides the generated SDAP and PDCP configuration to the CU-UP?

| Company | Response |
| --- | --- |
| Ericsson | Yes |
| Deutsche Telekom | Yes Please not that in eNB case there is no SDAP (just for ng-eNB). |
| Huawei | Yes. Also agree with DT’s comments on SDAP. |
| Huawei | Yes. Also agree with DT’s comments on SDAP. |

The same principle is proposed for the S-NSSAI. From [4]: “For each PDU session resource to be setup or modified, the CU-CP shall provide the S-NSSAI to the CU-UP in the bearer context setup procedure, and the CU-CP may provide the S-NSSAI to the CU-UP in the bearer context modification procedure.”

Question 2.3: Should the CU-CP provides the S-NSSAI to the CU-UP in the bearer context setup (mandatory) procedure in the bearer context modification procedure (optional)?

| Company | Response |
| --- | --- |
| Ericsson | Yes |
| Deutsche Telekom | Yes |
| Huawei | Yes |

Now in [5], it is proposed to list the existing E1AP interface management functions and procedures, and decide if it is applicable to the interface for the CP-UP split in eNBs and ng-eNBs

Question 2.4: Please list the existing E1AP interface management functions and procedures which are also applicable to the interface for the CP-UP split in eNBs and ng-eNBs.

| Company | Response |
| --- | --- |
| Ericsson | Reset procedure, Error Indication procedure, Interface Setup procedure (both ways), Configuration Update procedure, Status Indication procedure |
| Deutsche Telekom | Agree with Ericsson covering Huawei’s proposal in [5] |
| Huawei | Same view as E/// and DT |
| Nokia | Reset procedure, Error Indication procedure, Interface Setup procedure (both ways), Configuration Update procedure, Status Indication procedure |

The parameters exchanged at interface setup/configuration update are discussed in [5]. It is proposed that the CU-UP signals:

- Supported ECGI(s)

- Supported S-NSSAI(s)

- Supported PLMN(s)

Question 2.5: What are the parameters which should be signaled by the CU-UP to the CU-CP at interface setup, and may be modified at configuration update?

| Company | Response |
| --- | --- |
| Ericsson | A list of supported PLMN(s) should be signaled. This list may contain a list of supported S-NSSAI(s). If it contains the list of supported ECGI(s) is FFS, depending on the deployment scenarios to be supported (e.g. this was agreed for gNBs in case CU-UP is collocated with the DU) |
| Deutsche Telekom | Supported ECGIs, S-NSSAIs and PLMN-IDs. |
| Huawei | Since we are talking one interface which covers both legacy eNB and NG-RAN eNB cases, maybe we could start from which parameters could not be applicable to both cases, e.g. slice related, SDAP related configuration, duplication related, etc., but anyway, ECGIs, S-NSSAIs and PLMN-IDs should be agreeable. |
| Nokia | All three of them. Supported ECGI(s), Supported S-NSSAI(s), and Supported PLMN(s). |

## 3.3 How to introduce new (ng-)eNB CP/UP split in E1AP specification

The following questions are only applicable if it is agreed to reuse the existing set of specifications (i.e. E1). In [6], some proposals are made on how to capture the CP-UP split in eNBs and ng-eNBs in the existing E1AP specification. These proposals are splt between sections 1 to 7, and 8 to 9. It is also proposed to reuse the existing UE AP IDs for the new logical entities.

Question 3.1: For sections 1 to 7, can the new eNB logical entities names be added next to each occurrence of the gNB-CU-CP and gNB-CU-UP, as proposed in [7]?

| Company | Response |
| --- | --- |
| Ericsson | Yes |
| Deutsche Telekom | Yes Just one comment w.r.t. CP-UP separation: This is done for higher protocol layers only, therefore we should only refer to CU-UP for eNBs and ng-eNBs to be in line with other already existing definitions for eNB/gNB decomposition (see also our comments to CB #31). |
| Huawei | Yes if we decide to reuse the existing E1 seriers for the new interface. BTW, what’s the meaning of the tiltle of 3.3 here, 2-step RACH?? |
| Nokia | No. Our view is that a separate set of E1’ specs is needed. |

In [6], it is proposed that for sections 8 and 9, a note establishing the equivalence between all the CP logical entities and between all the UP logical entities could be added, in order to avoid the need to add the new eNB logical entities names next to each occurrence of the gNB-CU-CP and gNB-CU-UP.

Question 3.2: Is a note sufficient to capture the CP-UP split in eNBs and ng-eNBs for sections 8 and 9?

| Company | Response |
| --- | --- |
| Ericsson | Yes |
| Deutsche Telekom | Yes |
| Huawei | Not sure, assuming we reuse the existing E1 seriers for the new interface. But a note would be a good practice to start with. |
| Nokia | No. Our view is that a separate set of E1’ specs is needed. |

In [6], it is proposed to reuse the existing UE AP IDs for the new logical entities, in order to avoid the need for new optional UE AP IDs in each UE-associated procedure.

Question 3.3: Can the existing UE AP IDs be reused for the new logical entities?

| Company | Response |
| --- | --- |
| Ericsson | Yes |
| Deutsche Telekom | Yes |
| Huawei | Yes |
| Nokia | No. The scenario with LTE with EPC connectivity is not same as that of gNB and we do not see it as appropriate. Instead, new UE AP IDs should be defined. |

# 4	Conclusion

Bearer context management and interface management

The following proposals can be agreed for the interface for the CP-UP split in eNBs and ng-eNBs:

- Bearer context setup, Bearer context release and Bearer context modification procedures are supported

- In NG-RAN, the control plane entity decides the flow-to-DRB mapping and provides the generated SDAP configuration. In both E-UTRAN and NG-RAN, the control plane entity provides the PDCP configuration to the user plane entity

- In NG-RAN, the control plane entity provides the S-NSSAI to the user plane entity in the bearer context setup (as mandatory IE) procedure in the bearer context modification procedure (as optional IE)

- Reset procedure, Error Indication procedure, Interface Setup procedure (both ways), Configuration Update procedure and Status Indication procedure are supported

How to introduce new (ng-)eNB CP/UP split in E1AP specification

The following proposal can be agreed if E1 interface is agreed to be used for (ng-)eNB CP/UP split:

- Introduce the new logical node names in sections 7 and 8 of E1AP

Open issues:

- FFS how to capture the new logical entities in section 9 of E1AP

- FFS if existing E1AP UE AP IDs can be reused

# 5	References

[1] RP-193181 - New WID: Enhanced eNB(s) architecture evolution (China Unicom, NTT Docomo)

[2] R3-210755 - CP-UP separation for eNBs (Ericsson)

[3] R3-210865 - General aspects and principles of the interface between CP and UP for eNB and ng-eNB (Huawei)

[4] R3-210867 - Bearer context management function and procedures of the interface between CP and UP for eNB and ng-eNB (Huawei)

[5] R3-210868 - Interface management function and procedures of the interface between CP and UP for eNB and ng-eNB (Huawei)

[6] R3-210758 - E1 changes needed for eNB CP-UP separation (Ericsson)

[7] R3-210759 - E1 changes needed for eNB CP-UP separation (Ericsson)

# Comments

This aspect still need further discussion

We propose that this is already captured as an agreement as well.

Wrong section title?

Good catch 😊