3GPP TSG-RAN WG3 Meeting #111-e	R3-20xxxx

25 January – 4 February 2021

Online

Agenda Item:	9.2.1

Source:	Huawei (moderator)

Title:	Summary of Offline Discussion on RAT type Handling

Document for:	Approval

# Introduction

CB: # 6_RATtypeHandling

HW,CMCC,VF,TIM,CT,DT

introduce abnormal conditions that the CN shall fail the S1/NG setup procedure if the CN does not support any one of the RATs provided by the RAN node and introduce cause value “no supported RAT”.

Include the supported RATs of the CN to RAN in NG/S1 SETUP RESPONSE and AMF/MME CONFIGURATION UPDATE.

ZTE

“Not supported RAT” failure cause is not necessary in S1AP/NGAP procedure

- further check details

(HW - moderator)

Summary of offline disc R3-210959

# For the Chairman’s Notes

//to be added

# Discussion

## If the CN does not support any RAT of the RAN node

In the discussion during last meeting, all the companies agrees that the S1/NG setup procedure and configuration update procedure should be failed, but there is no consensus on the need to update the specifications.

Take NGAP as an example, currently, in the In NG Setup procedure unsuccessful operation part, it is stated that:

If the AMF cannot accept the setup, it should respond with an NG SETUP FAILURE message and appropriate cause value.

But at the same time, it is also clearly defined in the abnormal conditions that

If the NG-RAN node initiates the procedure by sending an NG SETUP REQUEST message including the PLMN Identity IEs and none of the PLMNs provided by the NG-RAN node is identified by the AMF, then the AMF shall reject the NG Setup procedure with an appropriate cause value.

As it is not clear what is “cannot accept the setup”, especially if all the IEs are comprehended from CN point of view. Considering that the Broadcast PLMN List IE and the RAT Information IE are in the same level with TAC IE, and provides the key information for the RAN node, it is preferred to also clearly define the abnormal condition for that, to avoid any potential IoT issue.

Proposal 1: introduce abnormal conditions that the CN shall fail the S1/NG setup procedure if the CN does not support any one of the RATs provided by the RAN node, and introduce cause value “no supported RAT”.

Do you agree with the proposal?

| Company | Comment |
| --- | --- |
| Huawei | Yes, this abnormal condition needs to be clarified in the spec, to avoid any potential IoT issue. |
| China Telecom | Yes. The cause value for S1/NG setup failure is need to be defined in spec |
| Deutsche Telekom | Yes (abnormal case and cause value to be specified). |

## Provide the supported RATs of the CN to RAN

The supported RATs of the RAN node and CN nodes changes from release to release, for example:

- in Rel-13, the eNB and EPC may be configured to support NB-IoT besides WB-EUTRA

- in Rel-16, the ng-eNB and 5GC may be configured to support NB-IoT and unlisenced besides WB-EUTRA

RAN nodes and CN nodes are probably updated separately, and therefore the configuration effort are very huge, and misconfiguration between CN OAM and RAN OAM may happen, especially in case the CN and RAN nodes are comes from different vendors.

To avoid misconfiguration, to ease the OAM effort, to avoid the potential IoT issues such as UE access failure and Core network resource waste, it is needed to include the supported RATs of the CN to RAN in NG/S1 SETUP RESPONSE and AMF/MME CONFIGURATION UPDATE.

Proposal 2: Include the supported RATs of the CN to RAN in NG/S1 SETUP RESPONSE and AMF/MME CONFIGURATION UPDATE.

Do you agree with the proposal?

| Company | Comment |
| --- | --- |
| Huawei | Yes, it is needed to inform RAN node about it, only rely one RAN OAM and CN OAM interaction is not a good way. |
| China Telecom | Yes. In our understanding, the intention of providing supported RAT is to support automatic S1/NG connection configuration between RAN and CN. Therefore, some useful assistant information ,e.g., supported RAT, are needed. |
| Deutsche Telekom | Yes (support of simplified network operation in a multivendor environment; “plug’n’play” between RAN and CN). |

## About questions in R3-211023

A response paper is submitted in R3-211023 [7], in this section, we provide feedbacks to the main arguments in this paper.

R3-211023:

- If we are considering a legacy MME/AMF not supporting a specific RAT at all (e.g. NB-IoT), then an operator will normally not try to connect such NG-RAN node to MME/AMF at all.

- If we are considering a MME/AMF supporting a specific RAT in general (e.g. NB-IoT), but features related to this RAT (or others) are not enabled, then it is still questionable why the NG-RAN node is connected to the MME/AMF and, further, why having the connection setup launched knowing that MME/AMF shall reject it afterwards?

- It is also mentioned as second motivation in [1] to provide information on the supported RAT types in the CN to the NG-RAN node. The intention is to inform the RAN of what the CN is supporting. However, this is not logical since the CN will store the RAT type information of the TAI if it's supported.

- Initially, RAN-OAM has to take care that a proper MME/AMF will be selected by the RAN node based on the TAs a RAN node is serving. The address of the CN node(s) will be looked-up per TA. With this information, the RAN node establishes the SCTP connection and finally sends S1/NG Setup. A TA cannot contain NB-IoT and non-NB-IoT cells, so the look-up per TA should also result in selecting the proper CN node based on RAT. If NG Setup would end up in the wrong CN node, the look-up table for the TA would be misconfigured.

Feedback: invalid statement, if the CN only supports one RAT, and RAN node supports two RATs, it is still needed to allow connecting this RAN node to this CN. E.g., in case a MME/AMF not supporting NB-IoT and only supports WB-E-UTRA, it is still allowed to connect a RAN node supporting both RATs to this CN node. And meanwhile, the RAN node may not aware of whether the CN node supports NB-IoT or not.

R3-211023:

- Furthermore, the CR in [2] proposes to add a new cause value in the S1-AP/NG-AP messages for “non supported RAT”, with new procedural text for this cause value. This not only would create a bad example for adding new procedural text for each new added cause value (and there is a lot!), but it is also unnecessary when considering the aspects mentioned in the discussion paper about general RAN3 principles in AI 7 [3].

- In fact, looking at the criticalities, the RAT-Type/RAT Information IEs have been introduced with criticality “reject”, within the Supported TAs/Supported TA List IE that has also criticality “reject”. If the AMF/MME does not support the "RAT", abstract syntax check should already reject the S1/NG Setup/Configuration Update requests. Therefore, there is no need to add any new cause value for non-supported RAT, since the failure will happen.

Feedback: invalid statement, take S1AP as an example, as you may notice that the optional RAT Type IE only includes one code point, i.e. NB-IoT, that is to say, in case a RAT support WB-EUTRA, the RAN node will not include the RAT Type IE for that TAI, therefore although the criticality of the RAT Type IE is reject, if the RAN node connecting to a NB-IoT dedicated Core, this criticality reject IE cannot lead to the failure of the S1 setup.

Question: any further clarification?

| Company | Comment |
| --- | --- |

## About questions in R3-210204

A response paper is submitted in R3-210204 [6], in this section, we provide feedbacks to the main arguments in this paper.

The first part of this paper, is to discuss about the “fail the procedure in case at least one RAT of the RAN is not supported by CN”, considering that in this meeting, the proponents of [1] – [5] are not proposing this anymore, and therefore we skip this part.

For the latter part, the following statement can be found:

R3-210204:

Since the RAT type alignment should be guaranteed by O&M, and the “O&M Intervention” failure cause can already be indicated, so “Not supported RAT” failure cause is not necessary.

Observation 3: “O&M Intervention” failure cause can be used to indicate the O&M un-alignment(e.g. RAT type not alignment).

Proposal : “Not supported RAT” failure cause is not necessary in S1AP/NGAP procedure.

Feedback: “O&M Intervention” is defined as “The action is due to O&M intervention.”it is not something like OAM configuration mismatch. Considering of this specific case, it is preferred to have a clear cause for that.

Question: any further clarification?

| Company | Comment |
| --- | --- |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-210123 Consideration on RAT Type Handling (Huawei, CMCC, Vodafone, Telecom Italia, China Telecom, Deutsche Telekom)	discussion

R3-210124 Correction on RAT Information Handling (Huawei, CMCC, Vodafone, Telecom Italia, China Telecom, Deutsche Telekom) 	CR0537r, TS 38.413 v16.4.0, Rel-16, Cat. F

R3-210125 Correction on RAT Type Handling (Huawei, CMCC, Vodafone, Telecom Italia, China Telecom, Deutsche Telekom)	CR1802r, TS 36.413 v16.4.0, Rel-16, Cat. F

R3-210126 Supported RATs of the AMF (Huawei, CMCC, Vodafone, Telecom Italia, China Telecom, Deutsche Telekom)	CR0538r, TS 38.413 v16.4.0, Rel-16, Cat. F

R3-210127 Supported RATs of the MME (Huawei, CMCC, Vodafone, Telecom Italia, China Telecom, Deutsche Telekom)	CR1803r, TS 36.413 v16.4.0, Rel-16, Cat. F

R3-210204 Consideration on RAT Type Handling (ZTE)	discussion

R3-211023 Response to R3-210123 (Ericsson)	discussion