3GPP TSG-RAN WG3 #111-e						draft R3-211028

25 January – 4 February 2021

Online

Agenda Item:	22.2.3.

Source:	Samsung (moderator)

Title:	Summary of Offline Discussion on CB: # 72_MBS_PTP-PTM_DynChg

Document for:	Approval

# Introduction

CB: # 72_MBS_PTP-PTM_DynChg

HW

discuss dynamic switch between PTP and PTM based on the shared-PDCP architecture.

CU can make decision on whether P2P transmission has to be used for a UE for a MBS service, e.g., MBS packets delivered through UE-specific F1 tunnel, in such case the DU follows the CU’s decision.

If CU does not indicate that the UE has to use P2P transmission for a MBS service, e.g., MBS packets delivered through shared F1 tunnel, the DU makes decision on whether to use P2P or PTM over the radio.

The decision for the dynamic switch can be signaled to the UE by L1/L2 signaling. The final decision is up to RAN2.

CATT

gNB-DU triggers the Uu mode switch procedure between PTP and PTM for a given UE, if the PTM (MB-)N3 tunnel already exists.

discuss how to use the assistant information sent from the core network and “recommended” by SA2 for Uu mode switch procedure when gNB-CU/DU split architecture is used.

TDT

Support the configuration of each active/inactive PTM bearer for an MBS over F1

Support the configuration of each active/inactive PTP bearer for an MBS over F1

Support the PTM/PTP switch commander from a gNG-CU to a gNB-DU over F1

SS

PTP PTM dynamic switching is up to gNB implementation. In case of split gNB, it is up to CU-UP implementation. No additional switching mechanism (e.g. switching indication by MAC/PDCP/RRC) is necessary.

Bearer type change between MBS RB and unicast DRB is supported.

Assistance information is not needed for the PTP/PTM decision from 5GC.

A common tunnel for PTM and a UE dedicated tunnel for PTP in F1 are needed.

ZTE

requirements for delivery mode switching for NR MBS should at least include minimizing the switching latency and data loss.

DU decides the delivery mode for NR MBS.

Len,Moto

Dynamic PTM and PTP Switching function resides in gNB-DU to enable more efficient switching between PTM and PTP mode.

A shared GTP-U tunnel is used between gNB-CU/CU-UP and gNB-DU for both PTM and PTP modes corresponding to a MBS radio bearer.

An explicit PDCP status report is not needed sent from gNB-CU from the gNB-DU.

LG

The gNB-CU should determine PTP-PTM switching.

Opt1 (one shared F1-U GTP tunnel) should be ruled out irrespective of whether which node decides PTP-PTM switching.

F1-C impacts in case of switching decision in the DU:

- The signaling between adjacent gNB-DUs via the gNB-CU in order to align the radio or resource configuration for PTM transmission

- Transfer of the UE individual feedback on reception quality from the gNB-CU to gNB-DU for switching decision in the gNB-DU

- Indication of switching decision result together with lower layer configuration from the gNB-DU to the gNB-CU in order to provide the radio configuration for the MBS session to the UEs which are receiving the MBS traffic

CMCC

PTP is scheduled via the C-RNTI and PTM is scheduled via the G-RNTI.

Compromise solution: gNB-CU makes the decision on which modes is configured to the UE and dynamic switch function resides in gNB-DU to implement flexible scheduling according to the layer1 information.

*****

- consensus to let CU(-UP) decide, up to implementation?

- shared vs. dedicated tunnel?

- don’t concentrate too much on details

- if not possible to converge at this time, probably OK to leave FFS for now

(SS - moderator)

Summary of offline disc R3-211028

# For the Chairman’s Notes

Propose the following:

R3-21xxxa, R3-21xxxc merged

R3-21xxxc rev [in xxxg] – agreed

R3-21xxxd rev [in xxxh] – agreed

R3-21xxxe rev [in xxxi] – agreed

R3-21xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion [if needed]

## gNB-CU make PTP/PTM switch decision

### It was agreed the PTP-PTM Switching function is only applicable for a multicast MBS Session and resides in NG-RAN node. The NG-RAN node takes its decision based on information such as MBS Session QoS requirements, number of joined UEs, UE individual feedback on reception quality, and other criteria.

By the submitted contributions, many companies assume to use a common PDCP as the anchor for PTP/PTM switch [1][3][9]. Further, according to RAN2 email discussion, there is a clear majority thinking that split bearer like architecture as baseline for dynamic switch between PTP/PTM. Based on this, gNB-CU can decide the switch between PTP and PTM.

Q1: Assuming PDCP is the anchor for PTP/PTM switch, do companies agree gNB-CU can decide the dynamic switch between PTP and PTM?

| Company | Answer | Comment |
| --- | --- | --- |
| Samsung | Yes | We think for a multicast service, gNB can configure a MRB with PTM mode and then reconfigure it to use unicast DRB to carry MBS service. It is also a type of PTM PTP switch. It is based on RRC signaling. It is the decision of gNB-CU. But based on the majority view in previous discussion, common PDCP with two legs is assumed and split bearer like architecture is preferred. For the downlink transmission in DC split bearer, there is no configuration on downlink data path selection which is all up to NW implementation. So we think if using split bearer like for MBS service, gNB can choose a leg by gNB implementation. The chosen switching is not indicated to UE. Like the split bearer defined in DC. |
| Nokia | No | Which entity decides between CU and DU should wait for RAN1/RAN2 progress on the definition of which measurements will be used. To make an educated decision, it is needed to consider all criteria when known. |
| Huawei | Yes | CU can make decision on whether PTP transmission has to be used for a UE based on at least the following information: Required by ongoing procedure: In one case, to achieve losses handover, the target gNB needs to deliver the forwarded data via PTP transmission to compensate the progress gap; In another case, for UEs accessing a cell where MBS has already started, the network may schedule the missed data via P2P transmission. High layer feedback (e.g. L2 feedback) : CU is better aware of the high layer feedback, if supported. |
| Intel | Yes | If PDCP is the anchor, then it is logical to let CU make the decision |
| Lenovo, Motorola Mobility | Yes | Once it is agreed to support the one PDCP entity associated with one PTP leg and one PTM leg, it’s quite straight forward to let CU decide on the PTP/PTM switch relying on e.g.: Number of UEs in the MBS session QoS requirement of the QoS flow |
| Ericsson | no decision right now, what for RAN2 | we refuse to discuss this point w/o having a somewhat stable RAN2 concept of what they call “MRB” at hand. |
| CMCC | Yes | We support that gNB-CU makes the decision on dynamic switch. gNB-CU knows the number of UE joined an indicated multicast group. We also think RAN3 should discuss this since we are responsible for CU-DU split architecture. As far as we are concerned, RAN2 agrees gNB make the decision, but they may not discuss based on which information the decision is made |
| LG | Yes | If PDCP is the anchor for PTM-PTM switching, the gNB-CU can decide this switching. |

Q2: A related question is in case of CU-CP and CU-UP split architecture, do companies agree gNB-CU-UP hosting PDCP can decide dynamic switch between PTP and PTM?

| Company | Answer | Comment |
| --- | --- | --- |
| Samsung | Yes | If both PTP leg and PTM leg with a common PDCP is configured, it doesn’t mean the transmission is always active through two legs. The CU-UP can decide which leg to use, i.e. decide the switch between PTP and PTM. |
| Nokia | No | Which entity decides between CU and DU should wait for RAN1/RAN2 progress on the definition of which measurements will be used. To make an educated decision, it is needed to consider all criteria when known. |
| Huawei | Yes | As the anchor of the dynamic switch, PDCP at gNB-CU-UP should make the decision. |
| Intel | Yes |  |
| Lenovo, Motorola Mobility | Yes | If it is agreed to support the one PDCP entity associated with one PTP leg and one PTM leg |
| Ericsson | no decision right now, what for RAN2 | we refuse to discuss this point w/o having a somewhat stable RAN2 concept of what they call “MRB” at hand. |
| CMCC | Yes | Agree with Huawei. |

Q3: Do companies agree gNB-CU can make the decision based on the existing information, e.g. reporting from UE or reporting from DU using existing mechanism. It is up to gNB-CU implementation.

| Company | Answer | Comment |
| --- | --- | --- |
| Samsung | Yes | We think there are two type of PTP/PTM switch. As showed in Q1, one is switch between unicast DRB and MRB using common PDCP with PTM leg (may configure a PTP leg as well). This switch is decided by the CU-CP. The decision is made based on the user number and QoS parameter. No new information is needed. If using common PDCP with PTP and PTM leg, the switch is decided by CU-UP. Based on the reporting in the user plane and QoS requirement. It is up to CU-UP decision. |
| Nokia | No. | Which entity decides between CU and DU should wait for RAN1/RAN2 progress on the definition of which measurements will be used. To make an educated decision, it is needed to consider all criteria when known. |
| Huawei | Yes, but | It is up to gNB-CU implementation which information to be based on to make the decision. For reference, at least the information in our answer to Q1 can be considered. No need to pose any restriction on implementation. |
| Intel | Yes | Let CU implementation to choose |
| Lenovo, Motorola Mobility | Yes | If it is agreed to support the one PDCP entity associated with one PTP leg and one PTM leg. And we don’t see the need of introducing more information element to help CU decide so far. |
| Ericsson | no decision right now, what for RAN2 | we refuse to discuss this point w/o having a somewhat stable RAN2 concept of what they call “MRB” at hand. |
| CMCC | Yes | It is up to gNB-CU implementation. |
| LG | No | Whether the existing information or new information is used for PTP-PTM switching is not decided in RAN2. |

## gNB-DU make PTP/PTM switch decision

According to the proposal submitted, the gNB-DU controlling PTP/PTM switching is more efficient, in that the switching latency is shorter and the gNB-DU is easier to know if the QoS requirement of MBS for the given UE can be met.

Q4: Do companies agree gNB-DU can decide dynamic PTP/PTM switching?

| Company | Answer | Comment |
| --- | --- | --- |
| Samsung | No | Decision in DU maybe a little bit faster, pending to lower layer and Uu signaling design, but it is complicated. If DU decides, DU should notify the result to the PTP/PTM switching anchor. |
| Nokia | No. | Which entity decides between CU and DU should wait for RAN1/RAN2 progress on the definition of which measurements will be used. To make an educated decision, it is needed to consider all criteria when known. |
| Huawei | Yes | In case CU does not indicate that the UE has to use PTP transmission for a packet, it is up to the DU implementation to make decision on whether to use PTP or PTM based on at least the following information: Layer1 assistance information (e.g. beam information, CSI, L1 feedback ) |
| Intel | No | Agree with Samsung |
| Lenovo, Motorola Mobility | Yes | DU has better understanding on e.g. if a UE always replies NACK to PTM transmission. Thus, DU can also trigger the PTP/PTM switch. |
| Ericsson | no decision right now, what for RAN2 | we refuse to discuss this point w/o having a somewhat stable RAN2 concept of what they call “MRB” at hand. |
| CMCC | No |  |
| LG | No | If gNB-DU decides PTP-PTM switching, there may be many F1-C impacts such as the signaling for aligning the radio or resource configuration for PTM, transfer of the UE individual feedback to gNB-DU, and indication of switching decision result to gNB-DU. |

## Assistance information from CN

CN provides service related information, e.g. MBS Session QoS requirements, to the NG-RAN and the NG-RAN can use it when decide the switch between PTP/PTM. It is not belong to the assistance information discussed here. Besides that, more assistance information is discussed in [2] as showed in below:

- Suggested number of UEs for multicast delivery: This parameter seems to be a per-MBS-session parameter used to trigger or to decide per-cell mode switch rather than per-UE mode switch. Considering one physical gNB-DU entity may be shared by multiple gNB-CUs, it seems optimal for such parameters to be sent toward the gNB-DU when it wants to trigger per-cell mode switch.

- Delivery method information for an MBS session or QoS flow, e.g. whether PTP and/or PTM delivery mode are allowed: This parameter is obviously a common parameters which should be delivered in the MBS configuration. It should be sent toward the gNB-DU so that the gNB-DU will not request a mode switch to a mode not allowed. (RAN decide PTP or PTM, not from CN.

- Information of MBS services/groups subscribed by the UE, e.g. TMGI: This IE should anyhow be included over every interface, in order to indicate the UE is currently receiving this MBS session.

- UE capabilities, e.g. whether the UE supports PTM delivery mode: It is not sure whether there will be a separate e.g. “UE radio MBS capability” can be retrieved over the RRC layer directly. Nevertheless such information should be provided toward the gNB-DU so that it will never try to switch the mode toward a method not supported by the UE, regardless of how such capability is retrieved.

Q5: Do companies agree the assistance information from CN is useful for the PTP/PTM switch decision? If yes, pls also indicate which assistance information listed above is useful.

| Company | Answer | Comment |
| --- | --- | --- |
| Samsung | No | We think no need to receive assistance information from core network. |
| Nokia | No. | No need to receive assistance information from core network was already decided at last RAN3 and communicated by LS out. |
| Huawei | No | No need for assistance information from core network. |
| Intel | No |  |
| Lenovo, Motorola Mobility | No |  |
| Ericsson | No |  |
| CMCC | No | We don’t see the need for the assistance information so far. |
| LG | No |  |

## One Shared tunnel for PTM and PTP transmission

It was agreed to use a shared tunnel in F1 for PTM transmission. It is open whether the shared tunnel can be used for PTP transmission. There are two alternatives for PTM and PTP transmission in F1 discussed in the contributions:

- A shared tunnel for PTM transmission and a UE dedicated tunnel for PTP transmission.

- A shared tunnel for PTM transmission and PTP transmission.

Q6: Which alternative for PTM and PTP transmission in F1 is preferred?

| Company | Answer | Comment |
| --- | --- | --- |
| Samsung | Option A | With split bearer like architecture, it is straightforward to use option A. like PDCP duplication transmission, we use two different tunnels in F1, in this way, DU can map the received packets to the corresponding RLC directly. |
| Nokia | Option B (and open point for A) | The nominal case is use of option B. The DU decides to send the data over the PTP or PTM leg. In addition, it is FFS if an additional F1-U tunnel would be used for specific case e.g. only if RAN2 agrees to use PDCP retransmission. |
| Huawei | Option A | As described in our answer to Q1, CU can indicate DU to use PTP transmission per packet by delivering the packet via the UE dedicated tunnel. |
| Intel | Option B | It is more efficient to use just a shared tunnel for both PTM and PTP |
| CATT | Option A (slightly prefer) | This solution is good for PDCP-based retransmission—such retransmission is probably in per-UE manner, and thus more suitable to be delivered over PTP F1-U tunnels, or otherwise gNB-DU cannot distinguish which packet should be sent to which UE. |
| Lenovo, Motorola Mobility | Depends on whether CU or DU decides PTP-PTM switch | If the PTM/PTP switch is decided by the gNB-CU, a shared F1-U tunnel is used for PTM, which an individual F1-U tunnel for PTP and retransmission should be used. If the PTM/PTP switch is decided by the gNB-DU, a shared F1-U tunnel is used for both PTM and PTP, while an individual F1-U tunnel is used for retransmission |
| Ericsson | no decision right now, what for RAN2 | we refuse to discuss this point w/o having a somewhat stable RAN2 concept of what they call “MRB” at hand. |
| CMCC | Option A | Option A supports the PDCP retransmission for each UE for PTP transmission. Option B does not have any F1-U GTP tunnel per each UE for PTP transmission. |
| LG | Option A | Same view with CMCC |

# Conclusion, Recommendations [if needed]

If needed

# References

| [1] | R3-210276 | (TP to TS 38.401 BL CR) Decision on PTP and PTM (Huawei) |
| --- | --- | --- |
| [2] | R3-210312 | Discussion on dynamic change between PTM and PTP (CATT) |
| [3] | R3-210513 | Dynamic switch between PTM and PTP for RRC_CONNECTED UE (CHENGDU TD TECH LTD.) |
| [4] | R3-210533 | Dynamic Change Between PTP and PTM (BEIJING SAMSUNG TELECOM R&D) |
| [5] | R3-210604 | Mode switching for NR MBS (ZTE) |
| [6] | R3-210605 | TP to 38.300 BL CR on mode change between PTP and PTM (ZTE) |
| [7] | R3-210618 | (TP for BL CR 38.401) Dynamic switch between PTP and PTM (Lenovo, Motorola Mobility) |
| [8] | R3-210782 | Issues on dynamic change between PTP and PTM (LG Electronics) |
| [9] | R3-210913 | Discussion on dynamic change between PTP and PTM (CMCC) |