3GPP TSG-RAN WG3 #111-e	R3-211033

E-meeting, 25 January – 4 February 2021

Title: 	Summary of discussion for CB: # 77_ MBS_SvcCont_InactiveUEs

Source: 				CATT

Agenda item:		22.4

Document for:		Discussion and Decision

# 1	Introduction

This is the summary of email discussions on CB #77 of the RAN3 number 111e meeting.

CB: # 77_MBS_SvcCont_InactiveUEs

HW

UEs obtain target/new cell MTCH configuration of a Broadcast Service via target/new cell MCCH/SIB, i.e. no need to exchange target/neighbor cell MTCH configuration of a Broadcast Service via Xn interface.

reuse LTE mechanisms to maintain the broadcast service reception continuity, i.e. support NR MBS frequency layer prioritization, Neighbor cell broadcasting status for ongoing services, and NR MBS interesting indication report for RRC_CONNECTED mode UEs.

To support NR MBS frequency layer prioritization while avoid broadcasting a TMGI list for all MBS services, it is needed to introduce SAI or MBS service group ID for Broadcast Session, and exchange via Xn signaling or/and OAM.

To support Neighbor cell broadcasting status for ongoing services and NR MBS interesting indication report, it is needed to provide the cells list in MBS session start/update from CN to RAN, and the cell list shall include both the cells in the current gNB and also the cells in neighbor gNBs.

CATT

For broadcast session, the information related to MBS service area transmitted via N2 signaling, should contains all cells supporting this MBS service.

The area specific MCCH transmission should be limited to the case of intra-DU in R17.

Len,Moto

consider NR MDT functionality for collecting MBS measurements from UEs in RRC_IDLE and RRC_INACTIVE

(CATT - moderator)

Summary of offline disc R3-211033

# 2	For the Chairman’s Notes

To be added.

# 3	Discussion

## 3.1	MBS reception of idle/inactive UEs

According to the conclusion of last RAN2/3 meeting, whether the reception of multicast services is supported in idle/ inactive mode and the impact to RAN3, is pending RAN2 progress. Therefore, the SOD focuses on the reception of broadcast service for idle / inactive UEs .

### 3.1.1	The acquisition of new cell MTCH configuration of a Broadcast Service

According to the contribution[1], UEs obtain target/new cell MTCH configuration of a Broadcast Service via target/new cell MCCH/SIB, i.e. no need to exchange target/neighbor cell MTCH configuration of a Broadcast Service via Xn interface, as LTE.

Question 1：Do you agree that UEs obtain target/new cell MTCH configuration of a Broadcast Service via target/new cell MCCH/SIB？

| Company | Yes/No | Comments |
| --- | --- | --- |
| Samsung | Pending to RAN2 | How UE obtain need first see RAN2 conclusion. |
| Nokia | Pending to RAN2 |  |
| CATT | Pending to RAN2 |  |
| Ericsson | wait for RAN2 |  |
| Huawei | Yes | Need RAN2 confirm |
| ZTE | Pending to RAN2 |  |

### 3.1.2	Mechanism to support service continuity for broadcast service

RAN2 has discussed the basic mechanism of broadcast session, most companies support the reuse of LTE SC-PTM mechanism. In addition, in LTE, there are several mechanisms to support service continuity for MBMS[1]：

- Option 1: MBMS frequency layer prioritization

- Option 2: Neighbor cell broadcasting status for ongoing services

- Option 3: MII (MBMS interesting indication) report for RRC_CONNECTED mode UEs

According to the discussion of RAN2，supporting NR MBS frequency layer prioritization is considered as baseline for NR broadcast session. Furthermore, most companies support MBS Interest Indication for UEs in connected mode for NR MBS delivery mode 2.

Question 2：Do you agree that NR MBS frequency layer prioritization is considered as baseline to maintain service continuity for broadcast session？ And support MBMS interesting report for RRC_CONNECTED mode UEs？

| Company | Yes/No | Comments |
| --- | --- | --- |
| Samsung | Pending to RAN2 | We are fine to support interest indication from UE. It is pending to RAN2 conclusion. Frequency layer also need RAN2 input. |
| Nokia | Pending to RAN2 | OK for MBS Interest indication. Frequency layer prioritization pending RAN2. |
| CATT | Pending to RAN2 |  |
| Ericsson | wait for RAN2 |  |
| Huawei | Yes | Need RAN2 confirm |
| ZTE | Pending to RAN2 |  |

For option 2, there is still no technical inclination from RAN2, but for broadcast session, it seems reasonable to trigger unicast connection earlier if the MBS service that is receiving is not provided in neighbour cell.

Question 3：Do you agree that Neighbor cell broadcasting status for ongoing services should be supported for NR broadcast session？

| Company | Yes/No | Comments |
| --- | --- | --- |
| Samsung | Pending to RAN2 | Same as question 1, broadcasting information is discussed in RAN2. |
| Nokia | Pending to RAN2 |  |
| CATT | Pending to RAN2 |  |
| Ericsson | wait for RAN2 |  |
| Huawei | Yes | Need RAN2 confirm |
| ZTE | Pending to RAN2 |  |

### 3.1.3	The information to be transferred over NG interface for broadcast service

According to the contribution[1], to support option 1(SAI list and frequency list are broadcasted in SIB), legacy SAI or a new group ID need to be introduced into NG interface.

Question 4：Do you agree that legacy SAI or a new group ID need to be introduced into NG interface to support frequency based solution？

| Company | Yes/No | Comments |
| --- | --- | --- |
| Samsung | Yes/No | Service area is provided for the broadcast serving. We think it could be SAI. Not sure about the group ID. |
| Nokia | No. | Pending RAN2 about which indicator to use. Impacted interfaces FFS. |
| CATT | Yes | An ID similar to legacy SAI should be introduced into NG interface. |
| Ericsson | wait for RAN2 |  |
| Huawei | Yes | A group ID might be reasonable if SAI is not required for other functions. |
| ZTE | Yes/No | Agree with Samsung. Yes for SAI, not sure for group ID. |

Furthermore, to make the current serving cell know MBS service status of its neighboring cells or frequency [2], a list of cell ID should be signaled to NG-RAN via NG interface, which have been agreed in RAN3# 110 meeting, and the cell list at least include both the cells in the current gNB and also the cells in neighbor gNBs[1].

Question 5：Do you agree that for a broadcast service, a list of cell ID over NG interface at least include both the cells in the current gNB and also the cells in neighbor gNBs？

| Company | Yes/No | Comments |
| --- | --- | --- |
| Samsung | Yes | We agreed Broadcast service area info (e.g. a list of cell IDs) is indicated in the NGAP MBS session resource signalling for broadcasting. We think it is service area, so can including the cells in serving gNB and in neighbour gNB. |
| Nokia | Partly | It includes at least the cells of the current gNB. Whether it includes cells of the neighbor gNB depends on the questions above. |
| CATT | Yes | At least, for broadcast service, such a cell list is required. |
| Ericsson | Partly | NG signalling needs a broadcast area indication, that’s for sure. Whether this needs to be on cell level is not for sure. |
| Huawei | Yes | Cells in neighbor gNBs can be used for “Neighbor cell broadcasting status for ongoing services” |
| ZTE | Partly | Agree with Nokia. Cells of the current gNB should be included, but not sure for cells of neighbor gNB. |

### 3.1.4	The support of area specific MCCH transmission

According to the contribution[2], there is potential impact on RAN3 for area specific MCCH transmission, and in the case of intra-DU, this optimization can be supported by implementation, but for Inter-DU and Inter-CU, the impact on RAN3 interface will not be negligible.

Question 6：Do you agree that the area specific MCCH transmission should be limited to the case of intra-DU in R17？

| Company | Yes/No | Comments |
| --- | --- | --- |
| Samsung | Pending to RAN2 | We are not sure. It is seems reasonable, but related to MCCH conclusion. Pending to RAN2. |
| Nokia | Pending to RAN2 |  |
| CATT | Pending to RAN2 |  |
| Ericsson | wait for RAN2 |  |
| Huawei | Pending to RAN2 | RAN2 is still discussing on the need for area specific MCCH. |
| ZTE | Pending to RAN2 |  |

## 3.2	Measurements for NR MBS in idle/inactive

According to the contribution [3], in LTE, to verify the performance of DL transmissions w/o UL feedback, the collection of MBMS related measurements using MDT was agreed in Rel-12. Therefore, similar work can be done for NR MBS, e.g, with the logged MBS measurements collected from multiple UEs, the Gnb is enabled to verify the performance of MBS transmissions in RRC_IDLE and RRC_INACTIVE and can reconfigure the MBS service areas and MBS operation parameters if needed.

Question 7：Do you agree to consider NR MDT functionality for collecting MBS measurements from Ues in RRC_IDLE and RRC_INACTIVE.？

| Company | Yes/No | Comments |
| --- | --- | --- |
| Samsung | No |  |
| Nokia | Pending to RAN2 |  |
| CATT | No for the time being | It could be introduced in the later release of MBS. |
| Ericsson | wait for RAN2 |  |
| Huawei | No | Not needed at least in this version |
| ZTE | No |  |

## 3.3	Other issues

For idle/inactive UEs, if you have other issues to be discussed, please elaborate:

| Company | Yes/No | Comment |
| --- | --- | --- |

# 4	Conclusions

According to companies’ inputs, the followings are proposed:

# 5	Reference

- R3-210285  (TP to TS 38.300 BL CR) Service reception continuity for broadcast service (Huawei)

- R3-210464  MBS reception of Idle and In-active Ues (CATT)

- R3-210623  Considerations on measurements for NR MBS in idle/inactive (Lenovo, Motorola Mobility)