3GPP TSG-RAN WG3 #111-e	R3-211049

Online, 25 January - 5 February 2021

Agenda Item:	7

Source:	Ericsson (moderator)

Title:	CB: # 81_Ch10_NGAP_S1AP - Summary of email discussion

Document for:	Approval

# Introduction

This was captured during the online session:

CB: # 81_Ch10_NGAP_S1AP

- shall vs. may be considered not comprehended: shall seems better

- clarify other impacts (if any)

- impacts to e.g. E1AP/F1AP? Should check also other specs?

- not supported/not comprehended

- fix cover sheet: other specs affected

(E/// - moderator)

Summary of offline disc R3-211049

# For the Chairman’s Notes

Propose the following:

R3-211086 (revision of R3-210630) – agreed

R3-211087 (revision of R3-210631) – agreed

to be added, if any

# Discussion [if needed]

## General

The moderator understood from the online discussions, that the CRs submitted are supported in principle by many companies. Please speak up in case you have reservations to agree on them (given the suggested revisions). In case of reservations, please specify below, whether your reservation is general, concerns agreeing on them at RAN3#111 or concerns the suggested Release

| Company | Comment |
| --- | --- |

The following changes have been made to the CRs in [2] and [3]:

1)	The new specification text was changed from “... may be considered not comprehended” to “... shall be considered not comprehended” in [2] and [3].

2) The NGAP CR [2] cover sheet was modified to include the affected TSs: 38.423, 38.455, 38.463, 38.473, 37.463

3)	The S1AP CR [3] cover sheet was modifed to include the affected TSs: 36.423, 36.443, 36.444, 36.455, 36.459, 36.463

4)	Coversheet correction for the S1AP CR [3] (Release was missing)

Please provide comments, if any, to the modifications performed along the items above:

| Company | Comment |
| --- | --- |

## Applicability of chapter 10.2.3 for all criticality values

There were discussions on whether the changes in [2] and [3] would have any unwanted effect on IEs or IE groups with the criticality assigned to “ignore”.

The moderator understands that IEs or IE groups with the criticality assigned to “ignore” can indeed from an abstract syntax and functional group be “ignored” if not comprehended/supported. IEs and IE groups which, if not comprehended would not allow the procedure to be continued should be set to “reject”.

Please provide your further considerations, if any, below:

| Company | Comment |
| --- | --- |

## Other Identified issues

Please include below any other topic or correction missing in the ones listed above:

| Company | Comment |
| --- | --- |
| Ericsson | TS 38.455 Chapter 10 refers to chapter 10 in 36.455, while Chapter 9.0 refers to 38.413. Moderator suggests that this is corrected and triggered the rapporteur to provide CRs. |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-210629	Discussions on Chapter 10 in S1AP and NGAP (Ericsson), discussion

R3-210630	Correction for Chapter 10 (Ericsson), CR0558r, TS 38.413 Rel-16

R3-210631	Correction for Chapter 10 (Ericsson)	CR1804r, TS 36.413 Rel-16