3GPP TSG-RAN WG3 #111-e							R3-211050

25 January – 4 February 2021

Title:	Summary of offline discussion for LS on Small Data Transmission

Source:	Ericsson

Agenda Item:	8.1

Document for:	Approval

# Introduction

CB: # 82_SDT_LS

- no showstopper in RAN3

- need to clarify where RLC is processed? (to clarify further RAN3 work, if agreeable)

- clarify case for non-SD data coming?

- any clarifications to ask RAN2? (including e.g. assistance info?)

- clarify security concerns; if needed, add SA3 to LS

- should leave details to basket CB; concentrate on reply LS; no TUs for this topic at this meeting!

- merge if needed from other papers, LSs

(E/// - moderator)

Summary of offline disc R3-211050

0500 rev in R3-211051

# For the Chairman’s Notes

Propose the following:

R3-211051 – agreed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion

## Issue 1

Confirm no issue is foreseen from RAN3’s point of view to support anchor relocation scenario for small data transmission, by reusing the legacy context fetch procedure.

| Company | Comment |
| --- | --- |
| E/// | Yes |
| CMCC | Yes |
| Qualcomm | yes |
| CATT | Yes |

## Issue 2

To support non-anchor relocation case, RAN3 needs further discussion on the detailed solutions. Before that, we need to figure out if any impact is foreseen from RAN2’s agreement and assumption.

RAN2 has agreed that RLC configuration is stored in the UE context. Based on that, RAN3 would consider how to handle the data properly, i.e., normal context fetch as for anchor relocation case, partial context fetch (e.g., including RLC config and etc), or no context fetch. The feasibility and complexity of solutions should be analyzed after WI starts in RAN3.

At the same time, in the LS there is one assumption that RLC handling will be processed in the receiving gNB. Considering the openness of RAN3 solutions, should we reply to RAN2 that we prefer no restriction on which node to handle the RLC config and wait for further comparison?

| Company | Comment |
| --- | --- |
| E/// | In RAN2 there was no detailed discussion and analysis of clear benefits by capturing this. RAN3 needs to discuss all the possible solutions after checking the pros and cons. Reply to RAN2 that there should not be any restriction on which node to handle RLC config. We assume RLC handling can either reside in the receiving gNB or the last serving gNB. |
| CMCC | The same view as Ericsson, since the analysis on all the candidate solutions will be done when the WI in RAN3 starts, we should reply to RAN2 and indicates no RAN3 restrictions on which node to handle RLC configuration. |
| Qualcomm | Actually we don’t even think there was an agreement in RAN2 related to where the RLC layer is (the LS does not say it either), For now we should reply as indicated by Ericsson. |
| CATT | Similar view with E///. We could indicate RAN2 that how to proceed with RLC handling for SDT need to be further discussed. |

## Issue 3

Which node will be the decision maker for with or without anchor relocation?

| Company | Comment |
| --- | --- |
| E/// | The last serving gNB who has the UE context. |
| CMCC | The anchor gNB, i.e., the last serving gNB. |
| Qualcomm | As a “working assumption”, the last serving gNB/anchor. |
| CATT | The anchor gNB, i.e., the last serving gNB. |

## Issue 4

How to handle the first UL message containing DRB data for SDT?

- For anchor relocation case, the data can be buffered until the context fetch procedure is completed.

- For non-anchor relocation, the process has dependency on the final solution. Either the data is buffered in the receiving gNB until possible full/partial context fetch is done, or encapsulated and transferred to the last serving gNB after arrival.

| Company | Comment |
| --- | --- |
| E/// | From RAN3 point of view, the network solutions work no matter the data is buffered or not. Since the anchor gNB may decide whether to relocate the anchor or not, it is reasonable to buffer the data until the UE context retrieval procedure is completed. |
| CMCC | Yes for anchor relocation case, but for the non-anchor relocation case, it depends on the solutions which need further discussion. |
| Qualcomm | Agree with Ericsson and CMCC. Actually even for non-anchor relocation, buffering may be required – it depends on the final solution. |
| CATT | Agree with E///, CMCC, QC. For non-anchor relocation case: The data may need to be buffered in the receiving node if the RLC handling is in the receiving node. The data could be provided to the anchor timely, e.g. included in the Retrieve UE Context Request if RLC handling is proceed in the anchor. |

## Issue 5

If the conclusion to issue 3 is the last serving gNB, RAN3 may consider the introduction of UE assistance information to help the last serving gNB to make decision whether to relocate the anchor. Several options are on the table, i.e., BSR, traffic pattern, or a simple indicator to indicate single or multiple data.

| Company | Comment |
| --- | --- |
| E/// | The proposed assistance info may be beneficial. Final solution depends on how to interpret the information from UE. For now we don’t have to ask RAN2 for feedback unless any action of alignment is required. Instead, we can inform them that RAN3 is going to discuss this point. |
| CMCC | Yes, we can inform RAN2 assistance information is needed, details need further discussion. |
| Qualcomm | Agree with CMCC |
| CATT | Agree with CMCC. |

## Issue 6

Is there any scenario needs to be addressed without anchor relocation? For example, should the UE stay in INACTIVE or change to CONNECTED state if there is arrival of upcoming non-SDT data after SDT?

| Company | Comment |
| --- | --- |
| E/// | Leave to future discussion on scenarios. |
| CMCC | Seems not need to touch this aspect at this reply LS |
| Qualcomm | No need to discuss this for now. |
| CATT | Non business with the incoming LS, it could be discussed later. |

## Issue 7

In case of non-anchor relocation, if the newly arrived encrypted small data needs to be decoded in the receiving gNB, will it be any security issue since both nodes will be able to see the same data? Do we need to send this LS also to SA3?

| Company | Comment |
| --- | --- |
| E/// | Yes. Check with SA3. |
| CMCC | Yes |
| Qualcomm | Yes we mentioned this also – two nodes operating with same keys potentially. Whether we trigger SA3 now or later can be discussed. |
| CATT | No matter RLC handling is preceded in the receiving node or the anchor gNB, we assume the PDCP handling should be preceded in the anchor gNB definitely. Therefore, we do not see any need to decode the encrypted data in the receiving node in case of non-anchor relocation. In our understanding, following the security strategy of SA3, the same keys could not be used in different nodes. |

## Issue 8

How the DRB data is included in the first UL message? Either in RRCResumeRequest message or MAC SDU? Will this impact RAN3’s solution? Do we need to ask RAN2?

| Company | Comment |
| --- | --- |
| E/// | Wait for RAN2’s discussion in parallel. |
| CMCC | Monitor RAN2 progress, in our view, it is concatenated with the MAC SDU which carries RRCResumeRequest message |
| Qualcomm | This seems a useful thing to know, but we can leave to RAN2 to work on. |
| CATT | Internal checked with RAN2 colleague, it should be the separate MAC-SDU, not included in the RRCResumeRequest message. |

## Issue 9

Do we need to ask RAN2 whether the logical channel configuration is required at the receiving gNB when derive the RLC PDU?

| Company | Comment |
| --- | --- |
| E/// | No. It depends on which solution RAN3 will go for. |
| CMCC | Depends on solutions |
| Qualcomm | Not for now. |
| CATT | Pending to the solution decided for non-anchor relocation case. |

## Issue 10

Which node will determine the SDT bearer type (i.e., CG-SDT bearer and RACH-SDT bearer). Whether one DRB can be CG-SDT bearer and RACH-SDT or not?

| Company | Comment |
| --- | --- |
| E/// | Wait for progress in RAN2. |
| CMCC | RAN2 topic |
| Qualcomm | Can be left to RAN2. |
| CATT | Pending to RAN2. |

## Issue 11

Although CG-SDT is not within RAN3’s scope for SDT WI, some companies brought potential impacts by supporting CG-SDT over F1 interface. Do we need to ask RAN2 for any clarification?

| Company | Comment |
| --- | --- |
| E/// | No. F1 impacts should be discussed in RAN3. |
| CMCC | RAN3 could do the work on F1 impacts. RAN2 is not the WG to clarify the WI scope. CG-SDT is in the scope, if F1 impact is found, we can do the job |
| Qualcomm | Seems no need to ask for clarification: once we have actual TUs, this can be discussed based on proposals / analysis in RAN3. |
| CATT | No need to ask RAN2, the potential F1 impact could be further discussed in RAN3. |

# Conclusion, Recommendations

If needed

# References