3GPP TSG-RAN WG3#111-e			R3-211204

E-Meeting, 25 January – 04 February 2021

Title:	LS on Emergency Indicator in Emergency Fallback

Response to:

Release:	Rel-15/16

Work Item:	NR_newRAT-Core

Source:	RAN3

To:	SA2

Cc:

Contact Person:

#### Name:	Philippe Godin

Tel. Number:	+33 1 6040 0304

E-mail Address:	philippe.godin@nokia.com

Attachments:

1. Overall Description:

RAN3 has discussed the following statement in section 4.11.1.2.1 of TS 23.502:

If the handover is triggered due to Emergency fallback, the NG-RAN may forward the Emergency indication to the target eNB in the Source to Target Transparent Container, and the target eNB allocates radio bearer resources taking received indication into account

This indicator is currently not included in RAN3 Source to Target container.

Before proceeding with further alignment work, RAN3 would appreciate if SA2 could clarify the involved scenario and why this indicator needs to be transparent to CN nodes and could not be directly by CN node to target eNB? Note that eNB uses ARP to handle the emergency VoIP call.

2. Actions:

To SA2 group:

ACTION: 	RAN3 would like to ask SA2 to clarify the scenario and the need of this indicator in a transparent container before proceeding with alignment.

3. Date of Next TSG-RAN WG3 Meetings:

TSG-RAN WG3#112-e                       17 May – 27 May 2021			E-meeting