3GPP TSG-RAN WG3 #111-e	draft- R3-211060

Online, 25th January -5th February 2021

Agenda Item:	9.3.3

Source:	Ericsson (moderator)

Title:	Summary of Offline Discussion: E-RABs_that_cannot_be_handed_over

Document for:	Approval

# Introduction

CB: # 89_E-RABs_that_cannot_be_handed_over

- issue seems acknowledged

- prefer to avoid waiting for timer as per 25.413? Risk of rejecting SRVCC?

- CT1 solution? Issue with backwards-compatibility w.r.t. UEs? If preferable, liaise CT1?

(E/// - moderator)

Summary of offline disc R3-211060

# For the Chairman’s Notes

RAN3 agrees to send LS R3-211088

# Discussion

The issue discussed in [1] is with the introduction of NR, the PS bearers set up to 5G may not be able to handover to 3G, e.g.: 5G without TI cannot be handed over to 2/3G; PDNs setup in LTE with flags: “5GSIWK” or “5GCNRI” is set to 1 and sent to PGW/SMF, cannot be handed over to 2/3G either, because these PDNs are allocated with 5G PDU session ID and 5G QoS, etc. Similarly, some E-RAB from 2G/3G cannot be handed over to 5G.

The issue seems be acknowledged by RAN3.

According to the online discussion, RAN3 will send a LS to SA2 (CcCT1) for guidance and investigation from their side.

The draft LS to SA2 is prepared.

# Conclusion, Recommendations

It is agreed to send LS to SA2 (Cc CT1/CT4) to highlight the issue and ask for the guidance.

# References

R3-210889	Indicating E-RABs that cannot be handed over to 2G/3G or 5G (Ericsson)

R3-210890	Indicating E-RABs that cannot be handed over to 2G/3G or 5G (Ericsson)

R3-210891	Indicating E-RABs that cannot be handed over to 2G/3G or 5G (Ericsson)