3GPP TSG-RAN WG3 #111-e	draft-R3-210961

Online, 25th January -5th February 2021

Agenda Item:	9.3.3

Source:	Ericsson (moderator)

Title:	Summary of Offline Discussion on CB: # 8_ASrekey_EmergencyFallback

Document for:	Approval

# Introduction

CB: # 8_ASrekey_EmergencyFallback

Nok

specify abnormal condition for NG-RAN node to fail the procedure with UE Context Modification Failure

HW

leave the NG-RAN node handling for such rare and abnormal case to implementation

E///,ZTE

NG-RAN node shall only handle the Emergency Fallback in case it is requested together with AS Re-keying in the same UE context modification message; liaise back SA2

CATT

In case of collision between emergency fallback and AS re-keying, NG-RAN should succeed the UE Context Modification procedure, and indicate AMF AS re-keying is failed due to the collision of the procedures.

An indication should be introduced in the UE CONTEXT MODIFICATION RESPONSE message to indicate the failure of AS re-keying procedure due to the collision.

- consensus for “light” approach / leaving to implementation

- check details

(E/// - moderator)

Summary of offline disc R3-210961

# For the Chairman’s Notes

[TBD]

# Discussion

Among the interested companies’ contributions, the sets of solutions proposed to handle when AS rekeying and Emergency Fallback are requested in the same UE context Modification message are:

- to specify abnormal condition for NG-RAN node to fail the procedure with UE Context Modification Failure (Nokia in [1], [2], [3])

- to leave the NG-RAN node handling for such rare and abnormal case to implementation (Huawei in [4], [5], [6])

- to specify that NG-RAN should ignore the AS Rekeying and proceed with Emergency fallback (Ericsson, ZTE in [7], [8], [9]

- NG-RAN should succeed the UE Context Modification procedure and indicate AMF AS re-keying is failed due to the collision of the procedures. (CATT in [11], [12], [13])

A LS is also proposed to send back to SA2 to make a closure of the discuss related to the AS rekeying and Emergency fall back in [10].

As a first step, we discuss the four cases when old and new AMF and NG-RAN nodes are involved.

| Case | Configuration |
| --- | --- |
| Case 1 | New AMF, new NG-RAN node |
| Case 2 | New AMF, old NG-RAN node |
| Case 3 | Old AMF, old NG-RAN node |
| Case 4 | Old AMF, new NG-RAN node |

In below, two requests are “AS Rekeying request” and “Emergency Fallback” request.

New AMF:  means the AMF implemented the SA2 solution.

New NG-RAN node: means the NG-RAN node having the solution that we are discussing in this CB.

Question 1: for Case 1 and Case 2, the new AMF should make sure the two requests are not sent in the same UE context modification message. There should be no issue, do you agree?

| Company | Comment |
| --- | --- |
| Ericsson | Yes |

Question 2: Case 3 is legacy. It belongs to a normal operation that the two requests are sent in the same UE context modification message. Do you agree?

| Company | Comment |
| --- | --- |
| Ericsson | Yes The NGAP protocol allows the two requests to be sent in the same message and specify the handling that NG-RAN node should handle the two requests. |

Question 3: Case 4 is when the old AMF sends two requests in the same UE context modification message, what should a new NG-RAN node do? We need to find solution for this case, do you agree?

| Company | Comments |
| --- | --- |
| Ericsson | Yes. We think this is the case that we need a solution. And in our view, the solution should not differ so much with the legacy Case 3. We propose that the new NG-RAN node is allowed to ignore the AS rekeying request and only perform Emergency Fallback. Note that with this solution: the new NG-RAN node is still be able to perform as the old NG-RAN node to handle the two requests. The new NG-RAN node can ignore the AS Rekeying and only perform emergency fallback |

# Conclusion, Recommendations

If needed

# References

R3-210046	Correction of AS Rekeying and Emergency Fallback (Nokia, Nokia Shanghai Bell)	discussion

R3-210047	Correction of AS Rekeying and Emergency Fallback (Nokia, Nokia Shanghai Bell)	CR0531r, TS 38.413 v15.10.0, Rel-15, Cat. F

R3-210048	Correction of AS Rekeying and Emergency Fallback (Nokia, Nokia Shanghai Bell)	CR0532r, TS 38.413 v16.4.0, Rel-16, Cat. A

R3-210128	Consideration on AS-rekey and Emergency fallback (Huawei)	discussion

R3-210129	Correction on AS-rekey and Emergency fallback (Huawei)	CR0539r, TS 38.413 v15.10.0, Rel-15, Cat. F

R3-210130	Correction on AS-rekey and Emergency fallback (Huawei)	CR0540r, TS 38.413 v16.4.0, Rel-16, Cat. A

R3-210327	AS re-keying and Emergency Fallback in the UE Context Modification procedure (Ericsson)	discussion

R3-210328	Clarification of AS re-keying in the UE Context Modification procedure (Ericsson, ZTE)	CR0354r4, TS 38.413 v15.10.0, Rel-15, Cat. F

R3-210329	Clarification of AS re-keying in the UE Context Modification procedure (Ericsson, ZTE)	CR0355r4, TS 38.413 v16.4.0, Rel-16, Cat. A

R3-210330	Draft] Reply LS on AS rekeying handling (Ericsson)	LS out

R3-210466	Discussion on AS rekey and Emergency fallback (CATT)	discussion

R3-210467	Correction on collision of AS-rekey and Emergency fallback_NGAP Rel-15 (CATT)	CR0551r, TS 38.413 v15.10.0, Rel-15, Cat. F

R3-210468	Correction on collision of AS-rekey and Emergency fallback_NGAP Rel-16 (CATT)	CR0552r, TS 38.413 v16.4.0, Rel-16, Cat. A