3GPP TSG-RAN WG3 Meeting #111e	R3-211102

25 January -04 Feburary 2021

Online

| CR-Form-v12.1 |
| --- |
| CHANGE REQUEST |
|  | 38.401 | CR | 0168 | rev | 1 | Current version: | 16.4.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME |  | Radio Access Network | X | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Stage-2 CR on transmission stop for Rel-16 DAPS handover |
| --- | --- |
| Source to WG: | Samsung, Intel Corporation, CATT |
| Source to TSG: | R3 |
| Work item code: | NR_Mob_enh-Core |  | Date: | 2021-01-28 |
| Category: | F |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) … Rel-15 (Release 15) Rel-16 (Release 16) Rel-17 (Release 17) Rel-18 (Release 18) |
| Reason for change: | In TS38.401, a NOTE is given for inter-gNB-DU mobility as below: NOTE: In case of DAPS Handover, the UE CONTEXT MODIFICATION REQUEST message in step 5 does not indicate to stop the data transmission for the UE. Instead, the DL RRC Message Transfer procedure can be used which carries the handover command to the UE. The UE CONTEXT MODIFICATION REQUEST message that indicates to stop the data transmission for the UE is sent to the source gNB-DU once the gNB-CU knows that the UE has successfully accessed the target gNB-DU, for which the source gNB-DU sends a DDDS frame about the unsuccessfully transmitted downlink data to the gNB-CU. This note indicates that the source gNB-DU will perform as normal case (non-handover) for data packet transmission, i.e., gNB-CU continuously sends DL packets of DAPS bearers to the source gNB-DU Source gNB-DU continuously schedules DL resource for packet transmission of DAPS and non-DAPS bearers, where packets include the ones already buffered at the source gNB-DU for both DAPS and non-DAPS bearers and the ones from gNB-CU for DAPS bearers Source gNB-DU continuously schedules UL resource for packet transmission of DAPS and non-DAPS bearers These behaviors are not aligned with the intention of DAPS handover, and may cause that: non-DAPS bearers may interrupt the data transmission of DAPS bearers To solve the above problem, it is better to allow the source gNB-DU know the data transmission of which bearers should be stopped during the DAPS handover procedure. |
| Summary of change: | Clarify to stop transmission for bearers not subject to DAPS handover during DAPS inter-gNB-DU mobility Impact Analysis: Impact assessment towards the previous version of the specification (same release): This CR has isolated impact on the procedure for the inter-gNB-DU mobility |
| Consequences if not approved: | DAPS handover cannot work properly for CU-DU split case. |
| Clauses affected: | 8.2.1.1 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | x | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | x | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

| This CR's revision history: | Rev#1: Clarify the indication to stop transmission of non-DAPS bearer may be contained in Step 5. |
| --- | --- |

-------------------------------------------Change 1-------------------------------------------

## 8.2	Intra-gNB-CU Mobility

### 8.2.1	Intra-NR Mobility

#### 8.2.1.1	Inter-gNB-DU Mobility

This procedure is used for the case when the UE moves from one gNB-DU to another gNB-DU within the same gNB-CU during NR operation. Figure 8.2.1.1-1 shows the inter-gNB-DU mobility procedure for intra-NR.

Figure 8.2.1.1-1: Inter-gNB-DU Mobility for intra-NR

1.	The UE sends a MeasurementReport message to the source gNB-DU.

2.	The source gNB-DU sends an UL RRC MESSAGE TRANSFER message to the gNB-CU to convey the received MeasurementReport message.

2a.	The gNB-CU may send an UE CONTEXT MODIFICATION REQUEST message to the source gNB-DU to query the latest configuration.

2b.	The source gNB-DU responds with an UE CONTEXT MODIFICATION RESPONSE message that includes full configuration information.

3.	The gNB-CU sends an UE CONTEXT SETUP REQUEST message to the target gNB-DU to create an UE context and setup one or more data bearers. The UE CONTEXT SETUP REQUEST message includes a HandoverPreparationInformation. In case of NG-RAN sharing, the gNB-CU includes the serving PLMN ID (for SNPNs the serving SNPN ID).

4.	The target gNB-DU responds to the gNB-CU with an UE CONTEXT SETUP RESPONSE message.

5.	The gNB-CU sends a UE CONTEXT MODIFICATION REQUEST message to the source gNB-DU, which includes a generated RRCReconfiguration message and indicates to stop the data transmission for the UE. The source gNB-DU also sends a Downlink Data Delivery Status frame to inform the gNB-CU about the unsuccessfully transmitted downlink data to the UE.

NOTE:	In case of DAPS Handover, for step 5, the gNB-CU may indicate to stop the data transmission only for the DRB(s) not subject to DAPS handover. Instead, either the UE CONTEXT MODIFICATION REQUEST message or the DL RRC MESSAGE TRANSFER message can be used to carry the handover command to the UE. The UE CONTEXT MODIFICATION REQUEST message that indicates to stop the data transmission for the UE is sent to the source gNB-DU once the gNB-CU knows that the UE has successfully accessed the target gNB-DU, for which the source gNB-DU sends a DDDS frame about the unsuccessfully transmitted downlink data to the gNB-CU.

The source gNB-DU forwards the received RRCReconfiguration message to the UE.

7.	The source gNB-DU responds to the gNB-CU with the UE CONTEXT MODIFICATION RESPONSE message.

8.	A Random Access procedure is performed at the target gNB-DU. The target gNB-DU sends a Downlink Data Delivery Status frame to inform the gNB-CU. Downlink packets, which may include PDCP PDUs not successfully transmitted in the source gNB-DU, are sent from the gNB-CU to the target gNB-DU.

NOTE:	It is up to gNB-CU implementation whether to start sending DL User Data to gNB-DU before or after reception of the Downlink Data Delivery Status.

9.	The UE responds to the target gNB-DU with an RRCReconfigurationComplete message.

10.	The target gNB-DU sends an UL RRC MESSAGE TRANSFER message to the gNB-CU to convey the received RRCReconfigurationComplete message. Downlink packets are sent to the UE. Also, uplink packets are sent from the UE, which are forwarded to the gNB-CU through the target gNB-DU.

11.	The gNB-CU sends an UE CONTEXT RELEASE COMMAND message to the source gNB-DU.

12.	The source gNB-DU releases the UE context and responds the gNB-CU with an UE CONTEXT RELEASE COMPLETE message.