3GPP TSG-RAN WG3 #111-e							R3-211009

25 January – 4 February 2021

Online

Agenda Item:	14.2

Source:	ZTE (moderator)

Title:	Summary of Offline Discussion on MRDC2 - SCG (de)activation

Document for:	Approval

# Introduction

CB: # MRDC2-SCG_activation_deactivation

- Signaling design for MN initiated SCG (de)activation

- signaling design for SN initiated SCG (de)activation, check RAN2 progress

- How to handle the SCG (de)activation failure case?

- Any impact on Activity notification?

- Impact on F1 and E1 interfaces?

- Capture agreements as stage2/stage3 CRs and check details, split work, if needed

- List open issues for next meeting in the summary

(ZTE - moderator)

Summary of offline disc R3-211009

# For the Chairman’s Notes

[TBD]

# Discussion

It is proposed to divide the discussion into two phases:

-	Phase 1: Identify the issues to be discussed in RAN3

Deadline: Please provide your views by 11:00am UTC Wednesday January 27th (i.e. before the scheduled online session for IIoT)

-	Phase 2: Further discussion to capture agreements and open issues

Deadline: TBD pending outcome of Phase 1

## General issue

In the last RAN3 #110 e-meeting, the following agreements are achieved.

- MN can initiate SCG (de)activation during SN addition procedure, SN can decide whether to accept or reject SCG (de)activation request after receiving SN addition request message, FFS on how to reject it.

- MN initiated SN modification procedure can be used for support of SCG (de)activation, and SN can decide whether to accept or reject SCG (de)activation request after receiving SN modification request message.

- Activity Notification message sent from SN to MN, can be used for the MN to make final decision on SCG (de)activation. It is FFS whether no spec impacts or the Activity Notification message shall be enhanced, e.g., add a new SCG (de)activation suggestion IE.

In the RAN2 #112 e-meeting, the following agreement is also achieved, which is aligned with RAN3 agreement as above.

SCG activation state (activated/deactivated) can be configured at PSCell addition/change, RRC resume or HO.

## MN initiated SCG activation and deactivation

### TS36.423/38.423

SN addition request message

It is already agreed that SN addition request message can be used for SCG (de)activation. However, there is a question that whether current SN addition request message is by default configured with activation. In other word, for this message, the activation/deactivation indicator shall be set to deactivation if needed, if the activation/deactivation indicator is not existed, it means that SN addition request message is set to activation as legacy.

SN addition request acknowledge message/ SN addition request reject message

In this meeting, some contributions address to this issue, i.e., how to reject SCG (de)activation. There are 3 methods.

- Not allowed to reject SCG (de)activation (i.e., the SN shall send acknowledge message)

- Part fail (i.e., the SN shall send acknowledge message, but including different SCG (de)activation result from that in SN addition request message)

- Reject (i.e., the SN shall send reject message).

In rapporteur’s view, for simplicity, we can in the first step (i.e., as baseline) allow the SN to either accept or reject the request with adding a new Cause value (activation/deactivation reason), i.e., to reuse the legacy SN addition procedure as possible. Then we can further deeply think of it in the future meeting.

- SN addition request: Adding a new IE (e.g., SCG (de)activation request)

- SN addition request acknowledge :Adding a new IE (e.g., SCG (de)activation result)

- SN addition request reject message (Adding a new Cause value, e.g., SCG (de)activation reject)

Question 1a: Companies are kindly invited to input your view on which option for SN addition request?

| SN addition request: Adding a new IE (e.g., SCG (de)activation request) 1) 0=activate, 1=de-activate (if “activate” and if not included, the SCG is assumed active) 2) de-activate indicator (if not included the SCG is assumed active) |
| --- |
| Company | Yes/NO | Comment |
| ZTE | Yes | 1) |
| Nokia | Yes/No | For the ADD REQ and ACK, only the deactivation flag is needed – if not included the SCG is assumed active. |
| Samsung |  | Prefer to 1) |
| LGE |  | Agree with Nokia, only the deactivation flag is needed |
| Huawei |  | 1) |
| Lenovo, Motorola Mobility |  | 2) to align with the legacy. |
| InterDigital |  | 1) |
| E/// | Yes | 1 |
| CATT | Yes | 1) |
| Qualcomm | Yes | 1) |
| NEC |  | May be 2) is enough. |
| Google |  | 2) |

Summary: Option1: 8 companies, Option2: 4 companies.

WA 1: Add a new IE, e.g., “SCG activation requested” in the SN addition request message, if the IE is set to 0 or is not existed, the SCG is requested to activate. FFS: Add a new IE, e.g., “SCG activation requested” including “deactivation flag” in the SN addition request message, if the IE is not existed, the SCG is requested to activate.

Question 1b: Companies are kindly invited to input your view on which option for SN addition request acknowledge?

| SN addition request acknowledge: Adding a new IE (e.g., SCG (de)activation result) 1) 0=activate, 1=de-activate (if “activate” and if not included, the SCG is assumed active) 2) de-activate indicator (if not included the SCG is assumed active) 3) N/A: No enhancement |
| --- |
| Company | Yes/NO | Comment |
| ZTE | Yes | 1) |
| Nokia | Yes/No | For the ADD REQ and ACK, only the deactivation flag is needed – if not included the SCG is assumed active. |
| Samsung |  | 1) |
| LGE |  | only the deactivation flag is needed |
| Huawei |  | 1) |
| Lenovo, Motorola Mobility |  | 1) when MN initiates SN addition with SCG deactivated, it’s ok for the SN to partially reject the deactivation by indicating the SCG (de)activation result. When MN initiates SN addition with SCG activation, we don’t think partial rejection really makes sense. |
| InterDigital |  | 1) |
| E/// | Yes | 1, furthermore prefer to change to activated, de-activated as status. |
| CATT | Yes. | Same view as E/// |
| Qualcomm | Yes | 1), agree with Ericsson on change to status |
| NEC |  | Considering also backward compatibility with existing SN, 2) should be chosen. |
| Google |  | 2) |

Summary:  Option1: 8 companies and Option2: 4. If option1, one company further indicates that the SN is allowed to partially reject by response message including different SCG activation result if receiving SCG deactivated, otherwise, the SN shall reject by reject message.

WA 2: Add a new IE, e.g., “SCG activation result” in the SN addition response message, if the IE is set to 0, the SCG is activated. FFS1: If SCG is requested to activate, the SN can either partially reject by response message or fully reject by reject message. FFS2: Add a new IE, e.g., “SCG activation result” including “deactivation flag” in the SN addition response message, if the IE is not existed, the SCG is activated.

Question 1c: Companies are kindly invited to input your view on which option for SN addition request reject message?

| SN addition request reject: 1) Allow to reject with a new Cause 2) N/A: Not allow to reject |
| --- |
| Company | Yes/NO | Comment |
| ZTE | Yes | 1) |
| Nokia | Yes/No | For the ADD REQ and ACK, only the deactivation flag is needed – if not included the SCG is assumed active. |
| Samsung |  | For SN ADD REQ Reject, legacy message can be reused. We also prefer to allow the partial reject, i.e., using ADD REQ ACK message to reject the SCG (de-)activation. Moreover, when using this method, the cause value can be included. |
| LGE |  | For MN initiating SCG (de)activation during SN addition procedure, it seems that there is no reason that SN rejects SCG activation only. The rejection should be to the whole SN Addition procedure. Therefore, the existing cause value can be reused. |
| Huawei | No | The SCG activation/deactivation flag in the SN addition response, allows the SN to accept the SN addition and in the meanwhile do not accept the SCG activation/deactivation, so we do not see the need to do reject with a new cause. And it is allowed for the SN to reject the whole SN addition, and in such case, there seems no need to have this new cause as well. |
| Lenovo, Motorola Mobility |  | 1) |
| InterDigital |  | Agree with Huawei |
| E/// |  | We don’t see the necessity for SN to fail the addition procedure just for SCG (de)activation purpose. However, the tricky part is when a new cause value is introduced in the Cause IE, it can be used for all the cases anyway. |
| CATT |  | Agree with HW, use the response message for the SCG state rejection. But not reject the whole addition. |
| Qualcomm | No | The use case of SN addition rejection due to activation/deactivation failure is not clear. |
| NEC |  | Even if “if not included the SCG is assumed active” will be accepted, considering SN may reject for any reason (i.e. cannot even activate), then it should allow to reject with new Cause. |
| Google |  | 1) |

Summary:  Majority companies agree that the SN is allowed to partially reject the SCG deactivation request. But we do not achieve consensus on either fully or partially reject the SCG activation request.

Proposal 1: During SN addition procedure, if request of SCG deactivation, 1) SN uses the response message including “SCG activation” result to partially reject;

Open issue 1: During SN addition procedure, if reject the request of SCG (de)activation

1) SN uses the response message including “SCG deactivation” result to partially reject;

2) SN uses the reject message including new Cause value;

3) SN uses the reject message as legacy (without new Cause)

SN modification procedure

- SN modification request (Adding a new IE, e.g., SCG(de)activation request )

- SN modification request acknowledge (Adding a new IE, e.g., SCG(de)activation result)

- SN modification request reject message (Adding a new Cause value, e.g., SCG (de)activation reject)

Question 2a: Companies are kindly invited to input your view on which option for SN modification request?

| SN modification request (Adding a new IE, e.g., SCG(de)activation request ) 1) 0=activate, 1=de-activate (if “activate” and if not included, the SCG is assumed active) 2) de-activate indicator (if not included the SCG is assumed active) |
| --- |
| Company | Yes/NO | Comment |
| ZTE | Yes | 1) |
| Nokia | Yes/No | We prefer to avoid partial accept/reject for the modification procedures. So, only a flag in the MOD REQ is needed (SCG active/deactive). Here, a new cause may be needed. |
| Samsung |  | 1) |
| LGE |  | Two status changes are needed: To modify the activated to be de-active To modify the deactivated to be active Details can be FFS |
| Huawei |  | 1) |
| Lenovo, Motorola Mobility |  | 1) |
| InterDigital |  | 1) |
| E/// | Yes | 1 |
| CATT | Yes | 1) |
| Qualcomm | Yes | 1) |
| NEC | Yes | 2) is enough. |
| Google |  | 2) |

Summary: Option1: 9 companies and Option2: 3 companies.

WA 3: Add a new IE, e.g., “SCG activation requested” in the SN modification request message, if the IE is set to 0 or is not existed,  the SCG is activated.

Question 2b: Companies are kindly invited to input your view on which option for SN modification request acknowledge?

| SN modification acknowledge (Adding a new IE, e.g., SCG(de)activation result ) 1) 0=activate, 1=de-activate (if “activate” and if not included, the SCG is assumed active) 2) de-activate indicator (if not included the SCG is assumed active) 3) N/A: No enhancement |
| --- |
| Company | Yes/NO | Comment |
| ZTE | Yes | 1) |
| Nokia | Yes/No | We prefer to avoid partial accept/reject for the modification procedures. So, only a flag in the MOD REQ is needed (SCG active/deactive). Here, a new cause may be needed. |
| Samsung |  | 1) |
| LGE |  | Two status changes are needed: To modify the activated to be de-active To modify the deactivated to be active Details can be FFS |
| Huawei |  | 1) |
| Lenovo, Motorola Mobility |  | 1) In general, for MN initiated SN modification, we can support part fail. |
| Huawei |  | 1) |
| E/// | Yes | 1, prefer to change to activated, de-activated as status. |
| CATT |  | 1) |
| Qualcomm | Yes | 1) |
| NEC |  | Considering also backward compatibility with existing SN, 2) should be chosen. |
| Google |  | 2) |

Summary: Option1: 9 companies and Option2: 3 companies.

WA 4: Add a new IE, e.g., “SCG activation result” in the SN modification response message, if the IE is set to 0, the SCG is activated.

Question 2c: Companies are kindly invited to input your view on which option for SN modification request reject message?

| SN modification request reject: 1) Allow to reject with a new Cause 2) N/A: Not allow to reject |
| --- |
| Company | Yes/NO | Comment |
| ZTE | Yes | 1) |
| Nokia | Yes/No | For the ADD REQ and ACK, only the deactivation flag is needed – if not included the SCG is assumed active. |
| Samsung |  | For SN MOD REQ Reject, legacy message can be reused. We also prefer to allow the partial reject, i.e., using MOD REQ ACK message to reject the SCG (de-)activation. Moreover, when using this method, the cause value can be included. |
| LGE | Yes | Depending on the scenario, new cause should be allowed |
| Huawei | No | In case the SN modification includes other things requested to be modified, the SN can make the decision on whether reject the message or not for those things, as for SCG activation/deactivation, there is a SCG activation/deactivation flag in the response already. On the other hand, if the SN modification is only triggered for SCG activation/deactivation, then the reject message can be provide enough information and no need to have a new cause as well. |
| Lenovo, Motorola Mobility |  | 1) |
| InterDigital | No | Agree with Huawei |
| E/// | Yes | 1 |
| CATT |  | Agree with HW |
|  | No | We have response message to reject the activation/deactivation. The use case of changing reject message is not clear. |
| NEC | Qualcomm | Even if “if not included the SCG is assumed active” will be accepted, considering SN may reject for any reason (i.e. cannot even activate), then it should allow to reject with new Cause. |
| Google |  | 1) |

Summary:  Some companies agree that the SN is allowed to partially reject the SCG (de)activation request. But some companies also suggest to include fully reject with cause value.

Open issue 2: During SN modification procedure, if reject the request of SCG (de)activation

1) SN uses the response message including “SCG (de)activation” result to partially reject;

2) SN uses the reject message including new Cause value;

3) SN uses the reject message as legacy (without new Cause).

Handover procedure

In [R3-210403], it states that, during handover the target MN may decide to keep, change or release the SCG. Once it is identified that the target MN should be able to request the SN for an SCG activation state at PCell handover, the new indication(s) for SCG (de)activation should be introduced in the Handover Request procedure and used to inform the target MN of current SCG state within the source MN. Then the request for SCG activation state is transferred from the target MN to the target SN (which may be the same as the source SN in case the UE is operating in MR-DC and the target MN determines to keep the source SN after the handover).

In rapporteur’s view, if captured, the handover failure shall also be considered.

Question 3: Do companies agree with the following content for Handover procedure?

- Handover request(Adding a new IE, e.g., SCG(de)activation request )

- Handover request acknowledge(Adding a new IE, e.g., SCG(de)activation result)

- Handover preparation failure(Adding a new Cause value, e.g., SCG (de)activation reject)

| Company | Yes/NO | Comment |
| --- | --- | --- |
| ZTE | Yes |  |
| Nokia | No | At this moment, HO operation seems complete. If the SN changes, the target MN should decide on its own; if SN is the same, then the SN may let the target MN now about the state of the SCG in the ADD REQ ACK message. |
| Samsung | No | SCG (de-)activation during HO should be determined by the target MN, which relies on the SN addition procedure. |
| LGE | Yes |  |
| Huawei | No | Share the view with Samsung. |
| Lenovo, Motorola Mobility | See comment | For 1), it seems making sense to let target MN be aware of the current SCG (de)activation status and help target MN make the decision. However, we are not sure about 2) and 3). The new SCG(de)activation related configuration can be provided by the new SN in a RRC container and transmitted to UE without informing the source MN. In other word, the source MN does not need to know whether the new SCG is (de)activated. Also, even if the new SN may reject the SCG (de)activation requested by the target MN, we are not sure why that could be a reason to cause a preparation failure. |
| InterDigital | No | Agree with Huawei and Samsung |
| E/// | Yes | RAN2 is discussing the mobility case. We need to consider the case, e.g., if the target MN gets current SCG mode of operation from the source. |
| CATT | No | We should study further more. It may not be RAN3 impacted. The source MN just transfers the SCG activation state to target MN. It may be included in HandoverPreparationInformation which is RAN2 defined. |
| Qualcomm | No | It is up to target to decide SCG activation/deactivation. |
| NEC | No | For the moment it is FFS. |
| Google | No | FFS |

Summary:  Majority companies (8) do not support to introduce this produce.

FFS: X2/Xn Handover procedure is enhanced to support of SCG (de)activation.

Activity notification

Activity Notification message sent from SN to MN, can be used for the MN to make final decision on SCG (de)activation. It is FFS whether no spec impacts or the Activity Notification message shall be enhanced, e.g., add a new SCG (de)activation suggestion IE.

In [R3-210182], a new IE (“SCG Activation Suggested”) is introduced, but some companies think legacy message can be reused without enhancement.

Since majority companies suggest to not enhance the message, so far, rapporteur suggests to not enhance the Activity notification message for MN initiated SCG (de)activation.

Other procedures/messages

Question 4: Do companies suggest to introduce other procedures/messages for SCG (de)activation in X2/XnAP? If yes, please input your view.

| Company | Yes/NO | Comment |
| --- | --- | --- |
| Nokia | No | The Activity Notification may be used as it is now – changes would overlap with the SN-initiated modification. |
| Samsung | Yes | We have concerns on no enhancement to Activity Notification message. In our understanding, the Activity Notification message is used to indicate the activity. While the criteria for SCG (de-)active and sending UE to RRC inactive status may be different. For example, to deactivate SCG, no activity in 1 second may be enough, while to send UE to RRC inactive, no activity in 2 second is needed. In this sense, we would like to introduce the new IE for SCG activity indication, which is used to reflect the activity of SCG. |
| LGE | No | Unless RAN2 defines something that requires RAN3 enhancement |
| Huawei | No | Share the view with Nokia. |
| InterDigital | NO | Agree with Nokia/Huawei |
| E/// | No | Current procedure and IE will be able to provide enough information for triggering SCG (de)activation. |
| CATT |  | The Activity Notification may provide assist information (suggestion) for the MN initiate SCG (de)activation. I prefer to use the SN initiate SN modification required procedure for the SN initiate SCG (de)activation. |
| Qualcomm | No | Agree with Ericsson, Nokia, Huawei … |
| NEC | No | The Activity Notification can be reused with adding SCG Activation/Deactivation Request, for the purpose to let the SN to explicitly initiate the SCG Activation/deactivation |
| Google | No | Agree that Activity Notification may be reused as it is now |

Conclusion 1: Only one company suggests to introduce other X2/Xn message for support of SCG (de)activation.

### TS38.473

UE context setup procedure

For the same reason as X2/XnAP, the rapporteur provides the similar question.

- UE context setup request(Adding a new IE, e.g., SCG(de)activation request )

- UE context setup response(Adding a new IE, e.g., SCG(de)activation result)

- UE context setup failure ((Adding a new Cause value, e.g., SCG (de)activation reject)

- In UE context setup request, if the new IE is not configured or the new IE is set to e.g., SCG activation, the gNB-DU shall activate the SCG.

Question 5a: Companies are kindly invited to input your view on which option for UE context setup request?

| UE context setup request (Adding a new IE, e.g., SCG(de)activation request ) 1) 0=activate, 1=de-activate (if “activate” and if not included, the SCG is assumed active) 2) de-activate indicator (if not included the SCG is assumed active) |
| --- |
| Company | Yes/NO | Comment |
| ZTE | Yes | 1) |
| Nokia | Yes/No | As above – only a flag for deactivation is needed. |
| Samsung |  | 1) |
| LGE |  | FFS |
| Huawei |  | 1) |
| Lenovo, Motorola Mobility |  | 2) to align with the legacy |
| InterDigital |  | 1) |
| E/// | Yes | 1 |
| CATT | Yes | 1) |
| Qualcomm | Yes | 1) |
| NEC |  | 2) is enough. |
| Google |  | 2) |

Summary: Option1: 7 companies, Option2: 4 companies.

WA 5: Add a new IE, e.g., “SCG activation requested” in the UE context setup request message, if the IE is set to 0 or is not existed, the SCG is requested to activate. FFS: Add a new IE, e.g., “SCG activation requested” including “deactivation flag” in the UE context setup request message, if the IE is not existed, the SCG is requested to activate.

Question 5b: Companies are kindly invited to input your view on which option for UE context setup response?

| UE context setup response (Adding a new IE, e.g., SCG(de)activation result ) 1) 0=activate, 1=de-activate (if “activate” and if not included, the SCG is assumed active) 2) de-activate indicator (if not included the SCG is assumed active) 3) N/A: No enhancement |
| --- |
| Company | Yes/NO | Comment |
| ZTE | Yes | 1) |
| Nokia | Yes/No | As above – only a flag for deactivation is needed. |
| Samsung |  | 1) |
| LGE |  | FFS |
| Huawei |  | 1) |
| Lenovo, Motorola Mobility |  | 1) |
| InterDigital |  | 1) |
| E/// | Yes | 1, prefer to change to activated, de-activated as status. |
| CATT | Yes | 1 |
| Qualcomm | Yes | 1) |
| NEC |  | Considering also backward compatibility with existing DU, 2) should be chosen. |
| Google |  | 2) |

Summary:  Option1: 8 companies and Option2: 4.

WA 6: Add a new IE, e.g., “SCG activation result” in the UE context setup response message, if the IE is set to 0, the SCG is activated. FFS: Add a new IE, e.g., “SCG activation result” including “deactivation flag” in the UE context setup response message, if the IE is not existed, the SCG is activated.

Question 5c: Companies are kindly invited to input your view on which option for UE context setup failure message?

| UE context setup failure: 1) Allow to reject with a new Cause 2) N/A: Not allow to reject |
| --- |
| Company | Yes/NO | Comment |
| ZTE | Yes | 1) |
| Nokia | Yes/No | As above – only a flag for deactivation is needed. |
| Samsung |  | For reject, legacy failure can be reused. We also prefer to allow the partial reject, i.e., using UE Context Setup Response message to reject the SCG (de-)activation. Moreover, when using this method, the cause value can be included. |
| LGE |  | FFS |
| Huawei | No | Similar to the answers in Question 1c. |
| Lenovo, Motorola Mobility |  | 1) |
| InterDigital | No | Agree with Huawei |
| E/// |  | Same comment as for SN addition procedure over X2/Xn. No need to reject the whole procedure, but actual IE design allows. Or we can clarify in description. |
| CATT | No | Response message can be used for rejection |
| Qualcomm | No | No clear use case |
| NEC |  | Even if “if not included the SCG is assumed active” will be accepted, considering DU may reject for any reason (i.e. cannot even activate), then it should allow to reject with new Cause. |
| Google |  | 1) |

Summary:  Some companies agree that the gNB-DU is allowed to partially reject the SCG (de)activation request. But some companies also suggest to include fully reject with cause value.

Open issue 3: During UE context setup procedure, if reject the request of SCG (de)activation

1) gNB-DU uses the response message including “SCG (de)activation” result to partially reject;

2) gNB-DU uses the reject message including new Cause value;

3) gNB-DU uses the reject message as legacy (without new Cause).

UE Context Modification

Also same as X2/XnAP, we provide the following question.

- UE Context Modification request(Adding a new IE, e.g., SCG(de)activation request )

- UE Context Modification response(Adding a new IE, e.g., SCG(de)activation result)

- UE Context Modification failure (Adding a new Cause value, e.g., SCG (de)activation reject)

Question 6a: Companies are kindly invited to input your view on which option for UE Context Modification request?

| UE Context Modification request (Adding a new IE, e.g., SCG(de)activation request ) 1) 0=activate, 1=de-activate (if “activate” and if not included, the SCG is assumed active) 2) de-activate indicator (if not included the SCG is assumed active) |
| --- |
| Company | Yes/NO | Comment |
| ZTE | Yes | 1) |
| Nokia | Yes/No | As above – the flag should be added to the request only. Also, a cause for rejection is needed. |
| Samsung |  | 1) |
| LGE |  | FFS |
| Huawei |  | 1) |
| Lenovo, Motorola Mobility |  | 1) |
| InterDigital |  | 1) |
| E/// | Yes | 1 |
| CATT | Yes | 1 |
| Qualcomm | Yes | 1) |
| NEC |  | 2) is enough |
| Google |  | 2) |

Summary: Option1: 8 companies, Option2: 3 companies.

WA 7: Add a new IE, e.g., “SCG activation requested” in the UE Context Modification request message, if the IE is set to 0 or is not existed, the SCG is requested to activate. FFS: Add a new IE, e.g., “SCG activation requested” including “deactivation flag” in the UE Context Modification request message, if the IE is not existed, the SCG is requested to activate.

Question 6b: Companies are kindly invited to input your view on which option for UE Context Modification response?

| UE Context Modification response( (Adding a new IE, e.g., SCG(de)activation result ) 1) 0=activate, 1=de-activate (if “activate” and if not included, the SCG is assumed active) 2) de-activate indicator (if not included the SCG is assumed active) 3) N/A: No enhancement |
| --- |
| Company | Yes/NO | Comment |
| ZTE | Yes | 1) |
| Nokia | Yes/No | As above – the flag should be added to the request only. Also, a cause for rejection is needed. |
| Samsung |  | 1) |
| LGE |  | FFS |
| Huawei |  | 1) |
| Lenovo, Motorola Mobility |  | 1) We assume the scenario here is i.e. when MN sends SN modification request to SN. In general, for MN initiated SN modification, we can support part fail. |
| InterDigital |  | 1) |
| E/// | Yes | 1, prefer to change to activated, de-activated as status. |
| CATT |  | 1, agree with E/// |
| Qualcomm | Yes | 1) |
| NEC |  | Considering also backward compatibility with existing DU, 2) should be chosen. |
| Google |  | 2) |

Summary:  Option1: 7 companies and Option2: 3.

WA 8: Add a new IE, e.g., “SCG activation result” in the UE Context Modification response message, if the IE is set to 0, the SCG is activated. FFS: Add a new IE, e.g., “SCG activation result” including “deactivation flag” in the UE Context Modification response message, if the IE is not existed, the SCG is activated.

Question 6c: Companies are kindly invited to input your view on which option for UE Context Modification failure?

| UE Context Modification failure e: 1) Allow to reject with a new Cause 2) N/A: Not allow to reject |
| --- |
| Company | Yes/NO | Comment |
| ZTE | Yes | 1) |
| Nokia | Yes/No | As above – the flag should be added to the request only. Also, a cause for rejection is needed. |
| Samsung |  | For reject, legacy failure can be reused. We also prefer to allow the partial reject, i.e., using UE Context Modification Response message to reject the SCG (de-)activation. Moreover, when using this method, the cause value can be included. |
| LGE |  | FFS |
| Huawei | No | Similar to the answers in Question 2c. |
| Lenovo, Motorola Mobility |  | 1) |
| InterDigital | No | Agree with Huawei |
| E/// | Yes | 1 |
| CATT | NO |  |
| Qualcomm | No |  |
| NEC |  | 2) is enough. |
| Google |  | 2) |

Summary:  Some companies agree that the gNB-DU is allowed to partially reject the SCG (de)activation request. But some companies also suggest to include fully reject with cause value.

Open issue 4: During UE Context Modification procedure, if reject the request of SCG (de)activation

1) gNB-DU uses the response message including “SCG (de)activation” result to partially reject;

2) gNB-DU uses the reject message including new Cause value;

3) gNB-DU uses the reject message as legacy (without new Cause).

Other procedures/messages

Question 7: Do companies suggest to introduce other procedures/messages for SCG (de)activation in F1AP? If yes, please input your view.

| Company | Yes/NO | Comment |
| --- | --- | --- |
| Samsung |  | In our contribution, we discuss the detection node of the SCG activity, which can be either 1) multiple nodes, e.g., SN-DU, MN-CU-UP, SN-CU-UP, or 2) one node, i.e., SN-DU. The option 1) needs the alignment among multiple nodes on the activity detection criteria, while option 2) does not need the alignment. Thus, we think SCG activity detection can be relied on SN-DU only. Based on this, We think the enhancement to UE INACTIVITY NOTIFICATION message is needed. The reason is that the criteria for SCG (de-)activation and sending UE to RRC inactive status may be different. For example, to deactivate SCG, no activity in 1 second may be enough, while to send UE to RRC inactive, no activity in 2 second is needed. In this sense, we would like to introduce the new IE for SCG activity, which is used to reflect the activity of SCG. In summary, we think Enhancement to UE INACTIVITY NOTIFICATION message to include SCG activity information. |

Conclusion 2: Only one company suggests to introduce other F1 message for support of SCG (de)activation.

### TS38.463

Bearer context setup procedure

Question 8: Do companies agree with the following content for Bearer Context Setup procedure?

- Bearer Context Setup Request (Adding a new IE, e.g., SCG(de)activation request)

- Bearer Context Setup Response (Adding a new IE, e.g., SCG(de)activation result)

- Bearer Context Setup Failure (Adding a new Cause value, e.g., SCG (de)activation reject)

| Company | Yes/NO | Comment |
| --- | --- | --- |
| ZTE | Yes |  |
| Nokia | ? | This is a big FFS for us. In principle, what would be a scenario for signaling to the UP? SCG activation or deactivation should follow rather the data flow, not vice-versa. So, the UP does not need to knoe if SCG is active or not, does it? |
| Samsung |  | The enhancement to this procedure is needed. One example is: MN( SN-CU-CP: SN addition with SCG deactivation flag to establish a SN terminated split bearer. SN-CU-CP ( SN-CU-UP: Bearer Context Setup Request with SCG deactivation flag. In this request, a SN terminated split bearer is set up. The SN-CU-UP can decide to accept it or not. If “accept”, the SN-CU-UP can send the packets to MCG leg when packets are coming from CN. The details can follow similar way as Xn/F1. |
| LGE |  | FFS |
| Huawei |  | Yes for 1) and 2), No for 3) |
| Lenovo, Motorola Mobility | Yes with comment | We assume the scenario here is i.e. when MN sends SN addition request to SN. 1) yes, for adding new IE ONLY for SCG deactivation 2) 3) 4) yes In our understanding, e.g. if MN CU-UP is aware of the SCG deactivation, MN CU-UP may hold the data in its buffer and only transfer the data to SN when SCG is activated. |
| InterDigital |  | Agree with Huawei, but would be ok to keep FFS |
| E/// | Yes |  |
| CATT |  | Need further study |
| Qualcomm | Yes | 1), 2) |
| NEC |  | All for UP is to be FFS. |
| Google |  | FFS |

Summary:  For E1AP, 6 companies agree to keep it FFS, 7 companies agree to include it.

Option issue 5: E1AP shall be enhanced to support of SCG (de)activation, if included, the Bearer Context Setup procedure enhancement shall be aligned with X2/Xn/F1AP.

Question 9: Do companies agree with the following content for Bearer Context Modification procedure?

- Bearer Context Modification Request (Adding a new IE, e.g., SCG(de)activation request)

- Bearer Context Modification Response (Adding a new IE, e.g., SCG(de)activation result)

- Bearer Context Modification Failure (Adding a new Cause value, e.g., SCG (de)activation reject)

| Company | Yes/NO | Comment |
| --- | --- | --- |
| ZTE | Yes |  |
| Nokia | ? | See above. |
| Samsung |  | The details can follow the similar way as Xn/F1 |
| LGE |  | FFS |
| Huawei |  | Yes for 1) and 2), No for 3) |
| Lenovo, Motorola Mobility | Yes | We assume the scenario here is i.e. when MN sends SN modification request to SN. In general, for MN initiated SN modification, we can support part fail. |
| InterDigital |  | See above |
| E/// | Yes |  |
| CATT |  | Need further study |
| Qualcomm | Yes |  |
| NEC |  | FFS |
| Google |  | FFS |

Summary:  For E1AP, 6 companies agree to keep it FFS, 7 companies agree to include it.

Option issue 6: E1AP shall be enhanced to support of SCG (de)activation, if included, the Bearer Context Modification enhancement shall be aligned with X2/Xn/F1AP.

Other procedures/messages

Question 10: Do companies suggest to introduce other procedures/messages for SCG (de)activation in E1AP? If yes, please input your view.

| Company | Yes/NO | Comment |
| --- | --- | --- |

### New IEs

Refer to e.g., [R3-210182]

Request message (X2/Xn/F1/E1)

| IE/Group Name | Presence | Range | IE type and reference | Semantics description | Criticality | Assigned Criticality |
| --- | --- | --- | --- | --- | --- | --- |
| <Skip unchanged part> |
| SCG Activation Requested | O |  | ENUMERATED ( activate, de-activate, …) | SCG Activation Information-A |  |  |

| IE/Group Name | Presence | Range | IE type and reference | Semantics description | Criticality | Assigned Criticality |
| --- | --- | --- | --- | --- | --- | --- |
| <Skip unchanged part> |
| SCG Activation Requested | O |  | ENUMERATED ( de-activate, …) | SCG Activation Information-B |  |  |

Response message (X2/Xn/F1/E1)

| IE/Group Name | Presence | Range | IE type and reference | Semantics description | Criticality | Assigned Criticality |
| --- | --- | --- | --- | --- | --- | --- |
| <Skip unchanged part> |
| SCG Activation Response | O |  | ENUMERATED ( activate, de-activate, …) | SCG Activation Information-A |  |  |

| IE/Group Name | Presence | Range | IE type and reference | Semantics description | Criticality | Assigned Criticality |
| --- | --- | --- | --- | --- | --- | --- |
| <Skip unchanged part> |
| SCG Activation Response | O |  | ENUMERATED ( de-activate,…) | SCG Activation Information-B |  |  |

#### X.Y.Z SCG Activation Information-A

This IE indicates whether SCG activation or SCG deactivation is requested, response.

| IE/Group Name | Presence | Range | IE Type and Reference | Semantics Description |
| --- | --- | --- | --- | --- |
| SCG Activation Information | M |  | ENUMERATED ( activate, de-activate, …) |  |

#### X.Y.Z SCG Activation Information-B

This IE indicates whether SCG activation or SCG deactivation is requested, response.

| IE/Group Name | Presence | Range | IE Type and Reference | Semantics Description |
| --- | --- | --- | --- | --- |
| SCG Activation Information | M |  | ENUMERATED ( de-activate, …) |  |

Question 11: Do companies agree with the following content for the definition of the new IE?

- A new IE (“SCG Activation Requested”) added in the request message in X2AP, XnAP, F1AP and E1AP

- A new IE (“SCG Activation Response”) added in the response message in X2AP, XnAP, F1AP and E1AP

- A new IE (“SCG Activation Information”-A) defined as (“activate” and “de-activate”)

- A new IE (“SCG Activation Information”-B) defined as (“de-activation”)

| Company | Yes/NO | Comment |
| --- | --- | --- |
| ZTE | Yes | Prefer 3) to use union SCG Activation Information-A for all of request / response message. |
| Nokia | No | See principles above – in some cases only “not active” is enough. |
| Samsung |  | 1)&2), and both IEs can refer to the same SCG Activation Information |
| Huawei |  | Support 1, 2, 3. |
| Lenovo, Motorola Mobility | Yes |  |
| InterDigital |  | Support 1, 2, 3 |
| E/// | Yes | 1&2, to distinguish request and response. |
| CATT |  | Support 1,2,3. But for E1AP, we need further check |
| Qualcomm | Yes | 1), 2), 3) |
| Google |  | 4) |

Conclusion 3: This issue has been captured in the previous questions.

Cause value

When a node receives the request message including SCG (de)activation indication, some companies think the receiving node can reject the request due to e.g., the action failed because the requested SCG state is not accepted, so that a new cause value shall be added.

There are two references for the new Cause value in [R3-210086] and [R3-210404].

- A new Cause value IE “SCG resources needed” is defined as “The SCG resources are needed for data transmission” ([R3-210086])

- A new Cause value IE “Requested SCG state not available” is defined as “The action failed because the requested SCG state is not accepted.” ([R3-210404]).

Question 12: Do companies agree to introduce a new Cause value for SCG (de)activation rejection? If yes, which definition of the new IE do you prefer?

| SCG resources needed: The SCG resources are needed for data transmission” ([R3-210086]) Requested SCG state not available: The action failed because the requested SCG state is not accepted. ([R3-210404]). Other definition |
| --- |
| Company | Yes/NO | Comment |
| ZTE | Yes | Prefer to 2) |
| Nokia | Yes | 1 is better for rejection of deactivation, as discussed above |
| Samsung | Yes | 2) |
| LGE | Yes | 2 |
| Huawei | No | So far do not see strong need for the new cause, see response in Question 1c, 2c and 5c. |
| Lenovo, Motorola Mobility | Yes | 2) seems more generic can be applied to both activation/deactivation cases. |
| InterDigital | No | Open to this but no strong need seen so far |
| E/// | Yes | 2 |
| CATT |  | If use reject message as reject solution, I prefer 2) |
| Qualcomm | Yes | 2) |
| Google | Yes | Open to this |

Summary:  Option1: 1 companies and Option2: 7 companies, 3 companies suggest to open it.

WA 9: Introduce a new Cause value, e.g., “Requested SCG state not available” is defined as “The action failed because the requested SCG state is not accepted.”

### Flow charts

TS37.340

Two papers ([R3-210137] and [R3-210181]) provide the flow charts for TS37.340.

Question 13: Companies are kindly invited to input your view on the flow chart for TS37.340?

| Refer to 1) R3-210137 and 2) R3-210181 |
| --- |
| Company | Yes/NO | Comment |
| ZTE |  | Both fine. Do we need union flow chart including both SN addition and SN modification, or do we need separate flow chart? |
| Nokia | No | We are not sure if the signaling changes discussed above justify separate flows. |
| Samsung |  | We are fine to use either of two as the starting point. |
| Huawei |  | Maybe 1? as seems one flow chart is enough to show how things work. |
| Lenovo, Motorola Mobility | See comment | the first thing we need to discuss is whether we introduce separate subclause only for SCG deactivation/activation, like 1) and 2) are proposing. Or we capture the SCG (de)activation in the current SN addition (10.2) /modification (10.3) subclause? From what we can see, if we don’t introduce enhancement to e.g. the activity notification, the procedure looks very similar as the legacy SN addition/modification procedure only with new conveyed info. It could be simply captured in the procedure description text. |
| InterDigital |  | Probably only need one, number 1 seems ok |
| E/// |  | Use as starting point. Need to align with RAN2. |
| CATT |  | We need wait for the conclusion of whole solution. And then discuss the flow charts |
| Qualcomm |  | Use 1 as starting point |
| Google |  | Maybe using 1 as starting point |

WA 10: Start to introduce flow chart in both TS37.30 and TS38.401, considering company’s comments.

1- [R3-210137] 10.xx Deactivation and re-activation of SCG In MR-DC with NR SCG, the network can deactivate the SCG in the SN addition procedure and in the SN modification procedure. Figure 10.xx-1: Support of deactivation/re-activation of SCG in the SN addition procedure 1. The MN decides to deactivate the NR SCG before adding the NR SCG. 2. The MN triggers the SN addition procedure and informs the SN to deactivate the SCG. 3. The SN replied in the SN addition request acknowledge that the SCG is added and deactivated. 4. The MN informs the UE to deactivate the SCG [FFS, pending to RAN2]. 5/6. The MN receives the assistance information from the SN and the UE on the user traffic activity of the SCG. 7. The MN decides to re-activate the SCG. 8. The MN triggers the SN modification procedure and informs the SN to activate the SCG. 9. The SN replied in the SN modification request acknowledge that the SCG is activated. 10. The MN informs the UE to activate the SCG [FFS, pending to RAN2].

2- [R3-210181] 10.xx Support of SCG activation and deactivation 10.xx.1 MN initiated SCG activation and deactivation The following figures are used for support of MN initiated SCG (de)activation. Figure 10.xx.1-1: MN initiated SCG (de)activation through SN addition 1. The MN decides to configure SCG activation state, at PSCell addition/change, RRC resume or HO scenarios. 2. The MN triggers the MN initiated SN Addition procedure, requesting the SN to (de-) activate SCG. 3. The RRC (Connection) Reconfiguration procedure commences 4. The following steps are the same as those in SN addition procedure in Section 10.2. Figure 10.xx.1-2: MN initiated SCG (de)activation through SN modification 1. The SN notifies the MN about user data inactivity for SN terminated bearers (or about SCG activity suggestion). 2. The MN decides to keep the UE in RRC_CONNECTED and request SCG deactivation. 3/4. The MN triggers the MN initiated SN Modification procedure, and request the SN to de-activate SCG. 5/6. The UE is kept in RRC_CONNECTED and de-activates SCG (FFS: depending on RAN2). 7/8. After a period of SCG deactivation, upon activity notification from the SN, the MN decides to request SCG re-activation. 9/10. The MN initiates the MN initiated SN modification procedure to re-activate SCG.. 11. The RRC (Connection) Reconfiguration procedure commences. If the SCG configuration is to be updated, the new configuration is provided in the RRC(Connection)Reconfiguration message. 12. The following steps are the same as those in SN modification procedure in Section 10.3.

TS38.401

One paper ([R3-210138] provides the flow charts for TS38.401.

Question 14: Companies are kindly invited to input your view on the flow chart for TS38.401?

| Refer to R3-210138 |
| --- |
| Company | Yes/NO | Comment |
| Samsung |  | We have some concerns on the SCG (de-)activation based on modification procedure. For this procedure, we need discuss “which node detects the SCG activity?” first since it determines that how the SN-CU side decides to send the Activity Notification message. Option 1: if SCG activity is determined by SN-DU only, SN-CU can send the Activity Notification message based on UE Inactivity Notification message from SN-DU only Option 2: if SCG activity is determined by information from SN-DU, SN-CU-UP and MN-CU-UP together Before SN-CU-CP sends Activity Notification to MN-CU-CP, it needs collect activity information from SN-DU and each related SN-CU-UP Before MN-CU-CP makes decision, it needs collect activity information from SN-CU-CP and each related MN-CU-UP Apparently, the two options result in different flow chart. Thus, we need clarify this first before developing flow chart. |
| Huawei |  | Could be the start point. |
| Lenovo, Motorola Mobility | See comment | The current flow as well as in the current 38.401 spec, the E1 F1 procedures inside MN are not captured. Which we feel could be beneficial to capture for SCG activation/deactivation. For example, when MN CU-CP decides to activate/deactivate the SCG, it has two options: Option 1: MN CU-CP first informs MN CU-UP, DU about SCG activation/deactivation, and then sends SCG activation/deactivation request to SN. Option 2: MN CU-CP first sends SCG activation/deactivation request to SN, and then informs MN CU-UP, DU once SN acknowledges the request. Either way could work with pros and cons. It could be clearer to capture either option in 38.401. |
| InterDigital |  | Starting point |
| CATT |  | We need wait for the conclusion of whole solution. And then discuss the flow charts |

8.4 Multi-Connectivity operation //skip the unchanged part 8.4.x SCG deactivation/re-activation This clause gives the NR SCG deactivation/re-activation in MR-DC given that the SgNB consists of a gNB-CU and gNB-DU(s). SN addition procedure Figure 8.4.x-1: SCG deactivation/re-activation in SN addition procedure 1~2. refer to TS 37.340 [12]. 3~4.The CU-CP of SN sends the UE CONTEXT SETUP REQUEST message to the DU of SN to deactivate the SCG of the UE. 5~6.The CU-CP of SN sends the BEARER CONTEXT SETUP REQUEST message to the CU-UP of SN to deactivate the SCG of the UE. 7~8. refer to TS 37.340 [12]. 9. The CU-UP of SN sends the UE INACTIVITY NOTIFICATION to the CU-CP of SN to notify the use plane activity. 10~13. refer to TS 37.340 [12]. 14~15.The CU-CP of SN sends the UE CONTEXT MODIFICATION REQUEST message to the DU of SN to re-activate the SCG of the UE. 16~17.The CU-CP of SN sends the BEARER CONTEXT MODIFICATION REQUEST message to the CU-UP of SN to re-activate the SCG of the UE. 18~19. refer to TS 37.340 [12]. SN modification procedure Figure 8.4.x-2: SCG deactivation/re-activation in SN modification procedure 0-1. The CU-UP of SN sends the UE INACTIVITY NOTIFICATION to the CU-CP of SN to notify the use plane inactivity. 0-2~2. refer to TS 37.340 [12]. 3~4.The CU-CP of SN sends the UE CONTEXT MODIFICATION REQUEST message to the DU of SN to deactivate the SCG of the UE. 5~6.The CU-CP of SN sends the BEARER CONTEXT MODIFICATION REQUEST message to the CU-UP of SN to deactivate the SCG of the UE. 7~8. refer to TS 37.340 [12] 9. The CU-UP of SN sends the UE INACTIVITY NOTIFICATION to the CU-CP of SN to notify the use plane activity. 10~13. refer to TS 37.340 [12] 14~15.The CU-CP of SN sends the UE CONTEXT MODIFICATION REQUEST message to the DU of SN to re-activate the SCG of the UE. 16~17.The CU-CP of SN sends the BEARER CONTEXT MODIFICATION REQUEST message to the CU-UP of SN to re-activate the SCG of the UE. 18~19. refer to TS 37.340 [12].

## SN initiated SCG activation and deactivation

In the RAN3 #112 e-meeting, RAN2 has not made any progress for SN initiated SCG (de)activation. So, RAN3 shall still keep this topic open until RAN2 progress, then we can save much effort.

Question 15: Do companies agree to wait RAN2 progress for SN initiated SCG (de)activation?

| Company | Yes/NO | Comment |
| --- | --- | --- |
| ZTE | Yes | Suggest to leave it FFS. |
| Nokia | No | The scenario for SCG (de)activation is known, so RAN3 may progress (at least to agree some principles) assuming SCG state changes may be initiated from the SN. |
| Samsung | Yes | Wait for RAN2 |
| LGE | Yes | FFS |
| Huawei | Yes | Wait for RAN2. |
| Lenovo, Motorola Mobility | Yes |  |
| InterDigital | Yes |  |
| E/// | Yes |  |
| CATT | Yes |  |
| Qualcomm | Yes |  |

Proposal 2: Wait RAN2 progress for SN initiated SCG (de)activation.

In the last RAN3 #110 e-meeting, the following progress shall be checked by RAN2 progress.

FFS: Whether SN initiated SCG (de)activation is allowed for support of SCG (de)activation (i.e., whether SN is allowed to (de)activate SCG).

FFS: SN initiated SN modification required procedure can be used for support of SCG (de)activation

FFS: Activity notification message sent from MN to SN is helpful for SN to make good decision on SCG (de)activation. It is FFS whether no spec impacts or the Activity Notification message shall be enhanced, e.g., add a new SCG (de)activation suggestion IE.FFS: RAN3 has not achieved agreement whether MN can reject SCG (de)activation request after receiving SN modification required message.

However, since some companies provide contribution for the SN initiated SCG (de)activation, so rapporteur tries to push this issue, the following messages are considered.

- SN MODIFICATION REQUIRED

- SN MODIFICATION CONFIRM

- SN MODIFICATION REFUSE

- Activity Notification

Question 16a: Companies are kindly invited to input your view on which option for SN MODIFICATION REQUIRED?

| SN MODIFICATION REQUIRED (Adding a new IE, e.g., SCG(de)activation required) 1) 0=activate, 1=de-activate (if “activate” and if not included, the SCG is assumed active) 2) de-activate indicator (if not included the SCG is assumed active) |
| --- |
| Company | Yes/NO | Comment |
| ZTE | Yes | 1) |
| Samsung |  | Wait for RAN2 |
| Huawei |  | Wait for RAN2. |
| InterDigital |  | Wait for RAN2 |
| E/// | Yes | 1 |
| CATT |  | 1) |
| Qualcomm | Yes | 1) |

Question 16b: Companies are kindly invited to input your view on which option for SN MODIFICATION CONFIRM?

| SN MODIFICATION CONFIRM (Adding a new IE, e.g., SCG(de)activation confirm ) 1) 0=activate, 1=de-activate (if “activate” and if not included, the SCG is assumed active) 2) de-activate indicator (if not included the SCG is assumed active) 3) N/A: No enhancement |
| --- |
| Company | Yes/NO | Comment |
| ZTE | Yes | 1) |
| Samsung |  | Wait for RAN2 |
| Huawei |  | Wait for RAN2. |
| InterDigital |  | Wait for RAN2 |
| E/// | Yes | 1 |
| CATT |  | Depends on the solution, if the modification required trigger the MN sends modification request for SCG state change, no new IE needed. |
| Qualcomm | Yes | 1) |

Question 16c: Companies are kindly invited to input your view on which option for SN MODIFICATION REFUSE message?

| SN MODIFICATION REFUSE: 1) Allow to reject with a new Cause 2) N/A: Not allow to reject |
| --- |
| Company | Yes/NO | Comment |
| ZTE | Yes | 1) |
| Samsung |  | Wait for RAN2 |
| Huawei |  | Wait for RAN2. |
| InterDigital |  | Wait for RAN2 |
| E/// | Yes | 1 |
| CATT | Yes | 1 |
| Qualcomm |  | Wait for RAN2 |

Question 16d: Companies are kindly invited to input your view on which option for Activity Notification?

| Activity Notification (Adding a new IE, e.g., SCG(de)activation suggested ) 1) 0=activate, 1=de-activate (if “activate” and if not included, the SCG is assumed active) 2) de-activate indicator (if not included the SCG is assumed active) 3) N/A: No enhancement |
| --- |
| Company | Yes/NO | Comment |
| ZTE | Yes | 1) |
| Samsung |  | Wait for RAN2 |
| Huawei |  | Wait for RAN2. |
| InterDigital |  | Wait for RAN2 |
| E/// |  | 3 |
| CATT |  | 1) |
| Qualcomm |  | 3 |

# Conclusion, Recommendations [if needed]

After 1st round email discussion

Xn interface: MN initiated SN addition procedure:

WA 1: Add a new IE, e.g., “SCG activation requested” in the SN addition request message, while the detail code of this new IE is FFS.

E.g., if the IE is set to 1 or not existed, the SCG is requested to activate.  If the IE is set to 0, the SCG is requested to de-activate.

[Nokia] I’m not sure if I understand it, but only the part after “FFS” is correct: adding an “activate” flag will create redundancy in the signalling, which is inacceptable signalling design.

[Moderator] Many companies prefer WA1, and in case of MN initiated SN change, add an “activate” flag is useful for the target SN.

WA 2: Add a new IE, e.g., “SCG activation result” in the SN addition response message, while the detail code of this new IE is FFS.

[Nokia] Similar like above: only “deactivated” status is needed – otherwise, we’ll have redundancy in the signalling.

[Moderator] Same view as above.

E.g., if the IE is set to 0, the SCG is de-activated. If the IE is set to 1, the SCG is activated.

Open issue 1: During SN addition procedure, if the request of SCG (de)activation is rejected:

1) SN uses the response message including “SCG deactivation” result is sufficient;

2) or SN allows to use the reject message including new Cause value;

3) or SN allows to uses the reject message as legacy (without new Cause)

[Nokia] Please note that options 2 and 3 require that the flag in the ADD REQ has criticality “reject” – otherwise, if the SN is pre-Rel.17, it may accept the request and activate SCG even though the MN requested deactivation (legacy behaviour). Of course, this is all right to have criticality “reject”, but option 1 helps to avoid mistakes.

[Moderator] If go to option 2 and option, further discuss the criticality “reject” within request message.

MN initiated SN modification procedure

WA 3: Add a new IE, e.g., “SCG activation requested” in the SN modification request message, if the IE is set to 1, the SCG is requested to activate, if the IE is set to 0, the SCG is requested to de-activate

[Nokia] No, missing IE does not mean the SCG is to be activated – if it is not included, the status shall not change (so it shall remain activated or deactivated).

[Moderator] Thanks Kris, your view is correct, so I modified the WA3.

WA 4: Add a new IE, e.g., “SCG activation result” in the SN modification response message, if the IE is set to 1, the SCG is activated, if the IE is set to 0, the SCG is de-activated

Open issue 2: During SN modification procedure, if the request of SCG (de)activation is rejected:

1) SN uses the response message including “SCG (de)activation” is sufficient;

2) or SN allows to use the reject message including new Cause value;

3) or SN allows to use the reject message as legacy (without new Cause).

FFS: Whether X2/Xn Handover procedure needs to be enhanced to support of SCG (de)activation.

F1 interface: UE context setup procedure

WA 5: Add a new IE, e.g., “SCG activation requested” in the UE context setup request message, while the detail code of this new IE is aligned to X2/XnAP.

E.g., if the IE is set to 1 or not existed, the SCG is requested to activate.  If the IE is set to 0, the SCG is requested to de-activate.

WA 6: Add a new IE, e.g., “SCG activation result” in the UE context setup response message, while the detail code of this new IE is FFS.

E.g., if the IE is set to 0, the SCG is de-activated. If the IE is set to 1, the SCG is activated.

Open issue 3: During UE context setup procedure, if the request of SCG (de)activation is rejected:

1) gNB-DU uses the response message including “SCG (de)activation” is sufficient;

2) or gNB-DU allows to use the reject message including new Cause value;

3) or gNB-DU allows to use the reject message as legacy (without new Cause).

[Nokia] Similar comments as in case of the Addition procedure apply here.

F1 interface: UE Context Modification

WA 7: Add a new IE, e.g., “SCG activation requested” in the UE Context Modification request message, if the IE is set to 1, the SCG is requested to activate, if the IE is set to 0, the SCG is requested to de-activate.

WA 8: Add a new IE, e.g., “SCG activation result” in the UE Context Modification response message, if the IE is set to 1, the SCG is activated, if the IE is set to 0, the SCG is de-activated.

Open issue 4: During UE Context Modification procedure, if the request of SCG (de)activation is rejected:

1) gNB-DU uses the response message including “SCG (de)activation” is sufficient;

2) or gNB-DU allows to use the reject message including new Cause value;

3) or gNB-DU allows to use the reject message as legacy (without new Cause).

[Nokia] Similar comments as in case of the Modification procedure apply here.

Option issue 5: Whether E1AP shall be enhanced to support of SCG (de)activation, if included, the Bearer Context Setup procedure enhancement shall be aligned with X2/Xn/F1AP.

Option issue 6: Whether E1AP shall be enhanced to support of SCG (de)activation, if included, the Bearer Context Modification enhancement shall be aligned with X2/Xn/F1AP.

[Nokia] What is “option issue”?

[Moderator] Thanks Kris, your view is right, so I modified the open issue.

WA 9: Introduce a new Cause value for class1 procedure failure case, e.g., “Requested SCG state not available” is defined as “The action failed because the requested SCG state is not accepted.”

WA 10: Start to introduce flow chart in both TS37.30 and TS38.401, considering company’s comments.

[Nokia] But what would be the changes as compared to the classic Addition, Modification etc.? If nothing, then the flows are not necessary (yet).

[Moderator] We will introduce SCG status change in Rel-17, so independent flow chart to capture the new Rel-17 function is clear from classic Addition and Modification, and SN initiated procedure.

Proposal 2: Wait RAN2 progress for SN initiated SCG (de)activation.

Open issue 7: Which node detect the SCG activity to help the decision make of SCG (de-)activation.

Samsung: Current discussion is mainly focusing on the scenarios that after the MN has determined to (de-)active SCG, how to perform the signaling over X2/Xn/F1/E1 to configure the SCG (de-)activation. However, for this whole topic, we need clarify that the MN is based on which to make the final decision and also SN is based on which to send Activity Notification message.

In current specification, the following messages may be applicable to help MN make final decision:

-        DU -> CU: UE Inactivity Notification

-        UP -> CP: Bearer Context Inactivity Notification

-        SN -> MN: Activity Notification

However, how to use those messages to help MN make decision is unclear to us, e.g., simply reuse them for SCG (de-)activation or not. (Now, we only cover the Activity Notification message).

Also, in order to develop our stage2 flow chart, this aspect should be clear among us. Actually, in our contribution and comments, we mention this issue, i.e., “which node detect the SCG activity?”

# References

R3-210085 Principles for activation and deactivation of SCG resources (Nokia, Nokia Shanghai Bell) discussion

R3-210086 Enabling fast SCG activation/deactivation (Nokia, Nokia Shanghai Bell) CR0520r, TS 38.423 v16.4.0, Rel-17, Cat. B

R3-210087 Enabling fast SCG activation/deactivation (Nokia, Nokia Shanghai Bell) CR1567r, TS 36.423 v16.4.0, Rel-17, Cat. B

R3-210136 MN initiated SCG activation and deactivation (Huawei, InterDigital) discussion

R3-210137 Activation and de-activation of SCG (Huawei, InterDigital) draftCRr, TS 37.340 v16.4.0, Rel-17, Cat. B

R3-210138 Activation and de-activation of SCG (Huawei, InterDigital) CR0167r, TS 38.401 v16.4.0, Rel-17, Cat. B

R3-210180 Further discussion on SCG deactivation and activation (ZTE) discussion

R3-210181 CR 37.340 for support of SCG activation/deactivation (ZTE) draftCRr, TS 37.340 v16.4.0, Rel-17, Cat. B

R3-210182 CR 38.423 for support of SCG activation/deactivation (ZTE) CR0525r, TS 38.423 v16.4.0, Rel-17, Cat. B

R3-210239 SCG Activation / deactivation discussion (NEC) discussion

R3-210266 Discussion on SCG activation and deactivation (Samsung) discussion

R3-210267 CR on SCG (de-)activation over F1 (Samsung) CR0717r, TS 38.473 v16.4.0, Rel-17, Cat. B

R3-210268 CR on SCG (de-)activation over E1 (Samsung) CR0574r, TS 38.463 v16.4.0, Rel-17, Cat. B

R3-210352 Signaling support for SCG deactivation/activation (Qualcomm Incorporated) discussion

R3-210403 Support of SCG activation/de-activation (Ericsson) discussion

R3-210404 Support of SCG activation/de-activation over X2 (Ericsson) CR1577r, TS 36.423 v16.4.0, Rel-17, Cat. B

R3-210405 Support of SCG activation/de-activation over Xn (Ericsson) CR0545r, TS 38.423 v16.4.0, Rel-17, Cat. B

R3-210537 Open issues on Activation Deactivation for One SCG and SCells (LG Electronics) discussion

R3-210597 Left issues on SCG activation and deactivation (Lenovo, Motorola Mobility) discussion

R3-210598 SCG activation and deactivation impact on E1 interface (Lenovo, Motorola Mobility) discussion

R3-210599 Support of SCG Activation and Deactivation (Lenovo, Motorola Mobility) CR0575r, TS 38.463 v16.4.0, Rel-17, Cat. B

R3-210765 Discussion on efficient Activation/Deactivation Mechanism for SCG (CATT) discussion

R3-210766 CR for TS 38.423 on efficient Activation/Deactivation Mechanism for SCG (CATT) CR0564r, TS 38.423 v16.4.0, Rel-16, Cat. B

R3-210767 CR for TS 38.473 on efficient Activation/Deactivation Mechanism for SCG (CATT) CR0730r, TS 38.473 v16.4.0, Rel-16, Cat. B