3GPP TSG-RAN WG3 Meeting #111-e	R3-20xxxx

25 January – 4 February 2021

Online

Agenda Item:	14.3

Source:	Huawei (moderator)

Title:	Summary of Offline Discussion on PSCell_Change_Addition

Document for:	Discussion

# Introduction

CB: # MRDC3-PSCell_Change_Addition

- Check whether WAs from last meeting can be confirmed as agreements?

- Signalling design for CPA

- Signalling design for CPC

- How to support multiple candidate PSCell preparation in CPAC?

- Whether the SN Change procedure shall be extended to allow providing more than one target SN for CPC?

- Whether the direct inter-SN communication for preparations of CPC offer enough gain to start working on it?

- Whether and how to support early data forwarding and late data forwarding?

- Capture agreements as stage2/stage3 CRs and check details, split work, if needed

- LS reply to RAN2?

- List open issues for next meeting in the summary

(HW - moderator)

Summary of offline disc R3-211010

# For the Chairman’s Notes

Agreements:

WAs:

Open Issues:

# Discussion

## How to support multiple candidate PSCell preparation in CPAC?

In last RAN3 meeting, two options were listed as below:

- Option 1: prepare one PSCell in one CPAC procedure, use parallel CPAC procedures to prepare multiple PSCells

- Option 2: prepare multiple PSCells in one CPAC procedure

Before down selection of these two options, it is needed to first answer several questions related.

Take CPA as an example, the existing SN addition request ack only provide information related to one PSCell. In case of option1, the existing IEs can be reused for the one prepared PSCell. In case of option 2, it is needed to further analyses which information has to be provided in a per PSCell way.

| IE/Group Name | Presence |
| --- | --- |
| PDU Session Resources Admitted To Be Added List |  |
| >PDU Session Resources Admitted To Be Added Item |  |
| >>PDU Session ID | M |
| >>PDU Session Resource Setup Response Info – SN terminated | O |
| >>PDU Session Resource Setup Response Info – MN terminated | O |
| PDU Session Resources Not Admitted List | O |
| >PDU Session Resources Not Admitted List – SN terminated | O |
| >PDU Session Resources Not Admitted List – MN terminated | O |
| S-NG-RAN node to M-NG-RAN node Container | M |
| Admitted Split SRBs | O |
| RRC Config Indication | O |
| Criticality Diagnostics | O |
| Location Information at S-NODE | O |
| MR-DC Resource Coordination Information | O |
| Available fast MCG recovery via SRB3 | O |

Question 1: For Option 2, in case of CPA, which information needs to be provided per PSCell in the SN addition request ack? i.e. need to add information list for that.

| Company | Comment |
| --- | --- |
| Huawei | At least Location Information at SN, MRDC Resource Coordination information has to be different, or not include them in CPAC. SN to MN Container is pending to RAN2, in case one RRC container only includes information for one PSCell, and it is needed to include a list of containers. For other IEs, it is workable if set the limitation to use same setting for them for all the prepared PSCells, although it is sub-optimized from resource usage point of view, because of the different load, different interference, and different location for different PSCells. |
| Nokia | So far, it seems that neither location info nor the resource coordination is needed for a PSCell that is only conditionally prepared, not yet added. So single procedure seems all right. |
| ZTE | Agree with Nokia |
| LGE | The key point is how to handle “S-NG-RAN node to M-NG-RAN node Container”, for which RAN2 should be involved. LS to RAN2 and then decide finally is a better choice. |
| Ericsson | Agree with Nokia. These information can be provided in e.g. an equivalent of the HANDOVER SUCCESS message for CPAC. Agree also with LGE. Involvement of RAN2 is needed to decide if multiple containers are needed or if the target SN needs to provide multiple PSCell configuration in the same container |
| Google | For option 2 the cell specific information can probably be provided later upon CPA execution. |

For option 2, another thing needs to be decided is how to include the RRC container, whether multiple PSCells related information will be included in one RRC container, or the XnAP messages have to carry a list of RRC containers for the prepared PSCells.

Question 2: for option 2, whether to carry a single RRC container to include information for multiple PScells in the X2/XnAP message, or to carry multiple RRC containers, i.e. one RRC container for one PSCell?

| Company | Comment |
| --- | --- |
| Nokia | This is partially up to RAN2. Nonetheless, having multiple containers is no problem (see our TP). |
| ZTE | If RAN3 decides to use either a single or multiple RRC container, RAN3 can notify RAN2 of RAN3 decision. In our CR, we prefer to generate multiple RRC container, each related to one candidate PScell. |
| LGE | Checking by RAN2 is necessary. |
| Ericsson | We can ask RAN2, but both solutions are ok from a RAN3 point of view |
| Google | Separate RRC container per candidate PSCell works. |

### Decision on how many PSCells to be prepared?

It was agreed that Target SN to make the decision on the prepared PSCell or PSCells, but it is not clear which node makes decision on how many PSCells to prepare, should be the node initiates the CPAC procedure? Or should be the target SN?

Considering of option 1 and option 2, the specification changes will be:

|  | Decision on how many PSCells to be prepared | Specification impact |
| --- | --- | --- |
| Option 1 | Initiating node | May need for the Target SN to indicate to the initiating node about the limit of cells to be prepared (see Question 5) |
|  | Target SN | Target SN needs to inform the Initiating node the number of suggested PSCells. |
| Option 2 | Initiating node | Initiating node needs to inform the Target SN the number of suggested PSCells. |
|  | Target SN | May need for the initiating node to indicate to the target SN about the limit of cells to be prepared (see Question 4) |

Question 3: Which node makes decision on how many PSCells to be prepared? Initiating node or Target SN?

Please companies answer the question, and clarify the specification impact of your choice if you have different view with the table above.

| Company | Comment |
| --- | --- |
| Huawei | Initiating node |
| Nokia | The initiating node must be in control, if PSCells in multiple target SNs are prepared. The target node informs the initiating node about how many cells have been prepared (so that remaining may be offered to another target SN). |
| ZTE | Initiating node decides the maximum number of PScells to be prepared. |
| LGE | Initiating node |
| Ericsson | Initiating should have some control (e.g. max number, or required number), and will have the last word regarding the PSCells configured in the RRCReconfiguration message. But target SN should have some control too (e.g. should be able to provide less than the required number according to measurements or load) |
| Google | Initiating node |

To limit the number of prepared PSCells, for option 2, in case your answer to the question above is Target SN, do you think it is needed for the initiating node to indicate to the target SN about the limit of cells to be prepared?

Question 4: For option 2, if it is the Target SN to decide the number of PSCells, is it needed for the initiating node to indicate to the target SN about the limit of cells to be prepared?

| Company | Comment |
| --- | --- |
| Huawei | Yes |
| Nokia | Yes |
| ZTE | Yes |
| LGE | Yes |
| Ericsson | Yes |
| Google | Yes |

In case your answer to the question above is initiating node, for option 1, do you think it is needed for the Target SN to indicate to the initiating node about the limit of cells to be prepared?

Question 5: For option 1, if it is the initiating node to decide the number of PSCells, is it needed for the target SN to to indicate to the initiating node about the limit of cells to be prepared?

| Company | Comment |
| --- | --- |
| Huawei | Yes |
| Nokia | Well, yes, but not a “limit” but rather a kind of “request” (“for this UE, I could prepare up to X PSCells”). |
| ZTE | For simplicity and less inter-node signaling, we suggest that the initiating node decides the maximum of candidate PScells, and the target node decide to prepare the PScells within the scope. |
| LGE | Not definitely since the initiating node can try several times for the addition |
| Ericsson | Yes. We could use something similar to the mechanism defined for CHO (i.e. Maximum Number of CHO Preparations IE) |
| Google | Yes |

### Prepare multiple Target SNs in SN initiated inter-SN CPC

For option 1, as one PSCell is prepared in one CPAC procedure, in order to prepare multiple Target SNs in SN initiated inter-SN CPC, multiple procedures has to be triggered.

For option 2, prepare multiple PSCells in one CPAC procedure, in case of SN initiated inter-SN CPC, it is needed to decide whether it is allowed to prepare multiple PSCells in multiple target SNs by one SN Change procedure.

Question 6: For Option 2, whether it is allowed to prepare multiple PSCells in multiple target SNs by one SN Change procedure?

| Company | Comment |
| --- | --- |
| Huawei | No, it is better to only prepare multiple PSCells within one Target SN. Source SN could trigger separate SN Change for different target SN. |
| Nokia | Having a single SN Change procedure could be a good optimization, but either way is all right (FFS for the time being). |
| ZTE | No, agree with HW. |
| LGE | FFS |
| Ericsson | Option 2 is preferred, unless there is a major showstopper, which has not been identified yet. SN Change could include multiple target SN node IDs, which will trigger multiple SN Addition from MN |
| Google | FFS |

### A potential combined solution for option 1 and option 2?

Besides the option 1 and option 2 mentioned above, in [30], the following proposals can be found:

For CPA:

- MN sends only one SN ADD REQ message to the SN.

- Upon receiving one SN ADD REQ message, the SN replies multiple SN ADD REQ ACK messages if admission results are different for candidate PSCells.

- When replying multiple SN ADD REQ ACK messages, the SN uses the same SN X2/XnAP UE ID. That is, only one UE association is established between MN and SN. Different responses over multiple SN ADD REQ ACK messages are differentiated by a parallel identifier.

- Such parallel identifier is also used to differentiate subsequent procedures, e.g. X2AP Data Forwarding Address Indication, XnAP Xn-U Address Indication, Early Status Transfer, under the same UE association.

- FFS whether it is better to separate SN ADD REQ ACK message for each and every candidate PSCell or not.

For SN-initiated intra-SN CPC with MN involvement:

- The SN sends multiple SN MOD REQD messages if different modification or release of resources between MN and SN are required for candidate PSCells.

- When SN sends multiple SN MOD REQD messages, the same UE association (which has been operational) is kept. Different requests are differentiated by a parallel identifier.

- Such parallel identifier is also used to differentiate subsequent procedures, e.g. a nested MN-initiated SN modification procedure.

- For SN-initiated intra-SN CPC with MN involvement, FFS whether it is better to separate SN MOD REQD message for each and every candidate PSCell or not.

Question 7: Any view from the solution? Any comments?

| Company | Comment |
| --- | --- |
| Huawei | It is a good try, but it breaks the principle of Class 1 procedure, initiating node sends one request, and the peer node sends one reply... |
| Nokia | Same as Huawei: in class-1, there is one request and one response only. |
| ZTE | Agree with both HW and Nokia, one request and one response. |
| LGE | Agree with Huawei and Nokia |
| Ericsson | Agree with above comments |
| Google | The Class 1 procedure principle should be followed |

## Signalling design for CPA

### How to support CPA replace

In last meeting, it was agreed to support CPA by SN addition procedure. And it was FFS on how to support CPAC replace. Considering that there are MN initiated SN modification and SN initiated SN modification procedures, both of them could be used to support CPA replace.

Question 8: how to support CPA replace? Do you agree to reuse MN initiated SN modification and SN initiated SN modification procedures?

| Company | Comment |
| --- | --- |
| Huawei | Agree, support CPA replace by reuse SN modification procedures. |
| Nokia | Probably agree, though we’d prefer to consider it once we have the basic signaling for the preparation. |
| ZTE | Partly agree, we suggest to include MN/SN initiated SN modification. Moreover, we suggest to include MN/SN initiated SN release procedures (however, seems no stage 3 impact). |
| LGE | Or even SN Addition procedure can be a candidate since in Rel-16 we have agreed to use HO Request Procedure to replace the on-going CHO. So MN initiated SN addition/modification can be for further discussion as the candidates. |
| Ericsson | Agree with Nokia that we should first decide between single vs multiple preparation messages. I also agree that modification from the initiating node is needed. And cancellation from the receiving node (e.g. target SN in CPA). But we would prefer to further discuss the use-cases for modification of an existing CPAC configuration from the receiving node. |
| Google | Yes for reusing the MN initiated SN modification and we can see if there’s use cases for the SN initiated SN modification. |

### Handling of the conditional reconfiguration message

According to the RAN2 agreements below, for CPA, it is up to the MN to decide the execution condition of each candidate PSCell and MN is not required to indicate the execution condition to the other nodes.

For CPA and MN initiated Inter-SN CPC, the MN generates and transmits the conditional configuration message (i.e. RRCReconfiguration/RRCConnectionReconfiguration message) to the UE. The RRCReconfiguration provided by the candidate PSCell(s) is encapsulated in the final conditional reconfiguration message to the UE. The MN is not allowed to alter the RRCReconfiguration provided by the candidate PSCell(s). In MN initiated inter-SN CPC and CPA, the MN is not required to indicate the execution condition(s) to other involved entities (e.g. target SN, source SN).

The conditional reconfiguration message of each candidate PSCell should include the execution condition of one candidate PSCell and the RRC Reconfiguration message of this candidate PSCell. The MN needs to know the candidate PSCell ID when it receives the SN RRC reconfiguration message from the SN, therefore the target SN need to provide the prepared PSCell ID(s) to the MN.

Note that there was a working assumption in last meeting “target SN to provide the prepared PSCell id (or PSCell ids, if decided to be allowed) to the MN for CPA, MN initiated inter-SN CPC, and SN initiated inter-SN CPC”.

Question 9: Do you agree that in CPA,  MN does not send execution condition(s) to the Target SN, Target SN provides the prepared PSCell id(s) and the corresponding RRC container (RRCReconfiguration) to the MN, and then the MN generates and transmits the conditional configuration message to the UE?

| Company | Comment |
| --- | --- |
| Huawei | Agree |
| Nokia | This is partially up to RAN2 (who decides the condition and when) and partially already agreed (that the target provides the list of prepared PSCells). |
| ZTE | Agree |
| LGE | Mainly up to RAN2 |
| Ericsson | Need RAN2 progress. For example, in case single preparation message is used, it depends if multiple RRC containers are sent in the response or not |
| Google | Yes |

## Signalling design for MN initiated inter-SN CPC

### How to support MN initiated inter-SN CPC replace

In last meeting, it was agreed to reuse MN initiated SN Change procedure, i.e. CPA and SN release procedure to support MN initiated inter SN CPC. And it was FFS on how to support CPAC replace. Considering of the similarity of CPA and MN initiated inter-SN CPC, it seems also possible to reuse the MN initiated SN modification, SN initiated SN modification procedures together with SN release procedure to support MN initiated inter-SN CPC replace.

Question 10: how to support MN initiated inter-SN CPC replace? Do you agree to reuse MN initiated SN modification and SN initiated SN modification procedures, together with SN release procedure?

| Company | Comment |
| --- | --- |
| Huawei | Agree, support MN initiated inter-SN CPC replace by reuse SN modification procedures and SN release procedure. |
| Nokia | Probably agree, though we’d prefer to consider it once we have the basic signaling for the preparation. |
| ZTE | Agree with HW. |
| LGE | Similar to Q8, SN Addition/Modification procedure can be the BL for further discussion |
| Ericsson | Agree with Nokia. We can try to have a WA maybe. Ok in general for MN initiated SN modification and SN release procedures, but need further thinking SN initiated SN modification procedure. |
| Google | Yes for reusing the MN initiated SN modification and SN release procedures and we can see if there’s use cases for the SN initiated SN modification. |

### Handling of the conditional reconfiguration message

According to the RAN2 agreements below, for MN initiated inter-SN CPC, it is up to the MN to decide the execution condition of each candidate PSCell and MN is not required to indicate the execution condition to the other nodes.

For CPA and MN initiated Inter-SN CPC, the MN generates and transmits the conditional configuration message (i.e. RRCReconfiguration/RRCConnectionReconfiguration message) to the UE. The RRCReconfiguration provided by the candidate PSCell(s) is encapsulated in the final conditional reconfiguration message to the UE. The MN is not allowed to alter the RRCReconfiguration provided by the candidate PSCell(s). In MN initiated inter-SN CPC and CPA, the MN is not required to indicate the execution condition(s) to other involved entities (e.g. target SN, source SN).

The conditional reconfiguration message of each candidate PSCell should include the execution condition of one candidate PSCell and the RRC Reconfiguration message of this candidate PSCell. The MN needs to know the candidate PSCell ID when it receives the SN RRC reconfiguration message from the SN, therefore the target SN need to provide the prepared PSCell ID(s) to the MN.

Note that there was a working assumption in last meeting “target SN to provide the prepared PSCell id (or PSCell ids, if decided to be allowed) to the MN for CPA, MN initiated inter-SN CPC, and SN initiated inter-SN CPC”.

Question 11: Do you agree that in MN initiated inter-SN CPC, MN does not send execution condition(s) to the Target SN, Target SN provides the prepared PSCell id(s) and the corresponding RRC container (RRCReconfiguration) to the MN, and then the MN generates and transmits the conditional configuration message to the UE?

| Company | Comment |
| --- | --- |
| Huawei | Agree |
| Nokia | This is partially up to RAN2 (who decides the condition and when) and partially already agreed (that the target provides the list of prepared PSCells). |
| ZTE | Agree |
| LGE | Mainly up to RAN2 |
| Ericsson | Need RAN2 progress. For example, in case single preparation message is used, it depends if multiple RRC containers are sent in the response or not |
| Google | Yes |

## Signalling design for SN initiated inter-SN CPC

### How to support SN initiated inter-SN CPC replace

It was agreed to use SN initiated SN Change procedure to support SN initiated inter SN CPC. And how to support CPAC replace is FFS. Considering of the DC procedures, it seems straight forward to reuse the SN Change procedure and SN modification procedure to support SN initiated inter-SN CPC replace.

Question 12: how to support SN initiated inter-SN CPC replace? Do you agree to reuse SN Change procedure, together with MN initiated SN modification and SN initiated SN modification procedures, to support SN initiated inter-SN CPC replace?

| Company | Comment |
| --- | --- |
| Huawei | Agree, support SN initiated inter-SN CPC by reuse SN Change procedure and SN modification procedure. |
| Nokia | Probably agree, though we’d prefer to consider it once we have the basic signaling for the preparation. |
| ZTE | Agree with HW. |
| LGE | To reuse the SN Change procedure and SN Addition/modification procedure to support SN initiated inter-SN CPC replace, this can be BL for further decision. |
| Ericsson | Agree with Nokia |
| Google | Maybe discuss whether there is use case first |

### Whether the direct inter-SN communication for preparations of CPC offer enough gain to start working on it?

It was FFS if conditional SN change can be prepared directly between the involved SNs (depends on availability of SRB3).

The motivation of the direct communication between S-SN and T-SN is to avoid the MN for message interaction between SNs in the SN initiated inter-SN CPC.

In the last RAN2 meeting, RAN2 has agreed that the source SN needs to send the CPC information to the MN in this case.

8. For SN initiated inter-SN CPC, the MN generates CPC. The source SN sets the execution condition and communicates it to the MN. The MN generates the conditional reconfiguration message including the execution condition(s) provided by the source SN and RRCReconfiguration provided by the candidate PSCell(s).

Therefore it seems there is no need to support the direct communication between S-SN and T-SN.

Question 13: whether to support direct communication between S-SN and T-SN for SN initiated inter-SN CPC？

| Company | Comment |
| --- | --- |
| Huawei | No need, MN is anyway involved based on RAN2 agreement. |
| Nokia | We like the idea, but the gain may be too little. So neutral. |
| ZTE | No need. |
| LGE | Not necessary |
| Ericsson | No. We prefer not to break DC principle that MN is in charge of signaling to SN |
| Google | No |

### Handling of the conditional reconfiguration message

According to the RAN2 agreements below, for SN initiated inter-SN CPC, the source SN sets the execution condition and communicates it to the MN.

For SN initiated inter-SN CPC, the MN generates CPC. The source SN sets the execution condition and communicates it to the MN. The MN generates the conditional reconfiguration message including the execution condition(s) provided by the source SN and RRCReconfiguration provided by the candidate PSCell(s).

In RAN2 agreement, it is the MN to generate the conditional reconfiguration message, the conditional reconfiguration message of each candidate PSCell should include the execution condition of one candidate PSCell and the RRC Reconfiguration message of this candidate PSCell. There are two alternatives for the MN to generate such message:

Alternative 1: MN performs the association between the execution condition received from the source SN and the RRC configuration of the candidate PSCell received from the candidate SN.

Alternative 2: MN forwards the execution condition received from the source SN to the candidate SN. The candidate SN sends the execution condition and the RRC configuration of the candidate PSCell to the MN.

Note that there was a working assumption in last meeting “target SN to provide the prepared PSCell id (or PSCell ids, if decided to be allowed) to the MN for CPA, MN initiated inter-SN CPC, and SN initiated inter-SN CPC. In alternative 1 above, the target SN needs to provide the prepared PSCell id(s) to the MN, it is not needed in alternative 2.

Question 14: which alternative do you prefer for the MN handling?

| Company | Comment |
| --- | --- |
| Huawei | Prefer alt 2. In SN initiated inter-SN CPC, the MN does not need to know the association of the candidate PSCell and SN RRC configuration, and the MN does not need to store the execution condition received from the SN. Alternative 1 unnecessarily increases the complexity and handling load of the MN. |
| Nokia | Isn’t it RAN2’s topic? |
| ZTE | Prefer alt 1. Because for the alt 2, the execution condition will be forwarded from S-SN to MN then from MN to T-SN, then T-SN to UE. But, it may be RAN2’s issue. |
| LGE | Since “MN generates the conditional reconfiguration message including the execution condition(s) provided by the source SN and RRCReconfiguration provided by the candidate PSCell(s)”, MN should know the association anyway, right? |
| Ericsson | Both are feasible from RAN3 point of view, so it is up to RAN2 to decide |
| Google | Up to RAN2 decision |

## Support of Early Data forwarding

In R16 CHO, the early data forwarding is supported in order to reduce the latency of data forwarding. When the UE access the candidate cell, the network can send the early forwarded data to the UE. The source node forwards the PDCP SDU with SNs assigned by the source gNB to the candidate node. The source gNB sends the EARLY STATUS TRANSFER message to maintain HFN continuity by indicating PDCP SN and HFN of the first PDCP SDU that the source gNB forwards to the target gNB. The subsequent messages may be sent for discarding of already forwarded downlink PDCP SDUs in the target gNB.

In R15&R16, there are MN/SN terminated MCG/SCG/Split bearers in MR-DC. For MR-DC, user data forwarding may be performed between nodes whenever the logical node hosting the PDCP entity changes. The behavior of the node from which data is forwarded is the same as specified for the "source node" for handover, the behavior of the node to which data is forwarded is the same as specified for the "target node" for handover.

There was an working assumption to support Early Data Forwarding in CPAC, considering that early data forwarding can help to provide data to UE earlier and then improve the UE experience, do you agree to turn it to agreement to support Early Data Forwarding in CPAC?

WA: Support Early Data Forwarding in CPAC.

Question 15: Do you agree to Support Early Data Forwarding in CPAC?

| Company | Comment |
| --- | --- |
| Huawei | Support |
| Nokia | In case of CPC, early data forwarding may be done very much “on time”, i.e. when the UE finds the cell to access (see our paper). This should be supported. |
| ZTE | Can decide latter, so far, we are neutral. |
| LGE | Yes |
| Ericsson | Not sure that the full impact and complexity for all the cases (especially CPC involving multiple target SNs) have been identified. Prefer to keep this as a WA for now. Nokia’s proposal can be discussed as a legacy/late data forwarding optimization |
| Google | Neutral |

### Early data forwarding in MN initiated inter-SN CPC

In the MN initiated CPC, the CPC is trigged by the MN, the source SN needs to know the CPC triggering in order to send the early status transfer to the target SN.

There was a working assumption as below:

WA: in case of MN initiated inter-SN CPC, to support early data forwarding, the MN needs to inform source SN about CPC triggered (i.e. the successful reconfiguration of CPC at UE), details FFS.

Question 16: Do you agree to turn this working assumption into agreement? i.e. in case of MN initiated inter-SN CPC, to support early data forwarding, the MN needs to inform source SN about CPC triggered (i.e. the successful reconfiguration of CPC at UE)

| Company | Comment |
| --- | --- |
| Huawei | Agree |
| Nokia | In case of CPC, early data forwarding may be done very much “on time”, i.e. when the UE finds the cell to access. This should be supported. |
| ZTE | Can decide latter, so far, we are neutral. |
| LGE | Yes |
| Ericsson | To be discussed later |
| Google | Neutral |

Question 17: If your answer to the question above is yes, which message should be used for the MN to inform source SN about CPC triggered?

| Company | Comment |
| --- | --- |
| Huawei | Reuse the SN Reconfiguration Complete procedure to inform source SN about CPC triggered. The MN can inform the source SN after the UE has received the CPC configuration (e.g. the UE sends the MN RRC reconfiguration complete message after receiving the CPC configuration). |
| Nokia | Prefer FFS for the time being. |
| ZTE | Can decide latter, so far, we are neutral. |
| LGE | SN Reconfiguration Complete procedure can be used. |

### Early data forwarding in SN initiated inter-SN CPC

For option 2, prepare multiple PSCells in one CPAC procedure, in case of SN initiated inter-SN CPC, if it is decided to prepare multiple PSCells in multiple target SNs by one SN Change procedure in the discussion of section 3.1, to support early data forwarding, multiple data forwarding addresses should be added in the SN Change Confirm message.

Question 18: in case it is allow to prepare multiple PSCells in multiple target SNs by one SN Change procedure, do you agree to add multiple data forwarding address in the SN Change Confirm message, to support early data forwarding in case of SN initiated inter-SN CPC?

| Company | Comment |
| --- | --- |
| Huawei | Agree |
| Nokia | This may not be needed – forwarding would start only when the UE finds the target cell (“on time” forwarding). |
| ZTE | Can decide latter, so far, we are neutral. |
| LGE | Agree |
| Ericsson | That might be needed, but should first discuss if early data forwarding to multiple targets is to be supported |
| Google | Agree with Ericsson |

## Support of Late Data forwarding

As discussed in last meeting, in order to enable timely late data forwarding, the source SN must know when the UE arrives to the target SN. This can either be done based on the information from the target SN (as in case of CHO), or based on information that the UE could send to the MN, which would then forward it to the source SN (e.g. in the Release Request).

There was a working assumption achieved in last meeting, it is needed to further check if it is agreeable to turn it to agreement.

WA: in case of both MN and SN initiated inter-SN CPC, to support late data forwarding, it is needed to inform the source SN about the successful CPC execution and UE accesses to the target SN, details FFS. RAN3 waits for RAN2 progress before discussing further details.

Question 19: do you agree that in case of both MN and SN initiated inter-SN CPC, to support late data forwarding, it is needed to inform the source SN about the successful CPC execution and UE accesses to the target SN?

| Company | Comment |
| --- | --- |
| Huawei | Yes |
| Nokia | If “on time” forwarding is supported, late forwarding will not be needed. |
| ZTE | Can decide latter, so far, we are neutral. |
| LGE | Yes |
| Ericsson | I guess we now need to decide between a Bye/Success message received from the UE or from the target SN the UE successfully attaches |
| Google | Yes |

Question 20: If your answer to the question above is yes, how to inform the source SN about the successful CPC execution and UE accesses to the target SN

| Company | Comment |
| --- | --- |
| Huawei | Wait for RAN2 progress. |
| Nokia | Prefer FFS for the time being. |
| ZTE | Can decide latter, so far, we are neutral. |
| LGE | Pending to RAN2, prefer to align with CHO. |
| Google | Pending to RAN2 |

## Other Issues

If there are other issues needs to be discussed, please add in below:

### Issue x [if needed]

Description…

| Company | Comment |
| --- | --- |

# Second Round discussion

// to be updated after First Round discussion

## LS reply to RAN2?

RAN2 question in the received LS “Rel-17 CPAC is expected to support the preparation and configuration of multiple PSCell candidate cells. RAN3 is therefore asked to check whether the legacy XnAP/ X2AP signalling is sufficient or whether it shall be extended in Rel-17.”

## IEs to be included in the messages

e.g. CPAC indicator.

# References

- R3-210045 LS on Conditional PSCell Addition/Change agreements (RAN WG2)

- R3-210082 Discussion on further details of the inter-SN CPC (Nokia, Nokia Shanghai Bell)

- R3-210083 Enabling inter-SN conditional PSCell change (Nokia, Nokia Shanghai Bell)

- R3-210084 Enabling inter-SN conditional PSCell change (Nokia, Nokia Shanghai Bell)

- R3-210106 Discussion on Conditional PScell Addition/Change procedures (China Telecommunication)

- R3-210107 CR on 36.423 for introducing CPAC information in SgNB Addition procedure (China Telecommunication)

- R3-210108 CR on 38.423 for introducing CPAC information in SN Addition procedure (China Telecommunication)

- R3-210183 Discussion on CPA and CPC (ZTE)

- R3-210184 CR 36.423 for support of CPA and CPC (ZTE)

- R3-210185 CR 38.423 for support of CPA and CPC (ZTE)

- R3-210186 [draft] Reply LS on Conditional PSCell Addition/Change (ZTE)

- R3-210240 discussion on Conditional PSCell Addition and PSCell Change (NEC)

- R3-210353 CPA and MN initiated Inter-SN CPC procedures: preparation, execution, and data forwarding (Qualcomm Incorporated)

- R3-210354 SN initiated Inter-SN CPC procedure: preparation, execution, and data forwarding (Qualcomm Incorporated)

- R3-210502 (TP to TS 38.401) Consideration on conditional PSCell change/addition (Huawei)

- R3-210503 Support of conditional PSCell change/addition (Huawei)

- R3-210504 Support of conditional PSCell change/addition (Huawei)

- R3-210535 Open issues on conditional PScell Change/Addition (LG Electronics)

- R3-210542 TP for modification and release to prepared CPAC (Google Inc.)

- R3-210600 Left issues on CPAC (Lenovo, Motorola Mobility)

- R3-210601 [DRAFT] Reply LS on Conditional PSCell Addition/Change agreements (Lenovo, Motorola Mobility)

- R3-210744 Support of conditional PSCell change/addition (Ericsson)

- R3-210745 Conditional SN Addition (Ericsson)

- R3-210746 Conditional SN Addition (Ericsson)

- R3-210768 Some Considerations on How to Support CPAC (CATT)

- R3-210769 Introduction of support CPAC (CATT)

- R3-210857 Discussion on handling multiple PSCell candidates for CPAC (Samsung)

- R3-210862 Correction on the preparation of multiple PSCells in one CPAC procedure (Samsung)

- R3-210877 Correction on the preparation of one PSCell in one CPAC procedure (Samsung)

- R3-210945 Regarding inter MN-SN signaling design for CPAC (Intel Corporation)

# Agreements, working assumptions, open issues

## RAN3#110

In the RAN3#110 meeting, RAN3 has discussed the CPAC and has the following agreements and open issues.

RAN3 discuss CPAC in (NG) EN-DC and NR-DC.

Start to Focus on CPA, MN initiated inter-SN CPC, and SN initiated inter-SN CPC, if time allows, other cases can be discussed pending to RAN2 progress

Start CPAC discussion based on the conventional DC procedures:

CPA: SN addition procedure for CPA

MN initiated inter SN CPC: MN initiated SN Change procedure, i.e. CPA + SN release

SN initiated inter SN CPC: SN initiated SN Change procedure

FFS on direct inter-SN communication

Target SN to make the decision on the prepared PSCell or PSCells (if decided to be allowed).

WA: target SN to provide the prepared PSCell id (or PSCell ids, if decided to be allowed) to the MN for CPA, MN initiated inter-SN CPC, and SN initiated inter-SN CPC

WA: Support Early Data Forwarding in CPAC.

WA: in case of MN initiated inter-SN CPC, to support early data forwarding, the MN needs to inform source SN about CPC triggered (i.e. the successful reconfiguration of CPC at UE), details FFS.

Support Late Data Forwarding in CPAC.

WA: in case of both MN and SN initiated inter-SN CPC, to support late data forwarding, it is needed to inform the source SN about the successful CPC execution and UE accesses to the target SN, details FFS. RAN3 waits for RAN2 progress before discussing further details.

Open issues:

FFS on how to support CPAC replace, (SN modification procedures or SN Addition or others).

FFS on how to support multiple candidate PSCell preparation in CPAC:

Option 1: prepare one PSCell in one CPAC procedure, use parallel CPAC procedures to prepare multiple PSCells.

Need to introduce an indicator to distinguish the triggering of different PSCell preparation for the same UE”.

Option 2: prepare multiple PSCells in one CPAC procedure

FFS if multiple SN can be prepared in one SN initiated CPC procedure (SN Change Required).

FFS on how to handle the received CPC execution condition by the MN in case of SN initiated inter-SN CPC, pending to RAN2 progress.

It is pending to RAN2 on if it is needed for the Target SN to send CPAC success to the MN, and if it is needed, FFS on reusing HO Success or introduce a new class2 procedure.

FFS on F1AP and E1AP impacts.

FFS if conditional SN change can be prepared directly between the involved SNs (depends on availability of SRB3).