3GPP TSG-RAN WG3 Meeting #111-e	R3-211010

25 January – 4 February 2021

Online

Agenda Item:	14.3

Source:	Huawei (moderator)

Title:	Summary of Offline Discussion on PSCell_Change_Addition

Document for:	Discussion

# Introduction

CB: # MRDC3-PSCell_Change_Addition

- Check whether WAs from last meeting can be confirmed as agreements?

- Signalling design for CPA

- Signalling design for CPC

- How to support multiple candidate PSCell preparation in CPAC?

- Whether the SN Change procedure shall be extended to allow providing more than one target SN for CPC?

- Whether the direct inter-SN communication for preparations of CPC offer enough gain to start working on it?

- Whether and how to support early data forwarding and late data forwarding?

- Capture agreements as stage2/stage3 CRs and check details, split work, if needed

- LS reply to RAN2?

- List open issues for next meeting in the summary

(HW - moderator)

Summary of offline disc R3-211010

# For the Chairman’s Notes (Second Round)

//to be added

# Discussion (Second Round)

Progress in Chairman Notes after first round online discussion:

WA : Prepare multiple PSCells in one CPAC procedure. Do not provide Location Information and Resource Coordination information in CPAC, use same parameters for other IEs in the response message for different PSCells, FFS for single RRC container or multiple RRC containers which is pending to RAN2.

WA: Initiating node to make the decision on how many PSCells may be configured for UE.

FFS whether the initiating node send the suggested PSCell number and/or the maximum number of PSCells to the peer node.

Remaining part to be discussed in second round:

Proposed Agreements:

- In case of SN initiated inter-SN CPC, only prepare multiple PSCells in one target SN by one SN Change procedure.

- In CPA,  MN does not send execution condition(s) to the Target SN, Target SN provides the prepared PSCell id(s) and the corresponding RRC container (RRCReconfiguration) to the MN, and then the MN generates and transmits the conditional configuration message to the UE.

- In MN initiated inter-SN CPC, MN does not send execution condition(s) to the Target SN, Target SN provides the prepared PSCell id(s) and the corresponding RRC container (RRCReconfiguration) to the MN, and then the MN generates and transmits the conditional configuration message to the UE.

- Do not support direct communication between S-SN and T-SN for SN initiated inter-SN CPC

- Support early data forwarding in CPAC.

- Turn the previous WA to agreement: WA: in case of both MN and SN initiated inter-SN CPC, to support late data forwarding, it is needed to inform the source SN about the successful CPC execution and UE accesses to the target SN, details FFS. RAN3 waits for RAN2 progress before discussing further details.

Please companies feedback your comments for these proposed agreements:

| Company | Comment |
| --- | --- |
| Huawei | Ok |
| Samsung | Ok |

Proposed WAs:

- WA: CPA replace：reuse the MN/SN initiated SN modification procedures.

- WA: MN initiated inter-SN CPC replace: reuse MN initiated SN modification and SN initiated SN modification procedures, together with SN release procedure.

- WA: SN initiated inter-SN CPC replace: reuse SN Change procedure, together with MN initiated SN modification and SN initiated SN modification procedures.

Please companies feedback your comments for these proposed WAs:

| Company | Comment |
| --- | --- |
| Huawei | Ok |
| Samsung | Ok |

Content of the reply LS to RAN 2:

- Ask RAN2 to confirm RAN3 WAs and agreements related to RAN2 highlighted in blue above.

- About the first working assumption of Option 2, and ask their feedback on the RRC container design, one RRC container for one PSCell, or one RRC container for multiple PSCells and each related to one PSCell, inform them that there is a preference for the latter one.

- For SN initiated inter-SN CPC, ask RAN2 to feedback on the two alternatives:

  - Alternative 1: MN performs the association between the execution condition received from the source SN and the RRC configuration of the candidate PSCell received from the candidate SN.

  - Alternative 2: MN forwards the execution condition received from the source SN to the candidate SN. The candidate SN sends the execution condition and the RRC configuration of the candidate PSCell to the MN.

Please companies feedback your comments for these proposed content of reply LS to RAN2:

| Company | Comment |
| --- | --- |
| Huawei | Ok. Based on the discussion, the draft Reply LS will be provided to do the final review in next week. |
| Samsung | Ok |

# For the Chairman’s Notes (first round)

(1) Agreements:

- Prepare multiple PSCells in one CPAC procedure.

  - Do not provide Location Information and Resource Coordination information in CPAC, use same parameters for other IEs in the response message for different PSCells, FFS for RRC container(s).

- Initiating node to make the decision on how many PSCells to be prepared, initiating node informs the Target SN the number of suggested PSCells.

- In case of SN initiated inter-SN CPC, only prepare multiple PSCells in one target SN by one SN Change procedure.

- In CPA,  MN does not send execution condition(s) to the Target SN, Target SN provides the prepared PSCell id(s) and the corresponding RRC container (RRCReconfiguration) to the MN, and then the MN generates and transmits the conditional configuration message to the UE. (send to RAN2 to check this agreement)

- In MN initiated inter-SN CPC, MN does not send execution condition(s) to the Target SN, Target SN provides the prepared PSCell id(s) and the corresponding RRC container (RRCReconfiguration) to the MN, and then the MN generates and transmits the conditional configuration message to the UE. (send to RAN2 to check this agreement)

- Do not support direct communication between S-SN and T-SN for SN initiated inter-SN CPC

- Support early data forwarding in CPAC.

- Turn the previous WA to agreement: WA: in case of both MN and SN initiated inter-SN CPC, to support late data forwarding, it is needed to inform the source SN about the successful CPC execution and UE accesses to the target SN, details FFS. RAN3 waits for RAN2 progress before discussing further details.

(2) WAs:

- WA: CPA replace：reuse the MN/SN initiated SN modification procedures.

- WA: MN initiated inter-SN CPC replace: reuse MN initiated SN modification and SN initiated SN modification procedures, together with SN release procedure.

- WA: SN initiated inter-SN CPC replace: reuse SN Change procedure, together with MN initiated SN modification and SN initiated SN modification procedures.

(3) Moderator to provide a draft reply LS to RAN 2 about:

- Information RAN3 agreements to RAN2, especially the ones related to RAN2

- Inform RAN2 about the selection of option 2, and ask their feedback on the RRC container design, one RRC container for one PSCell, or one RRC container for multiple PSCells and each related to one PSCell, inform them that there is a preference for the latter one.

- For SN initiated inter-SN CPC, ask RAN2 to feedback on the two alternatives:

  - Alternative 1: MN performs the association between the execution condition received from the source SN and the RRC configuration of the candidate PSCell received from the candidate SN.

  - Alternative 2: MN forwards the execution condition received from the source SN to the candidate SN. The candidate SN sends the execution condition and the RRC configuration of the candidate PSCell to the MN.

# Discussion

## How to support multiple candidate PSCell preparation in CPAC?

In last RAN3 meeting, two options were listed as below:

- Option 1: prepare one PSCell in one CPAC procedure, use parallel CPAC procedures to prepare multiple PSCells

- Option 2: prepare multiple PSCells in one CPAC procedure

Before down selection of these two options, it is needed to first answer several questions related.

Take CPA as an example, the existing SN addition request ack only provide information related to one PSCell. In case of option1, the existing IEs can be reused for the one prepared PSCell. In case of option 2, it is needed to further analyses which information has to be provided in a per PSCell way.

| IE/Group Name | Presence |
| --- | --- |
| PDU Session Resources Admitted To Be Added List |  |
| >PDU Session Resources Admitted To Be Added Item |  |
| >>PDU Session ID | M |
| >>PDU Session Resource Setup Response Info – SN terminated | O |
| >>PDU Session Resource Setup Response Info – MN terminated | O |
| PDU Session Resources Not Admitted List | O |
| >PDU Session Resources Not Admitted List – SN terminated | O |
| >PDU Session Resources Not Admitted List – MN terminated | O |
| S-NG-RAN node to M-NG-RAN node Container | M |
| Admitted Split SRBs | O |
| RRC Config Indication | O |
| Criticality Diagnostics | O |
| Location Information at S-NODE | O |
| MR-DC Resource Coordination Information | O |
| Available fast MCG recovery via SRB3 | O |

Question 1: For Option 2, in case of CPA, which information needs to be provided per PSCell in the SN addition request ack? i.e. need to add information list for that.

| Company | Comment |
| --- | --- |
| Huawei | At least Location Information at SN, MRDC Resource Coordination information has to be different, or not include them in CPAC. SN to MN Container is pending to RAN2, in case one RRC container only includes information for one PSCell, and it is needed to include a list of containers. For other IEs, it is workable if set the limitation to use same setting for them for all the prepared PSCells, although it is sub-optimized from resource usage point of view, because of the different load, different interference, and different location for different PSCells. |
| Nokia | So far, it seems that neither location info nor the resource coordination is needed for a PSCell that is only conditionally prepared, not yet added. So single procedure seems all right. |
| ZTE | Agree with Nokia |
| LGE | The key point is how to handle “S-NG-RAN node to M-NG-RAN node Container”, for which RAN2 should be involved. LS to RAN2 and then decide finally is a better choice. |
| Ericsson | Agree with Nokia. These information can be provided in e.g. an equivalent of the HANDOVER SUCCESS message for CPAC. Agree also with LGE. Involvement of RAN2 is needed to decide if multiple containers are needed or if the target SN needs to provide multiple PSCell configuration in the same container |
| Google | For option 2 the cell specific information can probably be provided later upon CPA execution. |
| InterDigital | Agree with LGE, for the bigger issue, but it is not clear that location info or resource coordination is needed. |
| China Telecom | Agree with Nokia. |
| Lenovo, Motorola Mobility | Agree with Nokia |
| Intel | Option 2 requires huge changes to the contents of SN ADD REQ ACK message. On the other hand, triggering parallel procedures as Option 1 does not make sense as MN does not know how many PSCells that SN would like to configure for CPAC. The mandatorily included contents of the SN ADD REQ message (e.g. UE security capabilities, SN security key, Bearer/PDU session resources to be added, etc.) are all “not cell-specific” and thus don’t have to be repeated at all. Please note that, as we all are well aware of, the reason why we allowed parallel procedures for CHO in Rel-16 is because the HO preparation signaling design had been that the source requests HO for a specific target cell. In order to prepare HO for multiple candidate cells, it was natural to consider parallel procedures. But here is different. For SN addition. it has been designed that SN is responsible for choosing the right PSCell and SCG SCells on its own for the UE based on measurement information of the candidate cell lists and PCell ID provided from the MN. We strongly believe there is no reason to send multiple SN ADD REQ messages for CPA. Both options do not suit our needs indeed, and so we should really think out of the box. It would be a bad practice if we simply abandon the possibility for CPA that MN sends one request and SN can reply multiple back (if needed), simply due to what “class-1” should be. |
| Samsung | Agree with Nokia. |
| NEC | Since during CPA the PSCell is not yet final decided, the Location Information, Resource Coordination are not needed. However if these information corresponding to each PSCell need to be sent in advanced, extension is needed. |
| Qualcomm | Theoretically, all these IEs could be PSCell specific. If option 2 is used, we can pose some restriction to reduce the PSCell specific IEs, with the cost of some flexibility lose. |
| CATT | Agree with Nokia and LG, we should involve RAN2 check the container design. Also for the cell-specific information maybe rewrite after access successfully as Google suggestion. |

Moderator’s summary: majority of companies believe that the Location Information and Resource Coordination information are not needed to be provided when preparing the candidate PSCells, and can limit to use same parameters for other IEs for all PSCells, (RRC Container aspect will be summaried in next question part). And it can be understood that one company would like to use option 1, and one company could like to use a single request message to trigger multiple response messages, and most of the other companies prefer to use option 2.

Moderator’s proposal: Select option 2 as the way forward, and do not provide Location Information and Resource Coordination information in CPAC, use same parameters for other IEs in the response message for different PSCells, FFS for RRC container(s).

For option 2, another thing needs to be decided is how to include the RRC container, whether multiple PSCells related information will be included in one RRC container, or the XnAP messages have to carry a list of RRC containers for the prepared PSCells.

Question 2: for option 2, whether to carry a single RRC container to include information for multiple PScells in the X2/XnAP message, or to carry multiple RRC containers, i.e. one RRC container for one PSCell?

| Company | Comment |
| --- | --- |
| Nokia | This is partially up to RAN2. Nonetheless, having multiple containers is no problem (see our TP). |
| ZTE | If RAN3 decides to use either a single or multiple RRC container, RAN3 can notify RAN2 of RAN3 decision. In our CR, we prefer to generate multiple RRC container, each related to one candidate PScell. |
| LGE | Checking by RAN2 is necessary. |
| Ericsson | We can ask RAN2, but both solutions are ok from a RAN3 point of view |
| Google | Separate RRC container per candidate PSCell works. |
| InterDigital | Checking by RAN2 is necessary but both should be good for RAN3. |
| China Telecom | Both options seem OK, ask RAN2 if necessary. |
| Lenovo, Motorola Mobility | Upon RAN2 decision |
| Samsung | We agree this is upto RAN2, however, prefer multiple RRC container. In SN initiated inter-SN CPC, S-SN transfers PSCell candidates to the MN with triggering condition. When we agree to accept MN will not transfer the triggering condition to T-SN, MN should be able to remove the triggering condition, which needs decoding of RRC message when a single RRC is adopted. |
| NEC | Can coordinate with RAN2, having multiple RRC containers should be ok if RAN2 does not want to include multiple PSCell in one RRC container. |
| Qualcomm | Up to RAN2 |
| CATT | Upon RAN2 decision. Both are workable from RAN3 view |

Moderator’s summary: majority of companies think this is up to RAN2 decision, and 5 companise show the preference of using multiple RRC Containers, each related to one candidate PSCell.

Moderator’s proposal: Inform RAN2 about the selection of option 2, and ask their feedback on the RRC container design, inform them that there is a preference to use multiple RRC containers, each related to one candidate PScell.

### Decision on how many PSCells to be prepared?

It was agreed that Target SN to make the decision on the prepared PSCell or PSCells, but it is not clear which node makes decision on how many PSCells to prepare, should be the node initiates the CPAC procedure? Or should be the target SN?

Considering of option 1 and option 2, the specification changes will be:

|  | Decision on how many PSCells to be prepared | Specification impact |
| --- | --- | --- |
| Option 1 | Initiating node | May need for the Target SN to indicate to the initiating node about the limit of cells to be prepared (see Question 5) |
|  | Target SN | Target SN needs to inform the Initiating node the number of suggested PSCells. |
| Option 2 | Initiating node | Initiating node needs to inform the Target SN the number of suggested PSCells. |
|  | Target SN | May need for the initiating node to indicate to the target SN about the limit of cells to be prepared (see Question 4) |

Question 3: Which node makes decision on how many PSCells to be prepared? Initiating node or Target SN?

Please companies answer the question, and clarify the specification impact of your choice if you have different view with the table above.

| Company | Comment |
| --- | --- |
| Huawei | Initiating node |
| Nokia | The initiating node must be in control, if PSCells in multiple target SNs are prepared. The target node informs the initiating node about how many cells have been prepared (so that remaining may be offered to another target SN). |
| ZTE | Initiating node decides the maximum number of PScells to be prepared. |
| LGE | Initiating node |
| Ericsson | Initiating should have some control (e.g. max number, or required number), and will have the last word regarding the PSCells configured in the RRCReconfiguration message. But target SN should have some control too (e.g. should be able to provide less than the required number according to measurements or load) |
| Google | Initiating node |
| InterDigital | Initiating Node |
| China Telecom | Initiating node. |
| Lenovo, Motorola Mobility | Initiating node |
| Intel | Regardless of options, the initiating node should tell up to how many PSCells can be prepared. In terms of CPA, multiple SN nodes could be involved. The MN needs to make sure that total # of prepared PSCells does not exceed the limit for a UE, which is 8 by RAN2. |
| Samsung | Initiating node. |
| NEC | Target SN select the candidate PSCells, if there will be limitation considering multiple target SNs, then the Initiating node may indicate how many PSCells to be prepared. If only single target SN, then this indication is not needed. |
| Qualcomm | Initiating node decides the maximum number of PSCells for the target node, the target node decides the final PSCells numbers of the node. |
| CATT | Initiating node provide the required number, the target node prepare the PSCell within the numbers. |

Moderator’s summary: majority companies think that it should be the initiating node to make the decision on how many PSCells to be prepared, and therefore the initiating node needs to inform the Target SN the number of suggested PSCells.

Moderator’s proposal: initiating node to make the decision on how many PSCells to be prepared, and initiating node informs the Target SN the number of suggested PSCells.

To limit the number of prepared PSCells, for option 2, in case your answer to the question above is Target SN, do you think it is needed for the initiating node to indicate to the target SN about the limit of cells to be prepared?

Question 4: For option 2, if it is the Target SN to decide the number of PSCells, is it needed for the initiating node to indicate to the target SN about the limit of cells to be prepared?

| Company | Comment |
| --- | --- |
| Huawei | Yes |
| Nokia | Yes |
| ZTE | Yes |
| LGE | Yes |
| Ericsson | Yes |
| Google | Yes |
| InterDigital | Yes |
| China Telecom | Yes. |
| Lenovo, Motorola Mobility | Yes |
| Intel | Yes, please see above. |
| Samsung | Yes. |
| NEC | If multiple SNs will be prepared, then yes, otherwise if only single SN, then no need. |
| Qualcomm | Yes |
| CATT | Yes |

Moderator’s summary: all companies agree with the analyses, but based on the summary of Q3, there is no need to continue working on this aspect.

Moderator’s proposal: noted.

In case your answer to the question above is initiating node, for option 1, do you think it is needed for the Target SN to indicate to the initiating node about the limit of cells to be prepared?

Question 5: For option 1, if it is the initiating node to decide the number of PSCells, is it needed for the target SN to to indicate to the initiating node about the limit of cells to be prepared?

| Company | Comment |
| --- | --- |
| Huawei | Yes |
| Nokia | Well, yes, but not a “limit” but rather a kind of “request” (“for this UE, I could prepare up to X PSCells”). |
| ZTE | For simplicity and less inter-node signaling, we suggest that the initiating node decides the maximum of candidate PScells, and the target node decide to prepare the PScells within the scope. |
| LGE | Not definitely since the initiating node can try several times for the addition |
| Ericsson | Yes. We could use something similar to the mechanism defined for CHO (i.e. Maximum Number of CHO Preparations IE) |
| Google | Yes |
| InterDigital | Agree with Huawei, Ericsson. |
| China Telecom | Yes, we also agree with Ericsson, similar mechanism defined for CHO can be reused here. |
| Lenovo, Motorola Mobility | Similar view as ZTE We understand the intention to introduce some cooperation between nodes to prepare a proper number of PSCells at each SN node. However, to achieve this, MN needs to first add candidate SNs and gets limit of cells can be prepared at each candidate SN before really requesting the CPAC preparation. We are concerned about the signaling overhead, especially for SN initiated CPC, i.e. if the target SN needs to indicate (via MN) to the initiating SN about the limits of cells to be prepared, the signaling overhead would be too much. For simplicity, if the number of PSCells to be prepared is beyond the maximum number can be prepared by the target SN, the target SN simply only prepare a number of PSCells according to its own capability. |
| Intel | I still don’t understand why the initiating node decides the exact # of PSCells to be prepared. In terms of CPA, it is (and has been) totally up to SN to decide and choose the right PSCell and SCG SCells. This “SN’s control” should be honored. The initiating node just needs to tell “up to how many” can be prepared. |
| Samsung | Agree with Huawei. |
| NEC | Can be yes, SN should have a right to control its resource usage. |
| Qualcomm | Agree with ZTE |
| CATT | Agree with E/// |

Moderator’s summary: as this question is for option 1, considering of the summary of Q1, there is no need to continue working on this aspect.

Moderator’s proposal: noted

### Prepare multiple Target SNs in SN initiated inter-SN CPC

For option 1, as one PSCell is prepared in one CPAC procedure, in order to prepare multiple Target SNs in SN initiated inter-SN CPC, multiple procedures has to be triggered.

For option 2, prepare multiple PSCells in one CPAC procedure, in case of SN initiated inter-SN CPC, it is needed to decide whether it is allowed to prepare multiple PSCells in multiple target SNs by one SN Change procedure.

Question 6: For Option 2, whether it is allowed to prepare multiple PSCells in multiple target SNs by one SN Change procedure?

| Company | Comment | Moderator summary |
| --- | --- | --- |
| Huawei | No, it is better to only prepare multiple PSCells within one Target SN. Source SN could trigger separate SN Change for different target SN. | Single SN |
| Nokia | Having a single SN Change procedure could be a good optimization, but either way is all right (FFS for the time being). | Single SN or FFS |
| ZTE | No, agree with HW. | Single SN |
| LGE | FFS | FFS |
| Ericsson | Option 2 is preferred, unless there is a major showstopper, which has not been identified yet. SN Change could include multiple target SN node IDs, which will trigger multiple SN Addition from MN | Multiple SNs |
| Google | FFS | FFS |
| InterDigital | Agree with Huawei, but other option is probably possible | Single SN |
| China Telecom | FFS | FFS |
| Lenovo, Motorola Mobility | CPA and inter SN CPC is essentially add or change SNs, thus the PSCells preparation procedure should be at the granularity of per SN. Following the same spirit we prefer to only prepare multiple PSCells in one target cell during one SN change procedure. | Single SN |
| Intel | The SN-initiated inter-SN CPC is triggered from the source SN by sending “SN CHG REQD” message. Upon receiving this SN CHG REQD message, MN triggers SN addition toward the secondary node based on the target node ID included in that message, which is chosen by the source SN based on measurement info. There is no need to repeat this SN CHG REQD message. CPA can be used when the MN triggers SN addition toward that indicated target SN node. Then, the question is whether we should allow MN to trigger CPA toward multiple candidate target SNs beyond what was indicated from the source SN. If so, it impacts on the SN CHG CNFM message as MN may need to toss multiple data forwarding info. For now, it looks sufficient to trigger CPA toward only one target SN node. | Single SN |
| Samsung | No, multiple cells within a “single T-SN” should be supported. When multiple cells under different SNs are included in one message, there is much more thing to consider, like transferring RRC message from UE. | Single SN |
| NEC | If to have less impact on specification, one time one target SN is preferable. | Single SN |
| Qualcomm | Yes, agree with Ericsson | Multiple SNs |
| CATT | Agree with HW. | Single SN |

Moderator’s summary:  8.5 companies prefer single SN, 3.5 companies FFS, 2 companies prefer to prefer multiple SN.

Moderator’s proposal: in case of SN initiated inter-SN CPC, only prepare multiple PSCells in one target SN by one SN Change procedure.

### A potential combined solution for option 1 and option 2?

Besides the option 1 and option 2 mentioned above, in [30], the following proposals can be found:

For CPA:

- MN sends only one SN ADD REQ message to the SN.

- Upon receiving one SN ADD REQ message, the SN replies multiple SN ADD REQ ACK messages if admission results are different for candidate PSCells.

- When replying multiple SN ADD REQ ACK messages, the SN uses the same SN X2/XnAP UE ID. That is, only one UE association is established between MN and SN. Different responses over multiple SN ADD REQ ACK messages are differentiated by a parallel identifier.

- Such parallel identifier is also used to differentiate subsequent procedures, e.g. X2AP Data Forwarding Address Indication, XnAP Xn-U Address Indication, Early Status Transfer, under the same UE association.

- FFS whether it is better to separate SN ADD REQ ACK message for each and every candidate PSCell or not.

For SN-initiated intra-SN CPC with MN involvement:

- The SN sends multiple SN MOD REQD messages if different modification or release of resources between MN and SN are required for candidate PSCells.

- When SN sends multiple SN MOD REQD messages, the same UE association (which has been operational) is kept. Different requests are differentiated by a parallel identifier.

- Such parallel identifier is also used to differentiate subsequent procedures, e.g. a nested MN-initiated SN modification procedure.

- For SN-initiated intra-SN CPC with MN involvement, FFS whether it is better to separate SN MOD REQD message for each and every candidate PSCell or not.

Question 7: Any view from the solution? Any comments?

| Company | Comment |
| --- | --- |
| Huawei | It is a good try, but it breaks the principle of Class 1 procedure, initiating node sends one request, and the peer node sends one reply... |
| Nokia | Same as Huawei: in class-1, there is one request and one response only. |
| ZTE | Agree with both HW and Nokia, one request and one response. |
| LGE | Agree with Huawei and Nokia |
| Ericsson | Agree with above comments |
| Google | The Class 1 procedure principle should be followed |
| InterDigital | Agree with above comments |
| China Telecom | Agree with above. |
| Intel | As mentioned above, both options do not suit our needs, so we should think out of the box. We should be open for the possibility that MN sends one request and SN can reply multiple back (if needed), rather than simply following the conventional “class-1”. |
| Samsung | Agree with HW and Nokia. |
| NEC | One Request one response, this is class 1. Whether to introduce new e.g. class 3 procedure for this CPAC? Probably too much. |
| Qualcomm | Agree with Huawei, Nokia, ZTE, LGE, Ericsson, Google, InterDigital, CT. If we have to make this solution work, probably we can make the following response messages as a class 2 procedure. The response message in class 1 procedures tell source how many class 2 procedures will follow. |
| CATT | Agree with majority companies’ view. We should not break the principle for the class one procedure. In other word, the solution is not big different from option1. |

Moderator’s summary: majority companies prefer to not change the principle of Class 1 procedure.

Moderator’s proposal: noted.

## Signalling design for CPA

### How to support CPA replace

In last meeting, it was agreed to support CPA by SN addition procedure. And it was FFS on how to support CPAC replace. Considering that there are MN initiated SN modification and SN initiated SN modification procedures, both of them could be used to support CPA replace.

Question 8: how to support CPA replace? Do you agree to reuse MN initiated SN modification and SN initiated SN modification procedures?

| Company | Comment |
| --- | --- |
| Huawei | Agree, support CPA replace by reuse SN modification procedures. |
| Nokia | Probably agree, though we’d prefer to consider it once we have the basic signaling for the preparation. |
| ZTE | Partly agree, we suggest to include MN/SN initiated SN modification. Moreover, we suggest to include MN/SN initiated SN release procedures (however, seems no stage 3 impact). |
| LGE | Or even SN Addition procedure can be a candidate since in Rel-16 we have agreed to use HO Request Procedure to replace the on-going CHO. So MN initiated SN addition/modification can be for further discussion as the candidates. |
| Ericsson | Agree with Nokia that we should first decide between single vs multiple preparation messages. I also agree that modification from the initiating node is needed. And cancellation from the receiving node (e.g. target SN in CPA). But we would prefer to further discuss the use-cases for modification of an existing CPAC configuration from the receiving node. |
| Google | Yes for reusing the MN initiated SN modification and we can see if there’s use cases for the SN initiated SN modification. |
| InterDigital | Agree but support Nokia that final decision would be based on agreements for single vs. multiple preparation |
| China Telecom | Agree to reuse the MN/SN initiated SN modification procedures to support CPA replace. |
| Lenovo, Motorola Mobility | Agree with Nokia |
| Intel | I don’t understand why MN needs to modify conditional PSCell configuration that was prepared by SN. But if it is due to e.g. configuration change in MN side that may affect SN’s admission after conditional PSCell configurations have been prepared and configured to the UE, then we think that it is better to re-send SN ADD REQ message again, rather than using MN-initiated SN modification procedure. |
| Samsung | Agree with Nokia. We can discuss this later after reaching to the agreement on preparation. |
| NEC | agree |
| Qualcomm | Agree with China Telecom |
| CATT | Agree to use the modification procedure |

Moderator’s summary: majority companies prefer to reuse the MN/SN initiated SN modification procedures to support CPA replace. Few companies considers SN addition procedure and SN release procedure as well.

Moderator’s proposal: WA: reuse the MN/SN initiated SN modification procedures to support CPA replace.

### Handling of the conditional reconfiguration message

According to the RAN2 agreements below, for CPA, it is up to the MN to decide the execution condition of each candidate PSCell and MN is not required to indicate the execution condition to the other nodes.

For CPA and MN initiated Inter-SN CPC, the MN generates and transmits the conditional configuration message (i.e. RRCReconfiguration/RRCConnectionReconfiguration message) to the UE. The RRCReconfiguration provided by the candidate PSCell(s) is encapsulated in the final conditional reconfiguration message to the UE. The MN is not allowed to alter the RRCReconfiguration provided by the candidate PSCell(s). In MN initiated inter-SN CPC and CPA, the MN is not required to indicate the execution condition(s) to other involved entities (e.g. target SN, source SN).

The conditional reconfiguration message of each candidate PSCell should include the execution condition of one candidate PSCell and the RRC Reconfiguration message of this candidate PSCell. The MN needs to know the candidate PSCell ID when it receives the SN RRC reconfiguration message from the SN, therefore the target SN need to provide the prepared PSCell ID(s) to the MN.

Note that there was a working assumption in last meeting “target SN to provide the prepared PSCell id (or PSCell ids, if decided to be allowed) to the MN for CPA, MN initiated inter-SN CPC, and SN initiated inter-SN CPC”.

Question 9: Do you agree that in CPA,  MN does not send execution condition(s) to the Target SN, Target SN provides the prepared PSCell id(s) and the corresponding RRC container (RRCReconfiguration) to the MN, and then the MN generates and transmits the conditional configuration message to the UE?

| Company | Comment |
| --- | --- |
| Huawei | Agree |
| Nokia | This is partially up to RAN2 (who decides the condition and when) and partially already agreed (that the target provides the list of prepared PSCells). |
| ZTE | Agree |
| LGE | Mainly up to RAN2 |
| Ericsson | Need RAN2 progress. For example, in case single preparation message is used, it depends if multiple RRC containers are sent in the response or not |
| Google | Yes |
| InterDigital | Agree but needs RAN2 progress |
| China Telecom | Agree. |
| Lenovo, Motorola Mobility | Agree |
| Intel | Yes |
| Samsung | Yes. |
| NEC | Agreed. |
| Qualcomm | Agree |
| CATT | Yes |

Moderator’s summary: majority companies agree with the analyses, and some of them consider RAN2 progress is needed. Considering of the existing RAN2 agreements listed above has already been take into account, seems we could agree in RAN3 for these.

Moderator’s proposal:

Agreement: in CPA,  MN does not send execution condition(s) to the Target SN, Target SN provides the prepared PSCell id(s) and the corresponding RRC container (RRCReconfiguration) to the MN, and then the MN generates and transmits the conditional configuration message to the UE.

Inform RAN2 about it.

## Signalling design for MN initiated inter-SN CPC

### How to support MN initiated inter-SN CPC replace

In last meeting, it was agreed to reuse MN initiated SN Change procedure, i.e. CPA and SN release procedure to support MN initiated inter SN CPC. And it was FFS on how to support CPAC replace. Considering of the similarity of CPA and MN initiated inter-SN CPC, it seems also possible to reuse the MN initiated SN modification, SN initiated SN modification procedures together with SN release procedure to support MN initiated inter-SN CPC replace.

Question 10: how to support MN initiated inter-SN CPC replace? Do you agree to reuse MN initiated SN modification and SN initiated SN modification procedures, together with SN release procedure?

| Company | Comment |
| --- | --- |
| Huawei | Agree, support MN initiated inter-SN CPC replace by reuse SN modification procedures and SN release procedure. |
| Nokia | Probably agree, though we’d prefer to consider it once we have the basic signaling for the preparation. |
| ZTE | Agree with HW. |
| LGE | Similar to Q8, SN Addition/Modification procedure can be the BL for further discussion |
| Ericsson | Agree with Nokia. We can try to have a WA maybe. Ok in general for MN initiated SN modification and SN release procedures, but need further thinking SN initiated SN modification procedure. |
| Google | Yes for reusing the MN initiated SN modification and SN release procedures and we can see if there’s use cases for the SN initiated SN modification. |
| InterDigital | Agree with Huawei, but agree we can go with a WA to make sure it is consistent with our basic signaling |
| China Telecom | Agree to reuse the SN modification procedures to support MN initiated inter-SN CPC replace. |
| Lenovo, Motorola Mobility | Agree |
| Intel | No. As mentioned above, we think it is better to re-send SN ADD REQ message again, rather than using MN-initiated SN modification procedure. |
| Samsung | Same with the answer in Q7, we can discuss later. |
| NEC | agree. |
| Qualcomm | Agree with Huawei |

| CATT | Agree |
| --- | --- |

Moderator’s summary: majority companies agree with the analyses, some of them would like to make it as an WA, and one company could like to use SN add req instead of MN initiated SN modification.

Moderator’s proposal: WA: MN initiated inter-SN CPC replace: reuse MN initiated SN modification and SN initiated SN modification procedures, together with SN release procedure

### Handling of the conditional reconfiguration message

According to the RAN2 agreements below, for MN initiated inter-SN CPC, it is up to the MN to decide the execution condition of each candidate PSCell and MN is not required to indicate the execution condition to the other nodes.

For CPA and MN initiated Inter-SN CPC, the MN generates and transmits the conditional configuration message (i.e. RRCReconfiguration/RRCConnectionReconfiguration message) to the UE. The RRCReconfiguration provided by the candidate PSCell(s) is encapsulated in the final conditional reconfiguration message to the UE. The MN is not allowed to alter the RRCReconfiguration provided by the candidate PSCell(s). In MN initiated inter-SN CPC and CPA, the MN is not required to indicate the execution condition(s) to other involved entities (e.g. target SN, source SN).

The conditional reconfiguration message of each candidate PSCell should include the execution condition of one candidate PSCell and the RRC Reconfiguration message of this candidate PSCell. The MN needs to know the candidate PSCell ID when it receives the SN RRC reconfiguration message from the SN, therefore the target SN need to provide the prepared PSCell ID(s) to the MN.

Note that there was a working assumption in last meeting “target SN to provide the prepared PSCell id (or PSCell ids, if decided to be allowed) to the MN for CPA, MN initiated inter-SN CPC, and SN initiated inter-SN CPC”.

Question 11: Do you agree that in MN initiated inter-SN CPC, MN does not send execution condition(s) to the Target SN, Target SN provides the prepared PSCell id(s) and the corresponding RRC container (RRCReconfiguration) to the MN, and then the MN generates and transmits the conditional configuration message to the UE?

| Company | Comment |
| --- | --- |
| Huawei | Agree |
| Nokia | This is partially up to RAN2 (who decides the condition and when) and partially already agreed (that the target provides the list of prepared PSCells). |
| ZTE | Agree |
| LGE | Mainly up to RAN2 |
| Ericsson | Need RAN2 progress. For example, in case single preparation message is used, it depends if multiple RRC containers are sent in the response or not |
| Google | Yes |
| InterDigital | Agree but it does need RAN2 verification |
| China Telecom | Agree |
| Lenovo, Motorola Mobility | Agree |
| Intel | Yes |
| Samsung | Yes. |
| NEC | agree. |
| Qualcomm | Agree |
| CATT | agree |

Moderator’s summary: majority companies agree with the analyses, some of them think that it is up to RAN2,

Moderator’s proposal:

Agreement: in MN initiated inter-SN CPC, MN does not send execution condition(s) to the Target SN, Target SN provides the prepared PSCell id(s) and the corresponding RRC container (RRCReconfiguration) to the MN, and then the MN generates and transmits the conditional configuration message to the UE

Inform RAN2 about it.

## Signalling design for SN initiated inter-SN CPC

### How to support SN initiated inter-SN CPC replace

It was agreed to use SN initiated SN Change procedure to support SN initiated inter SN CPC. And how to support CPAC replace is FFS. Considering of the DC procedures, it seems straight forward to reuse the SN Change procedure and SN modification procedure to support SN initiated inter-SN CPC replace.

Question 12: how to support SN initiated inter-SN CPC replace? Do you agree to reuse SN Change procedure, together with MN initiated SN modification and SN initiated SN modification procedures, to support SN initiated inter-SN CPC replace?

| Company | Comment |
| --- | --- |
| Huawei | Agree, support SN initiated inter-SN CPC by reuse SN Change procedure and SN modification procedure. |
| Nokia | Probably agree, though we’d prefer to consider it once we have the basic signaling for the preparation. |
| ZTE | Agree with HW. |
| LGE | To reuse the SN Change procedure and SN Addition/modification procedure to support SN initiated inter-SN CPC replace, this can be BL for further decision. |
| Ericsson | Agree with Nokia |
| Google | Maybe discuss whether there is use case first |
| InterDigital | Agree but again should go slow to make sure we are aligned with basic signalling |
| China Telecom | Agree with HW. |
| Lenovo, Motorola Mobility | Agree |
| Intel | Again, for CPC replace triggered by the source SN, the source SN needs to send SN CHG REQD message again, if configuration has been changed in the source SN side after it has received the SN CHG CNFM message. The MN will send SN ADD REQ message again to the target SN so that the target SN can update conditional PSCell configurations accordingly. There is no need to use MN-initiated or SN-initiated modification procedures for modifying conditional PSCell configurations. |
| Samsung | Same with the answer in Q7, we can discuss later. |
| NEC | Agree. |
| Qualcomm | Agree with Huawei |
| CATT | Agree |

Moderator’s summary: majority companies agree with the analyses,

Moderator’s proposal: WA: SN initiated inter-SN CPC replace:  reuse SN Change procedure, together with MN initiated SN modification and SN initiated SN modification procedures

### Whether the direct inter-SN communication for preparations of CPC offer enough gain to start working on it?

It was FFS if conditional SN change can be prepared directly between the involved SNs (depends on availability of SRB3).

The motivation of the direct communication between S-SN and T-SN is to avoid the MN for message interaction between SNs in the SN initiated inter-SN CPC.

In the last RAN2 meeting, RAN2 has agreed that the source SN needs to send the CPC information to the MN in this case.

8. For SN initiated inter-SN CPC, the MN generates CPC. The source SN sets the execution condition and communicates it to the MN. The MN generates the conditional reconfiguration message including the execution condition(s) provided by the source SN and RRCReconfiguration provided by the candidate PSCell(s).

Therefore it seems there is no need to support the direct communication between S-SN and T-SN.

Question 13: whether to support direct communication between S-SN and T-SN for SN initiated inter-SN CPC？

| Company | Comment |
| --- | --- |
| Huawei | No need, MN is anyway involved based on RAN2 agreement. |
| Nokia | We like the idea, but the gain may be too little. So neutral. |
| ZTE | No need. |
| LGE | Not necessary |
| Ericsson | No. We prefer not to break DC principle that MN is in charge of signaling to SN |
| Google | No |
| InterDigital | No need |
| China Telecom | No need. |
| Lenovo, Motorola Mobility | No |
| Intel | Prefer FFS after we progress on basic signalling designs which are more important. |
| Samsung | No strong preference, but seems not needed. |
| NEC | Tend to agree no need to have direct inter-SN communication for this purpose. |
| Qualcomm | No |
| CATT | NO |

Moderator’s summary: majority companies say no.

Moderator’s proposal: do not support direct communication between S-SN and T-SN for SN initiated inter-SN CPC

### Handling of the conditional reconfiguration message

According to the RAN2 agreements below, for SN initiated inter-SN CPC, the source SN sets the execution condition and communicates it to the MN.

For SN initiated inter-SN CPC, the MN generates CPC. The source SN sets the execution condition and communicates it to the MN. The MN generates the conditional reconfiguration message including the execution condition(s) provided by the source SN and RRCReconfiguration provided by the candidate PSCell(s).

In RAN2 agreement, it is the MN to generate the conditional reconfiguration message, the conditional reconfiguration message of each candidate PSCell should include the execution condition of one candidate PSCell and the RRC Reconfiguration message of this candidate PSCell. There are two alternatives for the MN to generate such message:

Alternative 1: MN performs the association between the execution condition received from the source SN and the RRC configuration of the candidate PSCell received from the candidate SN.

Alternative 2: MN forwards the execution condition received from the source SN to the candidate SN. The candidate SN sends the execution condition and the RRC configuration of the candidate PSCell to the MN.

Note that there was a working assumption in last meeting “target SN to provide the prepared PSCell id (or PSCell ids, if decided to be allowed) to the MN for CPA, MN initiated inter-SN CPC, and SN initiated inter-SN CPC. In alternative 1 above, the target SN needs to provide the prepared PSCell id(s) to the MN, it is not needed in alternative 2.

Question 14: which alternative do you prefer for the MN handling?

| Company | Comment |
| --- | --- |
| Huawei | Prefer alt 2. In SN initiated inter-SN CPC, the MN does not need to know the association of the candidate PSCell and SN RRC configuration, and the MN does not need to store the execution condition received from the SN. Alternative 1 unnecessarily increases the complexity and handling load of the MN. |
| Nokia | Isn’t it RAN2’s topic? |
| ZTE | Prefer alt 1. Because for the alt 2, the execution condition will be forwarded from S-SN to MN then from MN to T-SN, then T-SN to UE. But, it may be RAN2’s issue. |
| LGE | Since “MN generates the conditional reconfiguration message including the execution condition(s) provided by the source SN and RRCReconfiguration provided by the candidate PSCell(s)”, MN should know the association anyway, right? |
| Ericsson | Both are feasible from RAN3 point of view, so it is up to RAN2 to decide |
| Google | Up to RAN2 decision |
| InterDigital | Agree with Ericsson |
| China Telecom | No strong view, it is up to RAN2. |
| Lenovo, Motorola Mobility | Prefer Alt 1. In our understanding, the target SN does not need to understand the execution condition generated by the source SN. |
| Intel | Prefer Alternative 1. But agree with Nokia. This is RAN2 topic. |
| Samsung | Prefer Alt 1. This is also related with our answer of Q2. |
| NEC | Not fully understand the question, hasn’t RAN2 agreed “The MN generates the conditional reconfiguration message including the execution condition(s) provided by the source SN”? |
| Qualcomm | Prefer Alt 1, up to RAN2 to make final decision. |
| CATT | Prefer alt 1. But it is upon RAN2 |

Moderator’s summary: one company prefer Alt 2, some companies prefer Alt 1, some companies thinks that both are feasible, and lots of companies thinks that it is up to RAN2.

Moderator’s proposal: inform the two alternatives to RAN2 ask for feedback.

## Support of Early Data forwarding

In R16 CHO, the early data forwarding is supported in order to reduce the latency of data forwarding. When the UE access the candidate cell, the network can send the early forwarded data to the UE. The source node forwards the PDCP SDU with SNs assigned by the source gNB to the candidate node. The source gNB sends the EARLY STATUS TRANSFER message to maintain HFN continuity by indicating PDCP SN and HFN of the first PDCP SDU that the source gNB forwards to the target gNB. The subsequent messages may be sent for discarding of already forwarded downlink PDCP SDUs in the target gNB.

In R15&R16, there are MN/SN terminated MCG/SCG/Split bearers in MR-DC. For MR-DC, user data forwarding may be performed between nodes whenever the logical node hosting the PDCP entity changes. The behavior of the node from which data is forwarded is the same as specified for the "source node" for handover, the behavior of the node to which data is forwarded is the same as specified for the "target node" for handover.

There was an working assumption to support Early Data Forwarding in CPAC, considering that early data forwarding can help to provide data to UE earlier and then improve the UE experience, do you agree to turn it to agreement to support Early Data Forwarding in CPAC?

WA: Support Early Data Forwarding in CPAC.

Question 15: Do you agree to Support Early Data Forwarding in CPAC?

| Company | Comment |
| --- | --- |
| Huawei | Support |
| Nokia | In case of CPC, early data forwarding may be done very much “on time”, i.e. when the UE finds the cell to access (see our paper). This should be supported. |
| ZTE | Can decide latter, so far, we are neutral. |
| LGE | Yes |
| Ericsson | Not sure that the full impact and complexity for all the cases (especially CPC involving multiple target SNs) have been identified. Prefer to keep this as a WA for now. Nokia’s proposal can be discussed as a legacy/late data forwarding optimization |
| Google | Neutral |
| InterDigital | Support |
| China Telecom | Yes |
| Lenovo, Motorola Mobility | Agree |
| Intel | Of course. |
| Samsung | Yes. |
| NEC | Agree with Nokia. |
| Qualcomm | Yes |
| CATT | Yes |

Moderator’s summary: majority companies support Early Data Forwarding in CPAC, as it is a WA in last meeting, let’s try if it could become to an agreement.

Moderator’s proposal: Support Early data forwarding in CPAC.

### Early data forwarding in MN initiated inter-SN CPC

In the MN initiated CPC, the CPC is trigged by the MN, the source SN needs to know the CPC triggering in order to send the early status transfer to the target SN.

There was a working assumption as below:

WA: in case of MN initiated inter-SN CPC, to support early data forwarding, the MN needs to inform source SN about CPC triggered (i.e. the successful reconfiguration of CPC at UE), details FFS.

Question 16: Do you agree to turn this working assumption into agreement? i.e. in case of MN initiated inter-SN CPC, to support early data forwarding, the MN needs to inform source SN about CPC triggered (i.e. the successful reconfiguration of CPC at UE)

| Company | Comment |
| --- | --- |
| Huawei | Agree |
| Nokia | In case of CPC, early data forwarding may be done very much “on time”, i.e. when the UE finds the cell to access. This should be supported. |
| ZTE | Can decide latter, so far, we are neutral. |
| LGE | Yes |
| Ericsson | To be discussed later |
| Google | Neutral |
| InterDigital | Agree but ok to discuss later |
| China Telecom | Prefer to discuss it later. |
| Lenovo, Motorola Mobility | Agree |
| Intel | The successful CPC reconfiguration to the UE will be informed to the source SN by the SN RECONFIG COMPLETE procedure from the MN. But if following Rel-16 CHO design, when the target SN triggers early data forwarding, the target SN will send Early Status Transfer message to the MN, which should be forwarded to the source SN. There seems no reason to additionally indicate the source SN that early data forwarding is performed by the target SN. |
| Samsung | Ok to discuss later. |
| NEC | Agree with Nokia. |
| Qualcomm | Agree |
| CATT | Agree |

Moderator’s summary: majority companies agree, some companies would like to discuss later. As it was an WA in last meeting, so nothing change for this meeting.

Moderator’s proposal: noted.

Question 17: If your answer to the question above is yes, which message should be used for the MN to inform source SN about CPC triggered?

| Company | Comment |
| --- | --- |
| Huawei | Reuse the SN Reconfiguration Complete procedure to inform source SN about CPC triggered. The MN can inform the source SN after the UE has received the CPC configuration (e.g. the UE sends the MN RRC reconfiguration complete message after receiving the CPC configuration). |
| Nokia | Prefer FFS for the time being. |
| ZTE | Can decide latter, so far, we are neutral. |
| LGE | SN Reconfiguration Complete procedure can be used. |
| China Telecom | Prefer to discuss it later. |
| Lenovo, Motorola Mobility | Agree with Huawei |
| Intel | Please see above comment. |
| Samsung | Prefer to discuss later. |
| NEC | FFS |
| Qualcomm | Can decide later. |
| CATT | Prefer to discuss it later. |

Moderator’s summary: nothing changed, still FFS

Moderator’s proposal: noted

### Early data forwarding in SN initiated inter-SN CPC

For option 2, prepare multiple PSCells in one CPAC procedure, in case of SN initiated inter-SN CPC, if it is decided to prepare multiple PSCells in multiple target SNs by one SN Change procedure in the discussion of section 3.1, to support early data forwarding, multiple data forwarding addresses should be added in the SN Change Confirm message.

Question 18: in case it is allow to prepare multiple PSCells in multiple target SNs by one SN Change procedure, do you agree to add multiple data forwarding address in the SN Change Confirm message, to support early data forwarding in case of SN initiated inter-SN CPC?

| Company | Comment |
| --- | --- |
| Huawei | Agree |
| Nokia | This may not be needed – forwarding would start only when the UE finds the target cell (“on time” forwarding). |
| ZTE | Can decide latter, so far, we are neutral. |
| LGE | Agree |
| Ericsson | That might be needed, but should first discuss if early data forwarding to multiple targets is to be supported |
| Google | Agree with Ericsson |
| InterDigital | Agree but should probably wait to confirm |
| China Telecom | Prefer to discuss it later. |
| Lenovo, Motorola Mobility | Agree |
| Intel | Even if MN triggers CPA toward the locked-on single target SN based on the node ID provided from the source SN via the SN CHG REQD message, there could be the case that multiple forwarding addresses are needed from that target SN (e.g. if CP-UP is separated and multiple CU-UP entities are involved in the target SN). So, Yes, agree but we prefer to allow MN to reply multiple SN CHG CNFM messages (rather than sticking to a single SN CHG CNFM message and enhancing it to include multiple forwarding addresses). We should be thinking out of the box! |
| Samsung | Agree with E///. |
| NEC | in case it is allow to prepare multiple PSCells in multiple target SNs by one SN Change procedure, agree |
| Qualcomm | Can be discussed later |
| CATT | Prefer to discuss it later. |

Moderator’s summary: based on the summary of Question 6, no need to further work on this aspect.

Moderator’s proposal: noted.

## Support of Late Data forwarding

As discussed in last meeting, in order to enable timely late data forwarding, the source SN must know when the UE arrives to the target SN. This can either be done based on the information from the target SN (as in case of CHO), or based on information that the UE could send to the MN, which would then forward it to the source SN (e.g. in the Release Request).

There was a working assumption achieved in last meeting, it is needed to further check if it is agreeable to turn it to agreement.

WA: in case of both MN and SN initiated inter-SN CPC, to support late data forwarding, it is needed to inform the source SN about the successful CPC execution and UE accesses to the target SN, details FFS. RAN3 waits for RAN2 progress before discussing further details.

Question 19: do you agree that in case of both MN and SN initiated inter-SN CPC, to support late data forwarding, it is needed to inform the source SN about the successful CPC execution and UE accesses to the target SN?

| Company | Comment |
| --- | --- |
| Huawei | Yes |
| Nokia | If “on time” forwarding is supported, late forwarding will not be needed. |
| ZTE | Can decide latter, so far, we are neutral. |
| LGE | Yes |
| Ericsson | I guess we now need to decide between a Bye/Success message received from the UE or from the target SN the UE successfully attaches |
| Google | Yes |
| China Telecom | Yes. |
| Lenovo, Motorola Mobility | Agree |
| Intel | Yes, following Rel-16 CHO design. |
| Samsung | Yes. |
| NEC | Yes |
| Qualcomm | Yes |
| CATT | Yes |

Question 20: If your answer to the question above is yes, how to inform the source SN about the successful CPC execution and UE accesses to the target SN

| Company | Comment |
| --- | --- |
| Huawei | Wait for RAN2 progress. |
| Nokia | Prefer FFS for the time being. |
| ZTE | Can decide latter, so far, we are neutral. |
| LGE | Pending to RAN2, prefer to align with CHO. |
| Google | Pending to RAN2 |
| China Telecom | Up to RAN2 progress, prefer to discuss it later. |
| Lenovo, Motorola Mobility | Wait for RAN2 progress |
| Intel | Easy. We can define another class-2 message (e.g. “PSCell Change Success”) similar to the HO SUCCESS message we specified for Rel-16 CHO. |
| Samsung | Agree with Intel. But there is an issue whether to use RRC message to inform of successful execution. Therefore, wait RAN2’s decision. |
| NEC | Wait for RAN2 progress |
| Qualcomm | Agree with Intel. But, we can wait for RAN2 progress. |
| CATT | Wait for RAN2 progress |

Moderator’s summary: majority companies agree with the first part of the previous WA, and the later part is pending to RAN2.

Moderator’s proposal: turn the WA to agreement: WA: in case of both MN and SN initiated inter-SN CPC, to support late data forwarding, it is needed to inform the source SN about the successful CPC execution and UE accesses to the target SN, details FFS. RAN3 waits for RAN2 progress before discussing further details.

## Other Issues

If there are other issues needs to be discussed, please add in below:

### Issue x [if needed]

Description…

| Company | Comment |
| --- | --- |

# Second Round discussion

// to be updated after First Round discussion

## LS reply to RAN2?

RAN2 question in the received LS “Rel-17 CPAC is expected to support the preparation and configuration of multiple PSCell candidate cells. RAN3 is therefore asked to check whether the legacy XnAP/ X2AP signalling is sufficient or whether it shall be extended in Rel-17.”

## IEs to be included in the messages

e.g. CPAC indicator.

# References

- R3-210045 LS on Conditional PSCell Addition/Change agreements (RAN WG2)

- R3-210082 Discussion on further details of the inter-SN CPC (Nokia, Nokia Shanghai Bell)

- R3-210083 Enabling inter-SN conditional PSCell change (Nokia, Nokia Shanghai Bell)

- R3-210084 Enabling inter-SN conditional PSCell change (Nokia, Nokia Shanghai Bell)

- R3-210106 Discussion on Conditional PScell Addition/Change procedures (China Telecommunication)

- R3-210107 CR on 36.423 for introducing CPAC information in SgNB Addition procedure (China Telecommunication)

- R3-210108 CR on 38.423 for introducing CPAC information in SN Addition procedure (China Telecommunication)

- R3-210183 Discussion on CPA and CPC (ZTE)

- R3-210184 CR 36.423 for support of CPA and CPC (ZTE)

- R3-210185 CR 38.423 for support of CPA and CPC (ZTE)

- R3-210186 [draft] Reply LS on Conditional PSCell Addition/Change (ZTE)

- R3-210240 discussion on Conditional PSCell Addition and PSCell Change (NEC)

- R3-210353 CPA and MN initiated Inter-SN CPC procedures: preparation, execution, and data forwarding (Qualcomm Incorporated)

- R3-210354 SN initiated Inter-SN CPC procedure: preparation, execution, and data forwarding (Qualcomm Incorporated)

- R3-210502 (TP to TS 38.401) Consideration on conditional PSCell change/addition (Huawei)

- R3-210503 Support of conditional PSCell change/addition (Huawei)

- R3-210504 Support of conditional PSCell change/addition (Huawei)

- R3-210535 Open issues on conditional PScell Change/Addition (LG Electronics)

- R3-210542 TP for modification and release to prepared CPAC (Google Inc.)

- R3-210600 Left issues on CPAC (Lenovo, Motorola Mobility)

- R3-210601 [DRAFT] Reply LS on Conditional PSCell Addition/Change agreements (Lenovo, Motorola Mobility)

- R3-210744 Support of conditional PSCell change/addition (Ericsson)

- R3-210745 Conditional SN Addition (Ericsson)

- R3-210746 Conditional SN Addition (Ericsson)

- R3-210768 Some Considerations on How to Support CPAC (CATT)

- R3-210769 Introduction of support CPAC (CATT)

- R3-210857 Discussion on handling multiple PSCell candidates for CPAC (Samsung)

- R3-210862 Correction on the preparation of multiple PSCells in one CPAC procedure (Samsung)

- R3-210877 Correction on the preparation of one PSCell in one CPAC procedure (Samsung)

- R3-210945 Regarding inter MN-SN signaling design for CPAC (Intel Corporation)

# Agreements, working assumptions, open issues

## RAN3#110

In the RAN3#110 meeting, RAN3 has discussed the CPAC and has the following agreements and open issues.

RAN3 discuss CPAC in (NG) EN-DC and NR-DC.

Start to Focus on CPA, MN initiated inter-SN CPC, and SN initiated inter-SN CPC, if time allows, other cases can be discussed pending to RAN2 progress

Start CPAC discussion based on the conventional DC procedures:

CPA: SN addition procedure for CPA

MN initiated inter SN CPC: MN initiated SN Change procedure, i.e. CPA + SN release

SN initiated inter SN CPC: SN initiated SN Change procedure

FFS on direct inter-SN communication

Target SN to make the decision on the prepared PSCell or PSCells (if decided to be allowed).

WA: target SN to provide the prepared PSCell id (or PSCell ids, if decided to be allowed) to the MN for CPA, MN initiated inter-SN CPC, and SN initiated inter-SN CPC

WA: Support Early Data Forwarding in CPAC.

WA: in case of MN initiated inter-SN CPC, to support early data forwarding, the MN needs to inform source SN about CPC triggered (i.e. the successful reconfiguration of CPC at UE), details FFS.

Support Late Data Forwarding in CPAC.

WA: in case of both MN and SN initiated inter-SN CPC, to support late data forwarding, it is needed to inform the source SN about the successful CPC execution and UE accesses to the target SN, details FFS. RAN3 waits for RAN2 progress before discussing further details.

Open issues:

FFS on how to support CPAC replace, (SN modification procedures or SN Addition or others).

FFS on how to support multiple candidate PSCell preparation in CPAC:

Option 1: prepare one PSCell in one CPAC procedure, use parallel CPAC procedures to prepare multiple PSCells.

Need to introduce an indicator to distinguish the triggering of different PSCell preparation for the same UE”.

Option 2: prepare multiple PSCells in one CPAC procedure

FFS if multiple SN can be prepared in one SN initiated CPC procedure (SN Change Required).

FFS on how to handle the received CPC execution condition by the MN in case of SN initiated inter-SN CPC, pending to RAN2 progress.

It is pending to RAN2 on if it is needed for the Target SN to send CPAC success to the MN, and if it is needed, FFS on reusing HO Success or introduce a new class2 procedure.

FFS on F1AP and E1AP impacts.

FFS if conditional SN change can be prepared directly between the involved SNs (depends on availability of SRB3).