3GPP TSG-RAN WG3 #111-e	R3-211137

Online, 25 Jan – 04 Feb, 2021

Agenda Item:	21.3

Source:	Samsung (moderator)

Title:	CB: # NRIIOT3-New_QoS_Parameters - Summary of email discussion

Document for:	Discussion

# Introduction

CB: # NRIIOT3-New_QoS_Parameters

- Introduce Survival Time as an optional IE within the TSC Assistance Information IE or wait for the progress on the Survival Time from SA2 and RAN2? Check LS in R3-210028

- For other TSCAI QoS parameters, waiting for SA2 and RAN2 decision?

- Some new QoS related parameters are required to be included in Assistance Information in order to reflect correctly the status of HARQ transmission in the corresponding node, e.g., Average HARQ Failure Rate and Average HARQ Retransmission Rate? Clarify the definitions of The UL Radio Quality Index and The DL Radio Quality Index? Enhance the Assistance Information reporting mechanism?

- Capture agreements and open issues in the summary

(SS - moderator)

Summary of offline disc R3-211022

# For the Chairman’s Notes

Propose the following:

Proposal: The survival time is part of the TSCAI parameter

Discuss the open issue at next RAN3 meeting after further progress in RAN2/SA2 prior to RAN3#111

- details of Survival Time e.g.  minimum and maximum value of Survival Time.

- whether to include Survival Time for uplink

- the exact encoding, whether aperiodic type is allowed.

Discuss BLCRs at next RAN3 meeting.

# Discussion – Phase II

Agreements achieved after the first round of discussion:

Introduce Survival Time into RAN3 specifications in principle. FFS on the details e.g.  minimum and maximum value of Survival Time.

Introduce Survival Time at NG/Xn/E1/F1 interface.

Survival Time is included for downlink.  It’s still FFS whether to include Survival Time for uplink

Survival Time can be expressed with the time. FFS on e.g., the exact encoding, whether aperiodic type is allowed.

Wait for RAN2/SA2 on new TSCAI parameters.

For the second round, the moderator would like to have some discussion on the open issues and the possibility of BLCRs.

The open issues:

FFS on the details e.g. minimum and maximum value of Survival Time.

It’s still FFS whether to include Survival Time for uplink

FFS on e.g., the exact encoding of Survival Time, whether aperiodic type is allowed.

Q1: Besides the open issues above, any other issue which needs to be discussed at next meeting

| Company | Comment |
| --- | --- |
| Nokia | The agreements from the first round of discussion unfortunately do not mention that Survival Time is part of TSCAI. However, I believe this is very clear from SA2, and perhaps we did not capture it during the online discussion due to the very limited time we had. From SA2 TR: “Survival Time is transferred as part of the TSCAI parameter but the TSCAI may not always comprise of Survival time”. It would be nice if we could add this agreement during the second round as an additional “low hanging fruit”. |
| ZTE | Agree with Nokia. In addition, it is necessary to discuss the problem of extended periodicity values mentioned by Q7 in Phase I. It may be difficult to reach an agreement at this meeting, but we can set the issue to FFS. |
| Ericsson | It is also my understanding that survival time is transferred in the TSCAI parameter, as optional IE. If in April the other groups e.g. RAN2 could solve the FFS, for the next meeting it would be more clear for us. |
| Samsung | We also have the same understanding that the Survival Time is transferred as part of the TSCAI as optional IE. Other details for the Survival Time would be discussed in the next meeting after further discussion in RAN2/SA2. |

Moderator summary:

Seems the following is agreeable

Proposal: The survival time is part of the TSCAI parameter

Discuss those open issue at next RAN3 meeting after further progress in RAN2/SA2 prior to RAN3#111

Q2: Among those open issues, which needs to be discussed at RAN3 and which should wait for the conclusion in other WGs

| Company | Comment |
| --- | --- |
| Nokia | In our understanding, all of the listed open issues could potentially be progressed by RAN3 at the next meeting, either by RAN3 decisions, or after further careful checking of e.g. TR 23.700-20, or further progress in RAN2/SA2 prior to RAN3#111. In some cases, an FFS seems to directly conflict with existing SA2 agreements (e.g. “FFS whether aperiodic type is allowed”, while SA2 has agreed that Survival Time is part of TSCAI which by definition is periodic). Here, I would like to suggest that RAN3 base its discussion/decisions on latest RAN2/SA2 agreements (with appropriately placed TBD/FFS), and avoid speculating on future RAN2/SA2 decisions – we can always revise our BL CRs if RAN2/SA2 changes their decisions, but in the meantime we should try to make progress. |
| CATT | The first item can be handled and decided by RAN3 The second one, need wait to Ran2 decision The third one: the exact encoding of Survival Time can be decided by RAN3. whether aperiodic type is allowed, need check SA2 TR |
| ZTE | In our view, mainly the second FFS (whether to include Survival Time for uplink) needs to wait further for RAN2's conclusion. For the first FFS, RAN3 can get a corresponding range of values by using a general Survival Time unit (e.g. time value) and the description of periodic cases in TS 22.104, and this range can also include aperiodic cases. We can not only avoid the discussion of whether to allow aperiodic, but also avoid subsequent modifications and enhancements. For the third FFS, since the use case of Survival Time in aperiodic services is already included in TS 22.104, and SA2 is also discussing the content of aperiodic type. Thus, we think that considering the aperiodic type of Survival Time is a general approach. |
| Ericsson | AS in Q1. |
| Huawei | Well, these issues anyway would be contribution driven to discuss. We feel like the details e.g. the minimum/maximum value can be RAN3 task. The rest may be related to other groups, but nothing prevents from contributing and discussing in RAN3. |
| Samsung | We think these open issues would be discussed in the next meeting after further discussion in RAN2/SA2. |

Moderator summary:

Discuss those open issue at next RAN3 meeting after further progress in RAN2/SA2 prior to RAN3#111

Q3: Do you prefer to prepare BLCRs for NG/Xn/E1/F1/Stage2 with FFS in this meeting?

| Company | Comment |
| --- | --- |
| Nokia | No strong view, but it could be a clear/clean way to capture the open issues. If we do agree to have a BL CR, my suggestion would be to have only NGAP at this meeting, and then generate Xn/E1/F1/Stage2 during a future RAN3 meeting once the NGAP BL CR is more stable (to avoid tedious mirroring exercises among BL CRs during the early stages of discussion). |
| CATT | I suggest have the BLCR in the future meeting. We just have quite simple change. To avoid spending effort to maintain the CR in each meeting, we can have the BLCR later. Also like Nokia said, even we want to create BLCR in this meeting, we can only create the NGAP . |
| ZTE | We prefer to prepare BLCRs in this meeting, in order to push the progress. |
| Ericsson | If we agree that the Survival time is in TSCAI, I think it is enough progress for this meeting. No need for BL CRS at this meeting. The details are most FFS at this stage. It is very easy to do the CRs at the next meeting. We can coordinate before the next meeting, when we know the agreement from the RAN1/2 next meeting. E.g. Ericsson can be responsible of the XnAP CR and ensure the latest agreements are included, the uncertain part are marked with FFS. |
| Huawei | Given the very limited agreement, it is better to have BL CRs at next meeting. |

Moderator summary:

Discuss BLCRs at next RAN3 meeting.

# Discussion – Phase I

## Introduce Survival Time into RAN3 specifications

SA2 requests RAN2 & RAN3 to consider to include Survival Time in TSCAI from SMF to NG-RAN.

Some companies agree to introduce Survival Time into RAN3 specifications: [2], [3], [5], [6] and [8]

A company would like to wait for the progress on the Survival Time from SA2 and RAN2: [7]

Q1: Do you agree to introduce Survival Time into RAN3 specifications?

| Company | Comment |
| --- | --- |
| Nokia | YES. Survival Time has been agreed by SA2 in their study item conclusions captured in clause 8.4 of TS 23.700-20. Also, RAN2 acknowledged in a Reply LS to SA2 (R3-210028) that they will take into account the SA2 conclusion. |
| Huawei | Agree, as specified in the conclusion part of the TR 23.700-20. |
| CATT | Agree |
| Samsung | Agree |
| Ericsson | We should wait for RAN2 to resolve all the FFSs on this topic and the agreement is reached. |
| CMCC | Agree, this parameter has been agreed by SA2 and RAN2 |
| China Unicom | Agree |
| Qualcomm | Agree in principle (subject to further discussion/details bla bla – essentially pending on other groups) |
| Apple | Agree |
| ZTE | Agree |

Proposal 1: Introduce Survival Time into RAN3 specifications in principle. FFS on the details.

If it’s agreed to introduce Survival Time, the next questions is which interfaces should Survival Time be added at?

[2], [3], [6] and [8] propose to add Survival Time at Ng/Xn/E1/F1 interfaces.

Q2: Do you agree to introduce Survival Time at Ng/Xn/E1/F1 interfaces?

| Company | Comment |
| --- | --- |
| Nokia | YES. Since SA2 has concluded that Survival Time is transferred as part of TSCAI, it should be introduced on all interfaces that include TSCAI. |
| Huawei | Agree. |
| CATT | Agree |
| Samsung | YES. The Survival Time should be part of TSCAI. |
| Ericsson | If to introduce, it is in TSCAI |
| CMCC | Yes, part of TSCAI |
| China Unicom | Agree |
| Qualcomm | Agree and in principle as part of the TSCAI as mentioned already |
| Apple | Agree |
| ZTE | Agree |

Proposal 2: Introduce Survival Time at Ng/Xn/E1/F1 interface.

In addition, [2], [5] and [8] indicate Survival Time can be included for downlink and uplink.

[3] indicates Survival Time is just for downlink, and it’s still FFS about whether to include Survival Time for uplink.

There is no discussion for the issue from other companies.

Therefore it is common understanding that Survival Time is included for downlink once the question to Q1 is confirmed.

Q3: Do you agree to introduce Survival Time for uplink?

| Company | Comment |
| --- | --- |
| Nokia | YES. SA2 has already concluded to introduce Survival Time for both downlink and uplink. Additional parameters may also be added, but such parameters (if any) would be on top of (not instead of) Survival Time. |
| Huawei | Agree. Survival Time can be included for downlink and uplink independently. |
| CATT | Yes |
| Samsung | YES. In our understanding, SA2 has already introduced Survival Time for both downlink and uplink. |
| Ericsson | The same as in Q1. |
| CMCC | Yes |
| China Unicom | Agree to introduce Survival Time for both downlink and uplink. |
| Qualcomm | As in Q1 yes in principle but pending other groups for confirmation – there is no rush |
| Apple | Agree |
| ZTE | This question is set to FFS at this stage. In the uplink transmission, the survival time as a new application layer parameter, how to use the survival time on the RAN side has not been concluded. In other words, in the uplink transmission, there are two choices for the transmission of survival time: (i) transmission to gNB, (ii) transmission to UE. Thus, we think it is necessary for RAN2 to further discuss the above two options. |

Proposal 3: Survival Time is included for downlink.  It’s still FFS about whether to include Survival Time   for uplink

## The details of the IE Survival Time

If it’s agreed to introduce Survival Time, some detail issues should be discussed.

For the unit of Survival Time, [2], [3] and [5] propose it should be expressed in units of the data burst periodicity.

Q4: Do you agree the unit of Survival Time should be expressed in units of the data burst periodicity? If not, what’s the proposal?

| Company | Comment |
| --- | --- |
| Nokia | YES. SA2 conclusion states that Survival Time is specified in unit of “time” based on TSCAI periodicity parameter. |
| Huawei | Agree. |
| CATT | Yes |
| Samsung | We think the Survival Time can be expressed with the time value or the times of the TSCAI periodicity parameter, and either way can be workable. Samsung prefers using the time value to express the Survival Time. |
| Ericsson | In units of “time”. |
| CMCC | Expressed in time value or times of TSCAI periodicity, we should also consider the agreement in SA2 that Survival time is also applied to aperiodic traffic. |
| Apple | Yes |
| ZTE | No. Based on SA2, the unit of the parameter survival time is defined as time. For the value range of survival time, we think it can be analyzed from aperiodic/periodic deterministic communication. Although the survival time in the periodic deterministic communication is related to the TSCAI periodicity (e.g. the unit of “time” based on TSCAI periodicity parameter), the survival time is also applicable to the aperiodic deterministic communication.Based on the performance requirements of aperiodic deterministic communication in Table 5.3-1 of TS 22.104, it can be seen that one scenario provides the value of survival time of 16ms. Thus, we think that the unit of survival time should be expressed as time value. |

Proposal 4: Survival Time can be expressed with the time value or the times of the TSCAI periodicity parameter. FFS on which one to be used.

For the minimum value of Survival Time, [2] proposes it should be 1 while [3] and [5] propose it should be 0.

Q5: For the minimum value of Survival Time, 0 or 1 or any other value?

| Company | Comment |
| --- | --- |
| Nokia | Minimum value should be ‘1’. It is not clear to us what the semantics of value ‘0’ is. |
| Huawei | The survival time indicates as the maximum number of consecutive message transmission failures (i.e. whose loss can be tolerated). Value “0” indicates that no transmission failure is allowed. Another alternative is to set as FFS at this stage. |
| CATT | Agree with HW, set as FFS now |
| Samsung | We think it depends on which expression is used for the Survival Time. If the time value is used, we think ‘0’ could be the minimum value. |
| Ericsson | The same as in Q1. |
| CMCC | Depends on what the value “0” means. We agree this stage 3 details could be FFS |
| Qualcomm | Set as FFS but this needs care. In any case the whole IE (if we move that far) should be FFS pending etc |
| Apple | TS 22.104 has a few exceptional cases with services where survival time can be zero. There is also some further explanation in TR 22.832. When Survival time is ‘0’ a single message loss leads to application downtime. We prefer the minimum to be ‘0’ but this could be FFS at this stage. |
| ZTE | Minimum value should be ‘0’. Based on the fact that the survival time value is greater than or equal to three times the periodicity of TSC QoS flow, we can find that the range of periodicity (0..640000,...) us in TSCAI. Therefore, the minmum value of survival time should be set to ‘0’. |

Moderator’s summary:

FFS on the minimum value of Survival Time.

For the maximum value of Survival Time, [3] proposes it should be at least 180s, [5] propose 256 unit based on their TP, and [2] proposes it should be FFS.

Q6: For the maximum value of Survival Time, any view on this issue?

| Company | Comment |
| --- | --- |
| Nokia | In the performance requirements in clause 5.2 of TS 22.104, the maximum value in any of the use cases is 3 (i.e. 3 times the transfer interval, which can be considered as equivalent to data burst periodicity). Thus, a max value in the range 3 to 6 seems reasonable. |
| Huawei | Could be set as FFS at this stage. |
| CATT | Set as FFS |
| Samsung | The maximum value of the Survival Time needs to be 3 or more times of the maximum value of the Periodicity. |
| Ericsson | The same as in Q1. |
| CMCC | Stage 3 details, FFS |
| Qualcomm | Obvious FFS, if we get to the point of a baseline, the IE coding can be FFS anyway |
| Apple | Like minimum value, FFS for now. |
| ZTE | In some scenarios, the survival time value is greater than or equal to three times the transmission interval. Further, the target value for the maximum transmission interval (100 ms to 60s) in Table 5.2-1 of TS 22.104 is the plant asset management scenario. In other words, combined with the relationship that the survival time value is three times of the transmission interval, the maximum value of survival time is at least 180s. |

Moderator’s summary:

FFS on the maximum value of Survival Time.

In addition, [3] proposes that the maximum value of periodicity should be extended to 60000000 us.

Q7: Any view on this issue?

| Company | Comment |
| --- | --- |
| Nokia | This is unrelated to Survival Time and should perhaps be taken separately. But as an initial reaction, if periodicities much larger than 640ms need to be supported (e.g. up to 60 seconds), then it may be preferable to use different granularity (e.g. unit of seconds rather than microseconds). |
| Huawei | Too early to discuss the exact values. And the exact periodicity value can be set based on the SA1 requirement. |
| CATT | Discuss it later |
| Samsung | This is not directly related with the Survival Time. But extending the maximum value of the Periodicity needs to be discussed. |
| Ericsson | When the other groups reached agreement, the impact on the RAN3 spec can be settled. |
| ZTE | Based on the fact that the periodicity of TSC QoS flow is equal to the above transmission interval, we can find that the range of periodicity (0..640000,...) us in TSCAI can not meet the requirements of the maximum transmission interval in table 5.2-1 of TS 22.104. Therefore, it is necessary to extend the maximum periodicity of TSCAI to 60s, or another alternative is to set as FFS at this stage. |

Moderator’s summary:

No common understanding on the extension.

## Other new TSCAI parameters

Some new TSCAI parameters are discussed in the contributions:

- the communication service availability target: [3]

- additional QoS parameters reflecting level of service reliability: [5]

- Burst Spread: [3] and [6]

For a), b) and c), it’s proposed to wait for the conclusion from RAN2 and SA2.

Q8: Any view on this issue?

| Company | Comment |
| --- | --- |
| Nokia | New TSCAI parameters require decision by RAN2/SA2, so we should wait for their conclusions. |
| Huawei | For a), b), c), Ok to wait. |
| CATT | We need wait RAN2/SA2 conclusion |
| Ericsson | Wait for agreement in RAN2/SA2 |
| CMCC | Wait for RAN2 and SA2 |
| Qualcomm | As above, no reason to take any of these forward for now |
| Apple | Agree to wait for the conclusion on RAN2 and SA2. |
| ZTE | Agree with Nokia. |

Proposal 5: Wait for RAN2/SA2 on new TSCAI parameters.

## NR-U enhancement based on QoS related parameters

[4] discusses the necessary RAN enhancements. In legacy Assistance Information defined in TS 38.425, some parameters cannot reflect the status of HARQ transmission for a path, e.g. Average HARQ Failure and Average HARQ Retransmission. It could cause the receiver of assistance information make wrong decisions which may degrade network performance. In addition, the receiver of assistance information could not control Assistance Information reporting in efficient way and could not utilize the Assistance Information when necessary.

So [4] proposes to add the following parameters in Assistance Information:

Average HARQ Failure Rate and Average HARQ Retransmission Rate.

Q9: Do you agree the proposal?

| Company | Comment |
| --- | --- |
| Nokia | [4] does not seem related to any of the Rel-17 WID objectives, e.g. “new QoS related parameters… decided in SA2”, but rather assistance information (not TSCAI) in PDCP duplication? |
| Huawei | Seems not in the IIoT WI scope? Even the NR-U is already supported in R16. Then if not in the IioT WI scope, it is better to treat it as correction. |
| CATT | Agree with Nok and HW |
| Samsung | We think it’s beneficial to consider the enhancement from two directions. One is RAN enhancement based on new parameters decided by SA2. The other is to consider RAN enhancement for improvement of features for IIOT/URLLC. In order to let the hosting node to know the transmission status in the assisting node, some assisted information including Average HARQ Failure and Average HARQ Retransmission are provided to the hosting node. The hosting node control its data transmission based on those assisted information. The number of total HARQ transmission is variable and not a fixable value. In the following two cases, the hosting node will get the same information with Average HARQ Failure and Average HARQ Retransmission. The actual situation is quite different. But the hosting node cannot have differentiated handling for the two cases. there are 5 failures in total 10 transmissions during a time unit there are 5 failures in total 100 transmissions during same time unit In order to improve this, it is very helpful if the hosting node can get the Average HARQ failure/retransmission rate (the rate of the number of HARQ failure/retransmission to the number of total HARQ transmission.). Then the hosting node can better control its data transmission to the assisting node. |
| Ericsson | Similar view to CATT/HW/Nokia |
| CMCC | Same view as CATT/HW/Nokia |
| China Unicom | Same view as CATT/HW/Nokia/ Ericsson/CMCC |
| Qualcomm | Same view as CUC, proposals may be valid to discuss but seem more like TEI |
| Apple | Same view as CATT/HW/Nokia/Ericsson/CMCC/CU/Qualcomm |
| ZTE | Agree with Nokia and Huawei. |

Moderator’s summary:

No agreement on the proposal.

[4] proposes to consider to enhance the Assistance Information reporting mechanism e.g. periodic reporting.

Q10: Any view on this proposal?

| Company | Comment |
| --- | --- |
| Huawei | See our answer to Q9. |
| Samsung | The assistance information reporting depends on the Assistance Info. Report Polling Flag in DL USER DATA or depending on the assisting node implementation. The inefficiency of such reporting mechanism: If hosting node need multiple reporting in a long term, it has to send DL USER DATA with the flag one by one, and even an empty DL USER DATA if no data at that time. This introduces redundant transmission and wastes resources between hosting node and assisting node. The average window for some parameters in assistance information, e.g. average HARQ failure/retransmission, depends on the local configuration in assisting node. The hosting node may not get the expected granularity for different service type e.g. URLLC may need small granularity of the window in order to quick adjust the data transmission for URLLC service. It’s not mandatory to include the data of all Assistance Information Type in the report. It means that the node hosting the PDCP entity may not get the expected information from the corresponding node. In order to let the hosting node get the assisted information which are really helpful for efficient data transmission, we think it’s desirable to enhance assistance information reporting mechanism, e.g. with periodical reporting, or with the window, or with the required assistance information type in the polling message. |
| Ericsson | As in Q9 |
| CMCC | Same view as Q9 |
| China Unicom | Same view as Q9 |

Moderator’s summary:

No agreement on the proposal.

# Conclusion, Recommendations [if needed]

If needed

# References

R3-210028,	Reply LS on Use of Survival Time for Deterministic Applications in 5GS (RAN WG2)

R3-210094,	RAN3 impacts of Survival Time (Nokia, Nokia Shanghai Bell)

R3-210203,	Analysis of New QoS Related parameters (ZTE)

R3-210289,	NR-U enhancement based on QoS related parameters (Samsung)

R3-210483,	Introduction of the survival Time (Huawei)

R3-210779,	Discussion on new QoS related parameters (CATT)

R3-210876,	Discussion on Further enhanced NR-IIoT: QoS parameters related (Ericsson)

R3-210919,	Enhancements to support new QoS related parameters (CMCC)