3GPP TSG-RAN WG3 #111-e	R3-211022

Online, 25 Jan – 04 Feb, 2021

Agenda Item:	21.3

Source:	Samsung (moderator)

Title:	CB: # NRIIOT3-New_QoS_Parameters - Summary of email discussion

Document for:	Discussion

# Introduction

CB: # NRIIOT3-New_QoS_Parameters

- Introduce Survival Time as an optional IE within the TSC Assistance Information IE or wait for the progress on the Survival Time from SA2 and RAN2? Check LS in R3-210028

- For other TSCAI QoS parameters, waiting for SA2 and RAN2 decision?

- Some new QoS related parameters are required to be included in Assistance Information in order to reflect correctly the status of HARQ transmission in the corresponding node, e.g., Average HARQ Failure Rate and Average HARQ Retransmission Rate? Clarify the definitions of The UL Radio Quality Index and The DL Radio Quality Index? Enhance the Assistance Information reporting mechanism?

- Capture agreements and open issues in the summary

(SS - moderator)

Summary of offline disc R3-211022

# For the Chairman’s Notes

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

R3-20xxxd rev [in xxxh] – agreed

R3-20xxxe rev [in xxxi] – agreed

R3-20xxxf rev [in xxxj] – endorsed

# Discussion

## Introduce Survival Time into RAN3 specifications

SA2 requests RAN2 & RAN3 to consider to include Survival Time in TSCAI from SMF to NG-RAN.

Some companies agree to introduce Survival Time into RAN3 specifications: [2], [3], [5], [6] and [8]

A company would like to wait for the progress on the Survival Time from SA2 and RAN2: [7]

Q1: Do you agree to introduce Survival Time into RAN3 specifications?

| Company | Comment |
| --- | --- |
| Nokia | YES. Survival Time has been agreed by SA2 in their study item conclusions captured in clause 8.4 of TS 23.700-20. Also, RAN2 acknowledged in a Reply LS to SA2 (R3-210028) that they will take into account the SA2 conclusion. |
| Huawei | Agree, as specified in the conclusion part of the TR 23.700-20. |

If it’s agreed to introduce Survival Time, the next questions is which interfaces should Survival Time be added at?

[2], [3], [6] and [8] propose to add Survival Time at Ng/Xn/E1/F1 interfaces.

Q2: Do you agree to introduce Survival Time at Ng/Xn/E1/F1 interfaces?

| Company | Comment |
| --- | --- |
| Nokia | YES. Since SA2 has concluded that Survival Time is transferred as part of TSCAI, it should be introduced on all interfaces that include TSCAI. |
| Huawei | Agree. |

In addition, [2], [5] and [8] indicate Survival Time can be included for downlink and uplink.

[3] indicates Survival Time is just for downlink, and it’s still FFS about whether to include Survival Time for uplink.

There is no discussion for the issue from other companies.

Therefore it is common understanding that Survival Time is included for downlink once the question to Q1 is confirmed.

Q3: Do you agree to introduce Survival Time for uplink?

| Company | Comment |
| --- | --- |
| Nokia | YES. SA2 has already concluded to introduce Survival Time for both downlink and uplink. Additional parameters may also be added, but such parameters (if any) would be on top of (not instead of) Survival Time. |
| Huawei | Agree. Survival Time can be included for downlink and uplink independently. |

## The details of the IE Survival Time

If it’s agreed to introduce Survival Time, some detail issues should be discussed.

For the unit of Survival Time, [2], [3] and [5] propose it should be expressed in units of the data burst periodicity.

Q4: Do you agree the unit of Survival Time should be expressed in units of the data burst periodicity? If not, what’s the proposal?

| Company | Comment |
| --- | --- |
| Nokia | YES. SA2 conclusion states that Survival Time is specified in unit of “time” based on TSCAI periodicity parameter. |
| Huawei | Agree. |

For the minimum value of Survival Time, [2] proposes it should be 1 while [3] and [5] propose it should be 0.

Q5: For the minimum value of Survival Time, 0 or 1 or any other value?

| Company | Comment |
| --- | --- |
| Nokia | Minimum value should be ‘1’. It is not clear to us what the semantics of value ‘0’ is. |
| Huawei | The survival time indicates as the maximum number of consecutive message transmission failures (i.e. whose loss can be tolerated). Value “0” indicates that no transmission failure is allowed. Another alternative is to set as FFS at this stage. |

For the maximum value of Survival Time, [3] proposes it should be at least 180s, [5] propose 256 unit based on their TP, and [2] proposes it should be FFS.

Q6: For the maximum value of Survival Time, any view on this issue?

| Company | Comment |
| --- | --- |
| Nokia | In the performance requirements in clause 5.2 of TS 22.104, the maximum value in any of the use cases is 3 (i.e. 3 times the transfer interval, which can be considered as equivalent to data burst periodicity). Thus, a max value in the range 3 to 6 seems reasonable. |
| Huawei | Could be set as FFS at this stage. |

In addition, [3] proposes that the maximum value of periodicity should be extended to 60000000 us.

Q7: Any view on this issue?

| Company | Comment |
| --- | --- |
| Nokia | This is unrelated to Survival Time and should perhaps be taken separately. But as an initial reaction, if periodicities much larger than 640ms need to be supported (e.g. up to 60 seconds), then it may be preferable to use different granularity (e.g. unit of seconds rather than microseconds). |
| Huawei | Too early to discuss the exact values. And the exact periodicity value can be set based on the SA1 requirement. |

## Other new TSCAI parameters

Some new TSCAI parameters are discussed in the contributions:

- the communication service availability target: [3]

- additional QoS parameters reflecting level of service reliability: [5]

- Burst Spread: [3] and [6]

For a), b) and c), it’s proposed to wait for the conclusion from RAN2 and SA2.

Q8: Any view on this issue?

| Company | Comment |
| --- | --- |
| Nokia | New TSCAI parameters require decision by RAN2/SA2, so we should wait for their conclusions. |
| Huawei | For a), b), c), Ok to wait. |

## NR-U enhancement based on QoS related parameters

[4] discusses the necessary RAN enhancements. In legacy Assistance Information defined in TS 38.425, some parameters cannot reflect the status of HARQ transmission for a path, e.g. Average HARQ Failure and Average HARQ Retransmission. It could cause the receiver of assistance information make wrong decisions which may degrade network performance. In addition, the receiver of assistance information could not control Assistance Information reporting in efficient way and could not utilize the Assistance Information when necessary.

So [4] proposes to add the following parameters in Assistance Information:

Average HARQ Failure Rate and Average HARQ Retransmission Rate.

Q9: Do you agree the proposal?

| Company | Comment |
| --- | --- |
| Nokia | [4] does not seem related to any of the Rel-17 WID objectives, e.g. “new QoS related parameters… decided in SA2”, but rather assistance information (not TSCAI) in PDCP duplication? |
| Huawei | Seems not in the IIoT WI scope? Even the NR-U is already supported in R16. Then if not in the IIoT WI scope, it is better to treat it as correction. |

[4] proposes to consider to enhance the Assistance Information reporting mechanism e.g. periodic reporting.

Q10: Any view on this proposal?

| Company | Comment |
| --- | --- |
| Huawei | See our answer to Q9. |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-210028,	Reply LS on Use of Survival Time for Deterministic Applications in 5GS (RAN WG2)

R3-210094,	RAN3 impacts of Survival Time (Nokia, Nokia Shanghai Bell)

R3-210203,	Analysis of New QoS Related parameters (ZTE)

R3-210289,	NR-U enhancement based on QoS related parameters (Samsung)

R3-210483,	Introduction of the survival Time (Huawei)

R3-210779,	Discussion on new QoS related parameters (CATT)

R3-210876,	Discussion on Further enhanced NR-IIoT: QoS parameters related (Ericsson)

R3-210919,	Enhancements to support new QoS related parameters (CMCC)