3GPP TSG-RAN WG3 #111-e	R3-211022

Online, 25 Jan – 04 Feb, 2021

Agenda Item:	21.3

Source:	Samsung (moderator)

Title:	CB: # NRIIOT3-New_QoS_Parameters - Summary of email discussion

Document for:	Discussion

# Introduction

CB: # NRIIOT3-New_QoS_Parameters

- Introduce Survival Time as an optional IE within the TSC Assistance Information IE or wait for the progress on the Survival Time from SA2 and RAN2? Check LS in R3-210028

- For other TSCAI QoS parameters, waiting for SA2 and RAN2 decision?

- Some new QoS related parameters are required to be included in Assistance Information in order to reflect correctly the status of HARQ transmission in the corresponding node, e.g., Average HARQ Failure Rate and Average HARQ Retransmission Rate? Clarify the definitions of The UL Radio Quality Index and The DL Radio Quality Index? Enhance the Assistance Information reporting mechanism?

- Capture agreements and open issues in the summary

(SS - moderator)

Summary of offline disc R3-211022

# For the Chairman’s Notes

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

R3-20xxxd rev [in xxxh] – agreed

R3-20xxxe rev [in xxxi] – agreed

R3-20xxxf rev [in xxxj] – endorsed

# Discussion

## Introduce Survival Time into RAN3 specifications

SA2 requests RAN2 & RAN3 to consider to include Survival Time in TSCAI from SMF to NG-RAN.

Some companies agree to introduce Survival Time into RAN3 specifications: [2], [3], [5], [6] and [8]

A company would like to wait for the progress on the Survival Time from SA2 and RAN2: [7]

Q1: Do you agree to introduce Survival Time into RAN3 specifications?

| Company | Comment |
| --- | --- |
| Nokia | YES. Survival Time has been agreed by SA2 in their study item conclusions captured in clause 8.4 of TS 23.700-20. Also, RAN2 acknowledged in a Reply LS to SA2 (R3-210028) that they will take into account the SA2 conclusion. |
| Huawei | Agree, as specified in the conclusion part of the TR 23.700-20. |
| CATT | Agree |
| Samsung | Agree |
| Ericsson | We should wait for RAN2 to resolve all the FFSs on this topic and the agreement is reached. |
| CMCC | Agree, this parameter has been agreed by SA2 and RAN2 |
| China Unicom | Agree |
| Qualcomm | Agree in principle (subject to further discussion/details bla bla – essentially pending on other groups) |

If it’s agreed to introduce Survival Time, the next questions is which interfaces should Survival Time be added at?

[2], [3], [6] and [8] propose to add Survival Time at Ng/Xn/E1/F1 interfaces.

Q2: Do you agree to introduce Survival Time at Ng/Xn/E1/F1 interfaces?

| Company | Comment |
| --- | --- |
| Nokia | YES. Since SA2 has concluded that Survival Time is transferred as part of TSCAI, it should be introduced on all interfaces that include TSCAI. |
| Huawei | Agree. |
| CATT | Agree |
| Samsung | YES. The Survival Time should be part of TSCAI. |
| Ericsson | If to introduce, it is in TSCAI |
| CMCC | Yes, part of TSCAI |
| China Unicom | Agree |
| Qualcomm | Agree and in principle as part of the TSCAI as mentioned already |

In addition, [2], [5] and [8] indicate Survival Time can be included for downlink and uplink.

[3] indicates Survival Time is just for downlink, and it’s still FFS about whether to include Survival Time for uplink.

There is no discussion for the issue from other companies.

Therefore it is common understanding that Survival Time is included for downlink once the question to Q1 is confirmed.

Q3: Do you agree to introduce Survival Time for uplink?

| Company | Comment |
| --- | --- |
| Nokia | YES. SA2 has already concluded to introduce Survival Time for both downlink and uplink. Additional parameters may also be added, but such parameters (if any) would be on top of (not instead of) Survival Time. |
| Huawei | Agree. Survival Time can be included for downlink and uplink independently. |
| CATT | Yes |
| Samsung | YES. In our understanding, SA2 has already introduced Survival Time for both downlink and uplink. |
| Ericsson | The same as in Q1. |
| CMCC | Yes |
| China Unicom | Agree to introduce Survival Time for both downlink and uplink. |
| Qualcomm | As in Q1 yes in principle but pending other groups for confirmation – there is no rush |

## The details of the IE Survival Time

If it’s agreed to introduce Survival Time, some detail issues should be discussed.

For the unit of Survival Time, [2], [3] and [5] propose it should be expressed in units of the data burst periodicity.

Q4: Do you agree the unit of Survival Time should be expressed in units of the data burst periodicity? If not, what’s the proposal?

| Company | Comment |
| --- | --- |
| Nokia | YES. SA2 conclusion states that Survival Time is specified in unit of “time” based on TSCAI periodicity parameter. |
| Huawei | Agree. |
| CATT | Yes |
| Samsung | We think the Survival Time can be expressed with the time value or the times of the TSCAI periodicity parameter, and either way can be workable. Samsung prefers using the time value to express the Survival Time. |
| Ericsson | In units of “time”. |
| CMCC | Expressed in time value or times of TSCAI periodicity, we should also consider the agreement in SA2 that Survival time is also applied to aperiodic traffic. |

For the minimum value of Survival Time, [2] proposes it should be 1 while [3] and [5] propose it should be 0.

Q5: For the minimum value of Survival Time, 0 or 1 or any other value?

| Company | Comment |
| --- | --- |
| Nokia | Minimum value should be ‘1’. It is not clear to us what the semantics of value ‘0’ is. |
| Huawei | The survival time indicates as the maximum number of consecutive message transmission failures (i.e. whose loss can be tolerated). Value “0” indicates that no transmission failure is allowed. Another alternative is to set as FFS at this stage. |
| CATT | Agree with HW, set as FFS now |
| Samsung | We think it depends on which expression is used for the Survival Time. If the time value is used, we think ‘0’ could be the minimum value. |
| Ericsson | The same as in Q1. |
| CMCC | Depends on what the value “0” means. We agree this stage 3 details could be FFS |
| Qualcomm | Set as FFS but this needs care. In any case the whole IE (if we move that far) should be FFS pending etc |

For the maximum value of Survival Time, [3] proposes it should be at least 180s, [5] propose 256 unit based on their TP, and [2] proposes it should be FFS.

Q6: For the maximum value of Survival Time, any view on this issue?

| Company | Comment |
| --- | --- |
| Nokia | In the performance requirements in clause 5.2 of TS 22.104, the maximum value in any of the use cases is 3 (i.e. 3 times the transfer interval, which can be considered as equivalent to data burst periodicity). Thus, a max value in the range 3 to 6 seems reasonable. |
| Huawei | Could be set as FFS at this stage. |
| CATT | Set as FFS |
| Samsung | The maximum value of the Survival Time needs to be 3 or more times of the maximum value of the Periodicity. |
| Ericsson | The same as in Q1. |
| CMCC | Stage 3 details, FFS |
| Qualcomm | Obvious FFS, if we get to the point of a baseline, the IE coding can be FFS anyway |

In addition, [3] proposes that the maximum value of periodicity should be extended to 60000000 us.

Q7: Any view on this issue?

| Company | Comment |
| --- | --- |
| Nokia | This is unrelated to Survival Time and should perhaps be taken separately. But as an initial reaction, if periodicities much larger than 640ms need to be supported (e.g. up to 60 seconds), then it may be preferable to use different granularity (e.g. unit of seconds rather than microseconds). |
| Huawei | Too early to discuss the exact values. And the exact periodicity value can be set based on the SA1 requirement. |
| CATT | Discuss it later |
| Samsung | This is not directly related with the Survival Time. But extending the maximum value of the Periodicity needs to be discussed. |
| Ericsson | When the other groups reached agreement, the impact on the RAN3 spec can be settled. |

## Other new TSCAI parameters

Some new TSCAI parameters are discussed in the contributions:

- the communication service availability target: [3]

- additional QoS parameters reflecting level of service reliability: [5]

- Burst Spread: [3] and [6]

For a), b) and c), it’s proposed to wait for the conclusion from RAN2 and SA2.

Q8: Any view on this issue?

| Company | Comment |
| --- | --- |
| Nokia | New TSCAI parameters require decision by RAN2/SA2, so we should wait for their conclusions. |
| Huawei | For a), b), c), Ok to wait. |
| CATT | We need wait RAN2/SA2 conclusion |
| Ericsson | Wait for agreement in RAN2/SA2 |
| CMCC | Wait for RAN2 and SA2 |
| Qualcomm | As above, no reason to take any of these forward for now |

## NR-U enhancement based on QoS related parameters

[4] discusses the necessary RAN enhancements. In legacy Assistance Information defined in TS 38.425, some parameters cannot reflect the status of HARQ transmission for a path, e.g. Average HARQ Failure and Average HARQ Retransmission. It could cause the receiver of assistance information make wrong decisions which may degrade network performance. In addition, the receiver of assistance information could not control Assistance Information reporting in efficient way and could not utilize the Assistance Information when necessary.

So [4] proposes to add the following parameters in Assistance Information:

Average HARQ Failure Rate and Average HARQ Retransmission Rate.

Q9: Do you agree the proposal?

| Company | Comment |
| --- | --- |
| Nokia | [4] does not seem related to any of the Rel-17 WID objectives, e.g. “new QoS related parameters… decided in SA2”, but rather assistance information (not TSCAI) in PDCP duplication? |
| Huawei | Seems not in the IIoT WI scope? Even the NR-U is already supported in R16. Then if not in the IioT WI scope, it is better to treat it as correction. |
| CATT | Agree with Nok and HW |
| Samsung | We think it’s beneficial to consider the enhancement from two directions. One is RAN enhancement based on new parameters decided by SA2. The other is to consider RAN enhancement for improvement of features for IIOT/URLLC. In order to let the hosting node to know the transmission status in the assisting node, some assisted information including Average HARQ Failure and Average HARQ Retransmission are provided to the hosting node. The hosting node control its data transmission based on those assisted information. The number of total HARQ transmission is variable and not a fixable value. In the following two cases, the hosting node will get the same information with Average HARQ Failure and Average HARQ Retransmission. The actual situation is quite different. But the hosting node cannot have differentiated handling for the two cases. there are 5 failures in total 10 transmissions during a time unit there are 5 failures in total 100 transmissions during same time unit In order to improve this, it is very helpful if the hosting node can get the Average HARQ failure/retransmission rate (the rate of the number of HARQ failure/retransmission to the number of total HARQ transmission.). Then the hosting node can better control its data transmission to the assisting node. |
| Ericsson | Similar view to CATT/HW/Nokia |
| CMCC | Same view as CATT/HW/Nokia |
| China Unicom | Same view as CATT/HW/Nokia/ Ericsson/CMCC |
| Qualcomm | Same view as CUC, proposals may be valid to discuss but seem more like TEI |

[4] proposes to consider to enhance the Assistance Information reporting mechanism e.g. periodic reporting.

Q10: Any view on this proposal?

| Company | Comment |
| --- | --- |
| Huawei | See our answer to Q9. |
| Samsung | The assistance information reporting depends on the Assistance Info. Report Polling Flag in DL USER DATA or depending on the assisting node implementation. The inefficiency of such reporting mechanism: If hosting node need multiple reporting in a long term, it has to send DL USER DATA with the flag one by one, and even an empty DL USER DATA if no data at that time. This introduces redundant transmission and wastes resources between hosting node and assisting node. The average window for some parameters in assistance information, e.g. average HARQ failure/retransmission, depends on the local configuration in assisting node. The hosting node may not get the expected granularity for different service type e.g. URLLC may need small granularity of the window in order to quick adjust the data transmission for URLLC service. It’s not mandatory to include the data of all Assistance Information Type in the report. It means that the node hosting the PDCP entity may not get the expected information from the corresponding node. In order to let the hosting node get the assisted information which are really helpful for efficient data transmission, we think it’s desirable to enhance assistance information reporting mechanism, e.g. with periodical reporting, or with the window, or with the required assistance information type in the polling message. |
| Ericsson | As in Q9 |
| CMCC | Same view as Q9 |
| China Unicom | Same view as Q9 |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-210028,	Reply LS on Use of Survival Time for Deterministic Applications in 5GS (RAN WG2)

R3-210094,	RAN3 impacts of Survival Time (Nokia, Nokia Shanghai Bell)

R3-210203,	Analysis of New QoS Related parameters (ZTE)

R3-210289,	NR-U enhancement based on QoS related parameters (Samsung)

R3-210483,	Introduction of the survival Time (Huawei)

R3-210779,	Discussion on new QoS related parameters (CATT)

R3-210876,	Discussion on Further enhanced NR-IIoT: QoS parameters related (Ericsson)

R3-210919,	Enhancements to support new QoS related parameters (CMCC)