3GPP TSG-RAN WG3 #111-e							R3-21xxxx

25 January – 4 February 2021

Online

Agenda Item:	15.2

Source:	Huawei - Moderator

Title:	Summary of Offline Discussion on RAN Configuration and Reporting of QoE measurement

Document for:	Approval

# Introduction

CB: # NRQoE3-RANConfig_Report

- QoE support for new services, SA4 LS in R3-210041? Support non-3GPP standardized application? Support Time Sensitive Communication and liaise SA4?

- Support Management-based QoE solution where a UE identifier is optionally included in the QoE measurement configuration, to enable collecting QoE reports from an individual UE? Yes, E///. No. Nokia.

- Signalling for Management-based and Signalling-based QoE supports multiple QoE measurements for different service types for the same UE? Whether and how to deactivate one of the multiple QoE measurements? Need check by RAN?

- There is no need to introduce RAN autonomously triggered QoE measurement mechanism?

- Radio related assistance measurements used for QoE management are only meaningful when there is at least one on-going QoE recording session?

- QoE handling at RAN overload? QoE report suspending in RAN overload and RRC_IDLE/INACTIVE? Reply to SA4 LS in R3-210042

- Can RAN and/or OAM start/stop/pause/resume measurement collection at the UE? Independently or as per triggering conditions? For both legacy and RAN-visible QoE?

- Can RAN and/or OAM start/stop/pause/resume measurement reporting from the UE? Independently or as per triggering conditions? For both legacy and RAN-visible QoE?

- How to align radio measurements and QoE reports?

- Capture agreements as TP for TR

(HW - moderator)

Summary of offline disc R3-211013

# For the Chairman’s Notes

Propose to capture the following:

To be continued

# Discussion

Since this should be the last time for this SI, it seems that there are still many open issues, but some of them are pure stage 3 details, here moderator tried to, according to the guidance of this CB from chair, directly extract proposals from contributions and reformate to issues.

Issue 1: Support for new service, e.g. XR, URLLC, also including non-3GPP standardized application and TSC

Moderator’s note: we see some discussions in [6] [9] [10], also we see reply LS from SA4 in [1], we may need some consensus, e.g. to work on something which is also being discussed in SA4. Companies are invited to provide view for each service type mentioned here.

| Company | Comment |
| --- | --- |
| Huawei | In general, RAN3 should work on the service type(s) which is also being discussed in SA4. Based on this understanding, we think: XR could be introduced URLLC is a general description of a service category, we need to see which exact service type we are discussing; No need to discuss non-3GPP standardized application now, we could start this from SA4. No need to discuss TSC now, since TSC as a service type is knows by RAN via QoS parameter, and SA4 has not discussed TSC yet. |
| Samsung | As the objective of the SI is to support NR QoE for diverse services, we think it’s good to think about supporting non 3GPP service types, which may be customized by providers or operators, and may not be defined by SA4. But in our view the solution in [6] is not a complete solution, and it’s also too early to discuss the details. So we think we can consider to support all the service types needed by operators including SA4 defined or undefined service types, but details are FFS. |
| Nokia | Handling of particular aspects for specific service types seem premature - the study currently focuses on the general framework. |
| Qualcomm | XR can be introduced (SA4 already sent LS confirming this). Requirements for other service types mentioned such as URLLC (not clear at this time), non-3GPP, TSC should come from SA4. And we can always extend the supported service types once the framework is ready. |

Issue 2: Whether to support RAN autonomously triggered QoE measurement

Moderator’s note: we see some discussions in [9] [11] about RAN autonomously triggered QoE measurement. Please companies provide your view (yes/no) and comments if any.

| Company | View | Comments |
| --- | --- | --- |
| Samsung | Yes | In our view, RAN can trigger RAN visible QoE measurement configuration on demand, this is also discussed in CB RAN visible QoE. |
| Huawei | No | As explained in our paper, we think QoE measurement is an E2E measurement, not sure what could RAN get if triggered by RAN, in addition to RAN initiated MDT related measurements… |
| Nokia | No | Agree with HW. However if a use case can be defined where the RAN becomes the end consumer of a measurement done by the application layer, the framework should be extendable to cover such case. |
| Qualcomm | No | No need for RAN autonomously triggered QoE measurements for legacy QoE. Even if we support RAN visible QoE, we think RAN can’t autonomously trigger QoE measurements and can only control RAN visible QoE reporting interval if at all (UE APP will compute RAN visible QoE metrics and send it to UE AS which in turn will report to RAN on a periodic/event trigger (FFS) set by RAN). Can be discussed further in CB RAN visible QoE |

Issue 3: Whether a UE identifier is optionally included in the management based QoE measurement configuration

Moderator’s note: we see some discussions in [6] [8] about optionally including a UE identifier in the management based QoE measurement configuration, in order to enable collecting QoE reports from an individual UE. Please companies provide your view (yes/no) and comments if any.

| Company | View | Comments |
| --- | --- | --- |
| Samsung | Tend to No | For M-based QoE, it is gNB choose the UEs according to their capabilities for the given service type. In [6], it is said that OAM can choose the UE among UE identifiers provided by gNB, we don’t see the benefits that UE is selected by OAM instead of gNB, and as there are transmission delay btw OAM and gNB, there could be a situation that the UE selected by the OAM is not served by the given gNB anymore when the configuration is sent from OAM. |
| Huawei | Maybe not | Not sure the real intention, the intention of management is for OAM to give guidance/requirements for the RAN to select a specific UE, so what’s the point that OAM to select a UE directly without using signaling based one. |
| Nokia | No | If the OAM needs to activate QoE reporting for a specific UE, it should use s-based activation. |
| Qualcomm | No | Same view as Nokia |

Issue 4: Supports for multiple QoE measurements for the same UE? Whether and how to deactivate one of them? Need check by RAN2?

Moderator’s note: we see some discussions in [5] [6] [8] about supporting for multiple QoE measurements for the same UE for both signaling based and management based, whether and how to deactivate one of them, whether to need check by RAN2. Please companies provide your view (yes/no) and comments if any.

| Company | View | Comments |
| --- | --- | --- |
| Samsung | Yes | For S-based QoE, the QoE activation or deactivation is transmitted from CN, which means NG interface will be impact first, so support (de)activate multiple QoE measurement should be decided by RAN3 first. For M-based QoE, need check by RAN2. Regarding how to support, for activation, a list of QoE measurement configurations should be included in the activation message. For deactivation, a list of QoE references should be included in the deactivation message. |
| Huawei | Yes | Since there might be more than one service ongoing for a UE, it is natural to support multiple service of QoE measurement for the same time. For detailed mechanisms, it is mainly up to RAN2 to design. |
| Nokia | supportive | This seems useful. However it will be heavily UE impacting so needs confirmation by RAN2. |
| Qualcomm | Yes | This is SA5 requirement. RAN2 might define a UE capability whether UE supports multiple QoE configuration and reporting and also the signaling for the activation/deactivation over RRC (we can wait for RAN2 agreements). In RAN3, we should introduce signaling over Xn and NG for sending a list of QoE configurations (to support multiple QoE) at the same time and an option to deactivate a subset/all of the configured QoE by providing the QoE-referenceID. We can send an LS to SA5 (and cc RAN2) that RAN3 can support multiple QoE in normative phase and capture this in the TR. |

Issue 5: QoE handling at RAN overload

Moderator’s note: we see some discussions in [6] about how QoE measurement is handled at RAN overload scenario, the proposals could be summarized as follows:

For SA operation or EN-DC/NR-DC when both nodes are overloaded, RAN is allowed to

- Not to trigger new QoE measurement if requested

- Release/suspend ongoing QoE measurement, fulfilling SA4 and RAN2 agreements

- Suspend QoE reporting

For EN-DC/NR-DC when only one node is overloaded, RAN is allowed to

- QoE measurement is reported towards the non-overloaded RAN node, with reconfigured MCG/SCG SRB bearer

- previous overloaded node may request the QoE report from the other node when overload is solved, if analysis justify

Please companies provide your comments on each of the proposals above..

| Company | Comments |
| --- | --- |
| Samsung | For SA case, we prefer suspend or prolong QoE reporting which can keep the integrity of the QoE report even RAN overload. It means the QoE measurement is continue in UE application layer, cache QoE report will be performed. In our view, whoever (App layer or AS layer) implement this needs extra caching space, and it’s out of RAN3 scope. since SA4 is not in favor of caching QoE reports in application layer [R3-210042], so we need further check with RAN2 whether caching QoE reports in AS layer is feasible. For NSA case, we think the suspend and prolong QoE reporting can also be used. At this stage, we still not sure which SRB will be used for QoE report, whether the QoE report can be forwarded to SN, should be decided by RAN2. |
| Huawei | In general, we support to introduce some mechanisms for RAN to handle QoE measurement in case of overload, but detailed solutions should be up to RAN2 to design, since anyway it is mainly related with AS layer behavior, especially that SA4 expressed their unwillingness to do this in application layer. |
| Nokia | Should be done in the AS layer. Probably the UE should simply discard measurements that could not be conveyed due to RAN overload, hence avoiding new overload situation in the network when the reporting resumes. |
| Qualcomm | First of all, we think we can deprioritize all MR-DC scenarios for QoE in Rel-17. For SA, we agree RAN should introduce mechanisms to handle overload scenarios (RAN2 should handle RRC signaling for the same and whether UE AS will support caching QoE report or will discard them upon receiving from UE APP on RAN overload). Considering this is an important decision for supporting RAN overload (and also QoE for RRC_IDLE/RRC_INACTIVE) and involves multiple WGs, we have prepared an LS in R3-210356 to ask SA4 (we can cc RAN2) if they can consider caching at UE APP layer based on our discussion paper in R3-210355. Also prolonging QoE report interval as highlighted by Samsung is not preferred by us as this will involve both SA4 (communicating this new interval to APP layer) and RAN2 (caching reports at UE AS) |

Issue 6: Handling for QoE collection and QoE reporting

Moderator’s note: we see some discussions in [6] [7] about Handling for QoE collection and QoE reporting. The issues could be summarized as follows:

For both reporting and collection:

- Can RAN and/or OAM stop/re-start, pause/resume the operation at the UE? Are there any conditions for triggering such operation?

- Is such operation applicable to both legacy and RAN-visible QoE?

Please companies provide your view (yes/no) and comments if any.

| Company | Comments |
| --- | --- |
| Samsung | For handling of QoE configuration We observe that companies had different understandings on words such as start, stop, activate and deactivate. So we suggest clarify those words in the TR and follow the same principle in LTE. As in LTE QMC, there are only two words related to QoE configuration in TS36.300, which are “setup” and “release”, according to TS28.405, the activation means RAN setup configuration, deactivation means RAN release the configuration. In 36.300, it is said that “ E-UTRAN can release the application layer measurement configuration towards the UE at any time.” For NR QoE, which is based on LTE QoE, should also follow the same principle that RAN can release the application layer measurement configuration. But this doesn’t mean the QoE measurement will be stopped immediately in application layer, as in SA4, it is said that UE only checks the configuration when each session starts. The release operation will only affect session from the next session, not the on-going session. So in our view, RAN can release (i.e. stop QoE measurement from the next session) /setup (i.e. start QoE measurement from the next session) the QoE configuration for a UE according to its own purpose (e.g. RAN overload), it’s the same as LTE. For handling of QoE reporting. It’s kind of enhancement based on LTE QMC, as in LTE, RAN is not aware of QoE reporting configuration, in NR QoE, we think if RAN can configure QoE reporting in AS layer without impact the original report generation in application layer, it would be beneficial when RAN overload, of course this topic is discussed in issue 5. So in our view, to support QoE reporting suspending when RAN overload, RAN can suspend or prolong the QoE reporting in AS layer. And we think above operations in RAN are applicable to both legacy and RAN-visible QoE. |
| Huawei | For handling of QoE configuration, similar view as SS, just to simply stop/re-start or just release (which means this task is terminated) For handling of QoE reporting, we think RAN is allowed to suspend or delay the reporting, but detailed mechanism is up to RAN2 to design. We also think that above behavior applies to both legacy and RAN-visible QoE. |
| Nokia | We believe that the legacy LTE QMC specification in the RAN addressed AS layer and application layer simultaneously. So "release" also meant release of currently ongoing reporting. |
| Qualcomm | For handling of QoE configuration, same view as Samsung (RAN can setup or release the QoE configuration as needed) For handling of QoE reporting, RAN is allowed to suspend the QoE reporting (whether it is suspended at UE AS or UE APP is discussed in issue 5). We don’t prefer RAN to delay QoE reporting due to reasons mentioned in issue 5. And we think this can be applicable to both legacy and RAN-visible QoE. |

Issue 7: Handling for QoE measurement and its corresponding radio assisted measurement

Moderator’s note: we see some discussions in [12] [13] about handling for QoE measurement and its corresponding radio assisted measurement. The issues could be summarized as follows:

- If QoE measurement is stopped/released, this corresponding radio related assistance measurements should also be stopped/released. According to the indication from UE application layer?

- Bearer information (e.g. DRB list or QoS flow ID) related to the QoE measurement should be indicated to the gNB or QoE server for Correlation.

- the collection of the radio related assistance information should include all the serving gNBs that the UE went through during the corresponding time of one QoE report.

- the radio related assistance information should be provided along with the QoE report by UE, inside or outside of the QoE report container is FFS

Please companies provide your view and comments for each proposal above, if any.

| Company | Comments |
| --- | --- |
| Samsung | Yes, to all proposals. For radio related measurements The radio related measurements which are used to assist QoE analysis should only be started/stopped when the corresponding QoE measurement is start/end. And when QoE measurement starts/stops is the UE individual behavior, so the application layer should indicate it to the gNB and/or UE AS layer. Moreover, considering multiple recording sessions and multiple QoE measurements may appear at the same time, additional information such as QoE reference and recording session ID should be included in the indication for further correlation. In addition, if radio related measurement is to measure DRB, the DRB information should also be indicated to gNB or QoE server for correlation. For radio related information One QoE report may relate to the information from multiple gNBs that serve the UE during the collection time of the QoE report, so the radio related assistance information should include all the serving gNBs It would be easier and will have less impact if this information is collected from UE along with the QoE report instead of collecting from multiple serving gNBs. |
| Huawei | Not sure if we should go into details of each proposal, but in general, we think it is better that QoE measurement and its corresponding radio assisted measurement should be configured together and reported together. And the operation of suspending or releasing should also be applied to both. |
| Nokia | agree with Huawei |
| Qualcomm | All the proposals mentioned involve adding new “radio related information” such as session start/stop indication, bearer ID, serving gNB etc.. which are not agreed and we don’t prefer to include to not overcomplicate NR QoE. “Radio related measurements” can simply be the existing MDT reports. We can enable time alignment between MDT reports and QoE measurement, e.g. by using QoE reference ID to bind the MDT measurements to the QoE measurements which can be used by MCE for correlation purposes. |

Issue 8: General rules for MR-DC

Moderator’s note: we see some discussions in [9] about some general rules for MR DC operation when triggering QoE measurement. The issues could be summarized as follows:

- For MR-DC operation including NSA, only one node is allowed to configure the QoE measurement, and the MN could decide which node to configure the QoE measurement for a certain service type.

- For a gNB acting as SN, it could configure the QoE measurement directly towards that UE over SN leg.

| Company | Comments |
| --- | --- |
| Huawei | Yes. We think the proposals should be agreed as general principle for handling MR-DC case. |
| Nokia | This depends on RAN2 decision. |
| Qualcomm | Deprioritize MR-DC in Rel-17 |

Other issues:

If there are any other issues, please list here.

# Conclusion, Recommendations

See section 2.

# References

- R3-210041, LS Reply on New service type of NR QoE, (SA WG4)

- R3-210042, LS reply on QoE Measurement Collection, (SA WG4)

- R3-210355, QoE report suspending in RAN overload and RRC_IDLE/INACTIVE, (Qualcomm Incorporated)

- R3-210356, LS reply on QoE Measurement Collection, Qualcomm Incorporated

- R3-210507, Open issues in NR QoE solutions, (Samsung)

- R3-210527, pCR for TR 38.890: Handling of QoE Measurement and Reporting and Support for New Services, (Ericsson)

- R3-210658, (TP for TR 38.890) QoE measurement collection continuity vs. reporting continuity, (Nokia, Nokia Shanghai Bell)

- R3-210659, (TP for TR 38.890) QoE measurement configuration for specific UEs, (Nokia, Nokia Shanghai Bell)

- R3-210820, Further discussions on the remaining open issues of QoE configuration and reporting, (Huawei)

- R3-210848, Further consideration on NR QoE service and procedure, (ZTE)

- R3-210772, Discussion on RAN visible QoE configuration and reporting, CATT

- R3-210849, TP for TR 38890, (ZTE)

- R3-210509, Discussion on radio related measurements and information in NR QoE, Samsung