3GPP TSG-RAN WG3 #111-e					                 R3-211212

25 January – 4 February 2021

Online

Agenda item:	17.2

Source: 	ZTE

Title: 	TP for TR38.832 for conclusion on Solutions for scenarios 1,3,5,6

Document for:   Discussion and Approval

# Introduction

This contribution provides our TP on RAN3 part of TR38.832.

------------------------------ Start of change ---------------------------------------------------------------------

# Conclusion

Conclusion on Solutions for scenarios 1,3,5,6：

The solutions to support following RAN slicing scenarios are recommended by RAN3 to be specified in normative phase:

-	Resource shortage in case of Intra-RA mobility

-	Slice resource shortage for MR-DC

-	Slice overload in RAN node in absence of mobility

Solutions are expected to be refined during normative phase after feedback from SA2 and SA5.