3GPP TSG-RAN WG3 #112-e                                                                                   R3-212683

Online, 17th - 28th May, 2021

Agenda Item:	16.1

Source:	China Telecom (moderator)

Title:	Summary of Offline Discussion on Potential Enhancement on ePRN WI Scope

Document for:	Approval

# Introduction

This document aims to summarize the offline discussion on the enhanced NPN WI scope, the guidance for offline discussion is as follows:

CB: # 1001_PRN_GEN

- Work plan is noted

- Discuss potential enhancements to WI based on 2065

(CT - moderator)

Summary of offline disc R3-212683

The deadline is Friday, May 21, 24:00:00 UTC.

# For the Chairman’s Notes

Propose the following:

Proposal 1:	Work plan(R3-211709) is noted.

Proposal 2:	R3-212065 is noted as there is no agreement on including “Support for the simultaneous data service from PLMN and NPN and service continuity between two networks” into ePRN WI scope.

# Discussion

In R3-212065 [1], the support for the simultaneous VIAPA service from SNPN and PLMN and service continuity between SNPN and PLMN was mainly discussed.

According to the conclusions of eNPN SI [2], it was proposed to extend the ePRN WI scopes to support VIAPA as following:

- Support for Video, Imaging and Audio for Professional Applications (VIAPA) including:

  - Support for the simultaneous data service from PLMN and NPN and service continuity between two networks [RAN3, RAN2]

  - The necessary modifications over network interfaces (e.g. NG, Xn, F1, E1 etc) [RAN3]

Here, we welcome your opinions from all interested companies.

## Question: Do company agree to include “Support for the simultaneous data service from PLMN and NPN and service continuity between two networks” into the WI scopes?

Companies are invited to provide your views in the table

| Company | Yes / No | Comment |
| --- | --- | --- |
| Huawei |  | This should be discussed in RAN plenary instead. So far our understanding is that the VIAPA has no RAN3 impact. |
| Qualcomm | No | Agree with Huawei |
| ZTE | Yes | In our understanding, if UE have both subscriptions for SNPN and PLMN, the simultaneous VIAPA service from PLMN and SNPN and service continuity shall be supported. Hence, the latency should be improved to resume the services provided by overlay network. To support UE to receive data services from one network (e.g. NPN), and paging as well as data services from another network (e.g. PLMN) simultaneously may have RAN impacts. |
| Ericsson | No, No | Same view as Huawei and QC |
| China Telecom | Yes | The service continuity between PLMN and SNPN is the key issue for VIAPA and should be enhanced. |
| Nokia | No | Our understanding is aligned with Huawei, QC and Ericsson |

Moderator’s summary:

6 companies participated in this discussion and shared their views. 2 companies supported and 4 companies were against to include “Support for the simultaneous data service from PLMN and NPN and service continuity between two networks” into ePRN WI scope. Therefore, there is no consensus on extending the scope of PRN WID to include this.

# Conclusion, Recommendations [if needed]

The following is proposed:

Proposal 1:	Work plan(R3-211709) is noted

Proposal 2:	R3-212065 is noted as there is no agreement on including “Support for the simultaneous data service from PLMN and NPN and service continuity between two networks” into ePRN WI scope.

# References

- R3-212065, Consideration on the enhanced NPN WI scopes (ZTE Corporation)

- TR23.700-07, Study on enhanced support of non-public networks.