3GPP TSG RAN WG3 #112-e	R3-212839

Electronic, 17th – 28th May, 2021

| CR-Form-v12.1 |
| --- |
| CHANGE REQUEST |
|  | 38.413 | CR | 0594 | rev | 1 | Current version: | 16.5.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME |  | Radio Access Network | X | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Supporting enhanced private network |
| --- | --- |
| Source to WG: | Huawei |
| Source to TSG: | RAN3 |
| Work item code: | NG_RAN_PRN_enh |  | Date: | 2021-05-17 |
| Category: | B |  | Release: | Rel-17 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) … Rel-15 (Release 15) Rel-16 (Release 16) Rel-17 (Release 17) Rel-18 (Release 18) |
| Reason for change: | The new WID on Enhancement of Private Network Support for NG-RAN was agreed in RP-202363. There is need to specify RAN functions to support eNPN. |
| Summary of change: | Include the Onboarding Support in NG SETUP RESPONSE and AMF CONFIGURATION UPDATE for AMF selection in case of UE onboarding. Impact Analysis: Impact assessment towards the previous version of the specification (same release): This CR has isolated impact with the previous version of the specification (same release). The impact can be considered isolated because the change only affects the network interface management functions. |
| Consequences if not approved: | The eNPN feature is not supported. Not aligned with SA2 stage 2 specification. |
| Clauses affected: | 8.7.1.2, 8.7.3.2, 9.3.3.44 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |
| This CR's revision history: |  |

Change Begins

### 8.7.1	NG Setup

#### 8.7.1.1	General

The purpose of the NG Setup procedure is to exchange application level data needed for the NG-RAN node and the AMF to correctly interoperate on the NG-C interface. This procedure shall be the first NGAP procedure triggered after the TNL association has become operational. The procedure uses non-UE associated signalling.

This procedure erases any existing application level configuration data in the two nodes, replaces it by the one received and clears AMF overload state information at the NG-RAN node. If the NG-RAN node and AMF do not agree on retaining the UE contexts this procedure also re-initialises the NGAP UE-related contexts (if any) and erases all related signalling connections in the two nodes like an NG Reset procedure would do.

#### 8.7.1.2	Successful Operation

<Unchanged Text Omitted>

If the NID IE within the NPN Support IE is included within a Broadcast PLMN Item IE in the NG SETUP REQUEST message, the AMF shall consider that the NG-RAN node supports the indicated S-NSSAI(s) for the corresponding tracking area code for the SNPN identified by the PLMN Identity IE and the NID IE.

If the NID IE within the NPN Support IE is included within a PLMN Support Item IE in the NG SETUP RESPONSE message, the NG-RAN node shall consider that the AMF supports the SNPN identified by the PLMN Identity IE and the NID IE.

If the Onboarding Support IE is included within a NPN Support IE in the NG SETUP RESPONSE message, the NG-RAN node shall, if supported, consider that the AMF supports the UE onboarding for the SNPN identified by the PLMN Identity IE and the NID IE, as specified in TS 23.501 [9].

/***unchanged text omitted***/

<<<<<<<<<<<<<<<<<<<< Next Change >>>>>>>>>>>>>>>>>>>>

### 8.7.3	AMF Configuration Update

#### 8.7.3.1	General

The purpose of the AMF Configuration Update procedure is to update application level configuration data needed for the NG-RAN node and AMF to interoperate correctly on the NG-C interface. This procedure does not affect existing UE-related contexts, if any. The procedure uses non UE-associated signalling.

#### 8.7.3.2	Successful Operation

Figure 8.7.3.2-1: AMF configuration update: successful operation

<Unchanged Text Omitted>

If the NID IE within the NPN Support IE is included within a PLMN Support Item IE in the AMF CONFIGURATION UPDATE message, the NG-RAN node shall consider that the AMF supports the SNPN identified by the PLMN Identity IE and the NID IE.

If the Onboarding Support IE is included within a NPN Support IE in the AMF CONFIGURATION UPDATE message, the NG-RAN node shall, if supported, consider that the AMF supports the UE onboarding for the SNPN identified by the PLMN Identity IE and the NID IE, as specified in TS 23.501 [9].

<Unchanged Text Omitted>

#### 9.3.3.44	NPN Support

For SNPN, this IE identifies a supported SNPN together with the associated PLMN ID, and indicates the onboarding support at the AMF for the SNPN as specified in TS 23.501 [9].

| IE/Group Name | Presence | Range | IE type and reference | Semantics description | Criticality | Assigned Criticality |
| --- | --- | --- | --- | --- | --- | --- |
| CHOICE NPN Support | M |  |  |  | - |  |
| >SNPN |  |  |  |  |  |  |
| >>NID | M |  | 9.3.3.43 |  | - |  |
| >>Onboarding Support | O |  | ENUMERATED (true, ...) | Indication of onboarding support at the AMF. FFS whether this IE is included within the NPN Support IE, or outside of the NPN Support IE. | YES | reject |

Change Ends