3GPP TSG-RAN WG3 #112-e	R3-212674

Online, 17 – 28 May, 2021

Agenda Item:	12.3

Source:	Huawei (moderator)

Title:	Summary of Offline Discussion on IOT_Main

Document for:	Approval

# Introduction

CB: # 1102_IOT_Main

-  Irrespective of the options for UE to select paging carrier discussed in RAN2, can we assume container-based or IE-based approach for S1?

- If there is no agreement on either approach, we can still discuss the technical details of the CRs provided to the meeting without any indication of their endorsement

- Start with summary of offline, proceed to CRs are if there is consensus

(HW - moderator)

Summary of offline disc R3-212674

# For the Chairman’s Notes

//to be added

# Discussion

## Carrier Selection

### RAN3 impacts of the two RAN2 options

From the submitted papers, it is found that many companies mentioned both EPC and 5GC cases, it is needed first to clarify the supported scenarios.

Question 1: do you agree to discuss Carrier Selection in both EPC and 5GC scenarios?

| Company | Comment |
| --- | --- |
| Huawei | Yes, NB-IoT connecting to 5GC is supported since Rel-16, 36.331 is also updated to support NB-IoT connecting to 5GC, it is assumed that by default the Rel-17 discussion support both EPC and 5GC cases. |

To support CE based carrier selection, there are two options from RAN2:

    - Option 1: UE selects a paging carrier based on a rule configured by the network

    - Option 2: NW configures a specific paging carrier

Question 2: whether RAN3 needs to wait for RAN2 further progress to discuss their options?

| Company | Comment |
| --- | --- |
| Huawei | Yes, better to further proceed after RAN2 progress |

For RAN2 option 1, there seems a need to inform the RAN node about whether the UE is using the CE based carrier selection in CN Paging, and there are different views on how to propagate the information from the last serving RAN node to the CN, and from CN to the RAN nodes.

Question 3: in case option 1 is adopted by RAN2, if and how to propagate the information about “whether the UE is using the CE based carrier selection” from the last serving RAN node to the CN, and from CN to the RAN nodes?

| Company | if | how |
| --- | --- | --- |
| Huawei | YES | via inter-node RRC container, e.g. RRC UERadioPagingInformation-NB or UEPagingCoverageInformation-NB |

For RAN2 option2, there seems a need to provide the configured carrier to the RAN node in CN Paging, and there are different views on how to propagate the information from the last serving RAN node to the CN, and from CN to the RAN nodes.

Question 4: in case option 2 is adopted by RAN2, if and how to propagate the information about “configured carrier” from the last serving RAN node to the CN, and from CN to the RAN nodes?

| Company | if | how |
| --- | --- | --- |
| Huawei | YES | via inter-node RRC container, e.g. UEPagingCoverageInformation-NB |

### Potential RAN3 solutions

In R3-211917, there is a RAN3 solution mentioned, i.e. discuss whether it is needed to provide information from CN (based on subscription data, or NAS coordination between UE and CN) to RAN about whether the UE’s coverage level will not change or not, i.e. for some UEs (like bicycles) always in good coverage, some UEs (deployed in basement) always in bad coverage, then the eNB may take it into account for paging carrier selection.

Question 5: do you see the need to provide any other assistance information (besides the ones in the UE Differentiation Information) from CN to RAN to assist paging carrier selection?

| Company | Comment |
| --- | --- |
| Huawei | May be helpful, e.g. constant coverage level to indicate that the UE is always in good/bad coverage. |

## Other aspects of this WI

There is one paper submitted by the WI rapporteur in R3-211919 [7], provides the analyses of all the other objectives of this WI, concludes that except the Paging Carrier Selection, so far there is no other RAN3 impacts foreseen from the other objectives of the WI.

Question: do you agree that, except the Paging Carrier Selection, so far there is no other RAN3 impacts foreseen from the other objectives of the WI.

| Company | Comment |
| --- | --- |
| Huawei | Agree |

## Any other things to be discussed?

To be added.

| Company | Comment |
| --- | --- |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-211588	Discussion on Carrier Selection and Carrier Specific Configuration	ZTE	discussion

R3-211589	36.413 (Rel-17) Introduction of CEL based paging carrier selection for Option 1	ZTE	CR

R3-211590	36.413 (Rel-17) Introduction of paging carrier information for Option 2	ZTE	CR

R3-211649	Support of Carrier Selection based on coverage level	Nokia, Nokia Shanghai Bell	discussion

R3-211650	Support of Carrier Selection based on coverage level	Nokia, Nokia Shanghai Bell	CR

R3-211917	Consideration on NB-IoT Carrier Selection	Huawei	discussion

R3-211918	Support of Additional enhancements for NB-IoT and LTE-MTC	Huawei	CR

R3-211919	Consideration on Rel-17 enhancements for NB-IoT and LTE-MTC	Huawei	discussion

R3-212355	Discussion on NB-IoT paging carrier selection	Ericsson	discussion

R3-212715	Response paper to R3-211588, R3-211590, R3-211650, R3-211918 	Ericsson Telecomunicazioni SpA	response

R3-212674	CB: # 1102_IOT_Main - Summary of email discussion	Huawei - moderator	discussion