3GPP TSG-RAN WG3 #112-e	R3-212674

Online, 17 – 28 May, 2021

Agenda Item:	12.3

Source:	Huawei (moderator)

Title:	Summary of Offline Discussion on IOT_Main

Document for:	Approval

# Introduction

CB: # 1102_IOT_Main

-  Irrespective of the options for UE to select paging carrier discussed in RAN2, can we assume container-based or IE-based approach for S1?

- If there is no agreement on either approach, we can still discuss the technical details of the CRs provided to the meeting without any indication of their endorsement

- Start with summary of offline, proceed to CRs are if there is consensus

(HW - moderator)

Summary of offline disc R3-212674

# For the Chairman’s Notes

//to be added

# Discussion

## Carrier Selection

### RAN3 impacts of the two RAN2 options

From the submitted papers, it is found that many companies mentioned both EPC and 5GC cases, it is needed first to clarify the supported scenarios.

Question 1: do you agree to discuss Carrier Selection in both EPC and 5GC scenarios?

| Company | Comment |
| --- | --- |
| Huawei | Yes, NB-IoT connecting to 5GC is supported since Rel-16, 36.331 is also updated to support NB-IoT connecting to 5GC, it is assumed that by default the Rel-17 discussion support both EPC and 5GC cases. |
| ZTE | Same opinion as Huawei. |
| Ericsson | The WID scope in RP-201306 is only about EPS. We need to wait for a WID update from RAN, if the scenario for connected to 5GC should also be considered. |

To support CE based carrier selection, there are two options from RAN2:

    - Option 1: UE selects a paging carrier based on a rule configured by the network

    - Option 2: NW configures a specific paging carrier

Question 2: whether RAN3 needs to wait for RAN2 further progress to discuss their options?

| Company | Comment |
| --- | --- |
| Huawei | Yes, better to further proceed after RAN2 progress |
| ZTE | Yes, this mainly impacts on RAN2 specification, and is discussing in RAN2, RAN3 should wait for the RAN2 conclusion. |
| Ericsson | RAN2 discussed these two options two meetings ago, and in April meeting no agreement was made. As we have explained in our response paper [10], it’s too early to start assessing any RAN3 impacts. Agree with ZTE that this discussion is mainly RAN2 scope. |

For RAN2 option 1, there seems a need to inform the RAN node about whether the UE is using the CE based carrier selection in CN Paging, and there are different views on how to propagate the information from the last serving RAN node to the CN, and from CN to the RAN nodes.

Question 3: in case option 1 is adopted by RAN2, if and how to propagate the information about “whether the UE is using the CE based carrier selection” from the last serving RAN node to the CN, and from CN to the RAN nodes?

| Company | if | how |
| --- | --- | --- |
| Huawei | YES | via inter-node RRC container, e.g. RRC UERadioPagingInformation-NB or UEPagingCoverageInformation-NB |
| ZTE | Yes | We prefer to explicitly add Coverage Enhancement Level based paging carrier selection indication in Cell Identifier and Coverage Enhancement Level IE. Because RRC container UEPagingCoverageInformation corresponds the RAN3 Coverage Enhancement Level IE, and RRC container UERadioPagingInformation corresponds the RAN3 UE Radio Capability for Paging IE, both Coverage Enhancement Level IE and UE Radio Capability for Paging IE are not suitable to indicate the Coverage Enhancement Level based paging carrier selection. |
| Ericsson | - | Wait for RAN2 |

For RAN2 option2, there seems a need to provide the configured carrier to the RAN node in CN Paging, and there are different views on how to propagate the information from the last serving RAN node to the CN, and from CN to the RAN nodes.

Question 4: in case option 2 is adopted by RAN2, if and how to propagate the information about “configured carrier” from the last serving RAN node to the CN, and from CN to the RAN nodes?

| Company | if | how |
| --- | --- | --- |
| Huawei | YES | via inter-node RRC container, e.g. UEPagingCoverageInformation-NB |
| ZTE | YES | We prefer to explicitly define a new Paging Carrier Information RRC Container and add the container to the UE CONTEXT RELEASE COMPLETE, UE CONTEXT SUSPEND REQUEST, and PAGING message. Because RRC container UEPagingCoverageInformation corresponds the RAN3 Coverage Enhancement Level IE, the Coverage Enhancement Level IE is not suitable to carrythe paging carrier information. |
| Ericsson | - | Wait for RAN2 |

### Potential RAN3 solutions

In R3-211917, there is a RAN3 solution mentioned, i.e. discuss whether it is needed to provide information from CN (based on subscription data, or NAS coordination between UE and CN) to RAN about whether the UE’s coverage level will not change or not, i.e. for some UEs (like bicycles) always in good coverage, some UEs (deployed in basement) always in bad coverage, then the eNB may take it into account for paging carrier selection.

Question 5: do you see the need to provide any other assistance information (besides the ones in the UE Differentiation Information) from CN to RAN to assist paging carrier selection?

| Company | Comment |
| --- | --- |
| Huawei | May be helpful, e.g. constant coverage level to indicate that the UE is always in good/bad coverage. |
| ZTE | It depends on RAN2 solution, e.g. whether it is suitable for mobility UEs. So, we suggest to wait for the RAN2 conclusion. |
| Ericsson | We do not acknowledge this optimization. Subscription data, including e.g. traffic profiles, is already part of the UE context in RAN. |

## Other aspects of this WI

There is one paper submitted by the WI rapporteur in R3-211919 [7], provides the analyses of all the other objectives of this WI, concludes that except the Paging Carrier Selection, so far there is no other RAN3 impacts foreseen from the other objectives of the WI.

Question: do you agree that, except the Paging Carrier Selection, so far there is no other RAN3 impacts foreseen from the other objectives of the WI.

| Company | Comment |
| --- | --- |
| Huawei | Agree |
| ZTE | Agree. |
| Ericsson | There could be unforeseen issues that may appear and affect RAN3 later. |

## Any other things to be discussed?

To be added.

| Company | Comment |
| --- | --- |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-211588	Discussion on Carrier Selection and Carrier Specific Configuration	ZTE	discussion

R3-211589	36.413 (Rel-17) Introduction of CEL based paging carrier selection for Option 1	ZTE	CR

R3-211590	36.413 (Rel-17) Introduction of paging carrier information for Option 2	ZTE	CR

R3-211649	Support of Carrier Selection based on coverage level	Nokia, Nokia Shanghai Bell	discussion

R3-211650	Support of Carrier Selection based on coverage level	Nokia, Nokia Shanghai Bell	CR

R3-211917	Consideration on NB-IoT Carrier Selection	Huawei	discussion

R3-211918	Support of Additional enhancements for NB-IoT and LTE-MTC	Huawei	CR

R3-211919	Consideration on Rel-17 enhancements for NB-IoT and LTE-MTC	Huawei	discussion

R3-212355	Discussion on NB-IoT paging carrier selection	Ericsson	discussion

R3-212715	Response paper to R3-211588, R3-211590, R3-211650, R3-211918 	Ericsson Telecomunicazioni SpA	response

R3-212674	CB: # 1102_IOT_Main - Summary of email discussion	Huawei - moderator	discussion