3GPP TSG-RAN WG3 #112-e	R3-212747

Online, 17th - 27th May 2021

Agenda Item:	9.3.8

Source:	Qualcomm (moderator)

Title:	CB: # 115_InterMNresumeNoMNchg - Summary of email discussion

Document for:	Approval

# Introduction

CB: # 115_InterMNresumeNoMNchg

- confirm that it’s supported by RAN2?

- if so, is anything needed in RAN3 signaling?

- if so, consensus to have this in Rel-17? WI?

(QC - moderator)

# For the Chairman’s Notes (to be updated)

…

# Discussion

## Background

MN and SN have different coverage. So, when MN changes, SN may not need to be changed. Keeping SN in MN change avoids the signaling and delay of reconfiguring SN.

Inter-MN mobility without SN change has been supported in handover (defined in section 10.7.2 of TS 37.340, as shown below in figure 1), but not supported in RRC resume.

RRC resume with SCG (as shown in figure 2) has been defined in R16 as part of DCCA enhancement WID.

Figure 1: Inter-MN handover with/without MN initiated SN change procedure

Figure 2: SCG Restore in RRC resume

## Inter-MN resume without SN change

Paper [1] shows following example message flow to support inter-MN resume without SN change. The required RAN2 signaling enhancements have been defined in R16 DCCA enhancement WID. The gap to support this feature is in RAN3, i.e. transfer SN information in Retrieve UE Context procedure.

Figure 3: Inter-MN resume without SN change

In RRC Resume, gNB can reconfigure SCG or indicate UE to restore SCG.

RRCResume-v1610-IEs ::=             SEQUENCE {

idleModeMeasurementReq-r16          ENUMERATED {true}                                               OPTIONAL, -- Need N

restoreMCG-SCells-r16               ENUMERATED {true}                                               OPTIONAL, -- Need N

restoreSCG-r16                      ENUMERATED {true}                                               OPTIONAL, -- Need N

mrdc-SecondaryCellGroup-r16         CHOICE {

nr-SCG-r16                          OCTET STRING (CONTAINING RRCReconfiguration),

eutra-SCG-r16                       OCTET STRING

}                                                                                                   OPTIONAL, -- Cond RestoreSCG

needForGapsConfigNR-r16             SetupRelease {NeedForGapsConfigNR-r16}                          OPTIONAL, -- Need M

nonCriticalExtension                SEQUENCE{}                                                      OPTIONAL

}

In RRC Resume Complete message, UE sends scg-Response to the network to confirm the SCG configuration.

RRCResumeComplete-v1610-IEs ::=         SEQUENCE {

idleMeasAvailable-r16                   ENUMERATED {true}                                                       OPTIONAL,

measResultIdleEUTRA-r16                 MeasResultIdleEUTRA-r16                                                 OPTIONAL,

measResultIdleNR-r16                    MeasResultIdleNR-r16                                                    OPTIONAL,

scg-Response-r16                        CHOICE {

nr-SCG-Response                         OCTET STRING (CONTAINING RRCReconfigurationComplete),

eutra-SCG-Response                      OCTET STRING

}                                                                                                               OPTIONAL,

ue-MeasurementsAvailable-r16            UE-MeasurementsAvailable-r16                                            OPTIONAL,

mobilityHistoryAvail-r16                ENUMERATED {true}                                                       OPTIONAL,

mobilityState-r16                       ENUMERATED {normal, medium, high, spare}                                OPTIONAL,

needForGapsInfoNR-r16                   NeedForGapsInfoNR-r16                                                   OPTIONAL,

nonCriticalExtension                    RRCResumeComplete-v1640-IEs                                             OPTIONAL

}

Up to implementation, MN can decide SCG restore in Msg4 without UE measurement report, as shown in figure 2. In case MN decision in Msg4 (RRCResume) is not appropriate, the UE would know in the following SCG RACH procedure and gNB would know from Msg5 (RRCResumeComplete).

R16 DCCA enhancement WID also defined early measurement, which enables UE to report the measurement result early in Msg5. The MN can also tune its early decision based on the measurement result.

Observation 1: RAN2 has defined RRC signing for gNB to keep SCG in RRC resume.

Observation 2: RAN2 has defined mechanism for gNB to make decision on keeping SCG in RRC resume.

Question 1: do you see any gap in RAN2 spec to support inter-MN resume without SN change?

| Company | Yes/no | Comment |
| --- | --- | --- |
| Qualcomm | No |  |
| Huawei | No |  |
| Nokia | ? | Can’t verify this yet. But I assume there is no gap. Nonetheless, it does not mean RAN3 must support it in the same release, too. |

In RAN3, to support inter-MN resume with SN, the new MN needs to know the SN information from old MN, e.g. by Retrieved UE context procedure as proposed in [1]:

Proposal 2: Add “UE Context Reference at the S-NG-RAN node” (with SN node ID and SN XnAP UE ID, as defined in Handover Request) into Retrieve UE Context Response message.

If we take inter-MN handover without SN change procedure as example, target MN tells source MN to keep SN UE context and the accepted DRBs, PDU sessions, as proposed in [1]:

Proposal 3: Define new XnAP message “Retrieve UE Context Confirm” to carry following IEs equivalent to Handover Request Acknowledge

- SN UE Context Kept Indicator

- DRBs transferred to MN

- PDU Session Resources Admitted List.

Question 2: do you agree with proposal 2 and 3 on Retrieve UE Context procedure enhancement to support inter-MN resume without SN change?

| Company | Yes/no | Comment |
| --- | --- | --- |
| Qualcomm | Yes |  |
| Huawei | Yes | In general, Proposal 2 and 3 are OK. We think that the message name of “Retrieve UE Context Confirm” and the IEs in this message may need further check. Anyway, detailed can be discussed in TEI17. |
| Nokia | Yes | Such message may be needed – the question is, is it a “mistake” in Rel.16, or should it be added in Rel.17 (TEI17)? We’d prefer the latter. |

Question 3: do you see any other issue/gap to support this feature?

| Company | Yes/no | Comment |
| --- | --- | --- |
| Qualcomm | No |  |
| Huawei |  | Need further check |

## RRC reestablishment in different MN

The enhancement for Retrieve UE Context procedure is also useful for RRC reestablishment in different MN. If the new MN knows the SN information, it may reconfigure the same SN to the UE in RRCReconfiguration after RRCReestablishment.

Question 4: do you agree the enhancement to Retrieve UE Context procedure also benefits RRC reestablishment in different MN?

| Company | Yes/no | Comment |
| --- | --- | --- |
| Qualcomm | Yes |  |
| Huawei | yes | Agree to study whether this can be also applied to RRC reestablishment case further. |
| Nokia | Yes (likely) | Hard to comment ad-hoc, but likely yes. Requires further discussion. |

## Time plan

Based on above analysis, we can discuss when and how to support this feature.

Question 5: do you agree to support inter-MN resume without SN change? If yes, when & how do you prefer?

- TEI-16

- TEI-17

- New work item.

| Company | Yes/no | Comment |
| --- | --- | --- |
| Qualcomm | Yes | A is preferred, so that R16+ UE can enjoy the benefit of this feature early. B is also fine. |
| Huawei | yes | TEI17 is our preference considering the work load of this meeting. |
| Nokia | Yes | TEI17 |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-211747 Inter MN resume without SN change (Qualcomm Incorporated, China Telecom, T-Mobile USA), discussion

R3-211748 Inter MN resume without SN change (CR to 38.423) (Qualcomm Incorporated, China Telecom, T-Mobile USA), CR0596r, TS 38.423 v16.5.0, Rel-16, Cat. B