3GPP TSG-RAN WG3 #112-e	DRAFT R3-212659

Online, 1-11 June 2020

Agenda Item:	10.2.1.3

Source:	InterDigital (moderator)

Title:	Summary of Offline Discussion on CB: # 1203_SONMDT_SuccessHO

Document for:	Approval

# Introduction

CB: # 1203_SONMDT_SuccessHO

- Topics to discuss:

- XnAP, NGAP and F1AP impacts of SHR, including which messages to use, which information to include and how to encode it

- Any other topics based on contributions submitted

- Start with summary of offline, proceed to TPs if there is consensus

(ID - moderator)

Summary of offline disc R3-212659

The current agreements and chair notes on this topic are:

Define “Successful HO Report” as RRC container in XnAP

Xn Signaling to transmit Successful HO Report from the target to the source: ACCESS AND MOBILITY INDICATION message

NG Signaling to transmit Successful HO Report from the target to the source: UPLINK RAN CONFIGURATION TRANSFER and DOWNLINK RAN CONFIGURATION TRANSFER

F1 Signaling to transmit Successful Report from CU to DU: ACCESS AND MOBILITY INDICATION

We do not consider new successful handover scenarios: too early success handover, too late success handover and success handover to wrong cell in this release

“Successful HO Report” is defined as a list

RAN3 considers a UE Identifier (e.g. AP ID) for SHR in F1AP beneficial if there is no RAN2/RRC UE identifier inside the SHR; RAN3 needs to wait RAN2 progress before final decision.

FFS whether to introduce UP information in the SHR for DAPS optimization, RAN3 should confirm the progress of MRO for DAPS before further study and the detailed content in the SHR should be collaborated with RAN2.

FFS whether to study the information of SHR which can optimize the selection of candidate target cells in CHO.

To be continued...

The discussion covers the below documents:

| R3-211856 | Discussion on successful handover report (CATT) | discussion |
| --- | --- | --- |
| R3-212130 | Inter-RAT Successful Handover Report (ZTE) | discussion |
| R3-212131 | (TP for SON BL CR for TS 38.413) Successful Handover support (ZTE) | other |
| R3-212132 | (TP for SON BL CR for TS 38.423) Successful Handover support (ZTE) | other |
| R3-212133 | (TP for SON BL CR for TS 38.473) Successful Handover support (ZTE) | other |
| R3-212250 | Successful Handover Report for CHO and DAPS (Ericsson) | discussion |
| R3-212268 | Improving RAN visibility over CHO and DAPS procedures via SHR and RLF reports (InterDigital) | discussion |

As suggested by the vice chair, this discussion will proceed by first looking at the proposed enhancements to the baseline for SHO and trying to get consensus, and then as a second part look at endorsing TPs based on the consensus if possible.

# For the Chairman’s Notes

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

R3-20xxxd rev [in xxxh] – agreed

R3-20xxxe rev [in xxxi] – agreed

R3-20xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion

## Near Failures

In R3-R3-211856 Discussion on successful handover report, CATT makes proposals on handling near failures with the following 3 proposals:

Proposal 1: It is proposed source cell to send XNAP/NGAP message to previous handover source cell in case the near-failure is caused by the previous handover.

Proposal 2: It is proposed to introduce a message similar to HO Report or reuse HO Report for the message in P1.

Proposal 3: It is proposed to introduce a T310 report timer similar to UE reported timer to detect failure type.

What are your positions on these 3 proposals?

| Company | Comment |
| --- | --- |
| Qualcomm | If I understand the scenario correctly, this is the sequence of steps: Successful Handover from A -> B Bad radio link condition at B (T310 running) immediately upon HO Successful HO from B->C before RLF at B Successful HO Report is NOT sent from B->A as there were no PHY layer issues in A before handover. Neither is a Handover Report sent from B->A as there was no RLF. Successful HO Report is sent from C -> B with T310 running indication. It is proposed to send a Report from C->A indicating this near RLF at B. We are not sure what A can do to optimize with the knowledge that there was near RLF at B. If the intention is to avoid a “potential” wrong cell HO to B, we think the existing MRO detection for wrong cell HO in failure cases should suffice. |
| Nokia | We are not sure about the purpose of informing the A about the “near-RLF”. If the A>B HO was successful and B managed to execute a HO to C before RLF, there does not seem to be an issue to correct, right? |

## Inter-RAT

In R3-212130 Inter-RAT Successful Handover Report, ZTE proposes: in order to support inter-RAT SHR, to define a Choice IE type of“Successful HO Report”in XnAP, NGAP and F1AP.for both NR and LTE. Examples of the possible TPs are in R3-212131, R3-212132, R3-212133.

What are your positions on supporting inter-RAT SHR in this way?

| Company | Comment |
| --- | --- |
| Qualcomm | Not needed. Successful HO report is a new SON report introduced in NR and are not to be introduced in LTE. Therefore, we need not consider inter-RAT successful HO report |
| Nokia | Can be considered only later, once intra-NR reporting is defined. |

## UP Information to improve DAPS

In R3-212250 Ericsson suggests that source and target node (starting with the source node) would benefit from knowing the interruption time, the number of lost packets, or the number of duplications due to packet forwarding. As this information can only be retrieved from the UPF, they propose to create an LS to RAN2.

What are your positions on this proposal to liase RAN2?

| Company | Comment |
| --- | --- |
| Qualcomm | Interruption time might be useful. However, this might be already known via the new timers RAN2 introduce for MRO of DAPS HO. Other information seems to be low value. Maybe this can be discussed in RAN2 directly? |
| Nokia | We’re fine to let RAN2 know such UP measurements would be of interest. However, it has to be left up to RAN2 to decide if such reporting is feasible and reasonable. |

## Candidate cell improvements

In R3-212250 Ericsson and in R3-212268 InterDigital both suggest the use of SHR to optimize the number and which cells to prepare for CHO. The Ericsson paper had 3 related proposals:

Proposal 2: Include UP information for CHO and best cell(s) measurements in the SHR as a means to optimize CHO usage.

Proposal 3: RAN3 to study the optimization of the number of prepared cells.

Proposal 4: RAN3 to study methods to optimize early and late data forwarding.

What are your positions on these proposals?

| Company | Comment |
| --- | --- |
| Qualcomm | P2: Not clear on what is meant by UP information for CHO. RAN2 is already discussing whether to include best cell measurements in addition to candidate cell measurements. Can leave it to RAN2 decision. P3: This is related to measurements in P2; can be studied further P4: Maybe deprioritize this? |
| Nokia | P2: CHO was not meant to address UP issues (DAPS HO was defined for this), so addressing UP in case of CHO may not be necessary. P3 and P4: Yes, this may be interesting, but surely the decision would need to be based on actual solution proposals. |

## Any other comments

Are there any other topics/comments in this area?

| Company | Comment |
| --- | --- |

# Conclusion, Recommendations [if needed]

# References