3GPP TSG-RAN WG3 #112-e	R3-212664

Online, 17 – 28 May, 2021

Agenda Item:	x.y

Source:	Huawei (moderator)

Title:	Summary_of_CB # 1208_SONMDT_CCO

Document for:	Approval

# Introduction

CB: # 1208_SONMDT_CCO

-  Topics to discuss:

- CU(-CP?) detects CCO issues?

- What information is provided from CU to DU to fix the detected issue? CU sends either no suggested configuration, one set of configurations or multiple sets of suggested configurations? Type of CCO issue?

- DU informs the CU of the carried changes?

- alternative coverage configurations at a cell level and beam level?

- Coverage state and other information exchange in XnAP?

- Any other issue based on contributions submitted

- Start with summary of offline, proceed to TPs if there are agreements

(HW - moderator)

Summary of offline disc R3-212664

The discussion is structured in two phases, one before the online sessions and one after. The deadline for the first phase is Thursday 16:00 UTC

# For the Chairman’s Notes

Temporary results after 1st round

The current status of the discussions is that the situation is very much the same as the last meeting. There is no consensus on either options. There seems to be some support for the following two options;

- gNB DU decides what coverage configuration to choose based on assistance information from gNB-CU describing the issues identified and cells involved

- gNB DU decides what coverage configuration to choose based on assistance information from gNB-CU describing the issues identified and cells involved and (optionally) indicating preferred coverage configurations

But before forcing any conclusion, the moderator proposes to go one more round and discuss the following statements based on the feedback received so far and trying to harmonize the discussion.

The proposal for the online session is therefore to quickly discuss whether the following statements can be used as further basis for the discussion and identifying if there are any FFS that needs to be discussed in detail.

Ericsson: a general remark is that the description in the bullets below is very much centred around an OAM based solution, where, by means of OAM, gNB-CU becomes aware of the coverage configurations and perhaps RF/L1 capabilities of the gNB-DU. This is not the basis on which Solution a) above is developed. Solution a) is a RAN centric solution, where the gNB-CU highlights to gNB-DU a possible coverage and capacity problem, which is identified e.g. by means of L3 measurements, or by means of mobility failure monitoring, or by means of RACH Reports and Successfuyl HO reports monitoring. The gNB-CU can also identify the cell(s) involved with the issue. The gNB-CU can provide such assistance information to the gNB-DU (cells involved, type of problem) to the gNB-DU. The gNB-DU, on the basis of its own measurements at L1 and on the basis of learning from previous events, should pick a suitable coverage configuration.

Deutsche Telekom: We share the same views as Ericsson to the different bullet points listed by the moderator (except of the one on AI usage; more discussion is needed on details before setting a clear statement w.r.t. requirements on standardization for that).

- CCO is aiming at enabling coverage modifications by exchanging coverage configurations between nodes. One usage of the exchanged coverage configuration between nodes is to reduce the impact on MRO, since coverage modifications in neighbor node will impact the mobility decisions.

Ericsson: CCO is a function that improves mobility robustness, but also that improves network capacity (as the name says). In the past we have captured CCO as a feature improving mobility robustness and we said that coverage state indicators “may be used at the receiving eNB to adjust the functions of the Mobility Robustness Optimisation, e.g. by using the indicator to retrieve a previously stored Mobility Robustness Optimisation state”, but please note that this is one possible application of CCO. CCO should not be limited to MRO.

- The mapping from a set of allowed coverage configurations to corresponding lower layer resources (e.g RF, L1) are sent from OAM to the gNB (aggregated) and gNB-DU (disaggregated) and only these nodes knows the current resource situation of these lower layer resources

Ericsson: this statement is correct if “coverage configuration” here means the Cell Coverage State IE. Note that the specification of Cell Coverage State mapping to L1 parameters is rather course. Certainly if the same wanted to be achieved with NR a ot more details would dbe needed to achieve exact beam shaping etc. Whether this configuration is feasible it remains to be seen, as it might require configuration of beam-related parameters, which are sensitive information so far avoided by configuration.

- A second usage of CCO is to use the coordination between nodes to avoid creating coverage holes between cells from different nodes when changing coverage in one node by compensating in the other node.

Ericsson: Yes, and this is part of mobility robustness. If changes of coverage in one cell imply, e.g. leaving a coverage hole, then actions in neighbouring cells to compensate for that need to be taken otherwise mobility is not “robust”. Furthermore, this is part of the “Capacity Optimisation”, i.e. ensuring that cells have the right overlap and shape to optimally serve traffic.

- When trying to compensate for changes in node1 by modifying coverage in node2, there is no guarantee that node2 is able to compensate for an action in node1 due to e.g. resource limitations in node2. Whether this ability to compensate coverage holes between nodes is supported or not is up to the operator to decide and is configured by OAM

Ericsson: OAM configuration is one, perhaps obsolete, way of achieving coverage coordination between neighbour cells. Note that an OAM based approach cannot be dynamic (OAM is less reactive to changes in coverage due to environment (e.g. weather, obstacles)) and that this approach is questionable in multi vendor and RAN sharing. The approach that a 5G network should be able to support is RAN centric, where the RAN learns about neighbor cell coverage (e.g. via UE measurements) and adapts its coverage to that. The use of AI may greatly help in that. Note that the use of AI in this case does not necessarily require standardisation.

- If compensation between nodes are to be supported, OAM would need to configure, in addition to the coverage configurations (as described above) a set of suitable configurations combinations spanning configurations in each node and in neighbor nodes. This additional configuration would only contain suitable combinations of coverage configurations in each node and does not include the mapping to lower layer resources.

Ericsson: We think this is not how a 5G network should work. We are trying to improve 5G with respect to previous networks and make everything depend on manual OAM configurations carries a big burden on efficiency and cost of operation. Besides, as said above, a totally OAM based solution may not even be feasible form a standard point of view.

- If compensation between nodes are performed in the aggregated case, the involved nodes would perform this in a de-centralized manner based on the suitable configurations combinations and received information of coverage changes in neighbor nodes.

Ericsson: As explained, the nodes do not need necessarily to have a static and preconfigured set of “suitable configurations combinations”. Nodes can learn and select the optimal coverage configuration depending on their environment.

- If compensation between nodes are performed in the disaggregated case there are two options:

  - Centralized: where gNB-CU would could propose changes one or more gNB-DUs based on the suitable configurations combinations configured to the gNB-CU and the information on changes performed in neighbour gNB-DUs/gNBs . The final decision is up to gNB-DU, based on e.g. resource availability

Ericsson: We do not think this is the way it should work. gNB-CU should highlight a possible coverage and capacity problem, which is identified e.g. by means of L3 measurements, or by means of mobility failure monitoring, or by means of RACH Reports and Successfuyl HO reports monitoring. The gNB-CU can also identify the cell(s) involved with the issue. The gNB-CU can provide such assistance information to the gNB-DU (cells involved, type of problem) to the gNB-DU. The gNB-DU, on the basis of its own measurements at L1 and on the basis of learning from previous events, should pick a suitable coverage configuration.

  - De-centralized: where the gNB-DU would adjust based on suitable configurations combinations configured to the gNB-DU and the information on changes performed in neighbour gNB-DUs/gNBs.

Ericsson: again, we do not see the need of such static and configuration centric “suitable configurations combinations”. This can be done as a matter of implementation, but we should not develop the standard on the basis of that.

[to be done later]

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

R3-20xxxd rev [in xxxh] – agreed

R3-20xxxe rev [in xxxi] – agreed

R3-20xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Background

In CCO we have the following agreements and FFS

E-UTRAN CCO function should be considered as baseline for NG-RAN CCO solution for dynamic coverage changes with an index-based solution for coverage switching among deployment options

In NG-RAN scenario, a NG-RAN node may send to a neighbor NG-RAN node a coverage modification list which includes deployment related information concerning the serving cells

Exchange at least NG-RAN CGI, Cell Coverage State, Cell Deployment Status Indicator, Cell Replacing Info in NG-RAN NODE CONFIGURATION UPDATE message over Xn for coverage modification

DU signals to CU coverage related configuration information. Whether to include SSB beam information (on top of cell info) is FFS.

CSI-RS based beam coverage tuning is an optimization and is not covered as part of NR CCO for Rel-17

Open issues:

- FFS whether CCO over Xn is signaled as separate per cell state information and SSB state information or whether each cell state reflect a specific SSB configuration

- FFS who decides that a coverage modification is needed: gNB-DU or gNB-CU

- FFS who decides how to modify the coverage: gNB-DU or gNB-CU

# Round 1

## Issue 1 Functional split

Among the remaining FFS, the last two seems most important to resolve so it is proposed to start the discussion based on these. It should also be noted that we were not able to progress on this issue in last meeting.

Different flavors are described in the incoming papers.

- Option 1) One set of papers [R3-211691, R3-212125, R3-212261, R3-212585] suggest that the gNB-DU selects how to correct and gNB-CU does not give any recommended configurations.

  - Ericsson Comment: at least a number of papers proposes that the gNB-CU signals to the gNB-DU assistance information such as the type of problem and the cells involved. Hence, in this option, the gNB-CU is able to “influence” the actions of the gNB-DU

  - Option 1a) gNB-CU indicate the coverage problem to the gNB-DU, gNB-DU decides how to update it’s configurations.

- Option2) One set of papers [R3-212209, R3-212327] suggests that gNB-CU gives different configuration modifications to gNB-DU but gNB-DU decides which one to apply.

The reason this issue turned out to be difficult to agree can shortly be summarized as follows: The gNB-CU could trigger centralized decisions involving multiple gNB-DUs but the gNB-CU will not have detailed knowledge about the resource situation in gNB-DU.

Ericsson’s comment: there are more issues to add. Namely, gNB-CU does not necessarily know the coverage of each cell configuration option and therefore it may not be in a position to recommend a cell configuration change; the gNB-CU does not know the capabilities at RF and L1 of the gNB-DU and therefore it cannot suggest the adoption of a cell configuration state (for example, a cell configuration implying an increase in coverage of an SSB implies knowledge of whether the antenna arrays involved  are in a condition to activate the configuration)

Considering the above, and that the situation was the same at last meeting, it is assumed that it will be difficult to simply select between 1 or 2 in this first phase and the proposal is therefore to at least explore the possibilities for a compromise. But we can anyway start with a show of hands to assess the situation.

Question  4.1-1: which option (1 or 2) do you prefer.

| Company | Comment |
| --- | --- |
| Huawei | We prefer option 2 |
| Qualcomm | Is only option 1 possible based on the current definition of GNBDUFunction IOC in TS 28.541 i.e. it seems only DU is aware of the coverage state (antenna related parameters and beam related information) as highlighted by Observation 3 in our paper R3-212125? Observation 3: Sector carrier related information (DL/UL ARFCN, BW, maxTxPower, maxTxEIRP), antenna related parameters (coverage shape, digital tilt, digital azimuth) and beam related information (beam ID, beam tilt/azimuth, beam horizontal/vertical width etc.) are defined inside the GNBDUFunction InformationObjectClass (IOC) in TS 28.541. If CU has sufficient knowledge of the coverage state parameters, then we are okay with option 2 as CU can act as a SON coordination function and a central coverage coordination entity. Else we might have to go with option 1. |
| Deutsche Telekom | Same view as Qualcomm. CU is responsible for detecting coverage/capacity issues and indicates them to its DUs for resolution. Any recommendation on feasible configurations would require detailed knowledge of DU states at CU. |
| Nokia | We prefer option 2, even though we think that DU should execute if a new TRP beam coverage has been decided for coverage enhancements. Let’s briefly recap what CCO should be about. CCO should ensure coverage provisioning in first priority and can enhance capacity by flexible cell layout densification (and beamformed access with spatial multiplexing among the beams can seen a sort of flexible densification). But compared to LTE, NR distinguishes between SSB beams (being used for coverage and mobility) and CSI-RS beams (being used for capacity known as mMIMO). Therefore, if we consider SSB beams, we can only optimize coverage. The capacity driven background with splitting/merging as in LTE is only useful for CSI-RS. If the optimization is more capacity oriented with mMIMO grid of beam change, decision can be option 1. However, for coverage optimization with beam shaping a central decision is needed without any degree of freedom. Second, CCO as a SON use case will be based on statistical analysis of events like RLFs. A reported RLF has to be analyzed first in terms of its root cause, mobility failure, PCI collision or coverage, which is to be derived from the root cause analysis after RLF report. If and only if there is statistical significance of coverage issue corrections are decided, and these decisions are preferably carried out more centrally, since also for the root cause information from several entities is taken into account and coverage optimization means adaptation of beamforming, i.e. adaptation of the SSB beams, which should be mutual undertaking of the involved TRPs after proper root cause analysis. The instance, which decides is the SON instance, which should be rather central in CU or at OAM. |
| ZTE | Share the view with Qualcomm and DT, Option 1 is preferred. As the gNB-CU has indicated the CCO issue (e.g. coverage issue or capacity issue) to the gNB-DU. The gNB-DU is able to perform the coverage modification based on the L1/L2 measurement. |
| Ericsson | Option 1 as per modifications above First of all, and as added in our comments to the description of Option 1, Option 1 involves also assistance information from the gNB-CU to the gNB-DU by which the gNB-CU can steer the gNB-DU towards a potential problem and towards the cells involved in such issue. We share the understanding from Qualcomm, DT and ZTE. The gNB-DU is the only node in full control of its RF and L1 functions and resources. Hence a decision on coverage modification imposed by the gNB-CU implies full knowledge at the gNB-CU of the RF and L1 implementation at gNB-DU. The latter is clearly not supported in the standard. We would like also to add that, if the gNB-DU is provided with CCO information (e.g. RACH reports, RLF Reports, coverage state of neighbour cells) the gNB-DU can also learn what is the best coverage action to tackle a given CCO issue. This could in the future also connect to AI, where some processes can reside at the gNB-DU. |
| NEC | In our papers R3-211690 and R3-211691, we do not propose that “gNB-CU does not give any recommended configurations.” We propose that “The gNB-CU notifies the gNB-DU of the detected CCO issue (at cell/beam-level), and recommended actions to resolve this issue, using the GNB-CU CONFIGURATION UPDATE message.” In other words gNB-CU could recommend some actions to resolve CCO issue and could provide some supporting information to gNB-DU. gNB-DU has detailed knowledge of its resources and perform actions to resolve the issue indicted by gNB-CU and using recommendations and supporting information provided by gNB-CU. Closer to Option 1 than Option 2, but includes recommendations and supporting information from gNB-CU. |
| Samsung | Option 1a) gNB-CU can detect the coverage problem e.g. based on UE measurement report in RLF Report and indicate the problem to the gNB-DU. It’s the gNB-DU to decide how to make the optimization. The gNB-CU has no information on the coverage related configuration therefore cannot propose any valuable recommendatation. |

Moderator's summary:

- companies prefer option 1

- 2 companies prefer option 2

There is one compromise solution on the table:

- Option 3) In [R3-212209] there is also a proposed compromise that would enable both solutions depending on the configuration of the gNB-CU.

Question 4.1-2: Would a compromise solution, like e.g. option 3 be a possible route for further discussions? Or is the answer "no" - this route impossible, i.e. we need to force a decision on option 1 or 2.

| Company | Comment |
| --- | --- |
| Huawei | Yes |
| Qualcomm | Yes. If we can’t arrive on a consensus in Question 4.1-1, okay to go with this compromise solution. |
| Deutsche Telekom | Yes. But also the compromise requires for 2 of the 3 listed scenarios sufficient knowledge of DU’s coverage state parameters at CU (via OAM or signaling?). |
| Nokia | No. We think that we cannot copy LTE approach to NR, and we have to distinguish between capacity optimization where CSI-RS beams are considered and option 1 is possible, since this optimatization is more short term and follows spatiotemporal varying needs, i.e. is actually more RRM than SON. For coverage optimization, SSB beams are to be adapted or even newly shaped where central instance has to take the controlling task. Then, it would be option 2, without subclause giving DU the freedom to decide. |
| ZTE | Actually we still prefer Option 1, but the compromise solution could be taken into account. |
| Ericsson | The blocking point for this compromise option is that, as commented above, Option 2 implies full awareness of the RF and L1 implementation and status at the gNB-DU. This is not supported and not feasible to assume. We do understand the good will to find a compromise, but Option 2 seems simply not viable given the current RAN architecture. |
| NEC | This could also be a way forward. |
| NEC (Samsung?) | No. Agree the view of Ericsson. |

Moderator's summary:

- 5 companies think a compromise should be investigated

- 3 think we should choose either 1 or 2

Question 4.1-3: If answer to 4.1-2 is yes, are there any proposed changes that makes the compromise proposed in option 3 acceptable?

| Company | Comment |
| --- | --- |

Question 4.1-4: If answer to 4.1-2 is yes, but response to 4.1-3 is no, are there any other proposal for compromised solutions?

| Company | Comment |
| --- | --- |
| NEC | Direction proposed in R3-211690 and R3-211691 is in between Option 1 and Option 2 of Question 4.1-1. gNB-CU detects CCO issue, provides recommended actions and supporting information. gNB-DU takes action to resolve the issue taking into account recommendations and supporting information received from gNB-CU and notifies gNB-CU about taken action. |

# Conclusion, Recommendations [if needed]

[to be done later]

# References