3GPP TSG-RAN WG3 Meeting #112-e	R3-212667

17 - 27 May 2021

Online

Agenda Item:	10.2.5

Source:	Ericsson

Title:	Two-Step RACH Optimization - Summary of offline discussion

Document for:	Discussion and Decision

# 1	Introduction

The scope of the email discussion has been captured as followed:

CB: # 1211_SONMDT_2StepRACH - LS is noted - Topics to discuss: - Takeaways from the LS - timestamp associated with each RA attempt in the reported feedback information - indication of whether back-off was applied after the RA attempt - two alternatives for the coordination of scrambling sequence generation among gNBs - LS to RAN2? - Start with summary of offline, proceed to TPs if there are agreements (E/// - moderator) Summary of offline disc R3-212667

This contribution captures the email discussion.

# 2	For the chairman’s notes

To be captured later

# 3	Email discussion

## 3.1 2-step RA report optimization

Compare to previous meeting, RAN2 agreed some parameters for the RA-report, and started the discussion for some others. The agreements can be found in [1].

But some parameters are not discussed in RAN2 (yet?). Therefore, in [2], it is proposed to add few more parameters to the RA-report. These parameters are not yet discussed in RAN2, and therefore RAN3, as the leading group for SON, can start discussing it. Further work from RAN2 would for sure be needed if RAN3 takes some agreements, and therefore an LS to RAN2 may be sent after this discussion.

These parameters might also be relevant for 4-step RA. Therefore, it is proposed to discuss the relevance of each parameter separately below. Please also comment if you think this parameter is NOT equally applicable for 2-step RA and 4-step RA.

Question 1.1: Include a timestamp associated with each RA attempt in the reported feedback information?

| Company | Response |
| --- | --- |
| Ericsson | Yes. See [2] |
| Huawei | Yes. OK to have |
| Nokia | Not OK. CEF and RLF reports are already time stamped. But, RACH is random and can happen at different time instances (that depend also on the random backoff chosen by the UE). It is unclear what the network can do with detailed timestamp information of a RACH attempt that occurs at random. |
| Qualcomm | No. Requirement on UE to report timestamp associated with each RA attempt is too detailed information and is also probably not useful for RACH optimization. Even if NG-RAN can compute the time between different failed RA attempts using timestamp, NG-RAN can’t optimize RACH behavior at UE directly (certain things are random, e.g. backoff applied) |

Question 1.2: Include an indication of whether backoff was applied after the RA attempt in the feedback information?

| Company | Response |
| --- | --- |
| Ericsson | Yes. See [2] |
| Huawei | Maybe not. In RACH report, the UE has reported the no. of attempts and the contention detected indication. By those, the network may deduce that backoff was applied. |
| Nokia | Not OK. Network can determine if UE has applied backoff in between RA attempts since UE logs in the RA Report the number of RA attempts until a RA is successful. Also, if contention detected is set in the RA Report, then network knows that UE will apply backoff to retransmit next time. |
| Qualcomm | No. Network should know if UE applied backoff or not based on whether NG-RAN included BI field in RAR. Don’t see the value in UE reporting this back. |

## 3.2 Scrambling Sequence Generation Coordination Between gNB

In [3], the coordination of scrambling sequence generation between gNBs is discussed.  And two alternatives are described:

- a gNB has a default scrambling sequence initializing method using the PCI of its NR cells and it only informs its neighbours if it configures a different method

- no default method is considered and a gNB must always indicate the method it uses to initialize the scrambling sequence over its cells.

This was discussed during RAN3#111-e but no conclusion was reached. So, RAN3 needs to first discuss if such coordination is needed.

Question 2.1: Is scrambling Sequence Generation Coordination Between gNBs needed?

| Company | Response |
| --- | --- |
| Ericsson | Not needed. The scrambling sequence generator is computed with 3 coefficients as follows: dataScramblingIdentityPUSCH if configured / msgA-DataScramblingIndex Random access preamble RA-RNTI for MSGA / RNTI associated with PUSCH transmission It is not likely to get any collision due to using different method for the neighbour NR cells (the collision is negligible). The PUSCH resource collision is not likely, and it is very rare according to the formula when there is no preamble collision. If one coefficient is not chosen properly, there will be 2 more coefficients (or at least one coefficient that corresponds to random-access preamble coefficient) to generate different scrambling sequence for the neighbour cells. |
| Huawei | No strong vew. The scenario seems rare. The collision may occur only if two UEs from two neighour cells do RACH on the same PRACH resource with the same preamble, and the nID is configured as its neighbour cell’s PCI. |
| Nokia | nRNTI depends on the 2-step RACH Configuration of the neighbouring cells. If this is the same, then nRNTI will be also the same. nRAPID is just the preamble id (taking integer values in 0...63). It is possible that 2 UEs in different cells choose the same preamble ID. So, in our view this collision scenario is possible unless we coordinate the scrambling sequence between cells. The reason why this problem exists in MSGA PUSCH is that nRNTI used is the RA-RNTI which is derived only based on RACH occasion related parameters, and no UE-specific parameter (C-RNTI). Hence, if RACH Occasion is the same then RA-RNTI between neighbours will be also. On the other hand, in normal PUSCH, nRNTI is one of C-RNTI, MCS-C-RNTI, SP-CSI-RNTI, or CS-RNTI. |
| Qualcomm | No strong view. Same as Huawei. |

If the answer to question 2.1 is yes, please comment the 2 proposed alternatives (or any additional one) and state your preference.

Question 2.2: If Scrambling Sequence Generation Coordination Between gNBs is needed, which alternative(s) described in [3] do you support?

| Company | Response |
| --- | --- |
| Huawei | Exchange the nID over Xn. |
| Nokia | Exchange the used nID over Xn. |

# 4	Conclusion

Result of the email discussion to be captured here

# 5	References

[1] R3-211437 - Reply LS on RACH report for 2-step RACH (RAN2)

[2] R3-212252 - 2-step RACH optimization for SON (Ericsson)

[3] R3-212375 - Scrambling Sequence Generation Coordination Between gNB (Nokia, Nokia Shanghai Bell)