3GPP TSG-RAN WG3 #112-e	R3-212669

Online, 17 – 28 May, 2021

Agenda Item:	16.1

Source:	Huawei (moderator)

Title:	Summary of Offline Discussion on CB: # 1213_SONMDT_MDTEnh

Document for:	Approval

# Introduction

This contribution is to kick off the following discussion.

CB: # 1213_SONMDT_MDTEnh - Topics to discuss: - Claim that NR Frequency Band List is invalid in R16. - Add condition about when is able to select Area Scope of Neighbour Cells. - Introduce the “Report amount” as an optional IE to M4, M5, M6, M7 measurement configurations. - Drop the value “infinity” from the M4, M5, M6 and M7 measurement configurations. - Introduce the “Report amount” as optional IE to M4, M5, M6, M7 measurement configurations. - Propagation of user consent: - LS in is noted - LS out to SA3 - whether Management based MDT PLMN List will be propagated to the target node only if the target PLMN is included in the Management Based MDT PLMN List - AMF resends the Management based MDT PLMN list to the target node after Xn handover in Path Switch Request Ack message? - LS out to SA5 - Any other issue base on contributions submitted - start with summary of offline, proceed to TPs if there are agreements (HW - moderator) Summary of offline disc R3-212669

# For the Chairman’s Notes

# Discussion

### PLMN checking during UE context retrieval

In R3-212012, it is proposed:

Proposal 1: The source node propagates the signaling based MDT configuration if the signaling Based MDT PLMN List is available and contains one of the PLMNs of the target cell, and propagates the management based MDT allowed information if the Management Based MDT PLMN List is available and contains one of the PLMNs of the target cell.

Please provide your view on this.

| Company | Do you agree on the proposal? (Y/N) | Comment |
| --- | --- | --- |
| Qualcomm | Yes | As mentioned in R3-212012, the source node can know the broadcast PLMNs of the new cell (where UE resumes from RRC_INACTIVE) using the Xn Setup Request/Response message and can check if this belongs to the MDT PLMN list. Source node can then forward MDT config only if PLMN check is satisfied. |
| ZTE | Yes | Technicaly reasonable, while the issue is related to stage 2 and relate to OAM, consult RAN2/SA5 ‘s view is necessary. |
| Samsung | Maybe not needed | Wondering why has this proposal. It is already defined in the stage 3. |
| CATT | Maybe not needed | There is already similar text in 37.320: For NR, the MDT configuration received by signalling based trace messages for a specific UE will propagate during intra-PLMN handover, and may propagate during inter-PLMN handover if the Signalling Based MDT PLMN List is available and includes the target PLMN. The management based MDT allowed information propagates during inter-PLMN handover if the Management Based MDT PLMN List is available and includes the target PLMN why has this proposal? |
| Nokia | Yes | We believe this is within RAN3 realm, and can be agreed in RAN3 along the lines proposed. To Samsung: I checked again, but can't find this text included in TS 38.423 for the Retrieve UE Context procedure. |

### Adding missing procedural text for Management Based MDT PLMN List

In R3-212012, it says that the procedural text for the optional IE of Management Based MDT PLMN List in Retrieve UE Context Response message is missing, it is proposed to correct this issue as proposed in the TP.

Proposal 3: To agree on the procedural text for Management Based MDT PLMN List IE in Retrieve UE Context Response message.

Please provide your view on this.

| Company | Do you agree on the proposal? (Y/N) | Comment |
| --- | --- | --- |
| Qualcomm | Yes | Okay to add the procedural text. |
| ZTE | Yes |  |
| Samsung |  | It is related to the question 3.6. It is fine to make procedure text if it is missing for RRC-Inactive in stage 2. But we prefer to consider the conclusion in 3.6. Alignment between stage 2 and stage 3 is needed. We can revisit the procedure text it in second round. |
| CATT | Yes |  |
| Nokia | Yes | Okay to add the procedural text in TS 38.423. |

### Correction to Area scope configuration

In R3-212012, it says that there is misalignment between RAN2 and RAN3 specs on the area scope configuration. And the following options are listed to fix this issue:

- Send a LS to RAN2 to correct TS 38.331 which leads to a Rel-16 non-backward compatible change on Uu interface.

- Restrict the Area Scope of Neighbour Cells to be configured if the Area Scope of MDT is not PLMN wide in Rel-16 and later releases.

- Restrict the Area Scope of Neighbour Cells to be configured if the Area Scope of MDT is not PLMN wide only in Rel-16 and send a LS to RAN2 to correct TS 38.331 in Rel-17.

Please comment that which option is your preference?

| Company | Which option is your preference? | Comment |
| --- | --- | --- |
| Qualcomm | Option 2 | Option 2 is the simplest as it doesn’t affect RAN2 (ASN.1) and can be solved via NG-RAN implementation (i.e. ignore Area Scope of neighbor cells if Area Scope of MDT is PLMN wide). |
| ZTE |  | OAM can be informed to do the limitation. |
| Samsung |  | Agree with ZTE, those configurations are from OAM. OAM should ensure there is no collision between two IEs. |
| CATT |  | Agree OAM to make limitation |
| Nokia |  | According to R3-212012, the Area Scope of Neighbour Cells can't be configured in case of PLMN-wide area scope, because in TS 38.331, the areaConfiguration-r16 is optional, and the interFreqTargetList-r16 is encoded inside the areaConfiguration-r16. The problem is therefore under RAN2's responsibility, and only RAN2 can confirm the best way forward. We would be fine to send an LS to RAN2, who could decide whether action can be taken on their side or whether a network signalling work-around is preferable. |

### Correction to Frequency band info

In R3-212012, it says that there is misalignment between RAN2 and RAN3 specs on NR Frequency Info in Area Scope of Neighbor Cells IE.

Therefore, the NR Frequency Band configuration in the Area Scope of Neighbor Cells IE should be removed to align to RAN2 specification. Since this IE is mandatory, a backward compatible way is to specify to ignore the IE when received in the semantics description part.

Proposal 5: the NR Frequency Band List IE in NR Frequency Info IE in the Area Scope of Neighbour Cells IE shall be ignored if received.

Please provide your view on this.

| Company | Do you agree on the proposal? (Y/N) | Comment |
| --- | --- | --- |
| Qualcomm | Yes | Okay with Proposal 5 |
| ZTE | Yes |  |
| Samsung | Yes |  |
| CATT | Yes |  |
| Nokia | No | According to R3-212012, in TS 38.331, the NR Frequency Band configuration is missing in the InterFreqTargetInfo configured to the UE. Similar to the question above, the problem is therefore under RAN2's responsibility, and only RAN2 can confirm the best way forward. We would be fine to send an LS to RAN2, who could decide whether action can be taken on their side or whether a network signalling work-around is preferable. |

### Introduction of the Report Amount to M4, M5, M6, M7

In R3-212264， it is proposed to introduce the “Report amount” as an optional IE to M4, M5, M6, M7 measurement configurations.

Please provide your view on this.

| Company | Do you agree on the proposal? (Y/N) | Comment |
| --- | --- | --- |
| Qualcomm | Probably No | Although the intention is useful (provides flexibility in the number of samples to perform MDT measurements), this can be achieved indirectly via varying “Collection Period”. Also, this would need coordination with SA5 to provide the proposed “Report Amount” in MDT configuration from OAM. Also, D1 delay measurement as part of M6 involves UE and would then need NG-RAN to signal “Report Amount” to UE to be consistent with other parts of M6 measurement. |
| ZTE | Probably yes | Howerver, consult SA5 and RAN2 is necessary. To make sure the modification is useful for SA5 and feasible for RAN2. |
| Samsung |  | Detail configuration is defined by SA5/RAN2. Another way is to provide contributions directly to the decision group. |
| CATT | Probably No | The requirement may need to ask SA5 and RAN2. But in my opinion, the Collection Period for M4, M5, M6, M7 is enough to control measure report. |
| Nokia | Yes | The proposal seems beneficial. However, indeed this will impact TS 32.422, so need to consult SA5. There should be no RAN2 impact from these measurements. |

### PROPAGATION OF USER CONSENT AT Xn INTER-PLMN HO

The reply LS in R3-211463 from SA3 says that:

SA3 likes to answer that the source NG-RAN node can be allowed, in case of inter-PLMN Xn handover, to propagate the Management Based MDT PLMN List IE to the target NG-RAN node irrespective of the target PLMN being included or not included in the list, given the following conditions are met:

- The source NG-RAN node and the target NG-RAN node are managed by the same operator.

- MDT is not activated, or is stopped, when the UE is in a PLMN not covered by the consent.

SA3 also wants to inform RAN3 that a Release 17 study on user consent (TR 33.867) is under progress in SA3,  in which several aspects and use cases including the definition of user consent are being discussed.

There are three options to address the reply LS form SA3:

Option 1: as proposed in R3-212120, to replace the following texts

by

If the HANDOVER REQUEST message includes the Management Based MDT PLMN List IE, the target NG-RAN node shall take it into account irrespective of the target PLMN being included or not included in the list, given the following conditions are met:

- MDT is not activated, or is stopped, when the UE is in a PLMN not covered by the consent.

Option 2: as proposed in R3-211976, the Management Based MDT PLMN List IE is always transferred to the target node irrespective of whether the target PLMN is included in the Management Based MDT PLMN List IE or not.

The proposal is:

Proposal 1: 	It is proposed to agree the source NG-RAN can forward Management Based MDT PLMN List to the target NG-RAN if the source NG-RAN selects a serving PLMN which is not included in the Management Based MDT PLMN List.

Option 3: as proposed in R3-212002, the original principle is kept no change. And the AMF will resend the user consent info to NG-RAN node when the UE handovers back to a PLMN in the Management Based MDT PLMN List.

The proposal are:

Proposal 1: RAN3 to confirm that the Management based MDT PLMN List will be propagated to the target node only if the target PLMN is included in the Management Based MDT PLMN List.

Proposal 2: RAN 3 to agree that the AMF resends the Management based MDT PLMN list to the target node after Xn handover in Path Switch Request Ack message.

Please provide your view on this.

| Company | Which option do you agree on? (Option 1,2 and 3) | Comment |
| --- | --- | --- |
| Qualcomm | Option 1 | UE does PLMN check each time it performs MDT measurements. If PLMN check is not met, UE will not report MDT measurements and hence MDT is “stopped” (one of the conditions in SA3 reply LS). The propagation of user consent during inter-PLMN handovers irrespective of target PLMN being in MDT PLMN list is useful in case there is a handover back to a PLMN belonging to the MDT PLMN list. The text proposed by Option 1 considers SA3 reply LS and should be more appropriate than Option 2. Option 3 has signaling impacts. |
| ZTE | Option 1 | Option 1 enable target NG-RAN node continue check the situtaion, in case e.g UE reseletct PLMN in the target later. |
| Samsung | Option 1 or option 2 | We proposed option 2, but we are also fine to proposal 1. |
| CATT | Option 1 or option 2 | Option 2 is preferred. In my opinion, the Management Based MDT PLMN List IE shall be always transferred to the target node no matter whether the condition are met or not. But proposal 1 is also fine. |
| Nokia | Option 3 | We believe it is beneficial to keep the original principle, and believe that this option will satisfy the functional need in terms of not losing user consent information in the RAN in case of multiple handovers. |

# Conclusion, Recommendations [if needed]

If needed

# References

| R3-212012 | Miscellaneous corrections to MDT (Multiple TPs included) (Huawei) | other |
| --- | --- | --- |
| R3-212264 | (TP for MDT BL CR for TS 38.413, TS 38.423, TS 38.373, TS 38.463) Introduction of the Report Amount (Ericsson) | other |
| R3-212265 | [DRAFT] LS on the introduction of the Report amount configuration for the MDT measurements (Ericsson) | LS out |
| PROPAGATION OF USER CONSENT AT Xn INTER-PLMN HO |
| R3-211463 | Reply LS on propagation of user consent related information during Xn inter-PLMN handover (SA3) | LS in Move to 10.3.2.1 |
| R3-212120 | (TP for MDT BL CR for TS38.423) TP on updates related to the Management based MDT PLMN list processing based on the SA3 LS (Ericsson) | other Move to 10.3.2.1 |
| R3-212121 | (draft) Reply LS on Management Based MDT PLMN List (Ericsson) | LS out Move to 10.3.2.1 |
| R3-211976 | Propagation for Management Based MDT PLMN List (Samsung) | discussion Move to 10.3.2.1 |
| R3-211977 | Propagation for Management Based MDT PLMN List (Samsung) | CR0613r, TS 38.423 v16.5.0, Rel-16, Cat. F Move to 10.3.2.1 |
| R3-212002 | Discussion on propagation of user consent related information during Xn inter-PLMN handover (Huawei) | discussion Move to 10.3.2.1 |
| R3-212003 | Propagation of user consent related information during Xn inter-PLMN handover (Huawei) | CR0600r, TS 38.413 v16.5.0, Rel-16, Cat. F Move to 10.3.2.1 |