3GPP TSG-RAN WG3 #112-e	R3-212670

Online, 17 – 28 May, 2021

Agenda Item:	10.3.2.2

Source:	Qualcomm Inc. (moderator)

Title:	Summary of Offline Discussion on CB: # 1214_SONMDT_MDT-MR-DC

Document for:	Approval

# Introduction

This contribution is to kick off the following discussion.

CB: # 1214_SONMDT_MDT-MR-DC - Topics to discuss: - Introduce MDT Configuration NR2 IE within the MDT Configuration IE in NGAP and XnAP - Introduce S-Node MDT Activation message in XNAP - Revert agreement “Remove the restriction that only immediate MDT is supported for EN-DC” - Include an Early Measurements Relevant Flag under Logged MDT in MDT Activation NR IE in NGAP and XnAP - Source NG-RAN can indicate the logged MDT type (obtained from UE or from its UE context) and remaining active time for logged MDT (computed by source NG-RAN) over Xn and NG - Start with summary of offline, proceed to TPs if there are agreements (QC - moderator) Summary of offline disc R3-212670

# For the Chairman’s Notes

# Stage-1 Discussion

### MDT Configuration for NR-DC

In R3-212013, it is proposed:

Proposal 1: Introduce MDT Configuration NR2 IE within the MDT Configuration IE in NGAP and XnAP. Add the related descriptions in the following TPs.

| IE/Group Name | Presence | Range | IE type and reference | Semantics description |
| --- | --- | --- | --- | --- |
| MDT Configuration-NR | O |  | 9.2.3.126 | This IE applies for MN in NR-DC. |
| MDT Configuration-EUTRA | O |  | 9.2.3.127 |  |
| MDT Configuration-NR2 | O |  | 9.2.3.126 | This IE applies for SN in NR-DC. |

Please provide your view on this.

| Company | Do you agree on the proposal? (Y/N) | Comment |
| --- | --- | --- |
| Huawei | Yes |  |
| Nokia | not sure | Not sure to see the purpose of using different s-based MDT configurations in MN and SN when both PCell and PSCell are NR cells. This was not agreed by RAN2. In earlier RAN3 discussions the rationale of different s-based MDT configurations in MR-DC was due to different RATs (E-UTRA and NR). (R3-212013: "In MR-DC, the MN and SN may configure the UEs with different MDT configurations, thus requiring the AMF send at least two sets of MDT configurations to NG-RAN node.") |
| Ericsson |  | We share the views from Nokia. It should be first confirmed that an MN and SN of the same RAT are allowed to have different MDT configurations. Indeed this does not seem likely. For example, in case of M6 measurements, would Mn and SN have different configurations? If yes, and assuming an MN terminated split bearer, how can consistent measurements be captured if the MN and SN configurations are different? |
| Qualcomm |  | Agree with Nokia and Ericsson that the use case for different MDT configurations in a NR-DC case is not fully clear and not agreed by RAN2 yet. But possibly different MDT configurations for MN and SN could be useful in case of FR1-FR2 DC scenarios? MN and SN could be configured with different M1 configurations. Regarding Ericsson’s question on split bearers, OAM should probably make sure that the reporting interval is consistent? |

### S-Node Activation message in XnAP

In R3-212571, it is observed that for SN terminated MCG/split bearers and MN terminated SCG/split bearers, M6 delay includes MN part plus SN part and it is proposed that

Proposal : Introduce S-Node MDT Activation message in XNAP. Corresponding TP can be found in [1].

Figure 1: Signalling sequence for SN initiated M-based MDT for M6

Please provide your view on this.

| Company | Do you agree on the proposal? (Y/N) | Comment |
| --- | --- | --- |
| Huawei | No | Not sure this is needed or not. Shouldn’t we use the trace start message from the MN to the target SN? |
| Nokia | No | Needs further discussion. We understand that RAN2 works or will work on measurements for MR-DC, see also CB#1215 on L2 measurements. Also, the description and proposal in R3-212571 is not fully clear to us. E.g. it is mentioned "As shown in figure 2, take SN terminated split bearer for example, D4 refer to Average delay DL in PDCP of SN." but no relevant figure can be seen. Also in Fig. 1 above, the SN reports measurements to the MN which further reports to the TCE, while the assumption in CB#1215 is separate reporting from SN and MN to the TCE. Concerning the activation, I'm not sure it would be so relevant to support m-based activation of M6 for MN split bearers in the SN, maybe m-based activation of M6 only in the MN for such split bearers would be enough. |
| ZTE | Yes | If m-based activation of M6 only in the MN for such split bearers, then I think the proposal is not necessary. But if not, the proposal need to be taken into account. Without the indication, how can MN aware the MDT measurement triggered in SN and how to report MN part measurement result to TCE? |
| Ericsson |  | It seems that trace start could be used in this case. Need to clarify why a new procedure is needed. |
| Qualcomm |  | Not clear why SN should send MDT results to MN for m-based MDT. SN should send results to TCE independently. |

### Revert agreement on support for only immediate MDT for EN-DC

In R3-212127, it is proposed:

Proposal 1: Revert agreement “Remove the restriction that only immediate MDT is supported for EN-DC” from R3-110e to align with RAN2 agreement that SN configuration for logged MDT in MR-DC are not introduced.

Please provide your view on this.

| Company | Do you agree on the proposal? (Y/N) | Comment |
| --- | --- | --- |
| Huawei | yes |  |
| CATT | Yes |  |
| Nokia | Yes | RAN2 has agreed that SN node will not provide logged MDT configuration to the UE. So the restriction for EN-DC will remain in Rel-17. |
| ZTE | Yes |  |
| Qualcomm | Yes |  |

### Early Measurements Relevant Flag under Logged MDT

In R3-212127, it is proposed:

Proposal 2: Include an Early Measurements Relevant Flag under Logged MDT in MDT Activation NR IE in NGAP and XnAP to indicate to target node whether early measurements are relevant to logged MDT

Please provide your view on this.

| Company | Do you agree on the proposal? (Y/N) | Comment |
| --- | --- | --- |
| Huawei | Pending to RAN2 | It is still FFS in RAN2, right? |
| CATT |  | Wait for RAN2 decision |
| Nokia | Y | This seems needed. |
| ZTE |  | Can wait for RAN2’ progress. |
| Ericsson | Y | We think this is needed |
| Qualcomm | Yes | RAN2 agreed on the use case and the benefit of adding this flag. But there is still a FFS on whether to add the flag. Ok to wait for RAN2 final decision. |

### Logged MDT Type and remaining active time for logged MDT

In R3-212127, it is proposed:

Proposal 3: Source NG-RAN can indicate the logged MDT type (obtained from UE or from its UE context) and remaining active time for logged MDT (computed by source NG-RAN) over Xn and NG to assist the target NG-RAN in optimal configuration for management-based logged MDT.

Please provide your view on this.

| Company | Do you agree on the proposal? (Y/N) | Comment |
| --- | --- | --- |
| Huawei |  | We think that the solution may be workable for handover UEs. But it does not work for idle mode UEs. So the solution cannot cover all the scenarios. |
| CATT |  | Agree with Huawei. It may work for connected UE, But for idle UE, source NG-RAN cannot provide this information to target NG-RAN. |
| Nokia | No | RAN2 agreed: “Introduce the logged MDT type (i.e. the management based MDT or the signaling based MDT) in the logged MDT configuration.” However, it remains to be still decided if the type will be applicable to one or both MDT configuration types. Remaining time is not agreed in RAN2. |
| ZTE | Yes | At least, the solution can be apply to UE in RRC_CONNECTED &RRC_INACTIVE. For UE in RRC_IDLE, Ran can calculate the left time based on implementation. For example, holding for 2 hour. |
| Ericsson | No | We agreed to adopt a UE based solution to manage logged MDT across different RAN nodes. This solution is one of the network based ones, subject to all the drawbacks RAN3 discussed and acknowledged in the LS to RAN2 in R3-207176 |
| Qualcomm | Yes | Agree that UE based solution is planned to be adopted by RAN2 considering all RRC states. The proposal here is to use a network based solution as additional assistance (at least would work for RRC_CONNECTED and RRC_INACTIVE as acknowledged above) in case UE doesn’t provide logged MDT type (this might be a UE capability) or remaining time is not agreed by RAN2 (network can provide this information). |

### On-demand SI related configuration in Logged MDT

In R3-212127, it is proposed:

Proposal 4: If RAN2 agrees to enhance logged MDT for collecting On-demand SI related statistics, include On-demand SI related configuration in Logged MDT under MDT Activation NR which is be exchanged over NG and Xn

Please provide your view on this.

| Company | Do you agree on the proposal? (Y/N) | Comment |
| --- | --- | --- |
| Huawei |  | Pending to RAN2 progress. |
| CATT |  | Wait for RAN2 decision |
| Nokia | No | We need to wait for outcome of RAN2 discussion. |
| ZTE |  | Wait for RAN2 progress. |
| Ericsson |  | We should wait for RAN2 |
| Qualcomm |  | Okay to wait for RAN2 progress |

# Conclusion, Recommendations [if needed]

If needed

# References

| R3-212013 | MDT for MR-DC (Multiple TPs included) (Huawei) | other |
| --- | --- | --- |
| R3-212571 | MDT for MR-DC (ZTE) | discussion |
| R3-212572 | (TP for 38.423) MDT for MR-DC (ZTE) | other |
| R3-212127 | Mobility Enhancement Optimization (Qualcomm Incorporated) | discussion Move to 10.3.2.2 vChair: error in contribution title |