3GPP TSG-RAN WG3#112-e 	R3-212757

7th May – 27th 	May 2021

Agenda item:	9.3.8.1

Source:	CATT

Title:	CB: # 121_AbnormalConditionsHOprep

Document for:	Approval

# Introduction

CB: # 121_AbnormalConditionsHOprep - check IE usage - is CR needed? (CATT - moderator) Summary of offline disc R3-212757

Please comment before the Monday, 24. May, 24:00 UTC.

# For the Chairman’s Notes

Propose to capture the following: …

# Discussions

We would like to explanation the intention of these CRs first.  In previous meeting, we changed the PDU Session Resource Handover List IE from mandatory to optional since there may be no need to contact SMF when data forwarding is not needed for inter-system handover. There is following statement in current spec:

In case of intra-system handover, the AMF shall include the PDU Session Resource Handover List IE in the HANDOVER COMMAND message.

It means that the PDU Session Resource Handover List IE is a mandatory IE for intra-system handover, while it still optional for inter-system handover. Therefore, if no data forwarding is needed for intra-system handover, AMF do send PDU Session Resource Handover List IE but Handover Command Transfer would be empty, which means that it has no at least one valid associated GTP tunnel address pair. The current spec said that “without at least one valid associated GTP tunnel address pair (in either UL or DL), then the NG-RAN node shall consider it as a logical error” is not correct. Namely, there is no at least one valid associated GTP tunnel address pair in PDU Session Resource Handover List IE is not an abnormal case when data forwarding is not needed in intra-system handover.

Q1: Do you agree the intention of this CR? If no, please provide your view.

| Company | Answer | Comments |
| --- | --- | --- |
| CATT | Agree |  |
| Huawei | Agree | We acknowledge this issue. Otherwise, for intra-system handover without data forwarding, this may be considered as abnormal case (since no valid GTP tunnel address pair). The original paragraph in NGAP is copied from S1AP (which was agreed in LTE R3-103153). In S1AP HANDOVER COMMAND message, both the “DL Transport Layer Address” and “DL GTP-TEID” are optional, so the abnormal condition in S1AP is needed to specify the “pair” is considered as valid. But for NGAP HANDOVER COMMAND message, the forwarding address is encoded as “ 9.3.2.2 UP Transport Layer Information” IE, in which both the Endpoint IP Address and GTP-TEID are mandatory. So there is no issue here. So another way is to remove the whole 8.4.1.4 Abnormal Conditions. |
| Nokia | Agree |  |

Some companies may consider that whether the “pair” is needed in spec. (yellow highlight)

“In case of inter-system handover, if the NG-RAN node receives at least one PDU Session ID included in the PDU Session Resource Handover List IE without at least one valid associated GTP tunnel address pair (in either UL or DL), then the NG-RAN node shall consider it as a logical error and act as described in subclause 10.4. A GTP tunnel address pair is considered valid if both the GTP-TEID IE and the Endpoint IP Address IE are present.”

In our understanding, “pair” means (Endpoint IP Address, GTP-TEID) which is copy from LTE. They are included in UP Transport Layer Information in Handover Command Transfer IE

Q2: Do you agree the current statement. If no, please provide your suggestion.

| Company | Answer | Comments |
| --- | --- | --- |
| CATT | Agree |  |
| Huawei |  | See our answer to Q1. |
| Nokia | No | In our view the original intention of the specification was to make sure that at least one pair is correctly encoded when received. Please see our proposed possible rewording in CB folder. |

# Conclusion, Recommendations

If needed

# References

- R3-211794, Correction on Abnormal Conditions in Handover Preparation Procedure for R15 (CATT, Huawei)