3GPP TSG-RAN3 #112-e								R3-212623

Online, 17th – 27th May 2021

Agenda Item:	9.3.3

Source:	Ericsson (moderator)

Title:	SoD SCG release notification

Document for:	Approval

# Introduction

CB: # 27_NR-NR_DCconfigRelease

- (SS) SN-initiated SCG release is not currently supported; propose to introduce it in Xn

- (Nok) Consider whether to reuse current X2AP signaling or introduce a new flag; not currently possible to support this use in XnAP

- (E///) Not currently supported; agree indicator in X2AP, XnAP, F1AP

- (HW) Currently supported in both X2AP and XnAP; nothing needed

- (ZTE) Currently supported in X2AP; agree enhancement to XnAP, F1AP

- (Nok) Only if the SN initiated SCG release scenario is confirmed as supported over Xn by RAN3, changes can be considered over F1 to also allow a Master Node gNB-CU to signal its corresponding gNB-DU over F1 when a SCG has been released as a Release 16 optimization; no changes required over F1AP to indicate an SCG addition from M-gNB-CU to M-gNB-DU; MN does not use UE Context Setup procedure to indicate an SCG addition or SCG release

- (HW) MN-gNB-DU can be aware of SCG release via F1AP: UE CONTEXT SETUP REQUEST and UE CONTEXT MODIFICATION REQUEST messages, by using MR-DC Resource Coordination Information IE and CU to DU RRC Information IE (absence of pSCellFrequency IE and pSCellFrequencyEUTRA IE in the CG-Config message); we may need to include NR-DC case in semantics description

- (SS) SCG release indication is introduced in UE CONTEXT MODIFICATION REQUEST message to indicate SCG release at SN side

- (E///,Vz,DT,TI) signal over F1, X2 and Xn a new IE to indicate to the M-gNB-DU that an SCG is added or removed

- Consensus that this is a valid scenario

- 0) Do nothing, already supported; 1) Extend X2AP, XnAP, F1AP; 2) Extend XnAP, F1AP; 3) Extend X2AP only; 4) Do nothing in RAN3, extend RRC in RAN2?

- agree reply LS

(E/// - moderator)

# For the Chairman’s Notes

Propose the following:

R3-21xxxa, R3-21xxxc merged

R3-21xxxc rev [in xxxg] – agreed

R3-21xxxd rev [in xxxh] – agreed

R3-21xxxe rev [in xxxi] – agreed

R3-21xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion

The discussion implies decisions on two macro aspects:

- The need of notification concerning SCG status (added/removed) over X2/Xn

- The need of notification concerning SCG status (added/removed) over F1

## SCG Status signalling over X2/Xn

### SCG Status signalling over X2

In [1], [3] and [4] it is stated that information about removal of an SCG may be signalled to the MN over the X2 by means of the following IE

9.2.108 EN-DC Resource Configuration This IE contains the EN-DC resource configuration for an E-RAB, indicating the presence of PDCP at the en-gNB and Lower Layers at MCG and SCG. IE/Group Name Presence Range IE type and reference Semantics description Criticality Assigned Criticality PDCP at SgNB M ENUMERATED (present, not present) – MCG resources M ENUMERATED (present, not present) – SCG resources M ENUMERATED (present, not present) –

In particular, if the EN-DC resource configuration IE has the SCG resources IE set to “not present” for all bearers at the SN, the MN may deduce that the SN has no more SCGs served.

In [2] it is stated that

“In EN-DC, there is the EN-DC Resource Configuration IE; however, its original purpose was to enable decoding the CHOICE structure of the message, not to indicate the current state of the E-RAB (this is why it is not present in XnAP, where there is no CHOICE structure)”

And that

“In EN-DC, the EN-DC Resource Configuration IE could, in theory, be used as a bearer type change indicator and thus enable SN-initiated resource allocation change. However, it may then also enable SN-initiated change of the PDCP termination point”

[2] comes to the conclusion that the X2AP is incomplete when it comes to signalling of SCG status information and that either a new indication for SCG removal is added or a clarification is added about how the EN-DC resource configuration IE shall be interpreted.

[5] states that the X2AP is incomplete and that a new indication stating whether an SCG is removed or added at the SN is proposed for signalling from SN to MN over X2.

One general observation is that to achieve inter vendor interoperability, the interpretation of existing IEs (e.g. the EN-DC resource configuration IE) at the receiving node needs to be clearly described. As an example, a RAN node receiving an EN-DC resource configuration IE with PDCP at SgNB IE, MCG resources IE and SCG resources IE all set to “not present” may return an error message as such combination was never foreseen to be used when these IEs were introduced, neither the specifications describe how a receiver should deduce from such IEs that an SCG has been removed.

Companies are invited to provide their view on whether the addition of an indication of SCG removal is needed over X2, from SN to MN.

| Company | Comment |
| --- | --- |
| Ericsson | Needed The current X2AP specification cannot be left unchanged with the expectation that the EN-DC resource configuration IE is interpreted in a way to deduce SCG removal. TS36.423 does not describe the conditions in which the EN-DC resource configuration IE should indicate that an SCG has been removed. A change of how the receiver interprets the EN-DC resource configuration IE may result in non backwards compatible changes (namely an old RAN node may not deduce SCG removal correctly). The simplest and most interoperable solution is to add an explicit IE over the X2 indicating that the SCG has been removed by the SN |
| ZTE | Not needed. The current IE “EN-DC resource configuration IE” can be reused. For instance, when SCG is set to “Not present”, the SN requires to release SCG. |
| NTTDOCOMO | Not needed. For X2AP, SCG resource IE in EN-DC resource configuration IE can be to set “not present” to indicate the SCG release. Adding clarification of such usage of this IE is more preferable. |
| Huawei | Not needed. |
| Verizon | Needed. Explicit IE for SCG removal by SN would better suit interoperability and avoid ambiguity in interpretation of EN-DC Resource configuration IE. |
| Nokia | Some changes in X2AP are needed and the indicator is the most straightforward solution. In general, we fully agree with Ericsson. Of course, RAN3 may decide to introduce a functionally non-backward compatible change, but it has to be decided openly – can’t be assumed. Also, please note: the EN-DC resource config IE is not present in Xn exactly because it was needed only to decode the Choice structure. In XnAP there is no choice, so there is no EN-DC resource config IE! |
| Samsung | Not needed Companies seem to concern that the current specification does not clearly indicate the behavior of the receiver when receiving EN-DC Resource Configuration IE. However, this does not mean the information inside the IE cannot be used to determine the SCG removal. |
| CATT | Not needed EN-DC resource configuration IE could be used to deduce the presence of SCG resource. |
| NEC | Not needed. Can add clarification text for existing IE. Adding clarification for the existing IE does not mean it is a NBC change. Adding a new indicator IE would likely mean NBC for old node that has already taken the existing IE into usage. |
| Deutsche Telekom | Needed to create an interoperable and backward compatible solution (agree with statements by Ericsson, Verizon, Nokia). |
| Qualcomm | Not needed for X2. We can reuse EN-DC resource configuration IE. |

Moreover, [5] also proposes that the new IE introduced over the X2 can also indicate that an SCG has been added at the SN.

Companies are invited to provide their view on whether the addition of an indication of SCG addition is needed over X2, from SN to MN.

| Company | Comment |
| --- | --- |
| Ericsson | Needed Similarly to the previous case, the EN-DC resource configuration IE has not been introduced to indicate addition or removal of an SCG. Any assumption that such IE may be interpreted as to indicate an SCG addition may result in errors. Therefore, either the interpretation of the EN-DC resource configuration IE is corrected and clarified to clearly describe the case of SCG addition detection, or it is advantageous to have a clear and un-equivocal indication of SCG addition via a new IE. |
| ZTE | Not needed. |
| NTTDOCOMO | Not needed. |
| Huawei | Not needed. |
| Verizon | Needed. Agree with Ericsson’s comment above. An explicit IE would be better for interoperability. |
| Nokia | If the indicator for SCG release is decided to be needed, then it has to allow indicating SCG addition, too – obviously. Alternatively, if a NBC change is decided, we need to describe also usage of the EN-DC resource config IE in case of SCG addition. |
| Samsung | Not needed |
| CATT | Not needed EN-DC resource configuration IE could be used to deduce the presence of SCG resource. |
| NEC | Not needed. EN-DC resource configuration IE could be used to deduce the presence of SCG resource. |
| Deutsche Telekom | Needed (supporting Ericsson’s statement). |
| Qualcomm | Not needed |

### SCG Status ignaling over Xn

In [1], [2], [4] and [5] it is concluded that it is not possible to indicate over the Xn interface whether an SCG has been released by the SN.

[1], [4] and [5] also propose the addition of an explicit IE over the Xn interface, ignalin form the SN to the MN, to indicate that an SCG release occurred.

[3] states that there is no need of new additions over the Xn interface because “absence of pSCellFrequency IE and pSCellFrequencyEUTRA IE in the CG-Config message, could also be understood as SCG release by the MN”.

It needs to be pointed out that RAN2 already discussed whether the current RRC inter node messages can convey the information that an SCG has been released by the SN. A summary of that discussion is captured in the meeting minutes form RAN2-113-e, see below:

Hence, RAN2 contacted RAN3 to pursue a solution based on AP level extensions and for that the CR in R2-2100586, which attempted to clarify how RRC inter node messages should be interpreted to convey an indication of SCG release, has not been pursued.

On the basis of the above:

Companies are invited to provide their view on whether the addition of an indication of SCG removal is needed over Xn, from SN to MN.

| Company | Comment |
| --- | --- |
| Ericsson | Needed The current XnAP specification cannot be left unchanged with the expectation that the RRC CG-Config message will convey the indication of SCG release by the SN. TS38.331 does not describe the conditions in which the CG-Config IE should indicate that an SCG has been released. A change of how the receiver interprets the CG-Config may result in non backwards compatible changes (namely an old RAN node may not deduce SCG removal correctly). The simplest and most interoperable solution is to add an explicit IE over the Xn indicating that the SCG has been removed by the SN |
| ZTE | Needed. RAN2 has already discussed the RRC CG-config container, and agreed to not fix the CG-config description in the RAN2 protocol. Then RAN2 asks RAN3 to use either new or enhanced X2/XnAP signaling to support SCG release. So that. RAN3 needs to extend signaling to support it. In the LS，RAN3 is asked to support SCG release request. |
| NTTDOCOMO | Needed. |
| Huawei | Needed. |
| Verizon | Needed. |
| Nokia | Needed. Please note, RAN2 has asked us if the SCG release can be ignalin over X2/Xn. However, the structure of the CG-config is decided in RAN2, so any solution based on reading the RRC container is known in RAN2. Therefore, RAN2 must have ruled it out and have been interested in a solution based on AP ignaling. Such solution does not exist. |
| Samsung | Needed |
| CATT | Needed |
| NEC | We in our response paper R3-212635 try to understand if can make use of existing information, that may be able to know the SCG resource status from SN to MN, i.e. the indicated value (0=MCG, 1=SCG) in Cell Group ID IE of the UP Transport Parameters IE. if set to only one Cell Group ID IE with value “0”=MCG, that means the concerned DRB is SN Terminated MCG bearer (only MCG resource is configured), which can mean this is to release SCG resource if currently it is MCG and SCG resource. if set to two Cell Group ID Ies with value “0”=MCG and value “1”=SCG, that means the concerned DRB is SN Terminated split bearer. If this can be used to know, then no need new indicator. If this cannot be used, then need to extend ignaling to support. |
| Deutsche Telekom | Needed |
| Qualcomm | Needed |

Moreover, [5] also proposes that the new IE introduced over the Xn can also indicate that an SCG has been added at the SN.

Companies are invited to provide their view on whether the addition of an indication of SCG addition is needed over Xn, from SN to MN.

| Company | Comment |
| --- | --- |
| Ericsson | Needed Similarly to the previous case, the RRC CG-Config message has not been introduced to indicate addition or removal of an SCG. Any assumption that such IE may be interpreted as to indicate an SCG addition may result in errors. Therefore, either the interpretation of the CG-Config IE is corrected and clarified to clearly describe the case of SCG addition detection, or it is advantageous to have a clear and un-equivocal indication of SCG addition via a new IE over Xn |
| ZTE | Not Needed. SCG addition is out of LS. Meanwhile, in current MR-DC mechanism, SCG addition is not allowed by SN triggered. |
| NTTDOCOMO | No strong view. |
| Huawei | Not needed, share the view with ZTE. |
| Verizon | Needed, share view with Ericsson. |
| Nokia | Needed, obviously. Above, we’ve explained why the CG-config can’t be considered when responding to RAN2. So, if there the release requires an indicator, then SCG addition requires one, too. |
| Samsung | Not needed. We are unclear the intention of knowing the SCG is added. Originally, knowing the SCG removal is to help MN configure some lower layer parameters, e.g., band combination. SCG additional can be deduced from whether CG-config contains SCG configuration or not. |
| CATT | Although not required from RAN2, it seems needed to have this indication. |
| NEC | See comment above. |
| Deutsche Telekom | Needeed |
| Qualcomm | Not needed |

## SCG Status signalling over F1

In [6] it is stated that if RAN3 agrees to signal an indication of SCG removal from SN to MN over Xn, then the same indication should be signalled over F1 from gNB-CU to gNB-DU. In [5] the assumption is that an indication of SCG removal over F1, from gNB-CU to gNB-DU is related to the same indication sent over X2 and/or Xn from SN to MN.

Like in [6], [5] proposes that an explicit indication of SCG release is introduced over F1, signalled from the gNB-CU to the gNB-DU. A similar proposal is supported by [4], [5] and [8].

[7] states that “the absence of pSCellFrequency IE and pSCellFrequencyEUTRA IE in the CG-Config message, could also be understood as SCG release by the MN-gNB-DU”.

As for previous discussions, it should be clear that the inter node RRC messages, such a sCG-Config, have not been specified to notify of a release of the SCG. As seen in the previous section this was also confirmed by RAN2.

Companies are invited to provide their view on whether the addition of an indication of SCG removal is needed over F1, from gNB-CU to gNB-DU.

| Company | Comment |
| --- | --- |
| Ericsson | Needed The current F1AP specification cannot be left unchanged with the expectation that the RRC CG-Config messages will convey the indication of SCG release. TS38.331 does not describe the conditions in which the CG-Config should indicate that an SCG has been released. A change of how the receiver interprets the CG-Config may result in non backwards compatible changes (namely an old RAN node may not deduce SCG removal correctly). The simplest and most interoperable solution is to add an explicit IE over the F1 indicating that the SCG has been removed by the SN |
| ZTE | Needed. Both SCG release and addition are needed. In F1AP, gNB-CU can notify gNB-DU of SCG release or SCG addition. |
| NTTDOCOMO | Needed. |
| Huawei | Needed. |
| Verizon | Needed. |
| Nokia | Needed. However, the IE should only be applicable to UE Context Modification procedure. |
| Samsung | Needed Only for UE Context Modification procedure. In addition, we feel the corresponding change should be applied to W1 as well. |
| CATT | OK |
| Deutsche Telekom | Needed |
| Qualcomm | Needed |

Moreover, [5] also proposes that the new IE introduced over the F1 can also indicate that an SCG has been added.

Companies are invited to provide their view on whether the addition of an indication of SCG addition is needed over F1, from gNB-CU to gNB-DU.

| Company | Comment |
| --- | --- |
| Ericsson | Needed Similarly to the previous case, the RRC CG-Config message has not been introduced to indicate addition or removal of an SCG. Any assumption that such IE may be interpreted as to indicate an SCG addition may result in errors. Therefore, either the interpretation of the CG-Config IE is corrected and clarified to clearly describe the case of SCG addition detection, or it is advantageous to have a clear and un-equivocal indication of SCG addition over F1. |
| ZTE | Needed. Both SCG release and SCG addition are needed. In F1AP, gNB-CU can notify gNB-DU of either SCG release state or SCG addition state. In X2/Xn, it is the SCG release request from SN, and the MN can reject the request message, so that only SCG release is allowed. But in F1AP, it is the SCG release/addition notification. The gNB-DU shall accept and store the notification. |
| NTTDOCOMO | Needed. |
| Huawei | Needed. |
| Verizon | Needed. |
| Nokia | Not Needed. The SCG addition can already be indicated via the UL Configuration IE. That is, when a SCG is added, the M-gNB-CU can send a UE CONTEXT MODIFICATION REQUEST including UL Configuration IE which indicates how the resources at the receiving as well as on another node are utilized. Hence, inclusion of UL Configuration IE implicitly indicates an SCG addition. |
| Samsung | Not needed If the SCG is added. The CG-Config must have related configurations. |
| CATT | Based on comments from Nokia,UL configuration could indicate whether SCG resource is used or not.So,the new indication is not needed. |
| Deutsche Telekom | Needed |
| Qualcomm | Agree with Samsung. CG-Config has related information. |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-211931, “Discussion on SCG release over Xn”, Samsung

R3-21505,	“Consideration on SN-initiated SCG release”, Nokia, Nokia Shanghai Bell

R3-211529,	“Consideration on signalling SN initiated release of SCG”, Huawei

R3-211575, “Discussion on NR-NR DC Configuration Release”, ZTE

R3-212279, “How to release SCG configuration between MN-CU and MN-DU”, Ericsson, Verizon Wireless, Deutsche Telekom, Telecom Italia

R3-211406, Discussion on SCG addition and removal in disaggregated architecture, Nokia, Nokia Shanghai Bell

R3-211531, Information about SCG Release from MN-gNB-CU to MN-gNB-DU, Huawei

R3-211935, Discussion on SCG release over F1, Samsung