3GPP TSG-RAN WG3 Meeting #112-e	R3-212626

17 - 27 May 2021

Online

Agenda Item:	9.3.4.3

Source:	Ericsson

Title:	PDCP SN Handling for EPC to 5GC HO - Summary of offline discussion

Document for:	Discussion and Decision

# 1	Introduction

The scope of the email discussion has been captured as followed:

CB: # 30_DirectDataFwd_PDCP_SNhandling_EPC-5GC_HO - (Nok) issue related to PDCP SN assignment is still unresolved; reconsider if the solution based on an indication that forwarded data does not need PDCP SNs isn’t better for Rel-16; if decided negatively, the solution should be postponed until Rel.17 optimizations are discussed - (SS) Add PDCP SN Discard and Direct Forwarding Path Availability IE in BEARER CONTEXT SETUP REQUEST message - (E///) target CU-UP should be aware that the Bearer Context Setup procedure is associated to an inter-system HO - (HW) Add a new Handover Type indicator in the BEARER CONTEXT SETUP REQUEST message to indicate the EPS to 5GS handover with direct data forwarding (E/// - moderator) Summary of offline disc R3-212626

This contribution captures the email discussion.

# 2	For the chairman’s notes

To be captured later

# 3	Email discussion

## 3.1 Reconsidering agreements from RAN3#111-e

[1] is proposing to reconsider RAN3#111-e decision (i.e. target node may receive PDCP SN but will not forward it to the UE), and to discuss a possible solution at the source node for rel-17.

Question 1.1: Does RAN3 should reconsider last meeting agreement i.e. PDCP SNs can be forwarded by source SN to target node(s)?

| Company | Response |
| --- | --- |
| Ericsson | No. It was decided that only the NG-RAN node should be impacted. Also, it is preferable to let the target node decides if these PDCP SNs are useful or not (but for sure not sent to the UE) |

Question 1.2: Can the solution at the source node described in [1] be considered in rel-17?

| Company | Response |
| --- | --- |
| Ericsson | TEI-17 is contribution based. This will be discussed if submitted |

## 3.2 E1AP impact

[3], [5] and [6] (supported by discussion papers in [2] and [4]) are proposing different methods to inform the CU-UP about the special handling of the forwarded data for inter-system handover. The 2 options add new IE(s) in Bearer Context Setup Request message:

1. Discard PDCP SN IE and Direct Forwarding Path Availability IE (at PDU Session level) in [3]

2. Inter-system handover IE [4] or Handover type IE [6]

Question 2.1: Among the 2 solutions described above, what is the preferred option to inform the CU-UP about the special handling of the forwarded data for inter-system handover?

| Company | Preferred option | Comment |
| --- | --- | --- |
| Ericsson | 2 | 1 also works, but 2 is simpler (1 IE only) |

# 4	Conclusion

Result of the email discussion to be captured here

# 5	References

[1] R3-211516 - Next steps for direct data forwarding from EN-DC to NR SA (Nokia, Nokia Shanghai Bell)

[2] R3-211955 - PDCP SN Handling for EPC to 5GC HO (Samsung)

[3] R3-211956 - PDCP SN Handling and IP address selection for EPC to 5GC HO (Samsung)

[4] R3-212357 - PDCP SNs for forwarded PDCP SDUs from 4G to 5G (Ericsson)

[5] R3-212369 - Inter-system indicator for Bearer Context Setup (Ericsson)

[6] R3-212459 - PDCP SN issue for EPC to 5GC handover (Huawei)