3GPP TSG-RAN WG3 #112-e	R3-212711

Online, 17 – 28 May, 2021

Agenda Item:	23.2.1

Source:	Huawei (moderator)

Title:	Summary of Offline Discussion on General Aspects for Enhanced eNB Architecture Evolution

Document for:	Approval

# Introduction

CB: # 48_eNBarchEvo_General

- (HW,CMCC,CU)

Capture the definition of ng-eNB-CU-CP and ng-eNB-CU-UP in TS 38.401.

In order to align with NG-RAN architecture, there is no need to introduce logical entity as ng-eNB-CP and ng-eNB-UP, but a note could be used for clarification in case ng-eNB-DU is co-located with ng-eNB-CU-CP.

Capture the architecture and definition of eNB-CP and eNB-UP separation in TS 36.401.

Capture the interface management function, bearer context management function, TEIDs allocation function and the related procedures for CP-UP separation for ng-eNB and eNB in TS 38.460.

Reuse the existing IEs of UE AP IDs (gNB-CU-CP UE E1AP ID and gNB-CU-UP UE E1AP ID) and node IDs (gNB-CU-UP ID and gNB-CU-CP ID) with some clarifications.

allow E-UTRAN to use NR PDCP configured, based on existing E1 tabular architecture

- (E///)

Use TS 38.425 as UP specification for LTE CP-UP split in E-UTRAN

Capture architecture and definitions of eNB CP-UP separation in TS 36.401 and take TS 38.401 CP-UP separation sections as baseline

Further discuss if NR PDCP or NR PDCP + LTE PDCP are to be supported for eNBs connected to EPC

Use NR PDCP for ng-eNBs connected to 5GC

- Chair: revise as needed, check details and agree 2023, 2024 and 2196

(HW - moderator)

Summary of offline disc

# For the Chairman’s Notes

Propose the following:

Propose to capture the following:

Agreement text…

Agreement text…

# Discussion

## UP specification for LTE CP-UP split in E-UTRAN

In [5], to simplify the handling of the PDCP packets and the load balancing between MCG and SCG, it was proposed to use TS 38.425 as the UP specification between the two new entities in E-UTRAN.

Here the main discussion is about whether to agree to use TS 38.425 as the UP specification for LTE CP-UP split in E-UTRAN.

| Company | Comment |
| --- | --- |
| Nokia | It is agreeable to utilize 38.425. |
| Samsung | We agree on using TS 38.425 as the UP specification. |

## Naming of the new entities for legacy eNB

In [5], it was proposed to use eNB* for naming the logical node hosting the RRC/RLC/MAC/PHY and the control plane part of the PDCP protocol for an eNB.

In [1], it was pointed out that putting a symbol “*” as part of name is bit unformal, and eNB-CP was proposed for better reading.

It is therefore proposed to discuss the following：

Whether we should use eNB* or eNB-CP? Other suggestions for the naming are also welcome.

| Company | Comment |
| --- | --- |
| Nokia | eNB-CP and eNB-UP terms are agreeable for legacy eNB case. However, these need to be clearly indicated in the Stage 2 text proposals and figures, as well as how both C-Plane and U-Plane data traverses between these units. Clarification which interface is utilized for the user plane in particular, e.g., “E1’-U” (or something else) needs to be stated and included in the figures for stage 2. |
| Samsung | We don’t have strong preference, but eNB-CP and eNB-UP terms are slightly preferable. |

## Necessity to introduce logical entity as ng-eNB-CP and ng-eNB-UP

It was proposed in [1] that there is no need to introduce explicit definition for logical entity as ng-eNB-CP and ng-eNB-UP in order to align with NG-RAN architecture. Instead, a note could be used for clarification in case ng-eNB-DU is co-located with ng-eNB-CU-CP.

Here the main discussion is whether agree the above statement. The answer could be yes/no, and comments/reasoning of the answer is welcome.

| Company | Comment |
| --- | --- |
| Nokia | Not needed. |
| Samsung | Additional logical entity for ng-eNB is not needed. |

## Capturing the new architecture and definitions in TS 38.401 and TS 36.401

According to [1] and [5] there seems to be a common understanding to capture the definition of ng-eNB-CU-CP and ng-eNB-CU-UP in TS 38.401, and to capture architecture and definitions of eNB CP-UP separation in TS 36.401.

Hence, despite the naming issue described in 3.2, it is proposed to agree the following:

Capture the definition of ng-eNB CP-UP separation in TS 38.401 and capture the architecture and definitions of eNB CP-UP separation in TS 36.401.

| Company | Comment |
| --- | --- |
| Nokia | Agree as long as both Control and User plane interfaces used between the nodes are clearly defined in the proposals for Stage 2. That is, also in legacy eNB case, eNB-CP and eNB-UP need to be clearly indicated in the Stage 2 text proposals and figures, as well as how both C-Plane and U-Plane data traverses between these units. Clarification which interface is utilized for the user plane in particular, e.g., “E1’-U” (or something else) needs to be stated and included in the figures. |
| Samsung | Agree. |

## Reuse the existing IEs of UE AP IDs and node IDs with some clarifications.

In [1], it was suggested to reuse the existing UE AP IDs and refer them to the new logical entities instead of adding new optional IEs for each new logical entity for easy implementation.

Here the discussion is about whether agree to reuse the existing IEs of UE AP IDs (gNB-CU-CP UE E1AP ID and gNB-CU-UP UE E1AP ID) and node IDs (gNB-CU-UP ID and gNB-CU-CP ID) with some clarifications.

| Company | Comment |
| --- | --- |
| Nokia | New identifiers are needed. In our view, the legacy eNB support case (eNB-CP, eNB-UP) utilizes entities that differ from that of existing E1 interface in NG-RAN and hence new identifiers should be introduced. |
| Samsung | We agree on reusing the existing UE AP IDs with some clarifications. |

## PDCP for legacy case and NG-RAN case

In both [4] and [5], it reaches a common understanding that NR PDCP should be used for ng-eNBs connected to 5GC. In [5], it was proposed to discuss if NR PDCP or NR PDCP + LTE PDCP are to be supported for eNBs connected to EPC. In [4], it was also observed that the current E1 AP signalling already support PDCP configuration to be shared by E-UTRAN and NG-RAN, so [4] suggests to agree to allow E-UTRAN to use NR PDCP configured, based on existing E1 tabular architecture.

First, it is proposed to agree the following:

- Agree NR PDCP should be used for ng-eNBs connected to 5GC.

Then, we want to collect comments about PDCP configuration for legacy eNB. Specifically, whether agree that NR PDCP and LTE PDCP can both be used for legacy eNB based on existing E1 tabular architecture?

| Company | Comment |
| --- | --- |
| Nokia | For legacy eNB case, both NR PDCP and LTE PDCP should be supported. |
| Samsung | Agree on supporting both NR PDCP and LTE PDCP for legacy eNB. |

# Conclusion, Recommendations [if needed]

If needed

# References

- R3-212526, Further discussions on logical entities and corresponding definitions (Huawei, CMCC, China Unicom)

- R3-212023, CR to 38.401 on the introduction of ng-eNB CP-UP separation (Huawei, CMCC, China Unicom)

- R3-212024, CR to 36.401 on the introduction of eNB CP-UP separation (Huawei, China Unicom)

- R3-212022, Further discussions on implementing PDCP for legacy case and NG-RAN case (Huawei, China Unicom)

- R3-212193, CP-UP separation for eNBs (Ericsson)

- R3-212196, General principles for eNB CP-UP separation (Ericsson)