3GPP TSG-RAN WG3 Meeting #112-e	R3-212712

17 – 27 May 2021

Online

Agenda Item:	23.2.2

Source:	Ericsson

Title:	Signaling Transport - Summary of offline discussion

Document for:	Discussion and Decision

# 1	Introduction

The scope of the email discussion has been captured as followed:

CB: # 49_eNBarchEvo_SigTran - (HW) The functions as specified for E1 signaling bearer should also be supported over the new interface. Capture the new logical entities to each occurrence of gNB-CU-CP and gNB-CU-UP for ng-eNB-CU and eNB CP-UP separation in TS 38.462. - (E///) Update the Scope of TS38.462 as suggested Update the References clause of TS38.462 with the specs relevant to the LTE CU-UP separation Update the Definitions clause of TS38.462 with the terms relevant to the LTE CU-UP separation Clauses 4.1 (Function and protocol stack) and Clause 5 (Data link layer) can be left unchanged For Clause 6 (IP layer), add the new eNB logical entities names to each occurrence of the gNB-CU-CP and gNB-CU-UP For clause 7 (Transport layer), add a note establishing the equivalence between all the CP logical entities and between all the UP logical entities - Chair: merge/revise as agreeable 2026, 2197 (E/// - moderator) Summary of offline disc R3-212712

This contribution captures the email discussion.

# 2	For the chairman’s notes

To be captured later

# 3	Email discussion

During RAN3#111-e, the following agreements were taken:

- use SCTP as transport bearer for AP signaling

- reuse the E1 signaling bearer protocol stack for the new interface

- the same functions as specified for E1 signaling bearer should also be supported over the new interface

- DTLS over SCTP should be supported

- Multiple SCTP endpoints per CP/UP pair should be supported

- The first SCTP association could be triggered either by CP or by UP, but the additional SCTP associations should be initiated by UP

- SCTP multi-homing should also be supported

And in general the following was captured in Chairman’s notes:

Common understanding is that IPsec is feasible

Common understanding is that the same principles as for all current RAN3 interfaces are kept

## 3.1 Functions provided by E1 signalling bearer

It was already agreed that the same functions as specified for E1 signaling bearer should also be supported over the new interface. These functions are detailed in [2]:

- Provision of reliable transfer of E1AP message over E1 interface.

- Provision of networking and routeing function

- Provision of redundancy in the signalling network

- Support for flow control and congestion control

Question 1.1: Are all the functions described above applicable to E1 signalling bearer for LTE CP/UP split?

| Company | Response |
| --- | --- |
| Ericsson | Yes. Agreement should be captured in BL CR |

## 3.2 How to capture agreements and new logical nodes

In [4], there is a proposal for each section of 38.462. The following questions can be used to decide how to update each section with agreements and new logical nodes.

Question 2.1: How to capture agreements in section 1 Scope?

| Company | Response |
| --- | --- |
| Ericsson | Add new sentences including the new logical names, as in [5] |

Question 2.2: How to capture agreements in section 3 Definitions and abbreviations?

| Company | Response |
| --- | --- |
| Ericsson | Add only references to definitions, as in [5] |

Question 2.3: How to capture agreements in section 4 E1 signalling bearer?

| Company | Response |
| --- | --- |
| Ericsson | Can be left unchanged |

Question 2.4: How to capture agreements in section 5 Data link layer?

| Company | Response |
| --- | --- |
| Ericsson | Can be left unchanged |

Question 2.5: How to capture agreements in section 6 IP layer?

| Company | Response |
| --- | --- |
| Ericsson | Add the new eNB logical entities names to each occurrence of the gNB-CU-CP and gNB-CU-UP, as in [5] |

Question 2.6: How to capture agreements in section 7 Transport layer?

| Company | Response |
| --- | --- |
| Ericsson | Add a note establishing the equivalence between all the CP logical entities and between all the UP logical entities, as in [5] |

# 4	Conclusion

Result of the email discussion to be captured here

# 5	References

[1] RP-193181 - New WID: Enhanced eNB(s) architecture evolution (China Unicom, NTT Docomo)

[2] R3-212025 - Further discussions on signalling transport for the new interface (Huawei)

[3] R3-212026 - CR to 38.462 on the introduction of new interface

[4] R3-212194 - E1 Signaling Transport for eNB CP-UP separation (Ericsson)

[5] R3-212197 - E1 Signaling Transport for eNB CP-UP separation (Ericsson)