3GPP TSG-RAN WG3 #112-e	R3-212697

17 – 28 May 2021

Agenda Item:	20.2.1

Source:	Qualcomm Incorporated (moderator)

Title:	Summary of Offline Discussion on NTN Network Identifier Handling

Document for:	Approval

# Introduction

CB: # 78_NTN_NW_IDhandling

- (QC)

In NTN with earth-moving cells, mapped CGIs are generally used in NGAP unless otherwise stated.

In case either mapped or broadcast CGIs may be used in a specific procedure, add an optional indicator to signal which type of ID is used.

- (Nok)

The cell ID used in ULI, Paging Optimization, and Area of Interest is the “Mapped” cell ID;

The cell ID used in other cases is the “Uu” cell ID. FFS for the cell ID used in RNA.

- (E///)

Confirm that there is no stage 3 specification work need w.r.t. Target Cell Global ID IE contained in the XnAP HANDOVER REQUEST message. Consider the TP provided for TS 38.300.

Confirm that for NT cells, serving peer gNBs do not exchange served cell information within the List of Served Cells NR IE on XnAP.

- (HW)

For moving NTN cells, the Cell ID used over Uu should be a Cell ID selected in the set of the CGI fixed on Earth covered during the movement of the NTN beam. The Cell ID selected on Uu should not change during overall move of the NTN beam.

The Cell ID used on Uu is provided by OAM to the CU and the DU of the gNB. The mapping of the Cell ID used on Uu on CGI should be available in the CU and the DU

NG-RAN shall get UE location at least in terrestrial cell granularity when needed, e.g. not only at registration.

Discuss whether to apply V2X-like Zone definition is appropriated for the mapping of cell IDs used on Uu and fixed Earth CGI. The solution is pending to RAN2.

- (CMCC)

To actually use “fixed cell ID,” gNB needs to acquire UE location information to build the relationship between two types of cell ID.

RAN node maps the center of the serving cell for the UE to a geographical fixed Cell ID and provides it to AMF.

paging or handover procedure is related to “Uu” cell ID, not the “Virtual” cell ID.

- (CATT)

For NGAP Initial UE Message, NG-RAN node should still include only one “mapped CGI” as ULI. How to determine what CGI to include is up to implementation if the NG-RAN node cannot determine what “mapped cell” the UE is currently located in.

- Chair: work on st2 description for mapping – seems mapping can be configured/OAM and mapped CGIs could be generally used? Whether to mention specific cases? Whether to mention exchange over Xn? No or FFS st3 impact?

(QC - moderator)

Summary of offline disc R3-212697

# For the Chairman’s Notes

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

R3-20xxxd rev [in xxxh] – agreed

R3-20xxxe rev [in xxxi] – agreed

R3-20xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion

There are a number of aspects and proposals brought up, for convenience these are grouped as below:

- Usage of mapped CGIs in NG-RAN procedures and signalling

- Enablers for mapping (positioning acquisition)

- Other mapping aspects

## Usage of mapped CGIs in NG-RAN procedures and signalling

In [1] there is an analysis of NG functions / procedures, ending with the following proposal

Proposal 1[1]: In NTN with earth-moving cells, mapped CGIs are generally used in NGAP unless otherwise stated.

Proposal 2[1]: In case either mapped or broadcast CGIs may be used in a specific procedure, add an optional indicator to signal which type of ID is used.

[2] does a similar analysis, identifying the following uses

- Target Cell ID in HO

- UE History

- Paging optimization

- Area of Interest

- RRC Inactive (RNA)

Concluding that:

Proposal 1[2]: RAN3 agree following:

* the cell ID used in ULI, Paging Optimization, and Area of Interest is the “Mapped” cell ID.

* the cell ID used in other cases is the “Uu” cell ID. FFS for the cell ID used in RNA.

It also provides a stage 2 TP (section 16.x.5) which is effectively P1.

While [3] focusses on aspects also related to handover and cell relations, some of which may also be treated in other CBs. Its proposals are:

Proposal 1:	Confirm, that there is no stage 3 specification work need w.r.t. Target Cell Global ID IE contained in the XnAP HANDOVER REQUEST message. Consider the TP in Annex A for the BL CR for TS 38.300.

Proposal 2:	Confirm, that for NT cells, serving peer gNBs do not exchange served cell information within the List of Served Cells NR IE on XnAP.

It also includes a stage 2 TP containing P1. P1 rests on the basis “that it is safe to assume that the Target Cell Global ID is able to identify the actual target cell, irrespective of whether it represents a geo-fixed area or the actual broadcast cell ID, as long as the target gNB can distinguish the content of the Target Cell Global ID e.g. based on the cell ID numeric ranges or by a data base look-up”.

P2 seems to fall under the topic of cell relations, hence it is proposed to leave this discussion to CB#79.

Finally, [5] proposes (P3) that paging or handover procedure is related to “Uu” cell ID, not the “Virtual” cell ID. We should note however that paging had previously been discussed at the last meeting, and an agreement was taken. In our understanding, cell lists in paging optimization cannot be interpreted as Uu cells since there is no timing information attached to cell recommendations.

A possible way forward could consist of the following:

- Identify functions where mapped CGIs are always used – these for now could include ULI, AoI, Paging Optimization, PWS

- For handover signalling, assume that the nature of the target is either configured or can be deduced from the ID itself

- Other uses FFS (but handover approach could also apply)

- Possible merge of TPs in [2] and [3] to represent above (section 16.x.5) only

Please provide any view / comments on this topic and the proposal in bold below:

| Company | Comment |
| --- | --- |
| Thales | Agree to work on a merge of the TPs provided in [2] and [3] |
| Nokia | The 1st bullet is ok. The 2nd bullet may have issue. In case the HO msg includes a mapped cell ID, it may be difficult to identity the target “Uu” cell, since it is possible that part of more than 1 “Uu” cell (e.g. east of Uu cell#1 and west of Uu cell#2) are mapped to the same “mapped” cell ID. In addition, for mobility between TN and NTN, the TN gNB may not have the “mapped” cell ID and have to use the Uu cell ID. So it may better to use the “Uu” cell ID. The 3rd bullet is ok. The 4th bullet is ok. |

## Enablers for mapping (positioning acquisition)

We assume that the need for positioning acquisition (P1 of [5]) in being considered as part of the LS exchanges (see CB#4). Similarly, P3 in [4] (“NG-RAN shall get UE location at least in terrestrial cell granularity when needed e.g. not only at registration”) seems consensual and mostly handled elsewhere.

Then we have the following additional aspect from [4]:

Proposal 4:	RAN3 to discuss whether to apply V2X-like Zone definition is appropriated for the mapping of cell IDs used on Uu and fixed Earth CGI. The solution is pending to RAN2.

The moderator comment is that this appears to be a RAN2 matter, possibly related to an idea to obfuscate data for privacy reasons. Hence it is not clear how far RAN3 should discuss it here.

The moderator proposed way forward is:

- To reiterate the need for positioning information at least at TN cell granularity, and assume this is further treated in CB#4

- To assume that the proposal above is discussed in RAN2, and RAN3 can wait for the outcome

Please provide any view / comments on this topic and the proposal in bold below:

| Company | Comment |
| --- | --- |
| Thales | We agree with the need for positioning information at least at TN cell granularity We recommend to explicitly ask RAN2 through a liaison statement whether to apply V2X-like Zone definition is appropriated for the mapping of cell IDs used on Uu and fixed Earth CGI. |
| Nokia | Ok for the 1st bullet, but not sure for the 2nd bullet. It is unclear how the V2X-like zone helps, vs. using the UE’s GNSS info directly for mapping in the gNB. Anyway, this is mainly in RAN2 scope. RAN3 can discuss it later after RAN2 make a decision. |

## Other CGI mapping aspects: handling of Uu cell ID

Ref [4] has the following proposals:

Proposal 1:	For moving NTN cells, the Cell ID used over Uu should be a Cell ID selected in the set of the CGI fixed on Earth covered during the movement of the NTN beam. The Cell ID selected on Uu should not change during overall move of the NTN beam.

Proposal 2:	The Cell ID used on Uu is provided by OAM to the CU and the DU of the gNB. The mapping of the Cell ID used on Uu on CGI should be available in the CU and the DU

The moderator’s comment is that P1 is a possible implementation, but it is not clear that it needs to be mandated. P2 is also reasonable, since anyway the cell identifier needs to be broadcast and is known to the NG-RAN, but it is not clear what the impacts are. OAM requirements seem to be considered in other related CBs.

Please provide any view / comments on this topic and the proposals above:

| Company | Comment |
| --- | --- |
| Thales | Agree with both proposal. Recommend to agree explicitly that “The Cell ID used on Uu can be provided by OAM to the CU and the DU of the gNB. The relationship between the Cell ID used on Uu and the CGI should be available in the CU and the DU” |
| Nokia | For P1, It is unclear about the impact to RAN3 spec. As long there is a mapping in RAN and CN, it may be not matter whether the Uu cell ID is a cell ID selected from a set of CGI…., or any other cell ID. Please clarify the impact to RAN3 spec. For P2, CU performs the mapping. Could you please clarify why DU need to know the mapping? |

## Other CGI mapping aspects: further mapping details

Ref [5] has the following proposal:

Proposal 2: RAN node maps the center of the serving cell for the UE to a geographical fixed Cell ID and provides it to AMF.

The moderator’s comment is that this seems a possible implementation, but it is not clear that it needs to be mandated, or perhaps the proposal needs to be clarified. The mapping to a geographical fixed cell can be done based on the UE’s location and/or the known coverage of the current serving cell (although the former seems simpler, but the latter could be seen as a fallback when the UE’s location is not available).

Ref [6] looks at what happens when precise location is not available and proposes:

Proposal: For NGAP Initial UE Message, the NG-RAN node should still include only one “mapped CGI” as ULI. How to determine what CGI to include is up to implementation if the NG-RAN node cannot determine what “mapped cell” the UE is currently located within.

This seems related to above in the sense that the mapping for the UE may not be possible at TN granularity. Here there are options e.g. as above, take the center of the serving cell to realize the mapping, or alternatively use some kind of “large cell” identifier.

Note there is also some overlap with other discussions.

A general question is whether 3GPP should provide some guidance on the mapping, and also on the mapping for a UE when only very rough location information is available.

Please provide any view / comments on this topic and the proposals above:

| Company | Comment |
| --- | --- |
| Thales | It should be possible to define a CGI cell smaller than NTN beam foot print. The corresponding geographical area of a given CGI may be defined with the geographical location of its center and its range (e.g. in km). The shape of the CGI (e.g. circle, hexagonal, ..) can be implementation dependent. |
| Nokia | This may be an implementation issue. |

## Further aspects

Please add any further aspects that are in scope and were not included in the above:

| Company | Comment |
| --- | --- |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-211707, “General usage of cell identity signalling in NGAP” (Qualcomm Incorporated)

R3-211896, “(TP for BL CR for TS 38.300) Cell ID handling on NG interface” (Nokia, Nokia Shanghai Bell)

R3-212109, “Discussion on handling and applicability of Network Identifiers on Xn and NG interface” (Ericsson)

R3-212245, “On mapping of the Cell identities of NTN cells” (Huawei)

R3-212476, “Discussion on Network Identifier Handling” (CMCC)

R3-21181, “Discussion on CGI handling in RAN” (CATT)