3GPP TSG-RAN WG3 #112-e	R3-212605

Online, 17th - 27th May 2021

Agenda Item:	8.1

Source:	Ericsson (moderator)

Title:	CB: # 8_5GarchSatAccess - Summary of email discussion

Document for:	Approval

# Introduction

CB: # 8_5GarchSatAccess

- If approach b) is preferable, then UE location info is needed in the gNB? (related to other LS?)

- need reply?

(E/// - moderator)

[NWM] Summary of offline disc R3-212605

# For the Chairman’s Notes

Propose the following:

draft LS in R3-212113 (to be revised for final LS) agreed

# Discussion [if needed]

## Necessity of the LS

Please provide your view on the necessity of the LS.

| Company | Comment |
| --- | --- |
| Ericsson | Given the nature of this decision, which was a major step in RAN2 discussions, (and given the experienced unawareness of NSSF details in various WGs experienced in the past) it seems straight forward to confirm the necessity of the LS. |
| Thales | We agree on the need to reply to RAN2 on this topic to highlight what we expect in terms of function/behavior that needs to be defined by RAN2. |
| Nokia | Is the reply LS really needed? The RAN2 LS ask RAN3 to consider the RAN2 feedback on previous RAN3 question. The RAN3 BL CR already captured the mapped cell ID. UE location aspect is handled in a separate/dedicated LS (and it is also mentioned in the draft LS). We do not see a need for the LS. |
| Qualcomm | It seems that RAN2 somewhat split the LS discussions, so we either add any relevant points on the LS on UE Location or indeed reply to this. No objection to reply specifically to this LS. |

## Comments on the LS, if any

This is to collect comments, if any and if necessity is confirmed, on the LS as such.

| Company | Comment |
| --- | --- |
| Thales | About the proposed TP for the LS: With RAN2 confirmation that approach b) is preferable, it is then confirmed that the UE location information is needed in the gNB, as discussed in a dedicated LS in more detail (WHICH LS ?). RAN3 has discussed the use of user location information with respect to NNSF (please see the dedicated LS) (WHICH LS ?). Once such information is available in the gNB, the cell ID mapping necessary for approach b) is possible and approach b) is then fully supported. We should also take the opportunity to ask RAN2 about the following whether to apply V2X-like Zone definition is appropriated for the mapping of cell IDs used on Uu and fixed Earth CGI. (See CB#78) whether the gNB is able to detyect when the UE moves across the country border, in case the serving NTN cell serves part (or all) of more than 1 country (see CB#81) |
| Qualcomm | If we reply, it is preferable not to add any extra points to avoid continuing the parallel traffic. This reply should clearly point to the other LS for further traffic, For that reason, we would prefer to take out the second line (regarding NNSF) so we have a sharper closure. Then in the other LS we can have any considerations regarding what is available e.g. prior to AS security being set up, or any other such details. |

# References

R3-211430	Reply LS on SA WG2 assumptions from conclusion of study on architecture aspects for using satellite access in 5G (RAN2)	LS in

R3-212112	NTN architecture aspects and cell ID mapping (Ericsson), discussion

R3-212113	[DRAFT] [Reply] LS on SA WG2 assumptions from conclusion of study on architecture aspects for using satellite access in 5G (Ericsson), draft LS out