3GPP TSG-RAN WG3 #112-e							R3-212649

17-27 May 2021

Online

Agenda Item:	17.3

Source:	ZTE (moderator)

Title:	Summary of Offline Discussion on RANSlicing2-Slice_Conclusion

Document for:	Approval

# Introduction

# RANSlicing2-Slice_Conclusion

- TR updates:

- update the description of section 6.2.3.1 and 6.2.3.2 of the TR with the response from SA5 in R3-211633?  Nok

- Modify the evaluation table according to the feedback received from SA2 and SA5, as per text in R3-211624 and R3-211902? Qualcomm, HW

- Update the editor notes part in section 6.2 either removing it or changing it to be note in R3-211902? HW

- Capture agreements as TP for TR updates, revise/merge and check details, split work, if needed

- Remapping solution evaluation and conclusion:

- The Slice Resource Re-partitioning solution analysis based on SA5 LSin (section 6.2.3.1 and 6.2.3.2) ?  LS reply to SA5? E///

- RAN3 concluded that scenarios 2 and 4 in TR38.832 concern a situation of sub-optimal slice coverage planning, that can be resolved by slice coverage optimisation hence these scenarios should not be pursued in normative work? RAN3 concluded that the solutions addressing scenarios 2 and 4 are not deemed feasible due to their impact on CN and UE? E///

- Develop details of solutions in 6.2.3 (including OAM requirements if applicable) to the remaining scenarios (e.g. resource shortage in case of Intra-RA mobility, slice resource shortage for MR-DC and slice overload in RAN node in absence of mobility)? Qualcomm

- Update the conclusion of the TR to select one of the solutions described in 6.2.1 i.e. where re-mapping decision would be in the NG-RAN? Nok

- Only resource management solution is used to solve the resource shortage case? only slice remapping solutions are used to solve the not supported slice cases? CATT

- For solutions addressing scenario 1/3/5/6, continue to refine these solutions at the normative phase, which are already captured in the conclusion in TR 38.832. And the “after feedback from SA2 and SA5” in the conclusion part in Section 7.2 can be removed?For solutions addressing scenario 2/4, the 6.2.1.1.1 (Policy configured by OAM) may be further refined at the normative phase. And the conclusion part in section 7.2 can be updated accordingly? HW

- The solutions to support Scenarios 2 and 4 should be specified in normative phase? Solution 6.2.2, Solution 6.2.1.2.1.4,  Solutions 6.2.1.1.1 and 6.2.1.1.2 should be ruled out? Solutions 6.2.1.1.3 and 6.2.4 should be selected for normative work to support Scenarios 2 and 4 with the enhancement to change the slice of the on-going PDU session in CN and UE? LG

- RAN3 recommends all solutions in section 6.2.3 to normative phase? Send LS to SA5 to inform that RAN3 decides to implement solutions in section 6.2.3, and clearly indicate RAN3 requirements regarding each solution?  RAN3 recommends solution 6.2.1.1.1 (Policy configured by OAM) to normative phase? Send LS to SA2 to inform RAN3’s recommendation on CN/UE impacting solution? CMCC

- Solution 6.2.1 is recommended in normative phase? Samsung

- From SA5 and SA2 point of views, solutions in section 6.2.3.1, 6.2.3.2, 6.2.3.3 are feasible. It is propose to let SA5 decide whether to takes these candidate solutions in normative stage?  For policy generation in section 6.2.1.1.4, it is proposed to specify it in normative phase? Providing slice remapping/fallback information to CN should be removed from figure 6.2.2.1-1,figure 6.2.2.2-1, figure 6.2.2.6-1 and figure 6.2.2.7-1, the corresponding descriptions are also need to be removed. With this change, the message sequences in these figures can be candidate for slice remapping solutions in intra-RA scenario 1,3,5,6? Slice remapping solutions for inter-RA scenario 1,3,5,6 may need further evaluation in WI stage or postpone to later releases? ZTE

- Capture TP for conclusion

(ZTE - moderator)

Summary of offline disc R3-212649

Note:

Two rounds of discussion.

The first round email discussion plan to be end .(Thursday end of the day, 2021-5-20)

The second round email discussion plan to be end before the email deadline at second week(Thursday 12:00 UTC).

# For the Chairman’s Notes

Propose the following:

# Discussion

## Update suggestions for solution part of TR38.832

### Views on section 6.2 Solutions

#### Views on section 6.2.1 Re-mapping decision in NG-RAN node

One contribution [10] provide tow type modification proposals below

The first one is remove the editor note from section 6.2.1:

6.2.1	Re-mapping decision in NG-RAN node

In solutions where the target NG-RAN node decides the re-mapping at incoming handover, the target NG-RAN node should be aware of the re-mapping policy for the involved PDU session. The following options are available:

Q1: Please provide your view on the update suggestion.

| Company | Yes/No/Other view | Comment |
| --- | --- | --- |

The other one is change “Editor note ” to “Note” and remove FFS from TR in section 6.2.1, 6.2.2, 6.2.3.

One update example is shown below:

Note: Whether and how the UE is aware of slice remapping needs the involvement with SA2 if necessary.

Q2: Please provide your view on the update suggestion.

| Company | Yes/No/Other view | Comment |
| --- | --- | --- |

One contribution [14] provide modification proposal for this section, the detail is shown as below

##### 6.2.1.1.4	 Slice Re-mapping policy reuse information provide by CN (during Initial Context Setup)

Signaling in INITIAL CONTEXT SETUP REQUEST

During initial context setup, the CN includes in the INITIAL CONTEXT SETUP REQUEST message the Allowed NSSAI IE,which can be used for NG-RAN to for decision which Slice(s) can can be re-mapped for a PDU session or for UE.

In this option the granularity of the re-mapping policy is Per UE.

Example of per UE policy:

UE 1, any PDU session of S-NSSAI 1 <> re-mapped list (only one S-NSSAI in allowed NSSAI IE,which decided by NG-RAN node )

Signaling from Source NG-RAN node

At the time of handover, the source NG-RAN node includes in the Xn Handover Request message the current PDU Session, the associated S-NSSAI and also the Allowed NSSAI to which this PDU session can be mapped. The target NG-RAN node can decides which S-NSSAI can be selected from Allowed NSSAI and mapped the original S-NSSAI to an appropriate S-NSSAI.

In this option the granularity of the re-mapping policy is Per UE.

Example of per UE policy:

UE 1, any PDU session of S-NSSAI 1 <> re-mapped list (only one S-NSSAI in allowed NSSAI IE,which decided by NG-RAN node )

The above slice-remapping principle are applicable to intra-RA handover scenario, MR-DC scenario and intra NG-RAN node scenario.

Q3: Please provide your view on the modification.

| Company | Yes/NO/Other view | Comment |
| --- | --- | --- |

##### Views on section 6.2.1.2 Slice Re-mapping Message Sequence Charts

One contribution [14] provide modification proposal for this section, the detail is shown as below:

###### 6.2.1.2.1	Slice Remapping decision in target gNB at Xn based handover

Figure 6.2.1.2.1.1-1: Slice re-mapping/fallback determined by the T-gNB

- The AMF sends the Initial context setup message to the S-gNB including the Allowed NSSAI. Here the Allowed NSSAI is used for slice re-mapping.

- The S-gNB sends the HANDOVER REQUEST message to the T-gNB including the Allowed NSSAI.

- If the UE’s ongoing slice(s) is rejected in the target gNB, the target gNB takes the local slice load and the Allowed NSSAI into account and makes the slice re-mapping/fallback decision. .

- The T-gNB send the PATH SWITCH REQUEST message to the AMF which may include the slice remapping/fallback decision.

- The AMF responds the PATH SWITCH REQUEST ACKNOWLEDGE message.

Note:  The slice remapping/fallback decision contained in Path Switch Request message provides information for Core network, e.g. for Billing.

###### 6.2.1.2.2	Slice Remapping decision in target gNB at NG based handover

Figure 6.2.1.2.1.2-1: Slice re-mapping/fallback determined by the T-gNB

- The AMF sends the Initial context setup message to the S-gNB including the Allowed NSSAI. Here the Allowed NSSAI is used for slice re-mapping.

- The S-gNB sends the HANDOVER REQUIRED message to the AMF including the Allowed NSSAI.

- The AMF sends the HANDOVER REQUEST message to the T-gNB including the Allowed NSSAI.

- If the UE’s ongoing slice(s) is rejected in the target gNB, the target gNB takes the local slice load and the Allowed NSSAI into account and makes the slice re-mapping/fallback decision. The T-gNB may include the re-mapped/fallback decision in the HANDOVER REQUEST ACKNOWLEDGE message to the AMF.

- The AMF sends the HANDOVER COMMAND message to the S-gNB.

Note:  The slice remapping/fallback decision contained in Path Switch Request message provides information for Core network, e.g. for Billing.

.

###### 6.2.1.2.2.1	Slice Remapping decision in SN for MR-DC case

Figure 6.2.1.2.2.1-1: Slice re-mapping/fallback determined by the SN

- The MN sends the SN Addition Request message to the SN with the Allowed NSSAI. Here the Allowed NSSAI list is used for slice re-mapping.

- If the UE’s ongoing slice(s) is rejected by the SN, the SN takes the local slice load and the Allowed NSSAI into account and makes the slice re-mapping/fallback decision. The SN shall include the slice re-mapping/fallback decision in the SN Addition Request Acknowledge message to the MN.

- The MN may send the slice re-mapping/fallback decision to the AMF through the PDU Session Modification Indication message.

- The AMF responds the PDU Session Modification Confirmation message.

Note:  The slice remapping/fallback decision contained in Path Switch Request message provides information for Core network, e.g. for Billing.

###### 6.2.1.2.2.2	Slice Remapping decision in MN for MR-DC case

Figure 6.2.1.2.2.2-1: Slice re-mapping/fallback determined by the MN

- The MN makes the slice re-mapping/fallback decision and include the decision in the SN Addition Request message to the SN.

- The SN confirms the slice re-mapping/fallback decision made by the MN with the SN Addition Request Acknowledge message.

- The MN may send the slice re-mapping/fallback decision to the AMF through the PDU Session Modification Indication message.

- The AMF responds the PDU Session Modification Confirmation message.

Note:  The slice remapping/fallback decision contained in Path Switch Request message provides information for Core network, e.g. for Billing.

###### 6.2.1.2.5	Slice Remapping Solution for Scenario 6

At the same time the NG-RAN node may notice that another slice 2 which is not overloaded has resources available and is still compatible with the SLA of slice 1.

In short, there is a potential that some unloaded but "good enough or better" alternative slices in the RAN could be used for the subscriber to continue to receive service.

NG-RAN node may send the slice re-mapping/fallback decision to the AMF for e.g. billing.

Q4: Please provide your view on the update.

| Company | YES/NO/other view | Comment |
| --- | --- | --- |

Based on majorities view,

Conclusion 1: Wait views input

#### Views on section 6.2.3 Resource management in NG-RAN node

##### Views on section 6.2.3.1 Configuration Based Solution

One contribution [3] provide modification proposal for this section, the detail is shown as below:

6.2.3.1	Configuration Based Solution

The solution builds on the resource modelling described in TS 28.541. The following analysis is provided for the scenario 1 and scenario 2 respectively:

- Scenario 1: Slice resource shortage in case of Intra-RA mobility and Inter-RA mobility

As specified in TS 28.541, the slice re-mapping between different S-NSSAIs can be achieved via the prioritized resource modeling. For example, suppose UE’s ongoing slice is S-NSSAI 1 configured with rRMPolicyMaxRatio policy, which can use at least one of the shared resources, prioritized resources and dedicated resources. If the dedicated resources are not available, it can use other un-used prioritized and shared resources according to TS 28.541 as follows:

- it can explicitly use resources belonging to other S-NSSAIs;

- it cannot use the dedicated but not used resources of other S-NSSAIs;

- it can preempt the used  shared resources from other S-NSSAIs.

Q5: Please provide your view on the update.

| Company | YES/NO/other view | Comment |
| --- | --- | --- |

Based on majorities view,

Conclusion 1: Wait views input

### Views on section 6.3 of Solution evaluation

Three contributions [7][10][15] provide modification proposal for this section, the detail is shown as below:

Table 6.3-1: Evaluation of the solutions

| Criteria Solution | RAN impact | Core impact | OAM impact | UE impact | Effectiveness | Applicable scenarios |
| --- | --- | --- | --- | --- | --- | --- |
| 6.2.1: Re-mapping decision in NG-RAN node | 6.2.1.1.1: Policy configured by OAM | Option 2: RAN is configured with re-mapping policy from the OAM. RAN may signal the slice remapping decision to CN. | Option 1: CN is configured with re-mapping policy from the OAM. FFS if the CN needs to be notified in case of any slice-remapping, e.g. for charging purpose. CN performs slice remapping. CN reconfigures UE with NAS signalling to associate an ongoing PDU Session to a new S-NSSAI. Feasibility would require SA2 study. Option 2: CN is configured with re-mapping policy from the OAM. CN may be notified in case of any slice-remapping, e.g. for charging purpose. CN reconfigures UE with NAS signalling to associate an ongoing PDU Session to a new S-NSSAI. Involvement with SA2 may be needed for scenario 2/4. How the slice remapping is done in 5GC needs involvement with SA2 for scenario 2/4. | OAM configures slice re-mapping policy to the NG-RAN, CN (if verification is needed). | Option 1: UE needs to be reconfigured at NAS level to associate an ongoing PDU Session to a new S-NSSAI. Feasibility would require SA2 study. Option 2: UE needs to be reconfigured at NAS level to associate an ongoing PDU Session to a new S-NSSAI. Involvement with SA2 may be needed for scenario 2/4. | Option 1: Solution at the cost of CN, OAM, RAN and UE impact Required procedures in UE and CN are not supported. Feasibility would require SA2 study. | 1, 2, 3, 4, 5, 6 |
|  | 6.2.1.1.2/6.2.1.1.3: Policy configured by CN | Option 2; RAN is signalled with the remapping policy from CN/the source RAN node. RAN may signal the slice remapping decision to CN. | Option 1: CN is configured with remapping policy from the OAM, and signals the re-mapping policy to the NG-RAN. FFS if the CN needs to be notified in case of any slice-remapping, e.g. for charging purpose. CN performs slice remapping. CN reconfigures UE with NAS signalling to associate an ongoing PDU Session to a new S-NSSAI. Feasibility would require SA2 study. Option 2; CN is configured with remapping policy from the OAM, and signals the re-mapping policy to the NG-RAN. CN may be notified in case of any slice-remapping, e.g. for charging purpose. CN reconfigures UE with NAS signalling to associate an ongoing PDU Session to a new S-NSSAI. Involvement with SA2 may be needed for scenario 2/4. How the slice remapping is done in 5GC needs involvement with SA2 for scenario 2/4. | OAM configures slice re-mapping policy to the CN. | Option 1: UE needs to be reconfigured at NAS level to associate an ongoing PDU Session to a new S-NSSAI. Feasibility would require SA2 study. Option 2: UE needs to be reconfigured at NAS level to associate an ongoing PDU Session to a new S-NSSAI. Involvement with SA2 may be needed for scenario 2/4. | Solution at the cost of CN, OAM, RAN and UE impact Required procedures in UE and CN are not supported. Feasibility would require SA2 study. | 1, 2, 3, 4, 5, 6 |
|  | 6.2.1.1.4: Slice Re-mapping policy reuse information provide by CN | RAN leverage legacy information (e.g. Allowed NSSAI) provide by CN as input for re-mapping policy. If RAN decide to signal the slice remapping decision to CN,the usage of decision in CN is for billing. | No impact | No impact | No impact | Solution with RAN impact. | Intra-RA of 1,3,5,6 |
|  | 6.2.1.2.1.4: 5GC Solution based on SSC-mode 3 | RAN is signalled with the remapping policy from CN/the source RAN node if this option is used. It requires support of updated “SSC-mode 3”, e.g., the target node needs to temporarily accept the PDU session even if slice is not supported in the cell. | CN is configured with remapping policy from the OAM, and signals the re-mapping policy to the NG-RAN if this option is used. It requires modification of the “SSC mode 3” procedure in CN. Feasibility would require SA2 study.. | OAM configures slice re-mapping policy to the RAN if this option is used. | The update of “SSC-mode 3”. Feasibility would require SA2 study. | Solution with OAM, CN, RAN and UE impact Required procedures in UE and CN are not supported. Feasibility would require SA2 study. | 2, 4 |
| 6.2.2: Partially slice re-mapping in NG-RAN | Solution with CN involvement | Same as 6.2.1.1.2/6.2.1.1.3: Policy configured by CN | Same as 6.2.1.1.2/6.2.1.1.3: Policy configured by CN | Same as 6.2.1.1.2/6.2.1.1.3: Policy configured by CN | Same as 6.2.1.1.2/6.2.1.1.3: Policy configured by CN | Same as 6.2.1.1.2/6.2.1.1.3: Policy configured by CN | Same as 6.2.1.1.2/6.2.1.1.3: Policy configured by CN |
|  | Solution without CN involvement | RAN is configured with re-mapping policy from the OAM. New functionality to support semi-handover case. New behaviour in new gNB (allow usage by non-supported slice even though gNB does not support slice). Requires Xn support from inside old RA to any node inside new RA (unless continuity is broken later) | New functionality to support the new handover case, where the UE is connected to target but source maintains UE signalling connection with CN. It is FFS how the CN handles RA update from UE. | OAM configures slice re-mapping policy to the NG-RAN. | New functionality to support the new handover case, where the UE is connected to target but source maintains UE signalling connection with CN. RA procedure and consistency between allowed S-NSSAI in new RA are FFS. Involvement with SA2 may be needed. | Solution at the cost of CN, OAM, RAN and UE impact. Feasibility would require SA2 study. | 2, 4 |
| 6.2.3: Resource management in NG-RAN node | 6.2.3.1: Configuration based Solution | RAN is configured with re-mapping policy from the OAM. RAN may possibly signal the RAN-internal slice resource change to CN. | CN may be notified in case of any RAN-internal slice resource change e.g., for charging purpose. | OAM configures slice resource policy to the NG-RAN. A study in SA5 may be needed if further capabilities are deemed required by RAN beyond those already supported. | No impact | Simple and effective solution at the main cost of the OAM impact. | 1, 3, 5, 6. |
|  | 6.2.3.2: Slice resource re-partitioning | RAN is configured with re-mapping policy from the OAM. RAN may possibly signal the RAN-internal slice resource change to CN | CN may be notified in case of any RAN-internal slice resource change e.g., for charging purpose. | OAM configures slice resource re-mapping policy to the NG-RAN. A study in SA5 may be needed if further capabilities are deemed required by RAN beyond those already supported. | No impact | Simple and effective solution at the main cost of the OAM impact | 1, 3, 5, 6 |
|  | 6.2.3.3: Multi-carrier radio resource sharing | No impact. | No impact | No impact SA5 noted that the concept of RRMPolicyRatio is configurable per cell, but not per frequency. | No impact | Simple and effective solution. It requires the same slice coverage across different frequencies. | 1, 3, 5, 6 |
| 6.2.4: Slice Remapping decision in 5GC | No impact | CN is configured with remapping policy from the OAM. New intra-CN procedure is needed to change the slice for an ongoing PDU session. Feasibility would require SA2 study | OAM configures slice re-mapping policy to the CN. | UE needs to be reconfigured at NAS level to associate an ongoing PDU Session to a new S-NSSAI. Feasibility would require SA2 study . | Solution with OAM, CN and UE impact . Feasibility would require SA2 study Required procedures in UE and CN are not supported. | 2, 4 |

There are two different interprets on solution 6.2.1 Re-mapping decision in NG-RAN nod in the table.

Option 1:  For Scenario 1,2,3,4,5,6, CN performs slice remapping.CN reconfigures UE with NAS signalling to associate an ongoing PDU Session to a new S-NSSAI. Feasibility would require SA2 study.

Option 2:  CN may be notified in case of any slice-remapping, e.g. for charging purpose. For Scenario 2,4, CN reconfigures UE with NAS signalling to associate an ongoing PDU Session to a new S-NSSAI.  Involvement with SA2 may be needed for scenario 2/4.

Q6: Please provide your view on the options.

| Company | Option 1, 2, other view | Comment |
| --- | --- | --- |

One contribution [15] provide a new item for the table, the detail is shown as below:

6.2.1.1.4: Slice Re-mapping policy reuse information provide by CN

Q7: Please provide your view on the update.

| Company | Yes/No, other view | Comment |
| --- | --- | --- |

Based on majorities view,

Conclusion 1: Wait views input

## Update suggestions for conclusion part of TR38.832

### Views on Conclusions on Solutions for Scenarios 1, 3, 5, 6

One contribution [3] provide modification proposal for this section, the detail is shown as below:

Conclusions on Solutions for Scenarios 1, 3, 5, 6:

The solutions 6.2.3.1 and 6.2.3.2 to support following RAN slicing scenarios are recommended by RAN3 to be specified in normative phase:

-	Resource shortage in case of Intra-RA mobility

-	Slice resource shortage for MR-DC

-	Slice overload in RAN node in absence of mobility

The solutions 6.2.3.1 and 6.2.3.2 are expected to be refined during normative phase

One contribution [7] provide modification proposal for this section, the detail is shown as below:

For release 17, it is recommended that normative work is based on solutions that address the above without PDU session slice remapping in order to avoid CN and UE impacts (i.e., solutions described in 6.2.3, with details adapted as needed for application to the above scenarios).

In future releases, solutions that include slice remapping may be considered if supported by SA2..

One contribution [9] provide modification proposal for this section, the detail is shown as below:

The solutions to support scenarios 1,3,5,6 are recommended by RAN3 to be specified in normative phase:

-	The existing SA5 specification can be reused or enhanced for Resource management solution

-	Slice remapping not specified for these scenarios

One contribution [10] provide modification proposal for this section, the detail is shown as below:

The involvement with other groups is expected and can be continued during the normative phase.

One contribution [11] provide modification proposal for this section, the detail is shown as below

The following solutions were concluded to be feasible after receiving SA2 and SA5 feedback:

- Configuration based Solution (section 6.2.3.1 of TR38.832)

- Slice resource re-partitioning (section 6.2.3.2 of TR38.832)

- Multi-carrier radio resource sharing (section 6.2.3.3 of TR38.832)

One contribution [13] provide modification proposal for this section, the detail is shown as below

For non CN/UE impacting solutions which address scenarios 1, 3, 5, 6, RAN3 recommends all solutions in section 6.2.3 to normative phase.

For CN/UE impacting solutions which address all scenarios, RAN3 recommends solution 6.2.1.1.1 (Policy configured by OAM) to normative phase.

One contribution [14] provide modification proposal for this section, the detail is shown as below

The corresponding solutions need to be specified during normative phase in R17.

The standard impact are listed as below:

- Reusing/enhancing the Allowed NSSAI from CN as re-mapping policy used by NG-RAN node;

- For Xn and NG based handover, the Allowed NSSAI used for re-mapping needs to be transferred in the handover request message. Slice

- For MR-DC case, the slice re-mapping decision is allowed to be made in MN or SN, the corresponding signalling procedure needs to be supported.

- For all case in scenario 1,3,5,6, the slice remapping/fallback decision allowed to be send to CN for billing usage.

One contribution [16] provide a proposal :

solution 6.2.1 is recommended in normative phase.

Based on above analysis:

For solutions without including CN slice remapping:

5 companies [3][7][9][11][13] think solution 6.2.3.1 and 6.2.3.2 are feasible and 4 companies [3][7][9][11][13]propose the two solutions into normative phase.

4 companies[7][9][11][13] think solution 6.2.3.3 is feasible and 3 companies propose it into normative phase.

1 company [14] provide update solution 6.2.1.1.4 based on 6.2.1 and  propose it into normative phase.

Q8: For scenario 1,3,5,6 and solution without including CN slice remapping, Please provide your view that which solutions recommended in normative phase.

| Company | solution | Comment |
| --- | --- | --- |

For solutions with CN slice remapping:

4 company [16][13][10] think solution 6.2.1.1 is recommended in normative phase.

2 company  [13] think rest of 6.2.1 are also recommended in normative phase.

1 company  [7] thinks solutions that include slice remapping can be consider in future release.

Q9: For scenario 1,3,5,6 and solution with CN slice remapping, Please provide your view that which solutions recommended in normative phase.

| Company | solution | Comment |
| --- | --- | --- |

Q10: For scenario 1,3,5,6 , Please provide other view for solution recommended in normative phase, if any.

| Company | solution | Comment |
| --- | --- | --- |

Based on majorities view,

Conclusion 1: Wait views input

### Views on Conclusions on Solutions for Scenarios 2, 4

One contribution [7] provide modification proposal for this section, the detail is shown as below:

Conclusions on Solutions for Scenarios 2, 4:

RAN3 is not able to make any recommendations on solutions to support scenario 2 and 4 during the Study Item. All solutions addressing these scenarios have been found to have both UE and CN impacts that would require future study by SA2..

One contribution [8] provide modification proposal for this section, the detail is shown as below:

Conclusions on Solutions for Scenarios 2, 4:

RAN3 is not able to make any recommendations on solutions to support scenario 2 and 4 during the Study Item. RAN3 would like to postpone the feasibility of addressing scenario 2 and 4, including potential solution selection, until SA2’s feedback.

RAN3 makes the recommendation to select one of the solutions of section 6.2.1 where the re-mapping decision is done in the NG-RAN. Final selection among the solutions in 6.2.1 can take place in the work item phase.

And provide  a solution to limit impact of CN/UE of scenario 2,4:

Proposal 1: define a re-mapping “supporting UE” as a UE which will NOT locally tear down the PDU session when receiving an Allowed NSSAI not including the slice of the PDU session in the Register Update following the handover.

One contribution [9] provide modification proposal for this section, the detail is shown as below

The solutions to support scenarios 2, 4 are recommended by RAN3 to be specified in normative phase:

- Slice level slice remapping is specified

- Slice remapping policy is provided by CN

- Slice remapping decision in target gNB at Xn based handover

- Slice remapping decision in 5GC at NG based handover

One contribution [10] provide modification proposal for this section, the detail is shown as below

Conclusions on Solutions for Scenarios 2, 4:

For solutions addressing scenario 2/4, the 6.2.1.1.1 (Policy configured by OAM) may be further refined at the normative phase.

For the rest solutions, RAN3 is not able to make any recommendations during the Study Item.

One contribution [11] provide modification proposal for this section, the detail is shown as below

RAN3 has analysed solutions to Scenarios 2 and 4 after receiving feedback from SA2.

RAN3 concludes that scenarios 2 and 4 concern a situation of sub-optimal slice coverage planning, that can be resolved by slice coverage optimisation hence these scenarios should not be pursued in normative work.

RAN3 concluded that the solutions addressing scenarios 2 and 4 are not deemed feasible due to their impact on CN and UE.

One contribution [12] provide modification proposal for this section, the detail is shown as below

The following solutions to support Scenario 2 and 4 are recommended by RAN3 to be specified in normative phase:

-	Solution 6.2.1.1.3 (Slice Re-mapping policy configured by CN (during PDU session setup)),

-	Solution 6.2.4 (Slice Remapping decision in 5GC).

The following enhancements will be also progressed in the normative phase based on feedback from SA2 and CT1:

-	New intra-CN procedure to change the slice for an ongoing PDU session,

-	New NAS signaling with the UE in order to associate an ongoing PDU Session to a new S-NSSAI.

One contribution [15] provide a proposal :

solution 6.2.1 is recommended in normative phase.

Based on above analysis:

For solutions without including CN slice remapping:

1 company [3] thinks no recommendations on solutions to support scenario 2 and 4.

6 company [8] [9] [10] [12] [15] think to select one or all of the solutions of section 6.2.1 (e.g 6.2.1.1.1, 6.2.1.1.3 ) into normative stage. Final selection among the solutions in 6.2.1 can take place in the work item phase.

1 companies [11] thinks the scenario is not feasible.

Q11: For scenario 2,4 , Please provide other view for solution recommended in normative phase.

| Company | solutions | Comment |
| --- | --- | --- |

Based on majorities view,

Conclusion 1: Wait views input

## Views on LS ( Comments can be provided at 2nd round discussion )

### Response to SA5

An draft LS[5] was prepared for SA5 ,

RAN3 thanks SA2 for the LS reply on enhancement of RAN slicing. RAN3 took the replies from SA5 into account and concluded that the existing SA5 specifications are sufficient to support the “Configuration Based Solution” in section 6.2.3.1 of TR 38.832 v1.0.0 and the “Slice resource re-partitioning” solution in section 6.2.3.2 of TR38.832 v1.0.0. RAN3 will inform SA5 of any OAM requirements that may result from the work on Enhancements of RAN slicing.

Q1: Please provide your view on the LS.

| Company | Approach | Comment |
| --- | --- | --- |

### Response to SA2

An draft LS[6] was prepared for SA2,

RAN3 thanks SA2 for their reply LS on LS Enhancement of RAN Slicing. RAN3 has taken SA2’s evaluations into account and it has drawn the following conclusions with respect to solutions developed during the SI on Enhancements of RAN Slicing. The following solutions were concluded to be feasible after receiving SA2 and SA5 feedback: Configuration based Solution (section 6.2.3.1 of TR38.832) Slice resource re-partitioning (section 6.2.3.2 of TR38.832) Multi-carrier radio resource sharing (section 6.2.3.3 of TR38.832) RAN3 concluded that scenarios 2 and 4 in TR38.832 concern a situation of sub-optimal slice coverage planning, that can be resolved by slice coverage optimisation hence these scenarios should not be pursued in normative work. RAN3 concluded that the solutions addressing scenarios 2 and 4 are not deemed feasible due to their impact on CN and UE. Full conclusions and solutions details are captured in TR38.832

Q1: Please provide your view on the LS.

| Company | Approach | Comment |
| --- | --- | --- |

Based on majorities view,

Conclusion 1: Wait views input

## Any other stuff?

Please provide your view on the Proposal.

| Company | Yes/no/other view | Comment |
| --- | --- | --- |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-211452 Reply LS on feedback on RAN WG3 service continuity solutions (SA2)

R3-211469 Response to LS Reply LS on Enhancement of RAN Slicing (3GPP SA5)

R3-211633 Impact of SA5 feedback on Enhancement of RAN Slicing Slice Shortage solution  (Nokia, Nokia Shanghai Bell)

R3-212302 Discussion on Slice Resource Remapping solutions (Ericsson)

R3-212303 Response to LS Reply on Enhancement of RAN Slicing (Ericsson)

R3-212317 Reply LS on feedback on RAN WG3 service continuity solutions (Ericsson)

R3-211624 (TP for TR38.832) Revised evaluation and conclusions (Qualcomm Incorporated)

R3-211654 Down-selection of Solutions for Slice not supported at target  (Nokia, Nokia Shanghai Bell)

R3-211842 Discussion on Solutions Evaluation and Conclusions (CATT)

R3-211902 Final evaluation and conclusions of slicing service continuity (Huawei)

R3-212070 Conclusions on Enhancements for RAN Slicing (Ericsson)

R3-212402 Conclusion update on solutions for Scenarios 2 and 4 (LG Electronics Inc.)

R3-212501 Solution down-selection and conclusion for service continuity (CMCC)

R3-212574 Further consideration on RAN slicing (ZTE, China Telecom ,Lenovo, Motorola Mobility,China Unicom)

R3-212575 (TP for BL CR for TR 38.832) RAN Slicing (ZTE, China Telecom,Lenovo, Motorola Mobility,China Unicom)

R3-212420 Discussion on down-selection for RAN slicing enhancement (Samsung, ZTE)