3GPP TSG-RAN WG3 #112-e	draft-R3-212756

Online, 17th -27th May 2021

Agenda Item:	9.3.8.1

Source:	Ericsson (moderator)

Title:	Summary of Offline Discussion on CB: # 120_PDCPduplicationIssue

Document for:	Approval

# Introduction

CB: # 120_PDCPduplicationIssue

- no challenge to Rel-16 decisions (I hope)

- formulate a shared “problem statement”

- Seems consensus to address this in Rel-17

- Is this a (part of) IIoT enhancement WI or TEI17?

(E/// - moderator)

Summary of offline disc R3-212756

# For the Chairman’s Notes

RAN3 has agreed the blow:

TBD

# Discussion

Rel 16 NR-IIoT agreement:

RAN2 has specified the MAC CE handling that related to the PDCP duplication: The Duplication RLC Activation/Deactivation MAC CE is identified by a MAC subheader with eLCID as specified in Table 6.2.1-1b. It has a fixed size and consists of a single octet defined as follows (Figure 6.1.3.32-1). - DRB ID: This field indicates the identity of DRB for which the MAC CE applies. The length of the field is 5 bits; - RLCi: This field indicates the activation/deactivation status of PDCP duplication for the RLC entity i where i is ascending order of logical channel ID of secondary RLC entities in the order of MCG and SCG, for the DRB. The RLCi field is set to 1 to indicate that the PDCP duplication for the RLC entity i shall be activated. The RLCi field is set to 0 to indicate that the PDCP duplication for the RLC entity i shall be deactivated. Figure 6.1.3.32-1: Duplication RLC Activation/Deactivation MAC CE RAN3 concluded that the timing inter node coordination is not feasible, the inter node coordination for PDCP duplication is not feasible.

Issue:

In some configuration, the node using MAC CE may not be able to de/activate the cell (RLCi) reside in another Node correctly.

RAN3 Contributions:

Reference [1], [2], [3] are aiming to based on the Rel 16 NR-IIoT agreement, allow the MAC CE to be used.

Solution 1: PDCP entity indicate to the Node to use the MAC CE

Reference [4] is to rediscuss the inter-node coordination.

Solution 2: Introduce Assistance Information between Nodes via PDCP entity.

As way forward, companies are welcome to provide feedback on the following:

Question 1: The issue is in Rel 16, the Node may not be able to use MAC CE RLC de/activation correctly for NR-IIoT PDCP Duplication, do you agree?

| Company | Comment |
| --- | --- |
| Ericsson | Yes |
| Huawei | Yes and No. Note that the same thing exists for R15 packet duplication where there is no standard defined cooperation and seems workable. Here the wording “Correctly” may not fully reflect on the issue here. With the RAN3 conclusion above (no inter-node cooperation), this becomes (inter-)node blind operation or is left to node internal implementation, the same as R15. |

Question 2-1: Solution 1 does not challenge the Rel 16 decision, do you agree?

Question 2-2: Solution 1 can be discussed in Rel 16, do you agree?

| Company | Comment to Question 2-1 | Comment to Question 2-2 |
| --- | --- | --- |
| Ericsson | Yes | Yes. Solution 1 enables the node to be able to use the MAC CE in Rel 16. |
| Huawei | No. Solution 1 is regarded as signaling based solution requiring inter-node cooperation. | No. it can be further discussed in R17, and also this soltuion1 has RAN2 impact (Ran2 involvement is needed indeed) |

Question 3: Solution 2 challenges the Rel 16 decision, do you agree?

| Company | Comment |
| --- | --- |
| Ericsson | Yes. Refer to the Rel 16 agreements above. |
| Huawei | Yes. Solution 2 was discussed during R16, of course, this UP based solution requires inter-nodes to exchange assistance information. |

Question 4: If agreed to further discuss, should we discuss in TEI 17, or in Rel 17 NR-IIoT WID?

| Company | Comment |
| --- | --- |
| Ericsson | Prefer in TEI17. |
| Huawei | Prefer in TEI17. |

# Conclusion

TBD

# References

R3-211769	Handling PDCP Duplication (Ericsson, Intel Corporation)

R3-211770	Handling PDCP Duplication (Ericsson, Intel Corporation)

R3-211771	Handling PDCP Duplication (Ericsson, Intel Corporation)

R3-212550	Assistance information for UL duplication (Huawei, China Unicom)