3GPP TSG-RAN WG3 #114-e	R3-215931

Online, 01 – 11 Nov, 2021

Agenda Item:	14.1

Source:	Huawei (moderator)

Title:	Summary of Offline Discussion on ResetCorrec

Document for:	Approval

# Introduction

CB: # 103_ResetCorrec

- Clarify that e.g., PWS procedure is non-UE associated, does the configuration received for PWS should be removed during Reset all?

- Capture in Chair notes about the group common understandingothe

(HW - moderator)

Summary of offline disc R3-215931

# For the Chairman’s Notes

//to be added

# Discussion

The following observations are made in [1]:

- Observation 1: the F1AP/E1AP/W1AP: Reset procedure only resets the F1AP/E1AP/W1AP UE related contexts.

- Observation 2: the specifications say that the S1AP/NGAP: reset procedure initialise or re-initialise the E-UTRAN/RAN, X2AP/XnAP reset procedure reset the X2/Xn interface, and does not affect the application level configuration data exchanged during interface setup procedure or configuration update procedure.

- Observation 3: it is unclear if the S1AP/X2AP/ NGAP/XnAP Reset procedure resets the other non-UE-related context/signalling (i.e. CN overload status, Warning Message delivery, non-UE associated LPPA/NRPPA information, NR MBS broadcast info (R17), Periodic Resourcing Status Reporting.).

And during the online discussion it seems majority companies share the view that the Reset Procedure only impacts the UE related context/signaling.

Question 1: Do you agree that the S1AP/NGAP/X2AP/XnAP Reset procedure only impacts the UE related context/signaling?

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| one2many | Agree |  |

Question 2: whether the following context/signaling is reset during S1AP/NGAP/X2AP/XnAP Reset procedure or not?

Please fill the following table, especially if you do not agree with Question 1,

| Company | CN overload status | Warning Message Delivery | Non-UE associated LPPA/NRPPA | Periodic Resourcing Status Reporting | (R17) NR MBS broadcast |
| --- | --- | --- | --- | --- | --- |
| Huawei | Not reset | Not reset | Not reset | Not reset | Not reset |
| one2many |  | No Not reset |  |  |  |

In [2], it is proposed to update S1AP: Reset procedure description as below:

8.7.1 Reset 8.7.1.1 General The purpose of the Reset procedure is to initialise or re-initialise all or part of E-UTRAN S1AP UE-related contexts, in the event of a failure in the EPC or vice versa. This procedure does not affect the application level configuration data exchanged during, e.g., the S1 Setup procedure. The procedure uses non-UE associated signalling.

Question 3: do you agree to update S1AP: Reset procedure as above, any suggested wording?

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| one2many | Not agreed | A reset mechanism for PWS already exists: If the Cancel-All Warning Message Indicator is included in the PWS Cancel Request the gNB will cancel all ongoing broadcast in the area. Hence, no need to specify another reset mechanism. The proposed sentence: "This procedure does not affect the application level configuration data exchanged during, e.g., the S1 Setup procedure" does not capture this, because it is not configuration data. I'm not sure adding this sentence is helpful. |

In [4], it is proposed to update NGAP: NG Reset procedure description as below:

8.7.4 NG Reset 8.7.4.1 General The purpose of the NG Reset procedure is to initialise or re-initialise all or part of RAN NGAP UE-related contexts, in the event of a failure in the 5GC or vice versa. This procedure does not affect the application level configuration data exchanged during, e.g., the NG Setup procedure. The procedure uses non-UE associated signalling.

Question 4: do you agree to update NGAP: NG Reset procedure as above, any suggested wording?

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| one2many | Not agree | See comment for question 3. |

In [3], it is proposed to update X2AP: Reset procedure description as below:

8.3.4 Reset 8.3.4.1 General The purpose of the Reset procedure is to align the resources in eNB1 and eNB2, or the resources in eNB and en-gNB involved in the EN-DC in the event of an abnormal failure. The procedure resets all the UE related contexts over the X2 interface. This procedure doesn’t affect the application level configuration data exchanged during, e.g., the X2 Setup procedure, EN-DC X2 Setup procedure. The procedure uses non UE-associated signalling.

Question5: do you agree to update X2AP: Reset procedure as above, any suggested wording?

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Agree |  |

In [5], it is proposed to update XnAP: Reset procedure description as below:

8.4.4 Reset 8.4.4.1 General The purpose of the Reset procedure is to align the resources in the NG-RAN node1 and the NG-RAN node2 in the event of an abnormal failure. The procedure either resets all UE contexts or selected UE contexts. This procedure doesn’t affect the application level configuration data exchanged during, e.g., the Xn Setup procedure. The procedure uses non UE-associated signalling.

Question 6: do you agree to update XnAP: Reset procedure as below [5], any suggested wording?

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Agree |  |

Question 7: capture agreement made during this discussion into chairman notes.

//Second Round

# Conclusion, Recommendations [if needed]

If needed

# References

R3-215564 Clarification on the Reset procedure (Huawei, Orange)	Discussion

R3-215565 Clarification on Reset Procedure (Huawei, Orange)	CR1848r, TS 36.413 v16.7.0, Rel-16, Cat. F

R3-215566 Clarification on Reset Procedure (Huawei, Orange)	CR1644r, TS 36.423 v16.7.0, Rel-16, Cat. F

R3-215567 Clarification on Reset Procedure (Huawei, Orange)	CR0705r, TS 38.413 v16.7.0, Rel-16, Cat. F

R3-215568 Clarification on Reset Procedure (Huawei, Orange)	CR0707r, TS 38.423 v16.7.0, Rel-16, Cat. F