3GPP TSG-RAN WG3 #114-e	R3-215936

Online, 1  - 11 November 2021

Agenda Item:	9.3.6.1 Other Correction

Source:	NEC (moderator)

Title:	CB: # 105_ComNetwork_Instance

Document for:	Approval

# 1 Introduction

This was captured during the online session:

E///: The Common Network Instance is originated from Network Instance. Refer to TS23.501. Just transparency transmission, RAN3 does not need to care. NEC: The problem is the coding SS: It’s beneficial to have the reference to the OCTET STRING IE HW: Refer to TS29.244 instead of TS23.003 NEC: This IE needs to be awared by NG-RAN Nok: Check with CT4? If needed CB: # 105_ComNetwork_Instance - Check whether this IE is transparency towards NG-RAN？Check network instance as well? - Correct the reference spec？ (NEC - moderator) Summary of offline disc R3-215936

The deadline of first round of discussion is set to:  5/Nov (Fri)  11:59 UTC.

The deadline of second round  (if needed) of discussion is set to : 9/Nov (Tue) 11:59 UTC.

The R3-214937, R3-214938 and R3-214939 proposed the following (e.g. CR to 38/413):

9.3.1.120 Common Network Instance This IE provides the common network instance to be used by the NG-RAN node when selecting a particular transport network resource as described in TS 23.501 [9] in a format common with 5GC. IE/Group Name Presence Range IE type and reference Semantics description Common Network Instance M OCTET STRING Encoded as a Domain Name or an Access Point Name (APN) as per clause 9.1 of 3GPP TS 23.003[23] .

This offline discussion is trying to collect companies opinion for the received comments received during the online discussion.

# 2 For the Chairman’s Notes

TBD.

# 3 First Round of discussion (deadline is 5th Nov (Fri) 11:59 UTC)

## 3.1 discussion of the comments

### 3.1.1	Regarding the comment on Transparency of the Common Network Instance IE in NG-RAN node

It was commented that the Common Network Instance IE is transparent to the NG-RAN node, and that is defined as OCTET STRING.

Moderator understand that the NG-RAN node selects particular network resource identified by the  received Common Network Instance IE.  Furthermore, the Common Network Instance is passing over Xn interface for the target NG-RAN node to select network resource. Also same for E1 interface for the gNB-CU-UP to select network resource.  The NG-RAN node needs to interpret and understand how the Common Network Instance IE encoding (same as in 29.244 describes its encoding, as pointed out by one company during the online discussion).

Q1: Do you acknowledge the Moderator’s understanding that the Common Network Instance IE is not just simply transparent to NG-RAN node? If not, please provide your comment your understanding.

| Company | Yes/no | Comment |
| --- | --- | --- |

### 3.1.2	Regarding the comment on the Network Instance IE

It was asked to check also the Network Instance IE, which is defined as INTEGER (1..256) currently.

9.3.1.113 Network Instance This IE provides the network instance to be used by the NG-RAN node when selecting a particular transport network resource as described in TS 23.501 [9]. IE/Group Name Presence Range IE type and reference Semantics description Network Instance M INTEGER (1..256, …) .

It was commented that the 23.501 has description of the usage of Network Instance, the usage is same for the Common Network Instance IE.

The moderator understand that the usage of both Network Instance IE and Common Network Instance IE is the same.

Q2: Do you have same understanding that the usage of both Network Instance IE and Common Network Instance IE is the same? Please show if any more comment you want to express.

| Company | Yes/no | Comment |
| --- | --- | --- |

### 3.1.2	other

The moderator think further that, if anything will be added in the semantic description of the Common Network Instance IE, then the same will be needed also for Network Instance IE.

Q3: do you share the same understanding that, if need to have explanation in the Semantic Description, then the same apply to both Network Instance IE and Common Network Instance IE

| Company | Yes/no | Comment |
| --- | --- | --- |

## 3.2 The possible solutions

During the discussion, it is understood that there are several possible solutions.

Solution 1: as proposed in R3-214937, 4938, 4939.

| IE/Group Name | Presence | Range | IE type and reference | Semantics description |
| --- | --- | --- | --- | --- |
| Common Network Instance | M |  | OCTET STRING | Encoded as a Domain Name or an Access Point Name (APN) as per clause 9.1 of 3GPP TS 23.003[23] |

Solution 2: refer to 29.244 its encoding

| IE/Group Name | Presence | Range | IE type and reference | Semantics description |
| --- | --- | --- | --- | --- |
| Common Network Instance | M |  | OCTET STRING | Encoded as defined in Network Instance IE in 29.244 [xx] |

Solution 3: No need to add any more explanation

Solution 4: Other?

Q4: which solutions do you think is the most appropriate? if you have other solutions, please describe.

| Company | Which solution? | Comment |
| --- | --- | --- |

## 3.3 Summary of first round discussion

TBD

# 4 2nd round of discussion (if needed then deadline is 9th Nov (Tue) 11:59 UTC)

## 4.1

## 4.x Summary of first round discussion

# 5 Conclusion, Recommendations [if needed]

”

# 6 References

| R3-214937 | Adding reference for coding of Common Network Instance (NEC) | CR0671r, TS 38.413 v16.7.0, Rel-16, Cat. F |
| --- | --- | --- |
| R3-214938 | Adding reference for coding of Common Network Instance (NEC) | CR0677r, TS 38.423 v16.7.0, Rel-16, Cat. F ** |
| R3-214939 | Adding reference for coding of Common Network Instance (NEC) | CR0645r, TS 38.463 v16.7.0, Rel-16, Cat. F ** |