3GPP TSG-RAN WG3 #114-e	R3-215943

1 – 11 Nov 2021

Agenda Item:	9.3.6.1

Source:	Huawei (moderator)

Title:	Summary of Offline Discussion on NPN only cell

Document for:	Approval

# Introduction

CB: # 111_ULPDUSession

- Check group understanding on the directions

- Find the proper wording and update the figure

(HW - moderator)

Summary of offline disc R3-215944

# For the Chairman’s Notes

Propose to agree the following:

Proposal 1: TBD.

Proposal 1: TBD.

# Discussion – First round

At the beginning, below provides some background related to the NPN only cell and UE context retrieval procedure.

- NPN only cell

In TS 38.331, the NPN only cell is defined as follows.

NPN-only Cell: A cell that is only available for normal service for NPNs' subscriber. An NPN-capable UE determines that a cell is NPN-only Cell by detecting that the cellReservedForOtherUse IE is set to true while the npn-IdentityInfoList IE is present in CellAccessRelatedInfo.

As copied below in SIB1, the CellAccessRelatedInfo includes the plmn-IdentityInfoList, which is a mandatory IE. And it is clearly described that in case of NPN only cell, the plmn-IdentityInfoList shall only include one single element (including the PLMN Cell ID).

- ASN1START -- TAG-CELLACCESSRELATEDINFO-START CellAccessRelatedInfo ::= SEQUENCE { plmn-IdentityInfoList PLMN-IdentityInfoList, cellReservedForOtherUse ENUMERATED {true} OPTIONAL, -- Need R ..., [[ cellReservedForFutureUse-r16 ENUMERATED {true} OPTIONAL, -- Need R npn-IdentityInfoList-r16 NPN-IdentityInfoList-r16 OPTIONAL -- Need R ]] }

npn-IdentityInfoList <Skipped> In case of NPN-only cells the PLMN-IdentityList contains a single element that does not count to the limit of 12. The NPN index is defined as B+c1+c2+…+c(n-1)+d1+d2+…+d(m-1)+e(i) for the NPN identity included in the n-th entry of NPN-IdentityInfoList and in the m-th entry of npn-Identitylist within that NPN-IdentityInfoList entry, and the i-th entry of its corresponding NPN-Identity, where - B is the index used for the last PLMN in the PLMN-IdentittyInfoList; in NPN-only cells B is considered 0; <Skipped>

Observation: In case of NPN only cell, the PLMN-IdentityList contains a single element (including the PLMN cell ID) just for backwards compatibility purpose.

- Security key generation during UE context retrieval procedure

As described in R3-215160, in the RRC Resume procedure, the old NG-RAN node needs to calculate KNG-RAN* and include the result in the RETRIEVE UE CONTEXT RESPONSE message. According to clause A.11 of TS 33.501, KNG-RAN* is calculated based on the PCI and ARFCN of the target physical cell.

The target physical cell corresponds to the New Cell Identifier  IE in the RETRIEVE UE CONTEXT REQUEST message, which refers to the targetCellIdentity defined in TS 38.331.

| New Cell Identifier | M |  | NG-RAN Cell Identity 9.2.2.9 | RRC Resume: Corresponds to the targetCellIdentity within the VarResumeMAC-Input as specified in TS 38.331 [10] or the cellIdentity within the VarShortINACTIVE-MAC-Input as specified in TS 36.331 [14]. RRC Reestablishment: Corresponds to the targetCellIdentity within the VarShortMAC-Input as specified in TS 38.331 [10] or the cellIdentity within the VarShortMAC-Input as specified in TS 36.331 [14]. RRC Resume for UP CIoT Optimization: Corresponds to the cellIdentity within the VarShortResumeMAC-Input or VarShortResumeMAC-Input-NB as specified in TS 36.331 [14]. | YES | reject |
| --- | --- | --- | --- | --- | --- | --- |

In TS 38.331, it can be observed below that the targetCellIdentity corresponds to the first PLMN-Identity included in the PLMN-IdentityInfoList broadcasted in SIB1 of the target cell. That is, the targetCellIdentity is the first PLMN cell ID broadcast in SIB1.

– VarResumeMAC-Input The UE variable VarResumeMAC-Input specifies the input used to generate the resumeMAC-I during RRC Connection Resume procedure. VarResumeMAC-Input variable -- ASN1START -- TAG-VARRESUMEMAC-INPUT-START VarResumeMAC-Input ::= SEQUENCE { sourcePhysCellId PhysCellId, targetCellIdentity CellIdentity, source-c-RNTI RNTI-Value } -- TAG-VARRESUMEMAC-INPUT-STOP -- ASN1STOP VarResumeMAC-Input field descriptions targetCellIdentity An input variable used to calculate the resumeMAC-I. Set to the cellIdentity of the first PLMN-Identity included in the PLMN-IdentityInfoList broadcasted in SIB1 of the target cell i.e. the cell the UE is trying to resume. source-c-RNTI Set to C-RNTI that the UE had in the PCell it was connected to prior to suspension of the RRC connection. sourcePhysCellId Set to the physical cell identity of the PCell the UE was connected to prior to suspension of the RRC connection.

When the anchor RAN node receives the New Cell Identifier (corresponding to the first PLMN Cell ID) in the RETRIEVE UE CONTEXT REQUEST message, it shall check the Served Cell Information NR IE received of its neighbor NG-RAN exchanged during Xn setup/configuration update procedure, then acquire the PCI and ARFCN information. Finally the KNG-RAN* can be generated.

Observation: During the RETRIEVE UE CONTEXT procedure, upon the anchor NG-RAN node receives the New Cell Identifier (i.e. the first PLMN Cell ID), it can acquire the PCI and ARFCN information based on the first PLMN Cell ID, which are exchanged during the Xn setup/configuration update procedure.

Please provide any view / comments not clear below:

| Company | Comment |
| --- | --- |

## Problem description

The above procedure works well for non-NPN only cell, since during the Xn setup/configuration procedure, the first PLMN Cell ID will be exchanged.

However for NPN-only cell, the first PLMN cell ID (which is just for BC purpose as described above) may not be exchanged due to the following reasons.

First, in section 9.2.2.11 of TS 38.423, we have the following note under the Broadcast PLMN Identity Info List NR IE. The reason is that RAN2 has already specified that the PLMN-IdentityInfoList will not count to the limit of 12. While Broadcast PLMN Identity Info List NR IE only allows maximum of 12 element. This means the PLMN Cell ID will not be included in the Broadcast PLMN Identity Info List NR IE.

- “NOTE: In case of NPN-only cell, the PLMN Identities and associated information contained in the PLMN-IdentityInfoList IE are not included.”

Second, in TS 38.331, the broadcast of the first PLMN ID is just due to the BC purpose. And there is no any other usage. There is no reason to setup a PLMN Xn interface in case of NPN-only cell.

Take a step back, even if this PLMN Xn interface is setup, there may have some handover issues that the source node may handover a non-NPN UE to this NPN-only cell. The reason is that over Xn, so far there is no exchange of the “cellReservedForOtherUse”, thus the source node is not aware that the target node is a NPN-only.

Below provides one example:

Consider a NPN(CAG)-only cell which is shared by {PLMN A + CAG 1} and {PLMN B + CAG 2}. The SIB1 broadcast by this cell is shown below.

| SIB1 |
| --- |
| PCI | 1 |
| cellReservedForOtherUse | TRUE |
| plmn-IdentityInfoList | PLMN A, Cell 101 |
| npn-IdentityInfoList | PLMN A + CAG 1, Cell 102 PLMN B + CAG 2, Cell 103 |

In this example, it is reasonable that only two logical Xn interface (for NPN cell 102 and NPN cell 103 respectively) are setup while the PLMN cell (for cell 101) is not exchanged, as described above.

Then, since the PLMN cell (for cell 101) is not exchanged over Xn interface, the problem above may occur, i.e., the anchor node can not acquire the PCI/ARFCN from this PLMN Cell (cell 101).

Question 1: Do you think that the PLMN cell ID will not be exchanged over Xn interface in case of NPN-only cell case?

Please provide any view / comments on this topic and the question in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Yes, this PLMN cell ID in SIB1 is just for backwards compatibility purpose. There is no real need to exchange this PLMN cell ID over Xn interface, as analyzed above. |
| Qualcomm | We see two issues then: first the target cell ID is needed for the computation of the integrity protection, and second for the target key. But it seems that the network has an easy solution which is to set the dummy value to be the same as the first entry in the NPN list (and the anchor just uses that). It is not clear that the problem exists if this is done. [Huawei reply]. First, about the computation of the integrity protection (i.e. the resume MAC-I), there is no issue, since the UE will use the first entry (PLMN cell ID) of the new serving NG-RAN node for calculation, and the anchor NG-RAN node will use the PLMN cell ID in the RETRIEVE UE CONTEXT request for calculation. So the second issue is what we address here (to calculate the target key): How could the anchor NG-RAN node acquire the PCI and ARFCN information based on the first PLMN Cell ID to calculate the target key? The solution “dummy value to be the same as the first entry in the NPN list (and the anchor just uses that)” could work. But this seems an implementation solution (not defined in any specs), but not a standard one. We need a standardized solution to address the inter-operation issue. |
| Ericsson | if the proper setting of dummy values would not work, then it is probably rather an issue with the semantics. we do not agree on the necessity of the solution proposed by Huawei. So, either we agree on the approach outlined by QC or we need to tune the semantics. |

Question 2: If yes to Question 1, do you acknowledge this is an issue that we should consider?

Please provide any view / comments on this topic and the question in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Yes, we think this is an issue to address. And open to potential solutions. |
| Qualcomm | Please see above. |
| Ericsson | see above |

## Potential solutions (can be discussed if the issue is acknowledged first)

In R3-215160, it proposed to include the PCI and ARFCN associated with the New Cell Identifier in the RETRIEVE UE CONTEXT REQUEST message.

#### 9.2.3.aa	New Cell Identifier for Resume

This information element indicates additional information in case that the target cell is an NPN-only cell, as specified in TS 38.331 [10].

| IE/Group Name | Presence | Range | IE type and reference | Semantics description |
| --- | --- | --- | --- | --- |
| Target Cell PCI | M |  | NG-RAN Cell PCI 9.2.2.10 | The PCI accociated with the New Cell Identifier in case of RRC Resume. |
| ARFCN-DL | M |  | INTEGER (0.. maxNRARFCN) | The absolute frequency of SSB of the target PCell as specified in clause 13.3 of TS 38.300 [9]. |

| Range bound | Explanation |
| --- | --- |
| maxNRARFCN | Maximum value of NRARFCNs. Value is 3279165. |

Question 3: Your view of the solution or other potential solutions?

Please provide any view / comments on this topic and the question in bold below:

| Company | Comment |
| --- | --- |
| Qualcomm | This solution seems not to address the computation of the integrity protection. But as mentioned above, it seems that there is a simple configuration solution that addresses both potential issues. |

## Further aspects

Please add any further aspects that are in scope and were not included in the above:

| Company | Comment |
| --- | --- |

# Conclusion, Recommendations [if needed]

If needed

# References

| R3-215160 | Retrieve UE context for NPN only cell (Huawei, Deutsche Telekom, Orange) | CR0686r, TS 38.423 v16.7.0, Rel-16, Cat. F |
| --- | --- | --- |