3GPP TSG-RAN WG3 #114-e	R3-215819

Online, 01 – 11 Nov, 2021

Agenda Item:	8.3.1

Source:	Huawei (moderator)

Title:	Summary of Offline Discussion on InterMNHO_withoutSNChange

Document for:	Approval

# Introduction

CB: # 16_InterMNHO_withoutSNChange

- The usage of the SN UE X2/XnAP ID? Whether it can be interpreted by SN to retrieve the SCG configuration to provide delta configuration? Or introduce a new indicator in the SN ADDITION REQUEST message? Only using the RRC (sourceConfigSCG, scg-RB-Config) to decide delta configuration is already applied in other scenarios?

- Check group understanding and provide reply LS to RAN2

(HW - moderator)

Summary of offline disc R3-215819

RAN2 LS [1]:

For the inter-MN handover without SN change scenario, RAN2 discussed how MN can indicate whether SN should apply delta signalling or full configuration. For one of the options discussed, the signalling of the fields is as shown by the example below: Inter-MN HO without SN change (implies SN may provide delta configuration) SN UE X2/XnAP ID present sourceConfigSCG not present scg-RB-Config not present Inter-MN HO without SN change (implies SN must apply full configuration) SN UE X2/XnAP ID not present sourceConfigSCG not present scg-RB-Config not present RAN2 would like to ask RAN3 the following questions: Question 1: In the inter-MN handover without SN change scenario, is the SN UE X2/XnAP ID always required to be present when target MN sends SN Addition Request to SN? Question 2: For the same scenario, RAN2 would like to confirm with RAN3 if the receipt of SN UE X2/XnAP ID alone may be interpreted by SN to retrieve the SCG configuration to provide delta configuration?

# For the Chairman’s Notes

//to be added

# Discussion

## RAN2 Question 1

RAN2 Question 1: In the inter-MN handover without SN change scenario, is the SN UE X2/XnAP ID always required to be present when target MN sends SN Addition Request to SN?

The following replies could be found in the submitted papers:

| [R3-214760 ZTE] | No. In the inter-MN handover without SN change scenario, the SN UE X2/XnAP ID is not always required to be present. From RAN3 point of view, if the target MN decides to keep the source SN and the target MN allows the target SN to retrieve UE context stored in the source SN, the target MN will send UE X2/XnAP ID to SN. |
| --- | --- |
| [R3-214806 Nokia] | RAN3 understands the existing description in the TS 37.340 that the MN shall include the SN UE X2/XnAP ID when it wishes to enable the SN to identify the UE context. Therefore, it is not mandatory to include the ID always in this scenario. However, if the MN does not include the SN UE X2/XnAP ID, the SN has no mean to identify the existing UE context and must prepare the Addition anew. |
| [R3-214933 NEC] | Yes, In the inter-MN handover without SN change scenario, the SN UE X2/XnAP ID is always required to be present when target MN sends SN Addition Request to SN. |
| [R3-214991 Huawei] | In case the T-SN and S-SN are the same SN, the SN UE X2/XnAP ID may not be provided, and then the UE will be regarded as a new coming UE by the SN. |
| [R3-215048 CATT] | Yes. If the target MN decides to keep the SN, the target MN sends SN Addition Request to the SN including the SN UE X2/XnAP ID as a reference to the UE context in the SN. |
| [R3-215289 Ericsson] | Yes. |
| [R3-215511 Samsung] | In the inter-MN handover without SN change scenario, if the target MN decides the SN is kept, the SN UE X2/Xn AP ID is included. i.e. SN UE X2/XnAP ID is always required to be present in the inter-MN handover without SN change scenario. |

The answers from companies are quite different, two options can be found:

- Option 1: in case the source SN and the target SN are the same SN, the MN may decide to not provide SN UE X2/XnAP ID, and if the SN UE X2/XnAP ID is not included, the SN will treat the UE as a new coming UE.

- Option 2: in case the source SN and the target SN are the same SN, the MN has to provide SN UE X2/XnAP ID towards the SN.

From SN point of view, the things are quite clear, i.e. the presence/absence of SN UE X2/XnAP ID, will be understood by the SN as inter MN handover without/with SN change.

Question 1-1: Do you agree that: from SN point of view, in case the SN UE X2/XnAP ID is provided, it will be understood by the SN as inter MN handover without SN change, in case the SN UE X2/XnAP ID is not provided, it will be understood by the SN as inter MN handover with SN change.

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| ZTE | No | The SN can acknowledge that the UE context cannot be retrieved when this SN UE X2/XnAP ID is absent. |
| Samsung | Agree | From the stage 2 TS, if MN decides the UE context is kept, UE AP ID is included in Addition Request message. From SN point of view, from this IE, SN knows it is inter-MN without SN change. |

From the MN point of view, companies have different understanding on whether it is allowed for the MN to not provide SN UE X2/XnAP ID to the SN, in case the source SN and the target SN are the same SN.

There as two kinds of MN implementations:

- MN implementation 1: MN always provides SN UE X2/XnAP ID in such case.

- MN implementation 2: MN may not provide SN UE X2/XnAP ID in such case.

It is obviously that current different implementations are used by different companies, we need to answer whether these two kinds of implementations are allowed or not.

When we look at this question from interoperability view point, in case MN and SN come from different companies, and using different implementations, the following tables shows the results:

|  | MN | SN | In case the source SN and the target SN are the same SN |
| --- | --- | --- | --- |
| case 1 | Imp 1 | Imp 2 | The MN provides the SN UE X2/XnAP ID, the SN handles the procedure as without SN change. no issue found |
| case 2-1 | Imp 2 SN UE X2/XnAP ID included | Imp 1 | The MN provides the SN UE X2/XnAP ID, the SN handles the procedure as without SN change. no issue found |
| Case 2-2 | Imp 2 SN UE X2/XnAP ID not included | Imp 1 | The MN does not provide the SN UE X2/XnAP ID, the SN handles the procedure as with SN change, i.e. treat the UE as a new one. No issue found |

With this analyses, it is clearly that whichever the MN implementation is used, there is no interoperability issue, considering of the feedback from companies, both MN implementations current exists.

Note that normally the RAN3 specifications are written from the receiving node point of view, the current specifications (37.340 38.423 36.423) allow these two MN implementations.

Question 1-2: Do you agree that, for the two kinds of MN implementations, i.e. the MN always or may provide the SN UE X2/XnAP ID, there is no interoperability issue when these two implementations exist in the same network.

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| ZTE | Agree |  |
| Samsung | Not applicable | I think the condition to describe implementation is wrong, therefore, not sure the real difference between imp1 and imp2. It is clearly said in TS37.340, “during an Inter-Master Node handover, the target MN decides whether to keep or change the SN”. In case of source SN and target SN are the same physical node, but source SN doesn’t include UE AP ID in the HANDOVER RQUEST message, target MN can not do Imp1. That make imp1 is an impossible implementation. Companies have different descriptions from physical node point of view and from use case point of view. From physical node point of view, imp2 is correct. I think in stage 2, the description is from logical use case point of view. Inter-MN handover with SN unchanged in TS37.340 is not saying MN shall always provide UE AP ID if source SN and target SN are physically same node. But saying, if target MN decides to keep UE context in SN, target MN always include UE AP ID in Addition Request message. So if we change the condition using the wording in TS37.340 “in case MN decides the UE context is kept”, then only imp1 is aligning with TS37.340. This is exactly the question1 RAN2 asked. |

When we look into current specifications, it can be found that the 36423/38423 describes the IEs from receiving node point of view, there is no restriction on the two MN implementation:

X2AP spec:

If the SgNB UE X2AP ID IE is contained in the SGNB ADDITION REQUEST message, the en-gNB shall, if supported, store this information and use it as defined in TS 37.340 [32].

XnAP spec:

If the S-NG-RAN node UE XnAP ID IE is contained in the S-NODE ADDITION REQUEST message, the S-NG-RAN node shall, if supported, store this information and use it as defined in TS 37.340 [8].

For TS37.340, the with/without SN change is elaborated as whether the context at the SN is kept or moved, therefore in case the target SN and the source SN is the same RAN node, in case the MN do not want to keep using the context stored at the SN side, the specification allows the MN to not provide the SN UE X2/XnAP ID.

Question 1-3: Do you agree that there is no restriction on these two MN implementations in current specs?

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | agree |  |
| ZTE | agree |  |
| Samsung |  | As the answer to question 1-2. MN implementation 1 doesn’t reflect the case in TS37.340. The condition in specification is not source SN and target SN as same physical node. |

## RAN2 Question2

RAN2 Question 2: For the same scenario, RAN2 would like to confirm with RAN3 if the receipt of SN UE X2/XnAP ID alone may be interpreted by SN to retrieve the SCG configuration to provide delta configuration?

The following replies could be found in the submitted papers:

| [R3-214760 ZTE] | Yes/but. Upon reception of SN UE X2/XnAP ID included in the SN addition request message, the target SN knows that the SN is kept and can retrieve UE contexet as a reference. From RAN3 point of view, it is RAN2 issue that the target SN can provide delta config based on either the receipt of SN UE X2/XnAP ID or the presence of sourceConfigSCG and scg-RB-Config. |
| --- | --- |
| [R3-214806 Nokia] | RAN3 understands the existing description in the TS 37.340 that purpose of the SN UE X2/XnAP ID, if included in the Addition, is to enable the SN to find the existing UE context and thus the SCG configuration. Also, the MN is obliged to provide the SCG configuration separately only if the SN changes. Therefore, the SN may use the SN UE X2/XnAP ID alone to prepare the delta configuration. |
| [R3-214933 NEC] | The presence of SN UE X2/XnAP ID indicates the request is for inter-MN HO without SN change. For the delta configuration decision, RAN3 basic understandings is that, the SN should use the RRC IEs (souceConfigSCG, scg-RB-Config). However, RAN3 understands it is RAN2 scope how the SN UE X2/XnAP ID is used alone or together with other RRC IEs (sourceConfigSCG, scg-RB-Config) to apply delta configuration. |
| [R3-214991 Huawei] | Yes. |
| [R3-215048 CATT] | No. As long as the SN UE X2/XnAP ID is received, the SN can retrieve the whole set of UE context locally stored in it (maybe including the SCG RRC configuration), but its presence should not be interpreted as that RRC delta configuration is allowed. |
| [R3-215289 Ericsson] | It could be for the SN to apply delta configuration upon receipt of SN UE X2/XnAP ID alone, though it is unclear about the differentiation of full or delta configuration from the MN. Thus RAN3 agreed to introduce a new indicator in the SN ADDITION REQUEST message for this purpose. |
| [R3-215511 Samsung] | If SN receives SN UE X2/XnAP ID, the SN uses it as the reference to the UE context. SN configures delta configuration or full configuration based on the information included in the MN to SN RRC container. |

From our understanding, in case the MN does not provide enough information (no SN UE X2/XnAP ID, no RRC containers), SN has to use full configuration. But if the SN UE X2/XnAP ID and/or the RRC containers are received by the SN, the SN will have enough information to perform delta configuration.

In current specifications, there is no description about the MN control of full or delta SCG configuration in case SN have enough information to perform delta configuration, therefore in such case it will up to the SN to make the decision on whether to sue full or delta configuration.

Question 2-1: do you agree that: upon receiving the SN UE X2/XnAP ID, the SN will be able to find the stored UE context including the SCG configuration, in such case the SN will have enough information to perform delta configuration.

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| ZTE | Partial agree | The SN can do as TS37.340, as a reference to the UE context in the SN. Whether the SN can perform delta/full configuration seems fine but it is RAN2 issue. |
| Samsung | Partial agree | From RAN3 point of view, this reference is to the UE context. How to do delta/full is defined by RAN2. This IE originally is not used for delta/full configuration intension. |

Question 2-2: do you agree that: In case the SN finds the UE context by using SN UE X2/XnAP ID, in current specification, there is no description about the MN control of full or delta SCG configuration, and therefore it is up to the SN to make the decision on whether to use full or delta configuration.

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| ZTE | Agree |  |
| Samsung | Partial agree | For normal cases, MN can indicate its control of full or delta and SN can make its own decision. For this case, agree there is no such control based on existing RAN2 specification. Without the control, there is problem to let SN decides full or delta. The SN may decide a configuration not aligning with MN. E.g. MN can do full only, but SN decides a delta. |

## RAN3 answers to RAN2 questions

To be discussed in Second Round

| Company | Comment |
| --- | --- |

## TS 37.340 changes

To be discussed in Second Round

| Company | Comment |
| --- | --- |

## TS 38.423 changes

To be discussed in Second Round

| Company | Comment |
| --- | --- |

# Conclusion, Recommendations [if needed]

If needed

# References

R2-2106682 LS on inter-MN handover without SN change, Source: RAN2, To: RAN3

R3-214757 Discussion on inter-MN handover without SN change (ZTE)	discussion

R3-214758 Clarification on inter-MN handover without SN change in Rel-15 (ZTE)	draftCR

R3-214759 Clarification on inter-MN handover without SN change in Rel-16 (ZTE)	draftCR

R3-214760 [DRAFT] Reply LS on inter-MN handover without SN change (ZTE)	LS out To: RAN2 CC:

R3-214803 Indication for full or delta configuration in case of a HO without SN change (Nokia, Nokia Shanghai Bell)	discussion

R3-214804 Clarification of the RRC config preparation in case of a HO without SN change (Nokia, Nokia Shanghai Bell)	draftCR

R3-214805 Clarification of the RRC config preparation in case of a HO without SN change (Nokia, Nokia Shanghai Bell)	draftCR

R3-214806 Response LS on inter-MN handover without SN change (Nokia, Nokia Shanghai Bell)	LS out To: RAN2 CC:

R3-214933 Inter MN handover without SN change and proposed draft response LS (NEC)	discussion

R3-214988 Consideration on inter-MN handover without SN change (Huawei)	discussion

R3-214989 Clarification on delta or full RRC configuration in inter-MN handover without SN change (Huawei)	draftCR

R3-214990 Clarification on delta or full RRC configuration in inter-MN handover without SN change (Huawei)	draftCR

R3-214991 [DRAFT] LS on inter-MN handover without SN change (Huawei)	LS out To: RAN2 CC:

R3-215047 Discussion on the issue raised in the LS R2-2106682 (CATT)	discussion

R3-215048 [Draft] Reply LS on inter-MN handover without SN change (CATT)	LS out To: RAN2 CC:

R3-215288 RRC configuration during inter-MN handover without SN change (Ericsson)	discussion

R3-215289 [DRAFT] Reply LS on inter-MN handover without SN change (Ericsson)	LS out To: RAN2 CC:

R3-215290 Introducing RRC configuration indicator during inter-MN handover without SN change (Ericsson)	CR1615r1, TS 36.423 v15.11.0, Rel-15, Cat. F

R3-215291 Introducing RRC configuration indicator during inter-MN handover without SN change (Ericsson)	CR1616r1, TS 36.423 v16.7.0, Rel-16, Cat. A

R3-215292 Introducing RRC configuration indicator during inter-MN handover without SN change (Ericsson)	CR0654r1, TS 38.423 v15.13.0, Rel-15, Cat. F

R3-215293 Introducing RRC configuration indicator during inter-MN handover without SN change (Ericsson)	CR0655r1, TS 38.423 v16.7.0, Rel-16, Cat. A

R3-215510 Discussion on the Inter-MN HO without SN change (Samsung)	discussion

R3-215511 [Draft] Reply LS on inter-MN handover without SN change (Samsung)	LS out To: RAN2 CC: