3GPP TSG-RAN WG3 #114	R3-215831

1 - 11 Nov 2021

Online

Agenda Item:	9.3.6.1

Source:	Samsung - Moderator

Title:	Summary of Offline Discussion – F1-U Delay Measurement

Document for:	Approval

# Introduction

This is the summary document for the following come back:

CB: # 28_F1-Udelay

- Prefer solution 3 (use dedicated polling and add NR-U SN in DDDS), and solution 2 (add NR-U SN in DDDS) is also acceptable?

- Provide CR if agreeable

(Samsung - moderator)

Summary of offline disc R3-215831

Two phases of this email discussion:

- Phase 1 Deadline: 12:00AM UTC, 5th Nov.

- Phase 2 Deadline: 12:00AM UTC, 9thNov. Try to have an agreeable CR in the 2nd phase discussion.

# For the Chairman’s Notes

Propose the following:

Agree CR ….

# Discussion

Polling function and DDDS reporting can be used for F1-U delay measurement. So F1-U delay is (T4-T1)/2, where the inner DU feedback delay is negligible.

There are three candidate solutions:

- Solution 1: Reuse current polling function and DDDS reporting. No update is needed.

- Solution 2: Based on current polling function and DDDS reporting, add NR-U sequence number in DDDS.

- Solution 3: Use a dedicated polling function, and enhance DDDS reporting by adding NR-U sequence number. When the received dedicated polling equals to 1, DU feeds back the DDDS with NR-U sequence number immediately for F1-U delay measurement.

Solution 1 is the simplest one. But it may lead to wrong measurement when DU sends one DDDS before receiving the DL User Data with polling from CU-UP.

Solution 2 allows CU-UP to correctly identify which DL USER DATA with polling is the one that it should calculate F1-U delay. But adding NR-U SN in every polling-triggered DDDS may produce back-compatible problem and heavy overhead.

Solution 3 leads to high accurate and efficient measurement. The dedicated polling function informs DU that the polling is for F1-U delay measurement so that DU need to do the quick feedback to guarantee the negligible inner DU feedback delay. And DU adds NR-U SN in DDDS only when the received dedicated polling flag equals one, which makes the DDDS reporting more efficient.

Q1-1: Companies are invited to provide their views on above three solutions, which solution is preferred.

| Company | Preferred Solution 1, Solution 2 or Solution 3 | Comment |
| --- | --- | --- |
| Intel Corporation | Solution 2 or Solution 3 | It is clear that the current polling function (Solution 1) cannot meet the SA5 requirement of taking the feedback delay time into account when measuring F1-U delay. Either Solution 2 or Solution 3 should be introduced to make it supported. But we also agree with the moderator's analysis on Solution 2 that adding NR-U SN in every polling-triggered DDDS may incur heavy overhead. Or, if "immediate DDDS trigger" is a burden to implementation, we can consider Solution 3 variant that uses a dedicated polling, but reports feedback delay time in DDDS so that DU doesn't have to immediately trigger DDDS. |

Q1-2: If preferring any other solution, please provide here.

| Company | Comment |
| --- | --- |
| Intel Corporation | Please see the above for Solution 3 variant that does not have to mandate DU to trigger DDDS immediately and does not have the overload problem of Solution 2. If "immediate DDDS" is a serious burden to implementation, we can consider this Solution 3 variant. |

Moderator’s summary:

Majority of companies think …

Proposal 1: CR...

# Conclusion

The following is proposed:

Proposal 1: CR...

# References

R3-215559, Discussion on F1-U Delay Measurement for QoS Monitoring, Samsung, Verizon Wireless

R3-215560, Correction of F1-U delay measurement for QoS monitoring, CR0132r TS 38.425, Samsung, Verizon Wireless